## Slide 1: Lifting & Handling features
Erik NIlsson
Mechanical Engineer
ESS Chopper Group
www.europeanspallationsource.se
8 May, 2018

## Slide 2: Single point lifting
One point lifting – in combination with guide rods/rollers
  Simple engagement and disengagement
  Lack of height
Lifting eyes are left in place during operation
Visibility
  Ensure that the lift point is visible to the remote handling operator during hook engagement and disengagement.
Dimensioned for abnormal lifts (SF>5)
Approved components
  CODIPRO/Gradup DSR (M14 or larger) – Primary choice
  RUD VLBG (M18 or larger) – Secondary choice
CODIPRO DSR
RUD VLBG

## Slide 3: Adjustable lifting eye
Adjustable in x-direction (along the beam).
Compensate for COG alterations due to caused by cables and utilities.
Stabilize lift to minimize the risk of damaging equipment.
Example

## Slide 4: Current Hook assumption
Automatic lifting Hook
  One 5 ton lifting Hook
  One 20 ton lifting Hook

## Slide 5: Multiple point lifting
Tests performed
  Successful
  Not preferable
Specialized tool required
Approved components
  Use DIN580 or DIN582
  M20 or larger
  Material C-15 (1.1141)

## Slide 6: Lifting adapters
For some components integrated lifting adapters might be required