ESS LLRF RAMI Analysis
Jarosław Szewiński
April 25.04.2018
ESS LLRF Critical Design Review, Lund

---
Agenda
Layout of the equipment
Subsystems
Safety and RAMI requirements
Means of the transportation of the equipment to the facility
Acceptance test
Most frequent failures
Catastrophic events
Conventional hazards
Scheduled maintenance
 /
Jarosław Szewiński, ESS LLRF CDR, 25.04.2018, Lund

---
Layout of the equipment
LLRF Systems will be implemented in the MTCA.4 form factor standards, where single LLRF unit supporting one RF feedback loop (amplifiers, cavity, etc.), will be implemented using one MTCA.4 crate.

---
Subsystems
Single LLRF unit will be made of following components:
- MTCA.4 chassis
- Power supply
- Fans
- MCH – MicroTCA Connection Hub, the core crate management unit
- CPU board
- Timing board
- FPGA & ADC board
- DWC/VM board
- Piezo external power supply
- RTM Carrier AMC board (designed by PEG)
- LO RTM board (designed by PEG)
- Piezo driver RTM board (designed by PEG)

---
SAFETY AND RAMI REQUIREMENTS
Applicable regulations and standards
This will be discussed during Quality presentation
Radiation safety analysis
Described system will not generate any radiation by itself, and will not be exposed to ionizing radiation.

---
LO RTM Internal failure
- Probability: unlikely
- Caused by: internal
- Affects: Down-converters of 4 RF sections will not operate, resulting in LLRF system failure

---
LO RTM external failure
- Probability: depends on reliability of the external systems
- Caused by:
  - RTM Carrier failure
  - FPGA code error / software error / wrong parameters
  - Improper power level on one of the RF inputs
- Affects: Down-converters of 4 RF sections will not operate, resulting in LLRF system failure

---
Piezo RTM Internal failure
- Probability: unlikely
- Caused by: internally
- Affects:
  - Selected cavity may become detuned
  - piezo stack may become damaged

---
Piezo RTM external failure
- Probability: depends on reliability of the external systems
- Caused by:
  - RTM Carrier failure
  - FPGA code error / software error / wrong parameters
  - External power supply failure
  - Improper power level on the one of the inputs (in piezo sensor mode)
- Affects:
  - Selected cavity may become detuned
  - piezo stack may become damaged

---
RTM Carrier #1 (LO RTM)
Internal failure
- Probability: unlikely
- Caused by: internally
- Affects: LO Generation for given RF section (LO RTM external failure)
  - Communication with LO RTM lost in the best case
  - LO RTM damaged in the worst case

---
RTM Carrier #1 (LO RTM)
External failure
- Probability: depends on reliability of the external systems
- Caused by: MTCA components (power supply, etc.)
- Affects: LO Generation for given RF section (LO RTM external failure)
  - Communication with LO RTM lost in the best case
  - LO RTM damaged in the worst case

---
RTM Carrier #2 (Piezo RTM)
Internal failure
- Probability: unlikely
- Caused by: internally
- Affects: Piezo resonance control for given cavity (Piezo RTM external failure)
  - Communication lost with the Piezo RTM in the best case
  - Piezo RTM damaged (and possibly the stack) in the worst case

---
RTM Carrier #2 (Piezo RTM)
External failure
- Probability: depends on reliability of the external systems
- Caused by: MTCA components (power supply, etc.)
- Affects: Piezo resonance control for given cavity (Piezo RTM external failure)
  - Communication lost with the Piezo RTM in the best case
  - Piezo RTM damaged (and possibly the stack) in the worst case

---
Means of transportation of the equipment to the facility
Each LLRF system (one MTCA.4 chassis) will be packed into a single box, which should not weight more than 25 Kg, therefore no special equipment Is required for handling.

---
Acceptance test
Upon delivery of the LLRF systems, which was assembled and tested in Poland, commissioning at ESS site is needed. Foreseen procedure for commissioning is following:
After delivery and installation of the LLRF systems, which were assembled and tested in Poland, commissioning at the ESS site will be performed. Procedure for commissioning will be following:
- Visual inspection, if there are no problems caused by the transportation.
- Installation in the rack, connection of the cavity simulator
- MTCA.4 crate power-on
- Confirm proper operation of the MTCA components (MCH, CPU, power supplies and fans)
- Close the feedback and check the performance with Cavity Simulator
- Power-down the crate
- Re-attach the signals from the cavity simulator to the machine
Detailed acceptance test procedure will be agreed with the ESS before shipment.

---
Conventional hazards
In case of piezo cable damage, there is risk of electrical shock, due to output voltage of +/- 100V.

---
The End
Thank You for Your Attention !