## Slide 1: IRR for Ion Source Safety Fence - Introduction
Øystein Midttun
Ion source and LEBT system leader
www.europeanspallationsource.se
3 April 2018

## Slide 2: The ESS proton source is a microwave discharge ion source
2
Waveguide
Solenoid magnets
Plasma chamber
H2 gas injection
High voltage insulator
Extraction aperture
Extraction electrodes
Pumping ports
50 cm

## Slide 3: The plasma generator sits inside a high voltage platform

## Slide 4: Ion source at high voltage and low energy beam transport at ground potential

## Slide 5: We have designed a safety fence with two main functions
1: protect against the 75 kV of the high voltage platform
75 kV

## Slide 6: We have designed a safety fence with two main functions
2: protect against x-ray coming from the ion source when HV is on
fig 5
Report: PS-ESS radioprotection report 30.03.17, ESS-0114736
Normal operation:
< 15 µSv/h
Maximum observed:
380 µSv/h
Radiation level below
natural background
Measured dose rate levels
above natural background
Measurements at ion source test stand, INFN-LNS
2 mm lead shielding around the ion source

## Slide 7: Our goal is to safely run the ion source while there is access to the accelerator tunnel
Ion source commissioning can take place at the same time as installation (of other stuff)
No access control to the tunnel needed
PSS0 will ensure that there no one can approach the HV platform while it’s on
By lead shielding the HV safety fence, the area outside can be classified as a public radiation zone

## Slide 8: 3D model of high voltage safety fence
Floor-to-ceiling walls
2.5 m high, 2 mm thick
lead shielding
1 m high stainless steel mesh (2 mm spacing, IP3x)
Cooling water inlet
for the ion source
Additional lead shielding
around the LEBT

## Slide 9: 3D model of high voltage safety fence
Safety door
PSS0
Isolated 400 VAC
Fibre optic control cables

## Slide 10: Top view of high voltage safety fence
Entrance
Connection to grounding
mesh in the floor
Ion source
water cooling
Grounding system is not updated; we will connect
to one point in the grounding mesh of the tunnel floor

## Slide 11: Ion Source and fence designed for it
Description of the HV protection cage: ESS-0122281