## Slide 1: Tap Point story
Mateusz Żukociński
CDR meeting
Lund, 27.04.2018
Notes: Hello everyone! My name is Tomasz Leśniak. I am working

## Slide 2: PRL RF system concept

## Slide 3: PRL RF system concept
Tap Point

## Slide 4: PRL RF system concept
Basic functionality of Tap Point:
RF signal end distribution & filtering
multichannel RF output module for reference signal selection

## Slide 5: PRL RF system concept
Tap Point from system point of view:
local node for RF and temperature control system interconnection
thermal boundary conditioning
cabling and maintenance node

## Slide 6: PRL layout

## Slide 7: PRL layout

## Slide 8: PRL layout
2 x versions of Tap Points:
          3-way Tap Point
          6-way Tap Point
many output configurations (requires modular design)

## Slide 9: Tap Point requirements
Total number of Tap Points | x 58
Two frequency Tap Points | x 30
Single frequency Tap Points | x 28 (14 x 352 MHz & 14 x 704 MHz)
6-way Tap Points | x 36
3-way Tap Points | x 22
Total input power | ~+30 dBm (+27 dBm @ 352 MHz and +27 dBm @ 704 MHz) (with option to increase by 2-3 dB total depending on MO amplifier and final power budged of the PRL => up tp 33 dBm total)
Output power | ~+16 dBm @ 352 MHz and 704 MHz * (* providing as much power as possible (+16 dBm minimum) )
Unwanted signal suppression | > 60 dBc between 352 MHz and 704 MHz at each output

## Slide 10: Tap Point configuration list
PRLTAP-056 | 0 | 1 | 0 | 1 | 0 |  | 1 | 1 |  | 1 | 3-way
PRLTAP-057 | 0 | 1 | 0 | 1 | 0 |  | 1 | 1 |  | 1 | 3-way
PRLTAP-058 | 0 | 2 | 0 | 2 | 0 |  | 1 | 1 |  | 2 | 3-way
total | 155 | 49 | 4 | 70 | 138 | 30 | 28 | 14 | 14 | 208 | 
Tap Points | LLRF outputs | BPM outputs | LBM outputs | # 352MHz outputs | # 704MHz outputs | 2 x freq. | 1 x freq. | only 352MHz | only 704MHz | # total outputs used | version
PRLTAP-001 | 3 | 2 | 0 | 3 | 2 | 1 |  |  |  | 5 | 6-way
PRLTAP-002 | 1 | 2 | 1 | 2 | 2 | 1 |  |  |  | 4 | 6-way
PRLTAP-003 | 1 | 3 | 0 | 1 | 3 | 1 |  |  |  | 4 | 6-way
PRLTAP-004 | 1 | 1 | 0 | 1 | 1 | 1 |  |  |  | 2 | 3-way
PRLTAP-005 | 1 | 1 | 0 | 1 | 1 | 1 |  |  |  | 2 | 3-way
PRLTAP-006 | 1 | 1 | 0 | 1 | 1 | 1 |  |  |  | 2 | 3-way
PRLTAP-007 | 1 | 1 | 0 | 1 | 1 | 1 |  |  |  | 2 | 3-way
PRLTAP-008 | 0 | 1 | 1 | 1 | 1 | 1 |  |  |  | 2 | 3-way
PRLTAP-009 | 4 | 1 | 0 | 4 | 1 | 1 |  |  |  | 5 | 6-way
PRLTAP-010 | 4 | 1 | 0 | 4 | 1 | 1 |  |  |  | 5 | 6-way
PRLTAP-011 | 4 | 1 | 0 | 4 | 1 | 1 |  |  |  | 5 | 6-way
PRLTAP-012 | 4 | 1 | 0 | 4 | 1 | 1 |  |  |  | 5 | 6-way
PRLTAP-013 | 4 | 1 | 0 | 4 | 1 | 1 |  |  |  | 5 | 6-way
PRLTAP-014 | 4 | 1 | 0 | 4 | 1 | 1 |  |  |  | 5 | 6-way
PRLTAP-015 | 2 | 0 | 1 | 3 | 0 |  | 1 | 1 |  | 3 | 3-way
PRLTAP-016 | 4 | 1 | 0 | 1 | 4 | 1 |  |  |  | 5 | 6-way
PRLTAP-017 | 4 | 0 | 0 | 0 | 4 |  | 1 |  | 1 | 4 | 6-way
PRLTAP-018 | 4 | 1 | 0 | 1 | 4 | 1 |  |  |  | 5 | 6-way
PRLTAP-019 | 4 | 0 | 0 | 0 | 4 |  | 1 |  | 1 | 4 | 6-way

## Slide 11: Tap Point configuration list
PRLTAP-056 | 0 | 1 | 0 | 1 | 0 |  | 1 | 1 |  | 1 | 3-way
PRLTAP-057 | 0 | 1 | 0 | 1 | 0 |  | 1 | 1 |  | 1 | 3-way
PRLTAP-058 | 0 | 2 | 0 | 2 | 0 |  | 1 | 1 |  | 2 | 3-way
total | 155 | 49 | 4 | 70 | 138 | 30 | 28 | 14 | 14 | 208 | 
Tap Points | LLRF outputs | BPM outputs | LBM outputs | # 352MHz outputs | # 704MHz outputs | 2 x freq. | 1 x freq. | only 352MHz | only 704MHz | # total outputs used | version
PRLTAP-001 | 3 | 2 | 0 | 3 | 2 | 1 |  |  |  | 5 | 6-way
PRLTAP-002 | 1 | 2 | 1 | 2 | 2 | 1 |  |  |  | 4 | 6-way
PRLTAP-003 | 1 | 3 | 0 | 1 | 3 | 1 |  |  |  | 4 | 6-way
PRLTAP-004 | 1 | 1 | 0 | 1 | 1 | 1 |  |  |  | 2 | 3-way
PRLTAP-005 | 1 | 1 | 0 | 1 | 1 | 1 |  |  |  | 2 | 3-way
PRLTAP-006 | 1 | 1 | 0 | 1 | 1 | 1 |  |  |  | 2 | 3-way
PRLTAP-007 | 1 | 1 | 0 | 1 | 1 | 1 |  |  |  | 2 | 3-way
PRLTAP-008 | 0 | 1 | 1 | 1 | 1 | 1 |  |  |  | 2 | 3-way
PRLTAP-009 | 4 | 1 | 0 | 4 | 1 | 1 |  |  |  | 5 | 6-way
PRLTAP-010 | 4 | 1 | 0 | 4 | 1 | 1 |  |  |  | 5 | 6-way
PRLTAP-011 | 4 | 1 | 0 | 4 | 1 | 1 |  |  |  | 5 | 6-way
PRLTAP-012 | 4 | 1 | 0 | 4 | 1 | 1 |  |  |  | 5 | 6-way
PRLTAP-013 | 4 | 1 | 0 | 4 | 1 | 1 |  |  |  | 5 | 6-way
PRLTAP-014 | 4 | 1 | 0 | 4 | 1 | 1 |  |  |  | 5 | 6-way
PRLTAP-015 | 2 | 0 | 1 | 3 | 0 |  | 1 | 1 |  | 3 | 3-way
PRLTAP-016 | 4 | 1 | 0 | 1 | 4 | 1 |  |  |  | 5 | 6-way
PRLTAP-017 | 4 | 0 | 0 | 0 | 4 |  | 1 |  | 1 | 4 | 6-way
PRLTAP-018 | 4 | 1 | 0 | 1 | 4 | 1 |  |  |  | 5 | 6-way
PRLTAP-019 | 4 | 0 | 0 | 0 | 4 |  | 1 |  | 1 | 4 | 6-way
352 MHz outputs | 70
704 MHz outputs | 138
Test/spare outputs | 88
TOTAL 296 | 

## Slide 12: Tap Point mechanical design

## Slide 13: Tap Point mechanical design
RF performance
temperature stability -> heat transfers
space limitations
mechanical restrictions
ergonomics (assembly + cabling)
assembling & servicing
Not only RF !!

## Slide 14: Tap Point 3D implementation
Insulated Rigid line
Tap Points
Coupler

## Slide 15: Tap Point 3D implementation
PE or PP
foam insulation
directional
coupler
RF Split Box
(ex tap point)
mounting plate
cables to Stubs
jumper cable

## Slide 16: Tap Point 3D implementation
mounting plate
RF Split Box
(ex tap point)
Junction Box
(temperature control)
heating mat
thermal insulation

## Slide 17: Tap Point -> mounting plate
Mounting plate:
aluminium plate 3 mm thick
plate bended to keep symmetry
(center of gravity)
cutouts in the plate to minimize heat transfer

## Slide 18: Tap Point -> Junction Box
Junction Box functionality:
  combining Temperature CTRL cables in one place
  modularity of design
  ease of connecting/cabling & servicing

## Slide 19: Tap Point -> Junction Box
Junction Box functionality:
  combining Temperature CTRL cables in one place
  modularity of design
  ease of connecting/cabling & servicing
=> presentation by Radek Papis
dielectric pad => isolation of signal ground

## Slide 20: Tap Point -> PRL Split Box
RF Distribution Module functionality:
  spliting & filtering phase ref. signals
  minimize temp. drifts due to heat leak through RF cables -> separate temp. control loop
  ease of assembly
  ease of connecting/cabling & servicing

## Slide 21: Tap Point -> PRL Split Box
Internal structure:
  2 versions of RF Distribution Module
  - 6-way power splitter (30 pcs)
  - 3-way power splitter (28 pcs)
  diplexer in the input to select reference frequency
  hermetic metal enclosure
Design approach:
  PCB based solution (FR408 epoxy based laminate)
  COTS components
  modularity
Notes: is going to be realized as development

## Slide 22: Tap Point -> PRL Split Box - concept
Tap point with “diplexer + power dividers”
6-way Split Box
(“4+2” configuration)
3-way Split Box
(“2+1” configuration)

## Slide 23: Tap Point -> PRL Split Box - concept
Insertion Loss < 2 dB
Return Loss > 28 dB
signal separation ~70 dB
Diplexer itself

## Slide 24: Tap Point -> PRL Split Box - concept
8-way Tap Point
Insertion Loss < 10 dB
Return Loss > 17 dB
signal separation ~70 dB

## Slide 25: Tap Point -> PRL Split Box - concept
Meeting on 29.11.2017 (attendees: Anders Svenson, Stephen Molloy, Rihua Zeng, Mateusz Zukocinski)
do we need spare/test output with both frequencies (not filtered output)? → it is not necessary, we do not need spare/test outputs with both frequencies
shall we provide equal power to all Tap Point outputs (~+16 dBm) or shall we provide as much power as possible (e.g. +16…+19 dBm depending on configuration) – the second scenario (provide as much power as possible) seems to be better in terms of system power budget vs noise performance of reference signals receivers: DWC, VM, LOGM but may cause trouble if some modules are build only for specific fixed input power, e.g. Split Box??) → providing as much power as possible (+16 dBm minimum) is recommended – front-end circuits at BPM and LLRF cards have adjustable attenuators to level reference signal power
6-way Tap Point with diplexer
(equal output power)
6-way Tap Point with diplexer
(unequal output power)

## Slide 26: Tap Point -> PRL Split Box - concept
Meeting on 29.11.2017 (attendees: Anders Svenson, Stephen Molloy, Rihua Zeng, Mateusz Zukocinski)
do we need spare/test output with both frequencies (not filtered output)? → it is not necessary, we do not need spare/test outputs with both frequencies
shall we provide equal power to all Tap Point outputs (~+16 dBm) or shall we provide as much power as possible (e.g. +16…+19 dBm depending on configuration) – the second scenario (provide as much power as possible) seems to be better in terms of system power budget vs noise performance of reference signals receivers: DWC, VM, LOGM but may cause trouble if some modules are build only for specific fixed input power, e.g. Split Box??) → providing as much power as possible (+16 dBm minimum) is recommended – front-end circuits at BPM and LLRF cards have adjustable attenuators to level reference signal power
6-way Tap Point with diplexer
(equal output power)
6-way Tap Point with diplexer
(unequal output power)

## Slide 27: Tap Point -> PRL Split Box - design
Component | Model | Manufacturer
2-way power divider | JPS-2-900+ | Minicircuits
LPF filter - reflective | 0400LP15A0122 | Johanson
HPF filter - reflective | HFCN-440+ | Minicircuits
SMD components used to buid Tap Point PCB modules
Diplexer design
Circuit modeling/simulation
Electromagnetic modeling/simulation

## Slide 28: Tap Point -> PRL Split Box - design
Diplexer design - PCB layout for EM simulations

## Slide 29: Tap Point -> PRL Split Box - design
Diplexer design – modeling results (circuit vs EM)
diplexer is reflectionless in 352 MHz and 704 MHz bands
low insertion loss < 2 dB
very good matching > 25 dB
signals sepration ~70 dBc

## Slide 30: Tap Point -> PRL Split Box - design
Diplexer design – PCB layout

## Slide 31: Tap Point -> PRL Split Box - design
To build the Split Boxes for the PRL
the 5 different boards are needed:
diplexer
4-way power divider, right version
4-way power divider, left version
2-way power divider
1-way bypass

## Slide 32: Tap Point -> PRL Split Box - design
Diplexer design – PCB layout 3D

## Slide 33: Tap Point -> PRL Split Box - design
Power splitters design – PCB layout 3D
4-way power splitter, input on the left
4-way power splitter, input on the right

## Slide 34: Tap Point -> PRL Split Box - design
Power splitters design – PCB layout 3D
1-way bypass (through)
2-way power splitter

## Slide 35: Tap Point -> PRL Split Box - design
1-way bypass (through)
coax-to-microstrip transition - optimization

## Slide 36: Tap Point -> PRL Split Box - design
Stack-up Information:
2 layer Isola FR408
thickness of the dielectric (glass/epoxy core) = 0.508 mm
1 oz copper both sides
no Solder Mask on bottom layer
PCB manufacturing

## Slide 37: Tap Point -> PRL Split Box - design
Radiation hardness
Model: HFCN-440+ | Weight: 18.893 mg |  |  | 
HI PASS FLTR / SURF MT / RoHS |  |  |  | 
RoHS Compliant : Yes |  |  |  | 
Constituent | Description | CAS No. | Weight in mg | % by component
PC BOARD |  |  | 18,893 | 
ALUMINA - CERAMIC |  | 1344-28-1 | 8,162 | 43,20
SILICON DIOXIDE |  | 7631-86-9 | 4,459 | 23,60
LEAD OXIDE - EXEMPT |  | 1317-36-8 | 3,363 | 17,80
CALCIUM OXIDE |  | 1305-78-8 | 2,173 | 11,50
SILVER |  | 7440-22-4 | 0,659 | 3,49
NICKEL | BARRIER | 7440-02-0 | 0,021 | 0,11
TIN-100 | PLATING | 7440-31-5 | 0,057 | 0,30
Example of material declaration for highpass filter HFCN-440+ (MiniCircuits)

## Slide 38: Tap Point -> PRL Split Box - design
Module enclosure
universal design for 6…3-way modules
dimensions: 210 mm x 100 mm x 25 mm
hermetic: gasket under top cover & o-rings under N-type connectors

## Slide 39: Tap Point -> PRL Split Box - design
Module enclosure
radiation hard N-type connectors with Rexolite dielectric & o-rings & gasket material
N-type bulkhead connector
cup for covering unused N-type holes

## Slide 40: Tap Point -> prototype
INPUT
352 MHz & 704 MHz
OUTPUTS
diplexer
2-way divider
4-way divider
352 MHz
704 MHz
6-way Split Box (“2+4” configuration)

## Slide 41: Tap Point -> prototype
6-way Split Box (“2+4” configuration)
transmission to 352 MHz outputs
IL@352 MHz = 5.3dB
IL@704 MHz = 73.6dB
transmission to 704 MHz outputs
IL@352 MHz = 73.5dB,
IL@704 MHz = 9.6dB
input reflections
RL@352 MHz = 19.2dB, RL@704 MHz = 21.3dB

## Slide 42: Tap Point -> prototype
OUTPUTS
diplexer
4-way divider
2-way divider
352 MHz
704 MHz
INPUT
352 MHz & 704 MHz
6-way Split Box (“4+2” configuration)

## Slide 43: Tap Point -> prototype
6-way Split Box (“4+2” configuration)
transmission to 352 MHz outputs
IL@352 MHz = 8.7dB
IL@704 MHz = 77.6dB
transmission to 704 MHz outputs
IL@352 MHz = 70.0dB,
IL@704 MHz = 6.1dB
input reflections
RL@352 MHz = 23.6dB, RL@704 MHz = 23.3dB

## Slide 44: Tap Point -> status
RF Split Box
  diplexer boards design √
  spliter boards design √
  enclosure design √
  N-type connectors with Rexolite -> available from 2 companies (Jyebao & xxx) -> to be ordered…
  prototyping and testing (RF performance)
  minor design modifications
  full production documentation + ordering formalities
  production (64 pcs) & testing (FAT)
Junction Box
  design √
  prototyping in progress
Mounting bracket
  design √
  prototyping √
  production
Heating mats + sensors + isolating pads -> to be ordered…
Thermal insulating shell -> manufactureres selected (final 3D model of Tap Point needed to design the shell)
5/10 Watt dummy loads for dir. couplers (Rexolite) -> bought from JFW Industries Inc., USA)
short coaxial cable -> manufactureres selected -> to be ordered…
Costs are estimated

## Slide 45: Tap Point -> status
RF Split Box
  diplexer boards design √
  spliter boards design √
  enclosure design √
  N-type connectors with Rexolite -> available from 2 companies (Jyebao & xxx) -> to be ordered…
  prototyping and testing (RF performance)
  minor design modifications
  full production documentation + ordering formalities
  production (64 pcs) & testing (FAT)
Junction Box
  design √
  prototyping in progress
Mounting bracket
  design √
  prototyping √
  production
Heating mats + sensors + isolating pads -> to be ordered…
Thermal insulating shell -> manufactureres selected (final 3D model of Tap Point needed to design the shell)
5/10 Watt dummy loads for dir. couplers (Rexolite) -> bought from JFW Industries Inc., USA)
short coaxial cable -> manufactureres selected -> to be ordered…
Costs are estimated
Thank you!