## Slide 1: Using Mantid to process single crystal data
Vickie E Lynch lynchve@ornl.gov
IKON15/DMSC for SX Diffraction September 12, 2018

## Slide 2: Outline
Algorithms available in Mantid to process single crystal data
Reduction scripts and GUI
Normalization and visualization
3D profile fitting for peak integration
Reduction of modulated structures

## Slide 3: Algorithms available in Mantid to process single crystal data

## Slide 4: Loading and Converting Data
LoadEventNexus loads event data
ConvertToMD converts events to Q space.

## Slide 5: Geometry
Algorithms work for both rectangular detectors and tubes
Column=Tube; Row=Pixel
Peak centers can be between tubes
  Use tube-gap parameter
Resizing pixels does not work for tubes (needed for calibration)

## Slide 6: Experiment Planning & Mantid
CrystalPlan optimizes goniometer angles to maximize beam time usage.
Future version will use Mantid Instrument Definition, Goniometers, PredictPeaks and PointGroups.

## Slide 7: Calibrating Detectors
SCDCalibratePanels
  This algorithm calibrates Rectangular Detectors or tubes
  The initial path, panel centers and orientations are adjusted so the error in Q positions from the theoretical Q positions is minimized.
  Given a set of peaks indexed by h,k,l we modify the instrument parameters and then find Q in the sample frame that minimizes the following:
  Output saved as DetCal file and loaded with LoadIsawDetCal

## Slide 8: Single Crystal Peaks
FindPeaksMD
  Sorts all the boxes in the workspace by decreasing order of signal density (total weighted event sum divided by box volume).
  The centroid of the strongest boxes are considered peaks.
PredictPeaks
  Using a known crystal lattice and UB matrix, predict where single crystal peaks should be found in detector/TOF space
  Improving performance would help transition to experiment planning with Mantid

## Slide 9: Finding UB matrices
FindUBUsingFFT
  Best algorithm for finding UB for Niggli cell
FindUBUsingMinMaxD
FindUBUsingLatticeParameters
FindUBUsingIndexedPeaks
OptimizeLatticeForCellType
CalculateUMatrix
  Calculates U matrix from indexed peaks and lattice parameters

## Slide 10: Unit Cell Symmetry
ShowPossibleCells, SelectCellOfType, SelectCellWithForm
  “Lattice Symmetry and Identification – The Fundamental Role of Reduced Cells in Materials Characterization”, Alan D. Mighell, Vol. 106, Number 6, Nov-Dec 2001, Journal of Research of the National Institute of Standards and Technology.
  Transformation matrix from Niggli to Conventional Cell
PointGroup and SpaceGroup
  http://docs.mantidproject.org/nightly/concepts/PointAndSpaceGroups.html?highlight=pointgroup
  Factories exposed to python
  Written by Michael Wedel

## Slide 11: Indexing Peaks
IndexPeaks
  Index the peaks using the UB from the sample.

## Slide 12: Integrating Peaks in Reciprocal Space
Mantid spherical integration
Mantid ellipsoidal integration
Mantid cylindrical integration 1D profile fit, convolution of Gaussian and exponential

## Slide 13: Comparing Integration Algorithms
Schultz, A. J., et al. (2014). "Integration of neutron time-of-flight single-crystal Bragg peaks in reciprocal space." Journal of Applied Crystallography 47(3): 915-921 compared Mantid integration algorithms.
All the Q space integration methods were significantly better than detector-space method.
IntegrateEllipsoids is preferred for TOPAZ data
For weak peaks and high background, fitted profile best with convolution of Gaussian with an exponential.

## Slide 14: Viewing Peaks with SliceViewer
Checking peak integration volume

## Slide 15: Options for SliceViewer
Mantid has Crystallographic Convention option in Preferences
SliceViewer
  Non-orthogonal axes

## Slide 16: Corrections
SetSampleMaterial (bound hydrogen vs free hydrogen)
  Sets the absorption correction coefficients
SetDetScale
  Sets detector bank scales
AnvredCorrection )
  Lorentz correction and/or absorption correction (sphere)
ConvertToMD
  Lorentz correction
SaveHKL )

## Slide 17: Post-Reduction Algorithms
StatisticsOfPeaksWorkspace
  Similar output to xprep
  No. of Unique Reflections, Resolution range, Multiplicity, Mean, ((I)/sd(I)), Rmerge, Rpim, Data Completeness
SaveLauenorm
  Provide input files for the program LAUENORM which is used to perform a wavelength normalization for Laue data using symmetry equivalent reflections measured at different wavelengths.
SaveNexus, SaveIsawPeaks, SaveIsawUB, SaveHKL
  Output formats for single crystal peaks

## Slide 18: Reduction scripts and GUI

## Slide 19: SCD Event Data Reduction Interface
Interface for basic data reduction steps for one crystal orientation in a time-of-flight single crystal neutron diffraction experiment.
  loading data, converting to reciprocal space
  finding peaks
  finding a UB matrix
  choosing a conventional cell
  peak integration

## Slide 20: Parallel Python Reduction
After using the SCD reduction interface for one or two runs from a sequence of runs at different crystal orientations, there should be enough information to set up a configuration file.
See mantid/scripts/SCD_Reduction
A parallel reduction script can be run to produce a combined file of integrated intensities from all the runs.
Orientations are run at the same time in parallel so wallclock time is reduced.

## Slide 21: Timings of Parallel Reduction
Time for reducing one run (OpenMP):
  real 3m20.522s Wallclock Time
  user 3m2.982s CPU TIme
  sys 10m39.613s Malloc+I/O
  Speedup 4.14
Time for reducing 9 runs (OpenMP and threads):
  real 4m46.675s
  user 27m11.130s
  sys 31m25.036s
  Speedup 12.34

## Slide 22: GUI for Single Crystal Reduction Enables Autoreduction
New GUI for TOPAZ Reduction working
All of the corrections are applied without running additional scripts
A previous configuration file can be input for initial values
The resulting configuration file is copied and used to automatically reduce all future data for that experiment
Tabs from reduction GUI

## Slide 23: Normalization and Visualization
Andrei Savici, Steven Hahn, Tara Michels-Clark, Christina Hoffmann, Xiaoping Wang, Ross Whitfield, Vickie Lynch

## Slide 24: Normalizing Data
MDNormSCD
  Input the flux and solid angle calculated from vanadium and MDEventWorkspace calculated from sample.
  Large memory required.
  Run MDNormSCD for each sample.
  Sum the OutputWorkspaces and OutputNormalizationWorkspaces from MDNormSCD separately and then divide the two sums.
  Intensity will not be increased in overlap regions using this method.
Reference: Michels-Clark, T. M., et al. (2016). "Expanding Lorentz and spectrum corrections to large volumes of reciprocal space for single-crystal time-of-flight neutron diffraction." J Appl Crystallogr 49(Pt 2): 497-506.

## Slide 25: Integrating MD Histograms
IntegratePeaksMDHKL
  The units of the workspace must be HKL.
  The main usage will be for data normalized by MDNormSCD.
  A 3D box is created for each peak and the background and peak data are separated.
  The intensity and sigma of the intensity is found by summing.

## Slide 26: Live Data Viewer
Mantid + Matplotlib/Plotly
  Interactive alignment of peaks
  Picker gives information about peaks

## Slide 27: Vates Splatter Plot
Useful for viewing peaks
Uses ParaView

## Slide 28: Vates Simple Interface
Useful for viewing diffuse scattering.
Requires much memory.

## Slide 29: Vates Visualization Capabilities

## Slide 30: Diffuse Scattering
Single crystal 3D volume diffuse scattering data reduction has become routine on both CORELLI and TOPAZ
The use of crystal symmetry operations has been developed which improves the statistics of data collected
A 3D-delta PDF reduction method has been developed in Mantid and demonstrated on CORELLI and TOPAZ diffuse scattering
Symmetrized diffuse scattering from ZrO2
Left - HK0 Right - HK1

## Slide 31: Diffuse Scattering
3D-deltaPDF
Benzil 300K, y=0.5
DTO 680mk H=1.2 z=0
DTO 680mk H=1.2 z=0.25

## Slide 32: 3D Profile Fitting for Peak Integration
Brendan Sullivan, Rick Archibald, Leighton Coates, Xiaoping Wang, Franz Gallmeier, Jack Carpenter, Vickie Lynch, Paul Langan
Samples: Patricia Langan (ORNL), Holger Dobbek and Martin Bommer (Humboldt-Universitat zu Berlin), Robert McFeeters (University of Alabama, Huntsville), Martin Egli and Joel Harp (Vanderbilt University)
Data from the MaNDi and TOPAZ beamlines at the Spallation Neutron Source – Oak Ridge National Laboratory
Funding: NIH R01-GM071939

## Slide 33: Currently use peak-minus-background integration
Bragg peaks are complex 3D intensity profiles which can be integrated in detector space or reciprocal space
Detector space run into overlap
Reciprocal space separates peaks

## Slide 34: Shortcomings of peak-minus-background approaches
Weak Peaks
Detector Edges
Inaccurate Peak
Prediction
Varying Peak Sizes
Adjacent and
Overlapping Peaks
Integrate the tail
Profile fitting overcomes all of these issues!

## Slide 35: Details of peak integration
Goal of integration is to get I, σ(I) for each peak – need to define an integration volume
  Here: N / Nmax > 0.05
  Tunable parameter
Integrate peak:
Variance:
Poission Statistics
Fit Variance

## Slide 36: Profile fitting recovers intensities at detector edges
Look at peaks 15 detector pixels or fewer from the edge
Affects ~20% of peaks!
By forcing nearest neighbor profile we improve merging statistics
 | Profile Fitting | Spherical
Percent of Total Reflections | 20.1% (21.4%) | 25.4% (25.6%)
No. Unique Reflections | 14,928 (1,090) | 19,823 (759)
Multiplicity | 1.60 (1.38) | 2.02 (1.69)
Rpim | 15.3% (20.6%) | 22.8% (27.6%)
CC1/2 | 0.907 (0.432) | 0.834 (0.082)
Detector Edges

## Slide 37: Moderator emission and the Ikeda-Carpenter function
1985 – Ikeda Carpenter function describes moderator emission
SNS moderators have been modeled using MCSTAS
  We get fitting parameters from these
High TOF tail gives rise to tail in reciprocal space
For peak fitting – convolve with tophat function and Gaussian function

## Slide 38: Background from expected profile fit
Each voxel in intensity profile has a TOF associated with it
TOF profile is just a histogram of events
Can determine which voxels are peak vs. background by least squares fitting with expected profile

## Slide 39: Angular coordinates from bivariate normal distribution
TOF
In spherical coordinates, remaining two components are along scattering direction and around beam direction
Peaks in this direction are well-described by a bivariate Gaussian
Take these parameters and multiply by IC parameters to get 3D profile
Could do as full 3D fit, but (2+1)D fit computationally simpler and gives same answer

## Slide 40: Angular coordinates from bivariate normal distribution
TOF
In spherical coordinates, remaining two components are along scattering direction and around beam direction
Peaks in this direction are well-described by a bivariate Gaussian
Take these parameters and multiply by IC parameters to get 3D profile
Could do as full 3D fit, but (2+1)D fit computationally simpler and gives same answer

## Slide 41: Works well strong peaks not near detector edges
Strong Peak from TOPAZ
Strong Peak from MaNDi

## Slide 42: Weak peaks use profile of neighboring strong peak
Peak shape parameters vary slowly as you
go around detector sphere
So we can take the profile of the nearest
strong neighbor

## Slide 43: Case study: Perdeuterated β-lactamase mutant
Unit Cell Parameters | a = b = 73.7 Å, c = 99.8 Å | 
 | α = β = 90◦, γ = 120◦ | 
Space Group | P3221 | 
Number of Orientations | 11 | 
 | 3D Profile | Spherical
Resolution Range (Å) | 14.77 - 1.89 (1.96 - 1.89) | 14.77 – 1.89 (1.96 – 1.89)
No. Unique Reflections | 24,386 (2,144) | 24,918 (2,195)
Multiplicity | 4.86 (3.19) | 6.32 (4.57)
Mean I/σ(I) | 8.5 (2.7) | 7.4 (3.8)
Completeness | 96.6% (86.7%) | 96.7% (93.2%)
Rpim | 8.7% (16.1%) | 9.7% (14.1%)
CC1/2 | 0.958 (0.398) | 0.935 (0.076)
Rwork | 0.219 | 0.181
Rfree | 0.258 | 0.272
β-lactamases are a class of enzymes involved in antibiotic resistance
Diffracts excellently – great case for testing profile fitting
CC1/2 < 0.3:
  Profile fitting: < 1.9 Å
  Spherical: 2.2 Å
  ~0.3 Å increase
Keep I/σ(I) > 1
Rwork, Rfree from refinement on initial model
Sample: Patricia Langan - ORNL

## Slide 44: Case Study: Perdeuterated PaPth1
Unit Cell Parameters | a = b = 64.93 Å, c = 156.52 Å | 
 | α = β = 90◦, γ = 120◦ | 
Space Group | P6122 | 
Number of Orientations | 6 | 
 | 3D Profile | Spherical
No. Unique Reflections | 5,186 (493) | 4,598 (436)
Resolution Range (Å) | 12.92-2.60 (2.69-2.60) | 12.92-2.60 (2.69-2.60)
Multiplicity | 2.8 (2.3) | 2.5 (2.1)
Mean I/σ(I) | 6.5 (2.7) | 4.0 (2.4)
Completeness | 79.2% (78.6%) | 70.2% (69.5%)
Rpim | 10.9% (19.4%) | 16.3% (35.8%)
CC1/2 | 0.920 (0.350) | 0.858 (0.039)
Rwork | 0.272 | 0.323
Rfree | 0.350 | 0.382
Sample: Robert McFeeters - University of Alabama Huntsville
Initial refinement on preliminary model
Peptidyl-tRNA hydrolase 1 (PaPth1) catalyzes cleavage of peptidyl tRNA to free peptide and tRNA
  Important for bacteria to stay alive
Early dataset for MaNDi, initially pushed to ~2.8 Å.
CC1/2 < 0.3:
  Profile fitting: < 2.6 Å
  Spherical: ~2.9 Å
  ~0.3 Å increase

## Slide 45: Case study: H-D Exchanged Z-DNA
Left handed Z-DNA crystals diffract to 1 Å show X-rays with regular hydration pattern outside helix
  Still blind to visualizing H
RT Z-DNA with neutrons found 44 water molecules (~50%) at 1.8 Å resolution but could not water molecule determine orientation
Data collected in 48h from 0.25mm3 crystal
Spherical Integration: 1 water molecule
Profile fitting: 30 water molecules with tentative orientation
Sample: Martin Egli and Joel Harp, Vanderbilt University
2mFo-Fc at 1.5 rmsd
Very different
peak sizes

## Slide 46: 3D profile fitting is an algorithm in Mantid
Implemented profile fitting algorithm in Mantid Nightly as IntegratePeaksProfileFitting
Has companion Jupyter notebook for visualizing peak fits
Will be able to replace other integration algorithms in standard data SCD reduction workflows
Could be useful for re-analyzing old data

## Slide 47: Python script for TOPAZ
Load(Filename='/SNS/TOPAZ/IPTS-9918/0/15647/NeXus/TOPAZ_15647_event.nxs', OutputWorkspace='TOPAZ_15647_event', FilterByTofMin=500, FilterByTofMax=16666, LoadMonitors=True)
FilterBadPulses(InputWorkspace='TOPAZ_15647_event', OutputWorkspace='TOPAZ_15647_event', LowerCutoff=25)
LoadIsawDetCal(InputWorkspace='TOPAZ_15647_event', Filename='/SNS/TOPAZ/shared/PeakIntegration/calibration/TOPAZ_2016A.DetCal')
ConvertToMD(InputWorkspace='TOPAZ_15647_event', QDimensions='Q3D', dEAnalysisMode='Elastic', Q3DFrames='Q_lab', LorentzCorrection=True, OutputWorkspace='TOPAZ_15647_md', MinValues='-25,-25,-25', MaxValues='25,25,25', SplitInto='2', SplitThreshold=100, MaxRecursionDepth=14)
LoadIsawUB(InputWorkspace='TOPAZ_15647_md', Filename='/SNS/TOPAZ/shared/PeakIntegration/DataSet/Si2mm_2016A_15647_15669/15647_Niggli.mat')
LoadIsawPeaks(Filename='/SNS/TOPAZ/shared/PeakIntegration/DataSet/Si2mm_2016A_15647_15669/15647_Niggli.integrate', OutputWorkspace='TOPAZ_15647_peaks')
LoadIsawUB(InputWorkspace='TOPAZ_15647_peaks', Filename='/SNS/TOPAZ/shared/PeakIntegration/DataSet/Si2mm_2016A_15647_15669/15647_Niggli.mat')
LoadIsawUB(InputWorkspace='TOPAZ_15647_md', Filename='/SNS/TOPAZ/shared/PeakIntegration/DataSet/Si2mm_2016A_15647_15669/15647_Niggli.mat')
PredictPeaks(InputWorkspace='TOPAZ_15647_peaks', WavelengthMin=1, WavelengthMax=2, MinDSpacing=0.5, OutputWorkspace='TOPAZ_15647_peaks', EdgePixels=20)
SetInstrumentParameter(Workspace='TOPAZ_15647_peaks', ParameterName='peakMaskSize', ParameterType='Number', Value='6')
runNumber = int(mtd['TOPAZ_15647_peaks'].getPeak(0).getRunNumber())
IntegratePeaksProfileFitting(OutputPeaksWorkspace='peaks_ws_out', OutputParamsWorkspace='params_out',
InputWorkspace='TOPAZ_15647_md', PeaksWorkspace='TOPAZ_15647_peaks', RunNumber=runNumber,
UBFile='/SNS/TOPAZ/shared/PeakIntegration/DataSet/Si2mm_2016A_15647_15669/15647_Niggli.mat',
ModeratorCoefficientsFile='/SNS/TOPAZ/shared/ProfileFitting/franz_coefficients_2010.dat',
StrongPeakParamsFile='/SNS/users/vel/Dropbox (ORNL)/analysis/strongPeakParams_topaz_silicon.pkl')

## Slide 48: Profile fitting can recover intensities in 3He detectors
Different detector system: 3He tubes
There is a gap between each tube, set of tubes, and each bank
Profile fitting can recover the intensities in these gaps

## Slide 49: Planned for profile fitting
Image segmentation
through machine learning
Fit crystal and instrument
parameters
Overlapping Peaks

## Slide 50: Modulated Structures
Shiyun Liu, Xiaoping Wang, Vickie Lynch
Samples: Shiyun Liu, A. Banerjee, X.P. Wang, C.M. Hoffmann, M. Lumsden, B.C. Sales, K.J. Woo, B.C. Chakoumakos
Data from the TOPAZ beamlines at the Spallation Neutron Source – Oak Ridge National Laboratory
Funding: GO student

## Slide 51: Modulated Structure Example
No cross-terms of satellite observed
1d modulated Cmm2 with twinning
q2
q1
q1+q2
hk0
hk0.5

## Slide 52: Finding Modulation Vectors
Visual aid for identifying the satellite peaks
Finds clusters of peaks by binning the number of peaks in the collapsed HKL space into specified sized boxes
The resulting clusters of peaks are modulation vectors

## Slide 53: Modifications to Mantid
ModUB is added to the OrientedLattice class
Members ModHKL and errorModHKL are added to UnitCell class

## Slide 54: Modifications to Mantid cont.
(, , ) is the modulation vector i (i=1,2,3) in HKL space. And the relation between ModUB and ModHKL is:
New functions setModUB is added to OrientedLattice class, and setModHKL, getModHKL, setModerr1, setModerr2, setModerr3, setModVec1, setModVec2, setModVec3, getModerr(i), getModVec(i), getdh(i), getdherr(i), getdk(i), getdkerr(i), getdl(i), getdlerr(i) are added to UnitCell class. Value for ModHKL in UnitCell is set when the function setModUB is used in OrientedLattice.

## Slide 55: Modifications to Mantid cont.
IndexPeaks will now index both main reflections and satellites
  Will index up with up to 3 modulation vectors
  Uses maximum order of satellites to index
  Uses Boolean for whether to include satellites of crossed terms
  Use smaller tolerance than usual for main reflections with satellites
FindUBUsingIndexedPeaks uses the indexed peaks to calculate the UB and ModUB
FindUBUsingIndexedPeaksWithSatellites uses the indexed peaks from to calculate the UB and ModUB and has addition input for the modulation vectors

## Slide 56: Modifications to Mantid cont.
With dh,dk,dl as input for PredictSatellitePeaks, all the satellite peaks that hits the detector within the wavelength range are predicted
LoadIsawUB and SaveIsawUB now input/output three more columns if there is a modulation vector
  h k l m n p
IntegrateEllipoidsWithSatellites integrated both main and satellite peaks

## Slide 57: FindUBUsingIndexedPeaks with Satellites
FindUBUsingIndexedPeaks-[Notice] FindUBUsingIndexedPeaks started FindUBUsingIndexedPeaks-[Notice] Number of Indexed Peaks in Run 24281 is 1753 FindUBUsingIndexedPeaks-[Notice] Lattice Parameters: 7.592302 7.628449 7.096641 106.925624 100.586711 115.107697 332.912929 FindUBUsingIndexedPeaks-[Notice] Parameter Errors : 0.000584 0.000658 0.001245 0.010293 0.010415 0.007113 0.086289 FindUBUsingIndexedPeaks-[Notice] New UB will index 853 main Peaks with tolerance 0.12 and 902 Satellite Peaks with tolerance 0.1 ,out of 2157 Peaks FindUBUsingIndexedPeaks-[Notice] Lattice Parameters: 7.592302 7.628449 7.096641 106.925624 100.586711 115.107697 332.912929 FindUBUsingIndexedPeaks-[Notice] Parameter Errors : 0.000584 0.000658 0.001245 0.010293 0.010415 0.007113 0.086289 FindUBUsingIndexedPeaks-[Notice] Modulation Dimension is: 1 FindUBUsingIndexedPeaks-[Notice] Modulation Vector 1: [-0.490880,-0.442061,0.384217] FindUBUsingIndexedPeaks-[Notice] Modulation Vector 1 error: [0.006756,0.007009,0.008165] FindUBUsingIndexedPeaks-[Notice] FindUBUsingIndexedPeaks successful, Duration 0.01 seconds

## Slide 58: IndexPeaks with Satellites
IndexPeaks-[Notice] IndexPeaks started IndexPeaks-[Notice] Maximum Order: 2 IndexPeaks-[Notice] ALL Runs: indexed 1765 Peaks out of 2157 with tolerance of 0.12 IndexPeaks-[Notice] Out of 1765 Indexed Peaks 853 are Main Bragg Peaks, and 912 are satellite peaks IndexPeaks-[Notice] Average error in h,k,l for indexed peaks = 0.0149101 IndexPeaks-[Notice] Average error in h,k,l for indexed main peaks = 0.0145036 IndexPeaks-[Notice] Average error in h,k,l for indexed satellite peaks = 0.0152904 IndexPeaks-[Notice] Lattice Parameters: 7.592302 7.628449 7.096641 106.925624 100.586711 115.107697 332.912929 IndexPeaks-[Notice] Parameter Errors : 0.000584 0.000658 0.001245 0.010293 0.010415 0.007113 0.086289 IndexPeaks-[Notice] IndexPeaks successful, Duration 0.00 seconds

## Slide 59: Conclusions
Mantid algorithms are reducing single-crystal data
TOPAZ is using autoreduction with reduction GUI for setup
Large memory is needed for normalization of orientations and visualization of data.
  Visualization is very important for single crystal data.
3D Profile fitting for integration is available in Mantid
Reduction of data with modulated structures will soon be available in Mantid