## Slide 1: FullProf & Esmeralda
Céline Durniak
on behalf of Juan Rodriguez Carvajal
Single crystal diffraction workshop
IKON15
12 September 2018

## Slide 2: FullProf Suite

## Slide 3: FullProf Suite – Description of project
project started in 1990s
code in Fortran, GUI using Winteracter (commercial)
not open source
supported operating systems
(2 versions)
set of crystallographic programs, based on Crystallographic Fortran Modules Library (CrysFML)1
programs can be run in stand alone form or from a GUI
1: http://forge.epn-campus.eu/projects/crysfml

## Slide 4: FullProf Suite - Functionalities
mainly developed for Rietveld analysis of powder diffraction data for
  X-ray
    constant or variable step in scattering angle 2𝜃
  neutrons
    constant wavelength, TOF, nuclear and magnetic scattering, polarised neutrons
all options existing for powders exist also for single crystals.
for single crystal only
  refinement of domain (twins) populations
  secondary extinction parameters.
combined refinement of powder and single crystal data coming from different kinds of experiment on the same material.

## Slide 5: FullProf Suite - GUI
CheckGroup
crystal and magnetic structure refinement, multiple patterns, simulated annealing
unique set of independent reflections (twinning, incommensurate magnetic structures)
calculating basis functions of irreducible representations of space groups
graphical editor for input PCR files for FullProf
EdPCR
BasIreps
FullProf
DataRed
CIFs_to_PCR mCIF_to_PCR
Mol_to_PCR CrysCalc
Programs / Tools
Programs for crystallographic calculations

## Slide 6: Example – Naphthalene (D9 @ ILL)
Reciprocal Space Visualizer
CFL file
Measured region of reciprocal space

## Slide 7: Example – Naphthalene (D9 @ ILL)
7
Reciprocal Space Visualizer
CheckGroup
CFL file
HKL file
Measured region of reciprocal space
List of possible space groups

## Slide 8: Example – Naphthalene (D9 @ ILL)
8
Reciprocal Space Visualizer
CheckGroup
DataRed
CFL file
HKL file
Measured region of reciprocal space
List of possible space groups
Average of equivalent reflections
HKL file

## Slide 9: Example – Naphthalene (D9 @ ILL)
9
Reciprocal Space Visualizer
CheckGroup
DataRed
FullProf
Mol_tpcr
CFL file
HKL file
Measured region of reciprocal space
List of possible space groups
Pcr file
Intensity file
Average of equivalent reflections
HKL file

## Slide 10: Example – Naphthalene (D9 @ ILL)
10
Reciprocal Space Visualizer
CheckGroup
DataRed
FullProf
Mol_tpcr
CFL file
HKL file
Measured region of reciprocal space
List of possible space groups
Display of structure
FullProf Studio
Pcr file
Intensity file
Average of equivalent reflections
HKL file
Display of diffraction pattern

## Slide 11: FullProf Suite – Future plans & events
For both single crystals and powders
  merge molecular fragments from different structures
  generate automatic or manual z-matrices using a GUI
  settings of automatic planar restraints, combination or rigid-bodies with restraints...
Direct treatment of raw Laue integrated intensity data, without passing by the normalization step (extraction of wavelength-independent structure factors)
  a better control of the refinement of incident spectrum and extinction effects

## Slide 12: The Esmeralda Laue Suite

## Slide 13: Laue Diffraction with neutrons - Technique
Generally used in single crystal spallation sources diffractometers with the advantage of separating exact overlaps thanks to TOF analysis
In reactor sources overlap cannot be avoided but concerns ≤ 20% of reflections
Continuous flux ➜ high efficiency in data collection with cheap detectors
Advantages
very small crystals can be analysed
fast survey of the reciprocal space as a function of T, field, etc
Drawbacks
complexity of data treatment ➜ not as precise as monochromatic refinements
difficulties to model all physical effects affecting integrated intensities

## Slide 14: Laue neutron diffraction Data treatment using Esmeralda
project started in 2010
written in Fortran, Winteracter for GUI (commercial)
authors
  Juan Rodriguez-Carvajal (ILL)
  Luis Fuentes-Montero (Diamond facility UK)
  Petr Cermak (MLZ Germany, now in Prague)
repository
  https://forge.epn-campus.eu/projects/esmeralda
supported operating systems

## Slide 15: The Esmeralda Laue Suite - Structure of project
developed from CrysFML + several calculation modules specialized for Laue technique
Modularity: calculation modules separated from GUI modules
main GUI program (Esmeralda) can run other standalone console programs (more adapted to treat large amount of data)
Script files for running these programs (Cyclops2Cyl Laue_Orient, Ref_UB_Laue, Laue_kSearch, Laue_Integration, Normalize_Laue …) can be generated automatically from the GUI

## Slide 16: The Esmeralda Laue Suite – Data treatment workflow
Objectives
list of integrated intensities of well identified Bragg spots collected in series of images differing by the spindle angle associated with the rotation of the crystal
Data treatment
Manipulation of experimental images (geometric transformations)
Laue simulator
  Calculation of integrated + profile intensities
Indexing and refinement of the orientation matrix
Integration of Laue Spots
  Choice between 2 methods: 2D-Lehmann-Larsen and profile integration
Normalization of Laue intensities
  Extraction of wavelength independent structure factors

## Slide 17: The Esmeralda Laue Suite – Input
CFL file
(cell parameters, space group, name of the instrument file)
Esmeralda

## Slide 18: The Esmeralda Laue Suite – Input
18
CFL file
(cell parameters, space group, name of the instrument file)
Instrument file
geometrical characteristics of the instrument and detector system (flat or cylindrical)
Esmeralda

## Slide 19: The Esmeralda Laue Suite – Input
19
CFL file
(cell parameters, space group, name of the instrument file)
Instrument file
geometrical characteristics of the instrument and detector system (flat or cylindrical)
Esmeralda
Laue images files (tif, bmp, hbin, bin, img, raw, reo)

## Slide 20: The Esmeralda Laue Suite - Documentation
20/31

## Slide 21: The Esmeralda Laue Suite - Functionalities
Customisation of plots
3D surface visualisation of the Laue diffraction patterns
CYCLOPS @ ILL

## Slide 22: The Esmeralda Laue Suite - Functionalities
Customisation of plots
3D surface visualisation of the Laue diffraction patterns

## Slide 23
Customisation of plots
3D surface visualisation of the Laue diffraction patterns
Automatic peak search and crystal orientation
Manual control of specific parameters e.g. cell parameters, propagation vectors…
The Esmeralda Laue Suite - Functionalities
Modification of calculated pattern

## Slide 24: The Esmeralda Laue Suite - Functionalities
Customisation of plots
3D surface visualisation of the Laue diffraction patterns
Automatic peak search and crystal orientation
Manual control of specific parameters e.g. cell parameters, propagation vectors…
Least squares refinement of the orientation matrix, instrument offsets, crystal positioning, image distortions…

## Slide 25: The Esmeralda Laue Suite - Functionalities
Customisation of plots
3D surface visualisation of the Laue diffraction patterns
Automatic peak search and crystal orientation
Manual control of specific parameters e.g. cell parameters, propagation vectors…
Least squares refinement of the orientation matrix, instrument offsets, crystal positioning, image distortions…
Profile visualisation along a curve

## Slide 26
The Esmeralda Laue Suite - Functionalities
Customisation of plots
3D surface visualisation of the Laue diffraction patterns
Automatic peak search and crystal orientation
Manual control of specific parameters e.g. cell parameters, propagation vectors…
Least squares refinement of the orientation matrix, instrument offsets, crystal positioning, image distortions…
Profile visualisation along a curve
Determination of modulation / propagation vectors using Laue_kSearch
Peak integration
Vertical
Horizontal
Vertical & horizontal profiles integration
Integration – Calculated positions

## Slide 27
Customisation of plots
3D surface visualisation of the Laue diffraction patterns
Automatic peak search and crystal orientation
Manual control of specific parameters e.g. cell
parameters, propagation vectors…
Least squares refinement of the orientation matrix, instrument offsets, crystal positioning, image
distortions…
Profile visualisation along a curve
Determination of modulation / propagation vectors
using Laue_kSearch
Peak integration
Normalization of integrated intensities using Normalize_Laue ➜ wavelength-free squared structure factors
The Esmeralda Laue Suite - Functionalities

## Slide 28: Future developments for Esmeralda Laue Suite
Extension for superspace formalism
Update Laue Simulator. Strategy of data collection
Profile refinement in 2D
Implement Eulerian and Kappa cradles as orienting device
Calculation of approximate shape parameters of spots as a function of mosaicity, divergence and shape of the crystal before the integration process
Treatment of total integrated intensities within FullProf