## Slide 1: Remote Handling An update
Erik Nilsson
Mechanical Engineer
ESS Chopper Group
www.europeanspallationsource.se
13 September, 2018

## Slide 2: Overview
Workshop report
Technical updates and statuses
TG3 Information
Tooling introduction
ESS-0042943
ESS Requirements on neutron scattering instruments with respect to remote handling compatibility
Released
https://confluence.esss.lu.se/display/SD/NSS+Remote+handling+Homepage

## Slide 3: Quick reminder
‘Back’
Full-RH or No-RH
‘Front’
Full-RH or Limited-RH
After 48-72hrs
Front access
  RH only
Rear access
  Hands on (hotspot removed)
After 10-15days
Front access
  RH only
  or Hands (hotspot removed)
Rear access
  Hands on
Restricted activities
Separation
Notes: No in-situ RH maintenance is foreseen.
Installation is not considered a RH-activity.

## Slide 4: Remote Handling Workshop 2 – May 2018
12/15 instruments present
ESS technical updates
Share, discuss and progress
Next workshop in ~November

## Slide 5: Technical developments Rollers and Guides
Simplified rollers
Rollers
Built and being tested
Solutions discussed during workshop
Current status

## Slide 6: Technical developments Location and Alignment features
6
RH-Z realignment
Misumi dowels
Built and being tested
Solutions discussed during workshop
Current status

## Slide 7: Technical developments Lifting
7
In-house lifting system
Industrial lifting eye
Lifting eye suitable for automatic hook
(Industrial supply)
Solutions discussed during workshop
Current status

## Slide 8: Technical developments Connectors (Chopper example)
8
Supplier Controller
Inside
shielding
Outside
shielding
Installed
Chopper
A
B
C
1
2
Cables | Installation type | Special constraints | Approximate length
1 | Flexible | Radiation hardened or Replacement part | ~2m
2 | Fixed | Standard | 10-50m
Connectors | Connector type | Attachment | Note
A | Supplier Standard | On Equipment | 
B | LEMO B/K FNG, S, EPDM, PEEK or equivalent | On plate* | https://confluence.esss.lu.se/display/SD/Electrical+and+fluid+interfaces
C | Supplier standard | On Equipment | 
1
2
B
Currently finalising choice
of fluid connectors

## Slide 9: Technical developments RH Vacuum Flange
Multiple variants
Solutions discussed during workshop
Undergoing tests
Current status

## Slide 10: TG-3
Module definition and classification.
Shown considerations for handling, alignment and fastening.
Failure analysis of modules.
Case and reason when ESS best practices are not followed.
Case and reason when ESS standard RH equipment is not used.
C-SPEC extraction simulation
ESTIA Module definition and classification
BIFROST Handling considerations

## Slide 11: Tooling developments
Preliminary design during Autumn.
Definition of tool interfaces where applicable.
Head start with engagement tool and automated hook.
Engagement tool preliminary design

## Slide 12: Tooling developments
CRANE MOVIE

## Slide 13: Upcoming
Workshop 3 - November
Participation and feedback in Phase 2 / TG3 for all instruments.
Finalisation of Roller, alignment, positioning tests – September/Early October
Tools development start.

## Slide 14: Thank you for your attention https://confluence.esss.lu.se/display/SD/NSS+Remote+handling+Homepage Questions?
Notes: Add extra slides on what we are looking at.