 EEE integration and IOC
(Software interface with ICS)
Hinko Kocevar
Software Engineer
www.europeanspallationsource.se
14 May 2017

---
Overview
FC system is expected to be based on ESS standard platform (MicroTCA)
ESS choice of control system is EPICS (7)
Prefer ESS supported software support for standard platform and its constituents (if stable)
[Speaker Notes: Walk through: workflow from acceptances tests to commionning]

---
Faraday cup system SW
EPICS IOC shall be concerned with:
Digitizer
Motion control
High voltage bias control
Event receiver interface (timing system)
Use LEBT FC software as basis (not the Catania one)
Possible multiple FC systems per single EPICS IOC (due to the nature of the hardware modularity)

---
Digitizer
Will probably start working with whatever LEBT FC shall be powered with
AMC Struck SIS8300 (10 Msps, 16 bits)
RTM Struck SIS8900 (DC coupled)
EPICS support available in house (BPM, BCM, WS)
ICS is working on AMC IFC1410 + FMC????

---
Motion control
Ethercat based control using digital and analog I/O
Need to trigger the movement and monitor limit switches
Simple pneumatic based motion (no motors)
ESS support for Ethercat available
Partially demonstrated EPICS support for this candidate with lab setup (switches)
MPS/BIS interface?

---
High voltage bias control
Ethercat based control using digital and analog I/O
Need to control and monitor voltage and current limit
Simple analog protocol (not using USB)
Partially demonstrated EPICS support for this candidate with lab setup

---
Event receiver
AMC MRF EVR-300-MTCA
Need timing events, triggers, data timestamping (and clocks)
Community and ESS EPICS support available
Partially demonstrated EPICS support for this candidate with lab setup (need to test latest additions to the EVR software)
MPS/BIS interface?

---
Outlook
Re-use proven solutions (LEBT FC)
Use ESS supported modules (Ethercat, EVR)
Provide modular FC system software (ready for integration into ICS EPICS environment)

---
Questions ?