## Slide 1: ESS Machine Protection Technical Advisory Committee, TAC 18 Lund, Sweden A. Nordt
ESS Machine Protection Team
European Spallation Source ERIC, Sweden
FBIS Design Team (In-Kind-Contribution)
ZHAW, Winterthur, Switzerland
2018-10-18

## Slide 2: Overview
Machine Protection Integration Strategy
Status on the Fast Beam Interlock System (FBIS)
Status on FBIS Reliability Prediction
Issues/Concerns for MP at ESS

## Slide 3: Attention
The following slides are for TAC to READ
Slides will not be presented 1 by 1
Please ask questions per main topic

## Slide 4: Attention
Lets discuss MPS at ESS

## Slide 5: Reminder: What is Machine Protection?
MP is Happiness
  Happiness for the scientists
  Happiness for the Council
  Happiness for the staff
Time and money

## Slide 6: Reminder: What is Machine Protection?
Add Availability = ”Subtract Downtime”
Long Downtime
Short Downtime
6
Courtesy of Enric Bargalló (aligned with “ESS Reliability and Availability Requirements” ESS-0064499

## Slide 7: Reminder: MP-System of Systems (SoS)

## Slide 8: Reminder: Local vs Global Protection

## Slide 9
Short Summary:
Risk Management and Machine Protection Lifecycle
And how we integrate MP into ESS

## Slide 10: Inspired by International Standards

## Slide 11: Machine Protection Lifecycle
Analysis  Enric (sick leave), Ric (resigned/off by 2018-10-31), Johannes (50%)/consultant started 2018-10-01
Integration  Szandra, Annika (10%)
Implementation and Design  Manuel (MPS-VAC, MPS-ID, MPS-Target), Stephane (FBIS, LPS Raster Magnets), David (MPS-MAG, MPS-BMAG, MPS-NSS), Viktor (El. Design and installation), Fernando (Technician), Johannes (consultant/el. design 50%), team from ZHAW (FBIS), system-owners at ESS (e.g. Rafael M. for LPS RF)

## Slide 12: Details: How Does the Analysis Work?

## Slide 13: Example: Machine Protection for Target
Proton Beam Window
Target Wheel
Moderators
  Water
  Cryogenic
Reflectors
Tuning Beam Dump

## Slide 14: Analysis Example – 1041/2/3
Damage Events
Hazards
Overall Protection Functions
Protection Functions
  Sensors
  Logic Elements
  Actuators
  Protection Integrity Level
  Timing Requirements

## Slide 15: What Does Machine Protection Ask for?
System information
System designs
System analyses (risk, HAZOP etc.)
System interactions
Solutions
An open mind

## Slide 16: MP SoS – Information Item Structure
Question: What info do we need from whom?
The information item (document) structure is used for MP-SoS across ESS
Black information items/documents are developed and owned by the MP-SoS staff
Blue information items are owned by respective system owner
Note: The term "information item" is used to relieve some of the tension caused by the word "document"
This is compliant and in line with how the term is used in the ISO 15289 standard and is applied to the MP-SoS work

## Slide 17: MP SoS - Lifecycle
ESS Systems Engineering Management Handbook (ESS-0093443)
adapted for Machine Protection (MP-SEMP: ESS-0057245 rev2)

## Slide 18: MP SoS – Use Case Workshops
Protection requirements are derived from hazard and risk assessments
BUT: this is not enough and is a too 1 dimensional approach!
In addition we perform “use case” workshops to derive behavioral requirements for the different systems
Example use case: Change of beam destination (LEBT-FC to DTL4-FC):
Likely to happen frequently (tuning, commissioning)
Many systems required for efficient “handshaking” (avoid damage, confusion for operators, interlock deadlocks, operational impossibility)
All system stakeholders involved in workshops
Identified sequence of actions that will work
Optimized sequence
Documented

## Slide 19: MP SoS – Use Case Workshops
Logic details stored in Enterprise Architect (EA)
Simulation of logic
EA model shared with ZHAW team for FBIS development (logic in VHDL)
EA model serves reliability prediction effort made by ZHAW
This kind of work is not to be underestimated (importance + effort)

## Slide 20
Integration OK... BUT
Practically…
How is it all working together?
How do we want to make “good” beam?

## Slide 21: ESS Beam Production
Operators request beam from the control room
The Timing system sends event triggers to the Ion Source
Plasma is generated using H2 gas and RF power
Beam is extracted, sent to the Target and Neutron science starts

## Slide 22: Example: What if there is an issue with the target wheel?
Target needs to request a Beam stop
MPS/BIS will take care and stop beam through Actuators!
Forbid the Timing System to send the Timing triggers
Forbid feeding the Magnetron (FSU) (no RF)
Beam Interlock System

## Slide 23: Example: What if there is an issue e.g. with the target wheel (out of phase)?
Target needs to request a Beam stop
MPS will take care of it using the Actuators!
Forbid the Timing System to send the Timing triggers
Forbid feeding the Magnetron (FSU) (no RF)
Stop the HV power*
Deflect Beam using the LEBT Chopper
Deflect Beam using the MEBT Chopper
Beam Interlock System
*only for emergency

## Slide 24
A set of Machine Protection systems (MPSs) + Fast Beam Interlock System (FBIS)
These implement Global Protection Functions
FBIS
MPS Vac
MPS ID
MPS Mag
MPS Trg
What is the Beam Interlock System (BIS)?

## Slide 25: MPS Systems are…
MPS Vac : Vacuum protection
MPS ID : Insertable devices protection
MPS Mag : Magnets protection
MPS BMg : Bending Magnets protection
MPS Trg : Target protection
MPS NSS : Neutron instruments protection
FBIS
MPS Trg
PLC based interlock systems
- Ring topology with 1 fail safe CPU and multiple, distributed I/O
- Each I/O connects to a sensor (VVS, FC, EMU, WS, QV, QH,…)
Slow ! Reaction time > 10ms
MPS Vac
MPS ID
MPS Mag

## Slide 26: The Fast Beam Interlock System is…
SCU (Signal Converter Unit) concentrating signals from Sensor Systems and MPS PLC based systems
DLN (Decision Logic Node) concentrating signals from several SCUs, deriving global beam permit and acting on Actuators to stop Beam
FBIS
MPS Trg
DLN
DLN
DLN
DLN
DLN
SCU
SCU
MPS Vac
MPS ID
SCU
SCU
Fast ! Reaction time ~ 5us
FPGA based systems
- SCU HW design based on standard mechanical components (cPCI)
- DLN HW based on uTCA standard
MPS Mag
Actuators
SCU
SCU
DLN
DLN
DLN
MPS Vac
MPS ID
MPS Mag

## Slide 27: The Fast Beam Interlock System is…
DLN
SCU
IFC 1410
Sensor Systems
FPGA
CPU:
Less critical protection features (c language code)
Interface to EPICS
FPGA:
Critical logic to fulfill protection functions (VHDL hardware description language)
  Decides to remove the global beam permit and stop the beam activating the Actuators
  Decides to inhibit the beam if sensor systems are not ready
  check all MP related systems are properly configured (Beam destination, beam mode)
Optic fibers

## Slide 28: Fast Beam Interlock System
Where are we now with the FBIS development?
FBIS CDR#1 in March 2018
https://confluence.esss.lu.se/display/PS/FBIS+CDR+%28Part+1%29+-+March+2018
FBIS CDR#2 in August 2018
https://confluence.esss.lu.se/display/PS/FBIS+CDR+%28Part+2%29+-+August+2018

## Slide 29: Signal Conditioning Unit (SCU) Functional Behaviour
29

## Slide 30: Decision Logic Node (DLN) Functional Behaviour
30

## Slide 31: Basic Structure - Interfaces
31

## Slide 32: Detailed Design: DLN Breakdown Structure
32

## Slide 33: DLN: System Modules

## Slide 34: DLN: Internal BLockdiagram

## Slide 35: Detailed Design: SCU Breakdown Structure
35

## Slide 36: SCU: System Modules
36

## Slide 37: SCU: System Modules

## Slide 38: SCU: System Modules
38

## Slide 39: SCU: Internal Blockdiagram

## Slide 40
Development, Verification and Validation of the FBIS

## Slide 41: FBIS Lifecycle

## Slide 42: Incremental Development

## Slide 43: Incremental Development Lifecycle

## Slide 44: FBI System Development Process

## Slide 45: FBI System Development Process

## Slide 46: FBI System Development Process
46

## Slide 47: Hardware Development Process

## Slide 48: Hardware Development Process

## Slide 49: Hardware Development Process
49

## Slide 50: Hardware Development Process

## Slide 51: Firmware Development Process

## Slide 52: Firmware Development Process

## Slide 53: Firmware Development Process

## Slide 54: Firmware Development Process

## Slide 55: Firmware Development Process

## Slide 56: Firmware Development Process

## Slide 57: Software Development Process
57

## Slide 58: Software Development Process

## Slide 59: Software Development Process

## Slide 60: Software Development Process

## Slide 61: Software Development Process

## Slide 62: Software Development Process

## Slide 63
Some first results on FBIS Reliability Prediction

## Slide 64: Failure Rates in IEC 61508
64

## Slide 65: Failure Rates in IEC 61508

## Slide 66: Tool Chain: Isograph Reliability Prediction

## Slide 67: Tool Chain: Isograph Reliability Prediction

## Slide 68: Tool Chain: Isograph Reliability Prediction

## Slide 69: Reliability Block Diagram (RBD) Overview

## Slide 70: Tool Chain: PFH (average frequency of a dangerous failure per hour)

## Slide 71: Preliminary Results FBIS
71

## Slide 72: RBD FBIS (SCU and DLN)/ Sensitivity

## Slide 73: Results: PIL Level

## Slide 74: Protection Function Integrity Level Assessment
74

## Slide 75: PF Example Interceptive Devices
75

## Slide 76: PF Specification Example Interceptive Devices

## Slide 77: PF Integrity Level Assessment

## Slide 78: PF Documentation – Suggestion ID-PF-x

## Slide 79: Summary
Presented status on MP integration strategy
Gave an overview on FBIS development, verification and validation strategy
Presented overview on reliability predictions for FBIS and how to assess the integrity level of Protection Functions
Thanks a lot for the great work done by the team at ESS and at ZHAW (in kind partner)
It is complex but we are progressing step by step!

## Slide 80: Attention
Lets discuss …
What are the issues?
How to be BETTER?

## Slide 81: Issues/Concerns/Thoughts/Help?
Detailed MP V&V, commissioning & early operations plans are not yet fully developed (they might fall into InitOps phase): We are aware and working on this
Many related aspects are still open, e.g. threshold management, beam loss strategy, interlocks management, integration of MP into commissioning & operations (e.g. who decides on threshold/interlock changes, who has overall responsibility?) Interlocks working group planned
I think an MP representative shall be involved, shall have a mandate when developing the above.
ESS Machine Protection Committee has not representative from Operations on board: Carlo 

## Slide 82: Issues/Concerns/Thoughts
MP team has 2.5 experienced people (in OP and commissioning)
Not enough, hence,… we train our staff …
ESS MP has a framework agreement with CERN/LHC/LINAC4 - Operations team on training ESS staff on operations and commissioning with focus on Machine Protection, which is FANTASTIC!
Ric and Szandra attended start up of LHC (and LINAC4) in spring 2018 for 2 weeks (Ric however is leaving now , Enric was on sick leave already )
Plan to send Viktor and Fernando to CERN asap (to get inspired on commissioning support tools, installation issues, etc)

## Slide 83: Issues/Concerns/Thoughts/Help?
Its difficult to keep staff that is well trained
Replacement of staff leaving ESS is done on a timeline that doesn’t allow for handover
More support from upper management on this front would be extremely highly appreciated. We cannot keep up with a constant high pressure life-style for years!

## Slide 84: Awareness Please!
Radiation Safety (Analysis Method change in Spring 2018)
Analyses (TSS driven) indicate that MP plays important role for radiation safety
If communicated not correctly to SSM, this may become a concern
Latest approved Target event classification documents: ESS-0374897, ESS-0320231
Further ex: Can beam monitoring devices connected to MPS be used to detect earthquakes early on/used as layer of protection?

## Slide 85
Thank you

## Slide 86
BACK UP SLIDES

## Slide 87: Status Overview
https://confluence.esss.lu.se/display/PS/MP-SoS+Summary
https://confluence.esss.lu.se/display/PS/MPSVAC+and+MPSID+CDR
https://confluence.esss.lu.se/display/PS/Deployment

## Slide 88: Diagnostic and Proof Tests/Example

## Slide 89: Diagnostic and Proof Tests/Example

## Slide 90: Diagnostic and Proof Tests/Example

## Slide 91: Diagnostic and Proof Tests/Example

## Slide 92: Diagnostic and Proof Tests/Example

## Slide 93: Diagnostic and Proof Tests/Example

## Slide 94: Diagnostic and Proof Tests/Example

## Slide 95: FBIS RBD

## Slide 96: FBIS RBD: Sensitivity One SCU

## Slide 97: FBIS RBD: Sensitivity One Serializer only

## Slide 98: The MP Look 
MP in Erikaviolet RAL 4003

## Slide 99
MP connection boxes
MP Patch Panels

## Slide 100: Next Steps for FBIS

## Slide 101: Deliverables for FBIS / ZHAW

## Slide 102: Deliverables for FBIS / ZHAW

## Slide 103: Deliverables for FBIS / ZHAW

## Slide 104: Deliverables for FBIS / ZHAW

## Slide 105: Deliverables for FBIS / ZHAW

## Slide 106: Deliverables for FBIS / ZHAW

## Slide 107: We want to be ready for NC LINAC Commissioning
HOW?

## Slide 108: MP @ NC LINAC
MP systems needed to commission the nc linac:
FBIS (CDR passed: 2018-08)
MPSVAC (protection for vacuum gate valves) (CDR: 2018-10)
MPSID (protection for insertable devices) (CDR: 2018-10)
MPSMAG (protection for magnets) (PDR passed: 2018-10)
Interfaces to MPS systems/FBIS needed for nc LINAC commissioning:
BCMs (hw wise ok, interlock logic tbw)
BLMs: nBLM, ICBLM (hw wise ok, interlock logic tbw)
BPMs (hw wise ok, interlock logic tbw)
RFLPS’s (hw wise ok, interlock logic tbw)
Actuators (LEBT chopper, Ion Source (HV PS, FSU), Timing System, MEBT chopper (hw tested at IS test stand, logic clear)
EPICS (started)
Timing System (hw ok, logic in good state)