## Slide 1: Automation of Control System Configuration TAC 18
Karl Vestin
ESS/ICS
Date: 2018-10-18

## Slide 2: Topics
Automatic code and configuration generation
Risks and benefits of automatic code generation
Overview of ESS tool chain for automated code generation for control systems
Control System (CS) Entry
Controls Configuration Database (CCDB)
Input Output Controller (IOC) Factory
Programmable Logic Controller (PLC) Factory
  Background and technical solution
  Step-by-step PLC code generation
  Change management

## Slide 3: Automatic code and configuration generation
Definition
In computer science, the term automatic programming identifies a type of computer programming in which some mechanism generates a computer program to allow human programmers to write the code at a higher abstraction level.
There has been little agreement on the precise definition of automatic programming, mostly because its meaning has changed over time. David Parnas, tracing the history of "automatic programming" in published research, noted that in the 1940s it described automation of the manual process of punching paper tape. Later it referred to translation of high-level programming languages like Fortran and ALGOL. In fact, one of the earliest programs identifiable as a compiler was called Autocode. Parnas concluded that "automatic programming has always been a euphemism for programming in a higher-level language than was then available to the programmer.“
  Source: Wikipedia
Within the domain of control systems engineering the use of automatic code generation is uncontroversial as many control system topologies (most notably PLC system) makes heavy use of code generation from visual models.

## Slide 4: Risks and benefits of using automatic tools for generating code and configuration files
Risk
Tools can introduce systematic errors
Tools must be maintained
Adds complexity to configuration management
Tool chain dependencies can cause downtime
More tools require extra training
Benefit
Avoid duplicated information
Reduce manual writing
Reduce manual errors
Harmonize code standard
Improve development speed
Introduction of automatic tools for code generation and generation for configuration files is a risk-benefit analysis.
A typical conclusion of this analysis is that code generation is used to generate skeleton code and adding commonly reused “standard code”. But is some disciplines code generation is used in a more comprehensive fashion (e.g. safety controllers in automotive industry).

## Slide 5: Overview of tool chain for automatic code and configuration at ESS
CS Entry
(Inventory management)
CCDB
(Configuration database)
IOC Factory
(Java application)
PLC Factory
(Python script)
E3
(ESS EPICS Environment)
PLC Code
(TIA Portal)
Database for inventory management of the technical network equipment at ESS.
Provides the MAC and IP address for CCDB.

## Slide 6: Overview of tool chain for automatic code and configuration at ESS
CS Entry
(Inventory management)
CCDB
(Configuration database)
IOC Factory
(Java application)
PLC Factory
(Python script)
E3
(ESS EPICS Environment)
PLC Code
(TIA Portal)
Database for management of control system configurations at ESS.
Provides one commons source for the configuration data.

## Slide 7: Overview of tool chain for automatic code and configuration at ESS
CS Entry
(Inventory management)
CCDB
(Configuration database)
IOC Factory
(Java application)
PLC Factory
(Python script)
E3
(ESS EPICS Environment)
PLC Code
(TIA Portal)
The IOC Factory application generates EPICS IOCs based on configuration data pulled from the configuration database.
The generated code for the IOC is ready to deploy into the EPIC environment

## Slide 8: Overview of tool chain for automatic code and configuration at ESS
CS Entry
(Inventory management)
CCDB
(Configuration database)
IOC Factory
(Java application)
PLC Factory
(Python script)
E3
(ESS EPICS Environment)
PLC Code
(TIA Portal)
Consistent configuration
The factory script for stub code generation for Siemens TIA Portal as well as corresponding interface declarations for the EPICS IOC.

## Slide 9: CS Entry
CS Entry is a web based inventory management system for all network equipment on the ESS technical network
Used for creating and booting virtual machines and IOC’s on the technical network
Used to get MAC and IP address for specific devices for use in CCDB

## Slide 10: Controls Configuration Database (CCDB)
Contains configuration data for hardware and EPICS IOC’s for the entire ESS Integrated Control System.
Conceptual ideas for database structure inherited from community
User interface, REST interfaces and data structures are developed by ESS
Allows definition of properties
Allows definition of relations between control system components (e.g. connects, powers, controls etc).

## Slide 11: IOC Factory
Reads configuration data, dependencies and relations from CCDB
Generates startup scripts to start an EPICS IOC for the corresponding devices
Includes tools for previewing, browsing and inspecting IOCs deployed on the technical network
Includes version management of IOC configurations
Developed internally at ESS

## Slide 12: IOC Factory

## Slide 13: PLC Factory - Overview
Problem description: The ESS Integrated Control System (ICS) Division will make extensive use of Programmable Logic Controllers (PLCs) to implement the ESS controls. To ensure a consistent approach to PLC development, one proposed strategy is to store engineering information in the ESS Controls Configuration Database (CCDB), from where a client application could extract information to generate template files for use by the Siemens PLC development software.
2016
2017
2018
Read from CCDB
Manual generation of CCDB template files
Automation of CCDB template file generation
Archiver config
Autosave config
Generates templates files for the Siemens 1500 PLC family
Added support for Beckhoff TwinCat3
Notes: Autosave: Saves user editable parameters for the IOC to non-volatile storage. Makes parameters persist through power cycle.

## Slide 14: PLC Factory - Workflow
Planning
Project plan
P&ID
Devices
Define DEVICE TYPES
Create DEVICE LIST
CCDB
Create ESS names
I/O List
PLC Factory
TIA Portal
EPICS
Run python script
Data pulled from CCDB using REST
Import files generated by PLC Factory
Compile and test
Deploy in EPICS environment
Create CCDB types
Build project tree
Verify connection using EasyTester
Verify functionality

## Slide 15: PLC Factory - Workflow
Planning
Project plan
P&ID
Devices
Define DEVICE TYPES
Create DEVICE LIST
CCDB
Create ESS names
I/O List
PLC Factory
TIA Portal
EPICS
Run python script
Data pulled from CCDB using REST
Import files generated by PLC Factory
Compile and test
Deploy in EPICS environment
Create CCDB types
Build project tree
Verify connection using EasyTester
Verify functionality
Notes: Define device types: Create a set of “classes” for the different devices in you P&ID, based on common set if I/O’s. For each device type create a text file and attach to your device in CCDB.
Create device list: The list of specific devices of defined device types. Excel file.

## Slide 16: PLC Factory - Workflow
Planning
Project plan
P&ID
Devices
Define DEVICE TYPES
Create DEVICE LIST
CCDB
Build project tree
I/O List
PLC Factory
TIA Portal
EPICS
Run python script
Data pulled from CCDB using REST
Import files generated by PLC Factory
Compile and test
Deploy in EPICS environment
Create ESS names
Create CCDB types
Verify connection using EasyTester
Verify functionality

## Slide 17: PLC Factory - Workflow
Planning
Project plan
P&ID
Devices
Define DEVICE TYPES
Create DEVICE LIST
CCDB
Create ESS names
I/O List
PLC Factory
TIA Portal
EPICS
Run python script
Data pulled from CCDB using REST
Import files generated by PLC Factory
Compile and test
Deploy in EPICS environment
Create CCDB types
Build project tree
Verify connection using EasyTester
Verify functionality
Notes: --plc-interface=14 indicates TIA portal version
--eee indicates to generate IOC code

## Slide 18: PLC Factory - Workflow
Planning
Project plan
P&ID
Devices
Define DEVICE TYPES
Create DEVICE LIST
CCDB
Create ESS names
I/O List
PLC Factory
TIA Portal
EPICS
Run python script
Data pulled from CCDB using REST
Import files generated by PLC Factory
Compile and test
Deploy in EPICS environment
Create CCDB types
Build project tree
Verify connection using EasyTester
Verify functionality
Notes: Siemens TIA portal generates Pascal code from the imported PLC factory code

## Slide 19: PLC Factory - Workflow
Planning
Project plan
P&ID
Devices
Define DEVICE TYPES
Create DEVICE LIST
CCDB
Create ESS names
I/O List
PLC Factory
TIA Portal
EPICS
Run python script
Data pulled from CCDB using REST
Import files generated by PLC Factory
Compile and test
Deploy in EPICS environment
Verify connection using EasyTester
Verify functionality
Create CCDB types
Build project tree
Notes: EasyTester, 3rd party tool that checks communication between PLC and IOC

## Slide 20: PLC Factory – Change management
Procedure for making an update in generated configuration:
Update the definition file .def file for the device types
Update information in CCDB
Execute PLCFactory script
Update the generated external source file for the PLC project. This will overwrite changed PLC blocks.
Limitation: Generated PLC code cannot be changed manually. Any manual changes will be overwritten by the procedure above.
Revision management: The PLC Factory script is version managed along with source code in GIT.
Configuration management: No configuration management to ensure internal consistency between CCDB version <-> IOC Factory version <-> PLC factory version <-> Version of PLC source code. At present time not deemed necessary, but could be an area for future improvement.

## Slide 21: Summary
ESS has been working with tools for automating the configuration of control systems since 2016.
The plan going forward is to increase the integration between different parts of the tool chain to entirely remove manual steps in the process.
The automation has contributed positively to capability to deliver control systems
Problem areas identified in the areas of maintenance, change management and configuration management