## Slide 1: Update on Target Station Accident Analysis
Per Nilsson
CFD Specialist
www.europeanspallationsource.se
9 October, 2018
Notes: 18/10 13.30 Update on Target Station Accident Analysis (AA) 45m Saturn
- Monolith pressure relief system requirements and design
- Dose calculation procedure for accident analyses

## Slide 2: Outline
AA status
Monolith pressure relief
Dose calculations

## Slide 3: Charge
Does the design philosophy and the methodology for dose calculations provide a solid basis for licensing of the Target Station?
We also ask the committee to advice on how to improve the efficiency of the procedure for dose calculations.

## Slide 4: Summary in text to be read, not presented
The presentation covers two associated topics:
Design and analysis of the monolith pressure relief
Methodology for obtaining doses in the accident analyses
The monolith vessel is normally kept evacuated by pumps, but may be rapidly pressurised by large leaks from fluid systems. These pressurise in different ways and have different inventories. The wheel helium gives the fastest pressurisation but contains limited inventory. The cold moderator system has a similar capacity to pressurise, contains essentially no inventory, but hydrogen is explosive. The water systems cannot pressurise to relief, but contain significant inventory.
These capacities, together with requirements on thin neutron windows and a long distance to the outside, result in competing requirements on the relief line. The design pressure of the vessel and windows is 2 bar(g), which requires low pressure losses in the relief line. The closest path to the roof of the target building is about 45 m and there is very limited space around the monolith, preventing large dimensions, resulting in high losses.
The current design includes a rupture disc and an unfiltered direct release at the roof. This dynamic relief process has been simulated and it is concluded to be acceptable.
Is this sufficent and efficient or are there alternatives?
Each of the 22 target Accident Analyses (AAs) contain at least one, but most often several, calculated radiological doses. The AAs are currently under significant change to comply with authority requirements. Changes to parts of the analyses are expected to continue into operation.
The accident analysis and dose calculation procedure is composed of complicated and iterative parts, involving different competences. Initially, the inventories are calculated by specialist physicists, based on the design.
Now at a first stage, it has to be assumed that there is no functional safety system. The accident scenarios are found, developed and described, mainly by the engineers responsible for the design of the systems. Then the simplified descriptions of the flow of inventory are transferred from the engineers of the system to other specialist physicists. They calculate the dilution, decay, dispersion, exposure and finally the unmitigated doses. By these the engineers can assess whether safety functions are needed and what the requirements are on those, e.g. quality.
In the second stage, the same process is followed including the safety functions to confirm that the consequences, the mitigated doses, are acceptable compared to the objectives.
Both stages are wrapped up in the dose calculation and AA reports.
Is this sufficent and efficient or are there alternatives?

## Slide 5: Accident Analyses
22 AAs released early 2017, with that SSM application
Changes since then: - Review comments from SSM, e.g. tracability - New release fractions from tungsten, due to TOAST - Strictly deterministic process, assessing alternatives - Operational group functions, e.g. MPS, may be used - Different, separate framework for workers - Minor decreases in dose calculations
Handful revised with next SSM application, only public AA1, AA3, AA4, AA10, AA11, AA13 and AA14

## Slide 6: Monolith Vessel Pressure Relief

## Slide 7: Accidents
AA1 Wheel stop
AA2 Bad beam
AA3 Lost cooling
AA4 Wheel leaks
AA9 Hydrogen leak
All can pressurize
monolith vessel
Released AAs: Tightness required for workers

## Slide 8: Two problems
Rapid pressurization by helium or hydrogen
Significant inventory in water slowly evaporating
Optimal but difficult: Release the pressure then confine the inventory

## Slide 9: Void volumes in vessel
Relief in upper volume
Release in lower volume
->
Pressure difference

## Slide 10: Relief line solution
5 m DN350
40 m DN500
Unfiltered
Target roof at 30 m
Rupture disc

## Slide 11: Simplified model
NBW
PBW
Rupture disc to relief line
Shielding
Monolith vessel
Tungsten
in wheel helium
H2 in vacuum
Flange
5 m DN350
40 m DN500
Unfiltered
Target roof at 30 m
Wheel shaft and helium system
also modeled to get limited pressure
Upper volume
Lower volume

## Slide 12: Modelica (by Emil Lundh)
Model only handles one gas (chose helium)
Tricking by cold helium in relief line to mimick air
Well below 2 bar(g) = 3 bar(a)
Upper volume
Lower volume

## Slide 13: RELAP5 (by Pascal Veber)
Also well below 2 bar(g) = 3 bar(a)
Upper volume
Lower volume
Massflow about 25 kg/s 0.15 kg/m3 –> 170 m3/s

## Slide 14: RELAP5 (patch 5)
Due to size of the relief line
it works like a large vessel
Therefore additional length
makes small difference
(lower volume)

## Slide 15: Hydrogen release (by Hideki Tatsumoto)
Massflow about 1.4 kg/s 0.075 kg/m3 –> 19 m3/s
OK!

## Slide 16: Solution alternatives
Separate relief line (current solution) + Low pressure losses
Direct to stack - Higher pressure losses + More elevated release, via existing monitoring
Add filters or similar - Higher pressure losses + Removes particles
Relief valve instead of rupture disc - Active component + Releases pressure, then confines slow processes
Issues: What quality class Is monitoring required
Recommendations?

## Slide 17: Dose calculation procedure for accident analyses

## Slide 18: Dose calculation flow
Design
System & Operation
System Description
Calculate Activation
Inventory
Analyse Accident Unmitigated
Inventories & Flows Unmitigated
Calculate Doses Unmitigated
Doses Unmitigated
Analyse Accident Mitigated
Inventories & Flows Mitigated
Calculate Doses Mitigated
Doses Mitigated
Accident Analysis
Report Accident Analysis
Need and importance
of safety functions
Sufficiency
of safety functions
Show
safety case

## Slide 19: Analyse accident scenario - Unmitigated
Event initiation from hazard analysis
Probability -> Event class & dose limits
Sequence, e.g. quantifying - Heat load - Oxidiser access - Damage to MAR, e.g. tungsten - Combustion - Pressurisation and flow out

## Slide 20: Analyse accident scenario - Unmitigated
Operational group functions, e.g. MPS and pipe quality may be used
No safety functions, e.g. TSS and ventilation may not be used
Requires multiple alternatives

## Slide 21: Multiple release paths investigated
f
f
LP-101
LP-101b
LP-113
LP-113
LP-102b
LP-102
20 m
30 m
45 m
10 m
LP-104
f
Stack flow is more dispersed and diluted Ventilation is faster than leaks
Large rooms dilute and delay more
Large rooms may have higher leak rate
Which is worse? -> Calculate multiple!
EXAMPLE LEAK PATHS

## Slide 22: Transfer of flow description
Release | Affected | ARF | Release time | Inner volume | Volume flow | Emission height
Helium coolant | MAR*DR = 30 kg Target coolant | 1 | 100 s < t < 110 s | Monolith 4 m3 | Average 18 Nm3 /s for 10 s | 30 m
Filter particles | MAR*DR = 10 g Filter aerosols | 0.01 | 100 s < t < 110 s | Monolith 4 m3 | Average 18 Nm3 /s for 10 s | 30 m
Moderator water | MAR*DR = 400 kg Moderator Water | 0.46 | 100 s < t < 20000 s | Monolith 4 m3 | (in conversion to volume flow a density of 0.5 kg/m3 should be used) | 30 m
Tungsten target oxidation | MAR*DR = 54.7 kg Tungsten | Aerosols = 0.4 Volatiles = 0.4 Gases = 1 | 200 s < t < 1000s | Monolith 4 m3 |  | 30 m
Tungsten target diffusion | MAR*DR = 1100 kg Tungsten | Gases = 8.8*10-4 Hydrogen = 1 | 200 s < t < 1000s | Monolith 4 m3 | Following the same release rate as the tungsten | 30 m
Beryllium moderator melting | MAR*DR = 15.7 kg Beryllium | Aerosols = 0.01 Volatiles = 0.01 Gases = 1 | 200 s < t < 1000s | Monolith 4 m3 | Following the same release rate as tungsten | 30 m
Tungsten target explosion | MAR*DR*ARF = 54.7 kg tungsten | Aerosols = 0.003 Volatiles = 0.003 Gases = 0 | 5000 s | Monolith 4 m3 | Instantly, after 5000 seconds. | 30 m
EXAMPLE in AA3

## Slide 23: Transport and Decay
EXAMPLE in AA3
Each Line: one source
one model
one system of ODEs
Fit to Weibull function each
Solve

## Slide 24: Simpified volumes
V0
V2
V4
N0
N2
N4
N6
S

## Slide 25: Spread calculations
Gaussian plume
Relative concentration
Depends on e.g.
- Height
- Duration

## Slide 26: Exposure calculation
Different for the four exposures
Cloud shine
Inhalation (e.g. rate)
Ground shine (e.g. deposition)
Ingestion (e.g. deposition and consumptions)
All depend on location and duration

## Slide 27: Dose calculation
All of the above
Dose coefficients, here based on isotope

## Slide 28: n
Accident Analysis
Transport and Decay Calculations
Calculation Inner Source
Dose
Calculation
Average activity concentration
Dose
Inner Source Term
Inventory
Inventory
Flow
Weather Calculation
Relative Concentration
Deposition
and Exposure Calculation
Exposure Concentration
Calculation Inventories
Dose Coefficents (per isotope)
Exposure metrics (inhalate, cloud, ground, ingest)
Release heights
(10,20,30,45)
Outer Source Term
Release Fractions (per isotope)
Weather metrics
50 % & 90 %
Design and Operation
Calculation Outer Source
Methods:
Leif Spanier

## Slide 29: Time consuming process
For 1 well defined dose it takes of the order of a day to calculate sources, transport, (weather, exposure) and dose
Several files are generated, MathCad, Excel
Reports and reviews add on
Changes, iterations and errors multiply the times it is needed (22 AAs are done in the first round, but all are revised)
In the order of 100 dose calculations needed (22 AAs, several sources, alternative scenarios etc.)
Notes: 1 target line review
3 ESH reviewers

## Slide 30: Changes repeated
Review comments from SSM, e.g. Tracability
New release fractions from tungsten, due to TOAST
Strictly deterministic process, assessing alternatives
Operational group functions, e.g. MPS, may be used
Different, separate framework for workers
Minor decreases in dose calculations

## Slide 31: Strict alternative
Design
System & Operation
System Description
Calculate Activation
Inventory
Analyse Accident Unmitigated
Inventories & Flows Unmitigated
Calculate Doses Unmitigated
Doses Unmitigated
Analyse Accident Mitigated
Inventories & Flows Mitigated
Calculate Doses Mitigated
Doses Mitigated
Accident Analysis
Report Accident Analysis
Need and importance
of safety functions
Sufficiency
of safety functions
Show
safety case
Several reports

## Slide 32: Software alternative
Design
System & Operation
System Description
Calculate Activation
Inventory
Analyse Accident Unmitigated
Inventories & Flows Unmitigated
Doses Unmitigated
Analyse Accident Mitigated
Inventories & Flows Mitigated
Doses Mitigated
Accident Analysis
Report Accident Analysis
Need and importance
of safety functions
Sufficiency
of safety functions
Show
safety case
Calculate Doses Unmitigated
Calculate Doses Mitigated
Expert
Review
worst dose
Develop dose calculation software

## Slide 33: Simplifications?
Doses tabulated in some manner?

## Slide 34: Does the design philosophy and the methodology for dose calculations provide a solid basis for licensing of the Target Station? We also ask the committee to advice on how to improve the efficiency of the procedure for dose calculations.
Charge repeated