## Slide 1: Ion Source & Supporting Systems
Øystein Midttun
System Leader – Ion source and LEBT
SRR 1 – Ion Source & LEBT
2018-07-17--18

## Slide 2: System – Ion source
Plasma chamber
Extraction system
Pumping box
Solenoid
2 x steerer
Gate valve
Iris
Diagnostics tank
Gate valve
Solenoid
2 x steerer
Chopper
EMU H+V
Faraday cup
NPM H+V
Doppler shift
2 x TMP
Repeller
Repeller
ACCT
2 x TMP
Commissioning tank (RFQ)
2 x TMP
HV power supply
Isolation transformer
Collimator
Magnetron
H2 bottle
Ion source
LEBT 1
LEBT 2
3 x solenoid
Waveguide
Primary pump
Primary pump
High voltage (HV) platform
Ion source
Low energy beam transport (LEBT)
PSS0 controlled area
and radiation shielding
Front End and Magnets
Cooling water
Vacuum
PSS
Beam Diagnostics
Control system
ACCT
Voltage divider
EMU H+V
Faraday cup
NPM H+V
Doppler shift
HV controls
Ground potential controls
Beam stop
Alternative location of beam instruments for commissioning
N2 bottle
ACCT: AC current transformer
EMU: Emittance measurement unit
NPM: Non-invasive profile monitor
TMP: Turbomolecular pump

## Slide 3: Table of content
System Requirements
Specific safety and protection systems
Test & Verification
Open issues

## Slide 4: System Requirements – Beam parameters from the ion source
Particle Protons (H+)
Proton current 74 mA
Proton fraction > 75%
Energy 75 kV
Pulse length 6 ms
Repetition rate 14 Hz
Duty cycle 8%
Emittance (99%) 1.8 mm mrad
Stability
  Flat top ±2%
  Pulse to pulse ±3.5%

## Slide 5: Microwave discharge ion source
Waveguide
Solenoid magnets
Plasma chamber
H2 gas injection
High voltage insulator
Extraction electrodes
Pumping ports
50 cm

## Slide 6: The plasma generator sits inside a high voltage platform

## Slide 7: Electrode at ground potential extracts the beam from the plasma

## Slide 8: Specific safety systems – Hydrogen gas
H2 bottle
Injection point
– ATEX zone in unused part of the HV platform
– Build a “U” shape to isolate to H2 bottle from source of ignition
– Holes in the roof and door allows dilution of the gas in case of a leak
– ESS-0333368 - Risk assessment and area classification for the ion source hydrogen system

## Slide 9: Protection systems – Temperature sensors and flow meters on cooling water manifold
– Temperature switches on solenoids
– Controlled by the interlock system

## Slide 10: Test & Verification – ESS-0317305 - Ion source and LEBT verification plan
System testing
  High voltage
  Isolation transformer
  Magnetic system of plasma generator
  Magnetron and microwave injection
  Repeller electrode
  Gas injection
  Plasma generation
Protection systems testing
  Manual testing of interlocks, i.e. flow meters, temperature and pressure sensors

## Slide 11: Outstanding issues
# | System/Comp. | Status | Description | Due date | Remark
1 | Ion source test and verification | Not started | All tests in the verification plan | end-August | Procedure defined in ESS-0317305 - Ion source and LEBT verification plan
2 | ATEX zone | Being designed | “U” shape of aluminium (or steel) to enclose and hold the H2 bottle | mid-August | The ATEX classification of the area is completed