## Slide 1: Ion Source and LEBT control system topology, Interlock strategy
Saeed Haghtalab
Control System Engineer
SRR 1 – Ion Source & LEBT
2018-07-17--18

## Slide 2: System – Control System
Plasma chamber
Extraction system
Pumping box
Solenoid
2 x steerer
Gate valve
Iris
Diagnostics tank
Gate valve
Solenoid
2 x steerer
Chopper
EMU H+V
Faraday cup
NPM H+V
Doppler shift
2 x TMP
Repeller
Repeller
ACCT
2 x TMP
Commissioning tank (RFQ)
2 x TMP
HV power supply
Isolation transformer
Collimator
Magnetron
H2 bottle
Ion source
LEBT 1
LEBT 2
3 x solenoid
Waveguide
Primary pump
Primary pump
High voltage (HV) platform
Ion source
Low energy beam transport (LEBT)
PSS0 controlled area
and radiation shielding
Front End and Magnets
Cooling water
Vacuum
PSS
Beam Diagnostics
Control system
ACCT
Voltage divider
EMU H+V
Faraday cup
NPM H+V
Doppler shift
HV controls
Ground potential controls
Beam stop
Alternative location of beam instruments for commissioning
N2 bottle
ACCT: AC current transformer
EMU: Emittance measurement unit
NPM: Non-invasive profile monitor
TMP: Turbomolecular pump

## Slide 3: Table of content
System Requirements
Control System Architecture
Operating & safety procedures
Test & Verification
Outstanding issues

## Slide 4: System Requirements
Be based on ICS standards (EPICS, Naming, HW, SW toolchain, etc.)
Controls of equipment both in Ground and High Voltage Platform
Local protection system
Timing signals to ISrc-LEBT equipment and BD instruments
ESS-0214258 : ISrc and LEBT Controls - System Requirement Specification

## Slide 5: Control System Architecture - ISrc
Scalance
X204-2 (0)
CAT5 Ethernet (10.10.1.xxx)
Fibre
Modbus TCP
Serial, etc.
Serial Server
SCPI
Source Coils PS (x3)
Source IPC
Profinet
Magnetron
EtherCAT I/O - HV
EtherCAT I/O - GND
Source VME
HV PS
Repeller Electrodes PS (x2)
Source PLC
Remote I/O
ASCII
Mass Flow and Gauge Controller
SCPI
SCPI
Controls Equipment (PLC, IPC, I/O, etc.)
LINAC Equipment (PS, etc.)
Scalance X212-2 (1)
Modbus TCP
Scalance X212-2 (6)
ATU
Electrical, etc.
(physical I/O, power, etc.)
Scalance
X204-2 (2)
Scalance
X204-2 (3)
Scalance
X204-2 (5)
CU1561
CU1561
Scalance
X212-2 (4)
1
CAT5 Ethernet (10.10.0.xxx,
Channel Acces, boot, nfs,…)
ESS-0177833 : ISrc and LEBT Controls - Detailed Systems Design Document
Profinet
HV Platform
Source PLC

## Slide 6: Control System Architecture - LEBT
Controls Equipment (PLC, IPC, I/O, etc.)
LINAC Equipment (PS, etc.)
ESS-0177833 : ISrc and LEBT Controls - Detailed Systems Design Document
NPM IPC
ASCII
IRIS GB
EMU VME
EMU GB
EMU PLC
DSM
IPC
BCM MTCA
To ISRC
VME
To ISRC
VME
EMU IPC
EMU ECAT
1
To Source
VME
NPM
IRIS
Chopper
FC
EMU
DSM
BCM
DSM Spectrometer
Camera
FC MTCA
FC ECAT
Magnets
To ISRC
PLC
DSM ECAT
CAT5 Ethernet
Fibre
Serial, etc.
Electrical, etc.
(physical I/O, power, etc.)
NPM ECAT

## Slide 7: Operating Procedures

## Slide 8: Protection Procedures
ISrc-LEBT Control system doesn’t have any personal safety functionality.
ESS-0121186 : ISrc and LEBT Interlock PLC user manual

## Slide 9: Test & Verification
Automatic test tool “WeTest”:
  Reads scenario input.
  Write the PV value.
  Compare the write value with feedback.
  Generate verification report.
ESS-0265170 : ISrc-LEBT Control System Verification Plan
ESS-0135274 : ISrc-LEBT Acceptance Tests Report (Catania)

## Slide 10: Outstanding issues
# | System/Comp. | Status | Description | Due date | Remark
1 | ISrc-LEBT control system | Not started | Control Test and Verification | 2018-08-31 | 
2 | Lund Migration | In progress | Naming convention, SW toolchain | 2018-08-31 | 
3 | ISrc Control | In progress | Iris thermocouples Isolation transformer switches | 2018-07-20 | 
4 | FaradayCup – Ion Source | Not started | Remove FaradayCup controls from ISrc VME since controls are moved to MTCA | 2018-07-27 | 
5 | Iris Motion Control | In progress | Iris Geobrick motion control will be ported to EtherCAT |  | 

## Slide 11: LEBT

## Slide 12: High Voltage Lan

## Slide 13: Coils

## Slide 14: Magnetron

## Slide 15: Chopper Gas

## Slide 16: Solenoid 1

## Slide 17: Solenoid 2

## Slide 18: High Voltage

## Slide 19: Ground Lan

## Slide 20: Chopper 2

## Slide 21: Faraday Cup

## Slide 22: Chopper 2