## Slide 1: ESS Shielding Simulations MaGIC and Estia
Uwe Filges
Laboratory for scientific Developments and novel Materials (LDM)
Paul Scherrer Institut

## Slide 2: MAGiC beamline layout
polarized single crystal diffractometer at beamport W6
Cold & thermal beam extraction
Elliptic guide system with a kink at 80 m

## Slide 3
Chart: 
| 0.01 | 0.015 | 0.02 | 0.03 | 0.04 | 0.05 | 0.06 | 0.08 | 0.1 | 0.15 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.8 | 1.0 | 1.5 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 8.0 | 10.0 | 50.0
 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1551740 | 643100 | 2563150 | 3018140 | 5547380 | 0 | 2180120 | 0 | 11895100 | 0 | 0
Chart: 
| 1.0E-9 | 1.0E-8 | 2.5E-8 | 1.0E-7 | 2.0E-7 | 5.0E-7 | 1.0E-6 | 2.0E-6 | 5.0E-6 | 1.0E-5 | 2.0E-5 | 5.0E-5 | 0.0001 | 0.0002 | 0.0005 | 0.001 | 0.002 | 0.005 | 0.01 | 0.02 | 0.03 | 0.05 | 0.07 | 0.1 | 0.15 | 0.2 | 0.3 | 0.5 | 0.7 | 0.9 | 1.0 | 1.2 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 12.0 | 14.0 | 15.0 | 16.0 | 18.0 | 20.0 | 30.0 | 50.0 | 100.0 | 150.0 | 200.0 | 500.0 | 1000.0 | 2000.0
 | 0 | 2156930 | 8356400 | 22543400 | 9023670 | 2591130 | 823884 | 3631510 | 2232450 | 916409 | 2800480 | 1261420 | 0 | 0 | 1933920 | 2236060 | 1047120 | 985644 | 1294290 | 1147490 | 5166170 | 8033050 | 8018710 | 14730600 | 22464200 | 0 | 27969600 | 16245100 | 31704900 | 35408200 | 0 | 46727600 | 0 | 126500000 | 116456000 | 0 | 0 | 0 | 70030900 | 0 | 0 | 71450300 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
W6 – beam exit 30 mm x 38 mm
Neutron and prompt gamma dose rates at 5.5m (W6)
Energy (MeV)
Gamma dose rate (muSv/h)
Total: 27 Sv/h
Energy (MeV)
Neutron dose rate (muSv/h)
Total: 447 Sv/h
Note: no other beamports are modelled
W6 – beam entrance 30 mm x 124 mm
Neutron flux: 8.4*E9 n/s/cm2

## Slide 4
Chart: 
| 0.01 | 0.015 | 0.02 | 0.03 | 0.04 | 0.05 | 0.06 | 0.08 | 0.1 | 0.15 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.8 | 1.0 | 1.5 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 8.0 | 10.0 | 50.0
 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 17433.9 | 12005.7 | 15379.9 | 50454.4 | 34971.2 | 270939 | 53260.1 | 55071 | 85519.1 | 195083 | 3520.22 | 725.898
Chart: 
| 1.0E-9 | 1.0E-8 | 2.5E-8 | 1.0E-7 | 2.0E-7 | 5.0E-7 | 1.0E-6 | 2.0E-6 | 5.0E-6 | 1.0E-5 | 2.0E-5 | 5.0E-5 | 0.0001 | 0.0002 | 0.0005 | 0.001 | 0.002 | 0.005 | 0.01 | 0.02 | 0.03 | 0.05 | 0.07 | 0.1 | 0.15 | 0.2 | 0.3 | 0.5 | 0.7 | 0.9 | 1.0 | 1.2 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 12.0 | 14.0 | 15.0 | 16.0 | 18.0 | 20.0 | 30.0 | 50.0 | 100.0 | 150.0 | 200.0 | 500.0 | 1000.0 | 2000.0
 | 268.721 | 23010.9 | 93952.4 | 425566 | 100230 | 46640.7 | 31763.6 | 32380.1 | 65906.9 | 49241.9 | 32514.5 | 51999 | 30841.9 | 30841.2 | 72611.8 | 60738.8 | 28595.1 | 38973.1 | 45937.9 | 39297.6 | 53692.5 | 54685.7 | 75354.9 | 155832 | 174810 | 1212810 | 1047980 | 983983 | 719203 | 668098 | 247051 | 807555 | 1504820 | 1158830 | 973079 | 806250 | 316152 | 220140 | 163676 | 123666 | 100232 | 149825 | 115187 | 46705.5 | 40689.6 | 75148.7 | 61631 | 191404 | 143809 | 95198.9 | 30346.8 | 32710.3 | 29782.3 | 3565.69 | 214.669
Neutron and prompt gamma dose rates at 24.5 m (W6)
W6 – vacuum channel 10 cm x 10 cm (0.5 deg tilt)
Dose rates @ 24.5m
Energy (MeV)
Gamma dose rate (muSv/h)
Total: 0.79 Sv/h
Energy (MeV)
Neutron dose rate (muSv/h)
Total: 13.8 Sv/h
New SDEF-card defined for guide shielding calculations
Neutron dose rate
Gamma dose rate

## Slide 5
Neutron dose rates along guide system (W6)
A
D
B
Shielding around guide:
10 cm borated concrete
10 cm standard steel
50 cm standard concrete
cross section inside shielding: 50 cm x 50cm
New neutron source definition
(SDEF card)
Source – tally S: 13.8 Sv/h
@77m - tally A: 8.8 mSv/h
fast neutron flux: 4.7E4 n/cm2/s
@30m – outside guide shielding
tally B: 3.4 µSv/h
@50m ouside guide shielding
tally C: 1.9 µSv/h
@77m ouside guide shielding
tally D: 1.1 µSv/h
S
C

## Slide 6
Shielding the direct beam at 77m
Remember:
@77m center of beam: 8.8 mSv/h neutron dose rate
Beam dump consists of 50 cm
heavy concrete (4.9 g/cm3)
Concrete includes 5 % B4C
Behind beam dump:
n-dose rate : 1.6 µSv/h
g-dose rate : < 0.1 µSv/h
Detector size: d=6 cm
30 n/s/cm2

## Slide 7
150m Guide Shielding
F
Shielding around guide behind 77m:
2m heavy concrete with vacuum tube belt
75m standard concrete (0.5 m thickness)
Source – tally S: 13.8 Sv/h
@80m ouside guide shielding
tally E: 1.3 µSv/h
@150m inside guide shielding
tally F: 0.2 µSv/h
4.2 n/s/cm2
neutrons
E
Chart: 
Neutron background at 150 m

## Slide 8
High energy shutter setup
6 drums are positioned within the neutron bunker wall.
Drum Sequence:
Borax (50% epoxy / 50% B4C)
Standard steel
Standard steel
Borax
Standard steel
Tungsten/parafin (density 11.8 g/cm3)
Effective thickness: each drum 20 cm
n-dose rate: 15.2 µSv/h
g-dose rate: 0.5 µSv/h
(only prompt gammas from the drums)
N-Dose rate can be reduced more by replacing steel with tungsten drums.

## Slide 9: Estia – E2 Beamport
E2 – Estia beamport
Reflectometer at beamport E
Cold neutron beam line
Elliptic guide system (Selene) – only 40 m long

## Slide 10
Instrument Design Overview
Estia Beamline:
Only one Chopper
Elliptic feeder to Virtual Source

## Slide 11
Shielding Concept - Insert
Additional shielding Cu
large dimensions of the feeder (opening 210 mm x 68 mm)
Dose rate reduction by factor 2-3 by additional shielding inside feeder

## Slide 12
Shielding concept - inside the bunker
Virtual Source collimators
FeNi Tungsten
750 Sv/h (n-dose rate)
mainly neutrons < 8 MeV
35 kSv/h (n-dose rate)
Shielding block inside bunker wall
Cu + Hydrogen compound
LFeNi = 60 cm (opening 37 mm x 84 mm)
LW = 30 cm (opening 20 mm x 70 mm)
L Cu = 99.5 cm

## Slide 13
Shielding Concept – Along the Selene guide
Guide support
mineral cast (concrete with epoxy) or granite
Shielding block
mineral cast
Standard guide shielding (not optimised)
20 cm steel
50 cm borated concrete
Heavy concrete

## Slide 14: Dose rates outside the bunker
borated concrete (Carsten) 70 cm thickness
PSI mineral cast - around 25 cm
Copper collimator (to be optimized)
N-Dose detector position
1.2 µSv/h
Neutron flux after copper collimator
Energy (MeV)
Neutron flux (n/s/cm2 )
ca. 140 mSv/h

## Slide 15: PSI standard shielding
14 different standard geometries are available
9 types are used side-walls
5 types are special made for building bunker roofs
Materials
normal concrete
borated concrete (5% boron carbite)
scrap metal concrete (density around 4g/cm3)
Two types of crane connectors

## Slide 16: Bunker design
BOA % ICON beamline
Back wall
Borated concrete
Thickness: 1m
Side walls
Standard concrete
Thickness: 0.5 m
Roof
Normal concrete
Thickness: 0.5 m
Side walls between beamlines
Scrap metal concrete
Thickness: 0.5 m

## Slide 17: Cabling in the bunker
Chicane: yes or not ?
BOA: chicane with standard elements
in 1 m height from the floor
ICON: no chicane but the cable channel is in 2.5 m heigth from the floor
Cable channel never at the back-side

## Slide 18: Handling – practical issues
Standard blocks are built with a 45 deg edge around the block -> avoiding spalling/peeling during positioning
Another aspect: turning of the elements is possible
Problem: 4 blocks assembled results in a 2 cm x 2 cm
gap !!
Solution: gap filled with a Pb / PE laminat structure

## Slide 19: Guide shielding outside the bunker
shielding: 120 mm steel around the guide; 50 mm on the lower region
Additional shielding to public ways: 500 mm standard concrete blocks (fullfiled < 1 µSv/h)

## Slide 20: Guide shielding – Design
Shielding can be extended.
Guide shielding has steps.
Guide shielding stays on 10 cm foots.