## Slide 1: The wonderful world of motors from a mechanical engineers perspective.
Nick Webb

## Slide 2: Motion control team ISIS
Kyle
Simon
Ben
Jon
Nick
Steve

## Slide 3: Summary
Different types of motor and the applications you might use these in
What do we need to know to spec a motor
Motor calculations worked example

## Slide 4: Different types of motor and the applications you might use these in

## Slide 5: Choice of motor
Pneumatic
Hydraulic
Linear motor
piezo
Electric rotary
  Stepper
  Servo

## Slide 6: Pneumatic
PRO’S
  Air is free and everywhere
  Control and mechanics are basic
  Can be fast acting
  Good for in – out of the beam type operations
  Air wont become active the same way a oil will
  Clean (no hydraulic oil to leak)
  Can be designed to fail safe if air is lost
CON’s
  Noisy
  Control is basic
  Accuracy defined as dead stop

## Slide 7: Pneumatic application
ISIS use Pneumatics for safety shutters on vacuum tanks,
Neutron monitors in and out the beam

## Slide 8: Hydraulics
PRO’S
Very high force output can be available
Smooth operation/motion profile
System has some natural damping to it and can be designed to withstand shock loading
Can be position/velocity controlled with similar methods to motors
Very suited to linear motion applications
Compact installation as pump can be located away from where force/motion is required
Possible to run many actuators of different sizes off a single pump
CON’S
Hydraulic fluid (different fluids are available) can become active when used with neutrons
Different design skill-set to electrical systems
Requires maintenance staff trained in risks of hydraulic systems
Can be messy.
Users around hydraulics must be aware of the health hazards associated with hydraulic fluid and high pressure systems or the area must be controlled to prevent their access

## Slide 9: Hydraulic applications
At ISIS we use hydraulics to run the shutter on the TS2 due to fail safe properties
Engineering beamlines, stress rigs

## Slide 10: Linear motor
PRO’S
  Fast motion
  Compact design
  Less parts in the design
CON’S
  Holding force when used vertically
  Not suitable for some applications
  Less control over accuracy of motion

## Slide 11: Linear motor application
Commonly used on early slit designs
Vaccum chamber slits

## Slide 12: Piezo
PRO’S
  High resolution
  Non magnetic (polarised beamlines)
  Compact assembly
  Work well in vacuum
CON’S
  More difficult to control
  Cable length, tuning
  Cable size, fragile
  Maintenance
  Extra controller needed
  cost

## Slide 13: Piezo applications
ISIS use piezo motors mainly non magnetic slit assembly.

## Slide 14: Open loop stepper motor
PRO’S
  Add feedback to create a ‘Servo Stepper’ system
  Now seen as a cheap option by industrial users
  Inherent repeatability (step angles of 1.8° or 0.72°)
  Highest torque at low speeds
  Holding ‘detent’ torque
  Stepper motors exist for high radiation environments
CON’S
  Speed limitation (Useful speed 300 rpm
  Low resolution (200 to 500 magnetic steps)

## Slide 15: Stepper application
85% of motors at ISIS are stepper

## Slide 16: Servo Any motor with closed-loop feedback becomes a Servo system. (BLDC) Brush less DC waveform excited synchronous motor (PMSS) AC waveform excited synchronous motor with permanent magnets. Feedback can be resolver, hall sensors or encoders
PRO’S
  Higher speed applications (1000 rpm or above)
  Allows larger gearbox ratios to be used due to higher speed,
  More torque at higher speed, useful for moving large loads
  Fast response times - Useful for ‘tracking’ motion
    fast error correction
  BLDC motors exist for high radiation environments (Space use or ESS)
CON’S
  Needs tuning and feedback to work reliably
  Setup time is high compared to steppers
  Can go unstable on a loss of feedback
  Higher costs likely

## Slide 17: Servo applications
We use servo’s for high torque high speed applications, often stepper has torque but not speed
Freia blocker project that needed smother rotation

## Slide 18: What do we need to know to spec a motor
Load
Accuracy
Speed / duty cycle
Speed vs accuracy vs load
Acceleration
Environment

## Slide 19: Load
Horizontal
Vertical
Gravity
Friction
  Braked

## Slide 20: Accuracy
Calculate resolution by smallest step size
Resolution should be 10 times smaller than accuracy.
High accuracy stepper
Use full step for calculations (motion stop, power off conditions)

## Slide 21: Speed
How fast do you want to move?
10mm/s vs 100mm/s
Calculate real world numbers
Safety / momentum
Sample environment
Large rotations
Stepper torque 300rpm

## Slide 22: Speed vs accuracy vs torque
Motor can limit all 3 of these
Stepper 300rpm 200 steps/rotation
Can gearbox help

## Slide 23: Gearboxes
Adding 10/1 gearbox
  High accuracy
  Low speed
  Small amount extra backlash
  Extra heat
  Bigger assembly
  Encoder, where do you put it ?

## Slide 24: Gearboxes
Adding 1/10 gearbox
  lower accuracy
  Higher speed
  Backlash is amplified
  Extra heat
  Bigger assembly
  Encoder where do you put it ?

## Slide 25: Types of gearbox
Bevel
  90˚rotation change
  Can drive 2 axes from 1 motor
  Low friction
  Multiple ratio choices
  Choice of gear mesh
    Spiral
    Straight

## Slide 26: Choice of gear mesh
    Straight
      + Less Friction
      + Cheaper
      + force in all one direction
      + Needs lower spec bearings
      + less heat
      Needs bigger gear to transmit force
      Noise
      Back lash
    Spiral (Helical)
      + Lower noise
      + High contact area
      + Transmit more force
      More friction
      Expensive
      Thrust force
      Run hotter

## Slide 27: Planetary or Harmonic
Blue (outer circle): circular spline (fixed) Red (middle flexible circle): flex spline (attached to output shaft, which is not shown) Green (inner oval): wave generator (attached to input shaft; inner ball bearing and shaft are not shown)
PRO’S
No backlash
compactness and light weight
High gear ratios 30:1 up to 320:1
Good resolution and excellent repeatability
High torque capability
CON’S
Torsional stiffness
Back winding
Cost
Efficiency can be difficult to calculate

## Slide 28: Worm and wheel
PRO’S
High speed reduction
Silent operation
Self locking due efficiency
Compact geartrain
Can be high precision
CON’S
Manufacturing costs
Extra force needed to drive
Forces created in box
Heat
Heavy casing

## Slide 29: Acceleration
How fast do you need to get up to top speed
Faster accelerations = more torque

## Slide 30: What do we need to know about the environment to spec a motor
Environment
  Frame size
  Magnetic environment
  Vacuum environment
  Hot , cold
  Radiation levels

## Slide 31: Motor calculations worked examples

## Slide 32: Calculating force needed for a motion system (Basics vertical)
Newton’s 2nd law
Force = Mass x Acceleration
Force = Mass x Gravity
N = Kg x m/s²
98.1N = 10Kg x 9.81m/s²
In an inertial frame of reference, the vector sum of the forces F on an object is equal to the mass m of that object multiplied by the acceleration a of the object: F = ma

## Slide 33: Calculating force needed for a motion system (Basics vertical)
Newton 3rd law
Force = Mass x acceleration (Gravity)
Greater apposing force will create upwards motion and acceleration
When one body exerts a force on a second body, the second body simultaneously exerts a force equal in magnitude and opposite in direction on the first body.

## Slide 34: Calculating force needed for a motion system (Basics Horizontal)
Friction resistive force = Input Force x coefficient of friction
Moving an aluminium block on mild steel = 0.61
Use the 10kg box
98.1N = 10Kg x 9.81m/s²
59N = 98.1N x 0.61

## Slide 35: Calculating force needed for a motion system (Friction Basics Horizontal)
On roller bearings friction is 0.01
Use the 10kg box
98.1N = 10Kg x 9.81m/s²
1N = 98.1N x 0.01

## Slide 36: Calculating force needed for a motion system (Friction Basics Horizontal)
On roller bearings friction is 0.01
Use the 10kg box
98.1N = 10Kg x 9.81m/s²
1N = 98.1N x 0.01
Miss alignment of rail and drive couplings will increase friction massively. This will cause the force to rise.

## Slide 37: Calculating the torque needed to drive a leadscrew
Axial force, Gravity?
Lead or Pitch (distance travelled by 1 rotation of screw )
Screw Efficiency
Leadscrews: 20% - 80% Ballscrews: 90%
Efficiency of 50% or greater will back drive.
Screw lead’s less than 1/3 of leadscrew diameter do not back wind
10mm dimeter screw with 2mm lead = 41% Efficiency (< 50% will not back drive)
10mm diameter screw with 25mm lead = 83% Efficiency (> 50% will back drive)

## Slide 38: Calculating the torque needed to drive a leadscrew
10 kg
98.1N
Less than 50%
Wont back wind
Torque (Nm) =
Torque (Nm) =
= 0.05(Nm)

## Slide 39: Loki collimator
Specification
Maximum mass: 6,000 kg
Travel distance: 475 mm
Travel between guides: 250mm
Linear rails : f 0.01
Time to travel distance
Accuracy needed: +-0.01mm
In Vacuum
Constraints
Motor RPM : stepper useable RPM 300- 600
System Resolution (full step): 0.001mm
System lead = 1mm or 0.25mm
Screw jack constraints:
1mm lead with 200 step / rev 1 step = 0.005mm
Speed = 600 x 1 =600mm per minute
0.25mm lead with 200 step / rev 1 step =0.00125mm
Speed = 600 x 0.25 =150mm per minute
Which screwjack neither are correct ?
What about a gearbox?

## Slide 40: Loki collimator Adding a gearbox
Type of gearbox?
  Planetary
Ratio ?
  3:1
3/1 gearbox= 600step per mm
Resolution = 0.0016mm

## Slide 41: Loki collimator
Load
Pitch
Efficiency
Idling torque
Efficiency
Load:
Mass x Gravity x Friction
6000kg x 9.81m/s x 0.01
= 589 N = 0.6KN
Screw jack: 4mm pitch
Screw jack reduction 4:1
0.42 Nm =
+ 0.16 Nm
Drive torque= 0.42Nm

## Slide 42: Loki collimator Torque calculation
Drive Torque MG: 0.42Nm
What is Inertia??

## Slide 43: Calculating Inertia ? What is inertia? I=mr2
Inertia is an object’s resistance to a change in speed.
Controlled by mass of object and distance of mass from axis of rotation
A figure skater on the ice. When she spins with her arms close to her body, her mass is close to her axis of rotation and her rate of spin is fast. But when she extends her arms, the distance of her mass from the axis of rotation is increased, making her inertia larger and causing her to spin at a slower rate.
Solid diesel engine flywheel
Ultralight race engine flywheel

## Slide 44: Loki collimator Inertia
drive torque 0.42Nm
Select motor, vacuum, need to add 3:1 gearbox
Phytron vacuum steppers
350mNm torque x 3 = 1Nm (roughly)
Rotor inertia = 0.15 kg cm2
Screw jack inertia = 0.21kg cm2
To calculate load inertia =
2 x 10-6
0.6 2 x 10-6 =1.519 x 10-12 kg/cm2
Total Inertia J = 0.36Kg cm2
Inertia ratio = = =

## Slide 45: Loki collimator Inertia (adding 3:1 gearbox)
Gearbox inertia = 0.03 kg cm2
J = + gearbox inertia
J = + 0.03 = 0.07 kg cm2
Inertia ratio = = =

## Slide 46: Loki Collimator Angular Acceleration
ω’ = angular acceleration (rad/s2)
N = angular velocity (rpm)
t = acceleration time (s)
=
=
=
= 21 rad/s2
= 628 rad/s2

## Slide 47: Loki Collimator Total acceleration torque
Tacc=J. ω’
Tacc= 1.47 Nm
Tacc= 43 Nm
Will this work ??
Motor + gearbox torque = 1Nm
Tacc = torque due to acceleration (Nm)
J = inertia of the system (kgm2)
ω’ = angular acceleration (rad/s2)
J = 0.07(kgm2)
ω’ = 21(rad/s2)
ω’ = 628(rad/s2)

## Slide 48: Loki Collimator Total acceleration torque
Lower the acceleration to 6s
= = 10.5 rad/s2
Tacc=J. ω’ = 0.07 x 10.5 = 0.735 Nm
Torque total = acceleration torque + drive torque
0.735Nm + 0.42Nm = 1.155 Nm
Still not enough motor torque 

## Slide 49: Loki Collimator try a bigger motor
J = + 0.03 = 0.08 kg cm2
Tacc=J. ω’
0.08 x 10.5 = 0.84Nm
0.84Nm + 0.42Nm = 1.26 Nm
Motor torque with gearbox= 2.52Nm
Factor of safety of 2
What about Accuracy? Can we achieve 0.01mm
3/1 gearbox= 600step per mm
Resolution = 0.0016mm

## Slide 50: Loki Collimator speed calculation
Takes 6s to reach max velocity 200mm /minute
0.2 metres ÷ 60 seconds = 0.0033m/s
Acceleration =
Acceleration = =0.00055m/s2

## Slide 51: Loki Collimator speed calculation
at2
= x 0.00055 x 62
0.0099m = 9.9mm
Acceleration: 0.00055m/s2
Time taken: 6s

## Slide 52: Loki Collimator speed calculation
Time taken to travel between 250mm guide centres
Guide moves 10mm during acceleration and deceleration
How long does it take to travel 230mm
200 ÷ 60 = 3.33
230 ÷ 3.33 = 69s + 12s (accel +decel) = 81s

## Slide 53: Loki collimator Conclusion
Torque needed to move system = 1.26 Nm
Motor and gearbox torque = 2.52 Nm
Motor and gearbox FoS = 2:1
System Resolution = 0.001mm
Time taken to travel 250mm = 81s
Could we up the RPM ?
Could we fit a larger motor ?
Check with scientist if speed is ok ?

## Slide 54: Questions ??? (No difficult maths questions please)
Thankyou for you attention