## Slide 1: MEBT FC, WS, SC and EMU Status
Ángel Rodríguez Páramo
ESS-Bilbao
Beam Instrumentation Group
arparamo@essbilbao.org
November – 2018

## Slide 2: Summary
Introduction
Faraday Cup
Wire Scanners
Scrapers
EMU
Conclusions

## Slide 3: Introduction
ESS-Bilbao develops the MEBT as in-kind contribution to ESS
The MEBT PBI Includes
Interceptive: FC, WS, SC, EMU
Non-Interceptive: BPMs, ACCTs, FCT
  See Seadat Varnasseri talk
Control & Electronics
  See Idoia Mazkiaran talk
The MEBT PBI operates at:
3.63 MeV – 62.5 mA (230 kW)
Nominal Operation: 2.86 ms / 14 Hz
Commissioning Modes:
  Fast Tuning: 5 μs – 14 Hz
  Slow Tuning: 50 μs – 1 Hz

## Slide 4: Introduction
WS
FC
EMU
SC
FC
WS
EMU/Gr
EMU/Sl
SC

## Slide 5: Introduction
BI #1 Lund (Feb. 2016)
BI #2 Bilbao (Oct. 2016)
BI #3 Trieste (April 2017)
BI #4 Paris (Nov. 2017)
BI #5 Lund (Nov. 2018)

## Slide 6: Summary
Introduction
Faraday Cup
Wire Scanners
Scrapers
EMU
Conclusions

## Slide 7: FC
DESIGN
PRODUCTION
ESS CD/TDR (2013)
“For the MEBT Faraday Cup, the challenge is to keep the thermal load below the mechanical limits, given the small beam sizes and the large stopping power of 3 MeV protons.”
The FC is designed for current measurement and as a beam stopper for MEBT commissioning modes.
The FC has been manufactured with a 1 kV repeller for SE suppression and with a graphite collector to withstand the high intensity beam.
Integration with Control & Electronics and in the ESS-Bilbao injector have been done.

## Slide 8: FC: Integration
μTCA Crate
See also Idoia Mazkiaran talk
 | Inst. | FE | BE | MC | μTCA/VME
FC | BIO | BIO | BIO | BIO | BIO
WS | BIO | ET | ET | ESS | ESS
SC | BIO | ESS | ESS | BIO | ESS
EMU | BIO | BIO | BIO | BIO | BIO

## Slide 9: FC: Injector Test
Test Results
-SE Suppression Vrep~400V
Comparison to ACCTs
ESS-Bilbao Injector (45 keV-40 mA)
Electrostatic Field Simulation
- 200 V in the axis for Vrep-1 kV
- SE electrons with E up to ~100 eV*
GPT Simulation
-SE Suppression ~400V
* Drexler et al Physical Review A 53-3, 1996

## Slide 10: Summary
Introduction
Faraday Cup
Wire Scanners
Scrapers
EMU
Conclusions

## Slide 11: WS
DESIGN
ESS TDR
ESS-0020237
Cheymol et al.
PRODUCTION
The wire scanners are designed for measurement of beam profile at 3 MEBT locations in commissioning modes.
Equipped with 34 μm carbon wire and an alignment toolkit has been manufactured for wire placing.
Each carbon wire is connected to triaxial cabling with biased voltages of ± 100 V for minimisation of signal noises.

## Slide 12: WS Acceptance
Vacuum
Continuity
Wire Integrity
*Acceptance Procedure similar for FC, SC & EMU
Motion
FAT

## Slide 13: WS VIT
Signal Integrity from Fork to AFE*
*Change from LEMO FFA to Triax BNC required
Vertical Integration Test (VIT):
ESS-Bilbao Instrument
Elettra AFE & BE
ESS MC, μTCA and EPICs control

## Slide 14: Summary
Introduction
Faraday Cup
Wire Scanners
Scrapers
EMU
Conclusions

## Slide 15: SC
PRODUCTION
DESIGN
Bustinduy et al HB2014
SC are designed to remove beam halo at 3 MEBT locations.
Each scraper blade will remove 0.25 % or 625 W of beam under nominal operation.
To withstand beam irradiation TZM plates over a refrigerated steel support are included.
The TZM plate is electrically insulated with a kapton foil and is connected to a triaxial cable for signal acquisition.

## Slide 16: SC
The 6 SC have arrived to Bilbao:
  SC1 accepted
  Acceptance SC2-6 expected end Nov. 2018
The MC module for SC1&SC2 has been assembled.

## Slide 17: Summary
Introduction
Faraday Cup
Wire Scanners
Scrapers
EMU
Conclusions

## Slide 18: EMU
PRODUCTION
ESS-0020535
(Cheymol et al)
DESIGN
The EMU is composed by two slit and grid subsystems separated ~400 mm for measurement of the phase space in the horizontal and vertical directions.
The slits are made of graphite in order to withstand beam irradiation and have an aperture of 100 μm for minimisation of emittance reconstruction error.
For the grid a prototype has already been manufactured and tested with 24 tungsten wires of 35 μm separated 500 μm.

## Slide 19: EMU
The EMU is under manufacturing
  Arrival to Bilbao is expected for December
EMU Grid PCB Under Review
The BE has been assembled
The FE is being tested
The MC module for EMU/Slits has been assembled.
  For EMU/Grids in under manufacturing

## Slide 20: Summary
Introduction
Faraday Cup
Wire Scanners
Scrapers
EMU
Conclusions

## Slide 21: Conclusions
The FC has been produced, integrated and beam tested
The WS have been produced and the VIT performed
The SC have been produced and acceptance is ongoing
The EMU is under production, arrival expected in December

## Slide 22: Conclusions
Thank You!