## Slide 1
Overview of the JAEA-ADS accelerator
Yasuhiro Kondo, Jun Tamura, Bruce Yee-Rendon,
Fujio Maekawa, Shin’ichiro Meigo, and Hayanori Takei
Japan Atomic Energy Agency (JAEA)

## Slide 2
Contents
Overview of JAEA ADS
Development of linac for ADS at JAEA
Summary

## Slide 3: Nuclear waste problem
Recycle
ADS P&T
Wait 90Sr & 137Cs
decay
Direct disposal
Current policy
How to dispose nuclear waste is the common issue for all humanity.
Japan’s case
  Already exiting 18,000 tons
  If nuclear plant can restart, 1000 tons newly generated (/year/40 plants)
If Partitioning and Transmutation effectively work...,
100,000 y
300 y
Raw waste
HLW
After P&T
Natural U
Potential toxicity (Sv)
Year
Toxic period 1/300
Current plan of geological disposal
https://www.numo.or.jp/
10 km2 required
Disposal space 1/3

## Slide 4: History of JAEA ADS
Omega project start
ADS Conceptual
design
User operation start
1988
1990
2001
2011
Great e. Japan
earthquake
(severe accident of F1 plant)
2019
2009
10th anniversary
JHP start
JHF start
NSP
J-PARC start
KEK project
JAERI (JAEA)
project
included
jointed
Reconsidering
strategy
Concentrated on
J-PARC construction
Funding for TEF
got smaller and
smaller

## Slide 5: Aim of the JAEA ADS
700M
4500M
t1/2 (y)
nuclide
Dose rate
mass
/ton
t1/2 (y)
nuclide
Dose rate
mass
/ton
t1/2 (y)
nuclide
Dose rate
mass
/ton
t1/2 (y)
nuclide
Dose rate
mass
/ton
87.7
24000
6564
14.3
~
~
~
2.14M
432
7370
18.1
0.295M
28.8
1.53M
0.211M
6.5M
0.1M
15.7M
2.3M
30.1
Actinoid
Transuranium
Minor Actinoid
Reduce
  long-term toxicity of
  disposal space for
nuclear waste.
Focus on MA transmutation.
Major long lived nuclide
in 1 ton nuclear waste
Fission Products

## Slide 6: Transmutation of Minor Actinoids
Need ultimate neutron source (~1019 /s J-PARC: 1017 /s)
Example of fission reactions of Minor Actinoids
2.14My
11m
5s
21 h
5d
(stable)
(stable)
LLFP (~10%)
b
b
b
b
n
Fast neutron
fission
MA: High toxicity, burnable by chain reaction

## Slide 7
High intensity proton accelerator + subcritical reactor = ADS
Proton beam
Super-conducting LINAC
Max. 30 MW
Spallation target (LBE)
MA-fueled LBE-cooled subcritical core
Power generation
To accelerator
To grid
Fission energy
800 MW
100 MW
170 MW
270 MW
Features of ADS:
Chain reactions stop when the accelerator is turned off.
LBE is chemically stable.
 High safety is expected.
High MA-bearing fuel can be used.
 MA from 10 LWRs can be transmuted.
Accelerator power 1MW→30MW
Chain reaction x 30
Total 100 gain from existing neutron source

## Slide 8: Conceptual design : Reference ADS
Primary pump
Steam generator
Proton beam
Inner barrel
Beam duct
Beam window
Reactor vessel
Core barrel
Guard vessel
Core support structure
13.5m
11.8m
Beam energy : 1.5 GeV
Max. beam current : 20 mA
Spallation target : Pb-Bi eutectic (LBE)
Coolant : LBE
Max. keff = 0.97
Thermal output : 800 MWt
MA initial inventory : 2.5t (1000 mol)
Transmutation rate : 10%MA / Year (MA from 10 LWRs/year equivalent)
600EFPD (Effective Full Power Days) / 1 batch
Injector
Liq. He
RF
RFQ
DTL
RF
RF
RF
RF
RF
Superconducting linac
Notes: Next, the conceptual design of JAEA’s reference ADS
JAEA's reference design of ADS is a tank-type subcritical reactor.
The accelerated energy is 1.5 GeV. In order to keep the thermal power at 800 MW, the maximum beam current of the linac is set at 20 mA.
The linac consists of a series of 151 klystrons, which were designed for a 972 MHz RF wave. Maximum rated output power of the klystron is 750 kW.

## Slide 9
Neutron Science Project (NSP) at JAERI
IS
SC Linac
Neutron
Scattering
Transmutation
CW beam
Pulse beam
ring
100 MeV -> SC linac
N. Ouchi et al., SRF97, A02
M. Mizumoto et al, LINAC98, TU1004
N. Akaoka et al., SRF99, WEP020

## Slide 10: SFR development for NSC
O. Takeda et al, SRF01 PR013
Design 16 MV/m

## Slide 11: JAERI-KEK joint (JKJ) project → J-PARC (2001)
a
Neutron Science Project (NSP) @ JAERI
Japan Hadron Project (JHP) @ JAERI
Japan Proton Accelerator Research Complex
(J-PARC) @ JAEA
Jointed

## Slide 12: J-PARC linac – The last high-power warm proton linac?

## Slide 13
Transmutation Experimental Facility (TEF)
was one of the main facilities of J-PARC (MLF, HD, NU, and TEF)

## Slide 14
Elliptical cavity
developed for transmutation experiment at J-PARC
IS
2MeV-RFQ
50MeV-DTL
190MeV-SDTL
400MeV-ACS
Transmutation
experimental
facility
RF coupler
Heat insulation
vacuum vessel
HOM coupler
Tuner
System
11 cryomodules
This upgrade project for transmutation experiment was suspended
-> The elliptical cavity development in JAEA
has been stopped more than ten years.

## Slide 15
Beam energy | 400 – 600 MeV
Frequency | 972 MHz
β | 0.71 – 0.79
Num. of cell per cavity | 9
Num. of cavity per cryomodule | 2
Num. of cryomodule | 11
Total length | 57.7 m
Surface peak electric field (Esp) | 30 MV/m
Accelerating electric field (Eacc) | 9.7 – 11.1 MV/m
Synchronous phase | -30 deg
Number of klystrons | 11
Total RF power | 10 MW
Loaded Q value | 〜5E5
Parameters of J-PARC SCC
Esp/Eacc | 3.07
Bsp/Eacc | 5.54 mT/(MV/m)
R/Q | 478 Ω
Geometrical factor | 208 Ω
Coupling constant | 2.80 %
Elliptical cavity
developed for transmutation experiment at J-PARC
N. Ouchi, SRF09 FROBAU05

## Slide 16
ADS Plant
30MW-beam, 800MWth
・MA transmutation
J-PARC Transmutation Experimental Facility 250kW-beam
・Pb-Bi target ・ADS core
ADS Demo⇒MYRRHA
~2.4MW-beam, 50~100MWth
・Demonstration of ADS
Radiation damage of beam window material and LBE target
ADS technology without MA fuel (Pb-Bi core, Accelerator, Operation Experience)
Physics of MA-fueled sub-critical core driven by a proton beam
Power
2010
2020
2030
Year
2050
Basic tests (Pb-Bi loop, KUCA, etc.)
Lead the worldwide R&D for transmutation technology in cooperation with J-PARC, MYRRHA, etc.
Obtain knowledge & experiences to realize ADS in 2030th
Roadmap for Establishment of ADS (old)

## Slide 17
Enhancement on the development of advanced modeling and simulation, and high ­performance computing methods to improve designs of future ADS, reduce uncertainty in facilities development and construction costs.
J-PARC Transmutation Experimental Facility 250kW-beam
LBE target technology
Reactor physics
PSi Program
J-PARC’s
facility
Experimental ADS⇒MYRRHA
~2.4MW-beam, 50~100MWth
・Demonstration of ADS technology
and materials irradiation
Basic experiment with LBE loops and critical assemblies
Commercial ADS Plant
30MW-beam, 800MWth
Transmute MA from 10 LWR
Proton accelerator-driven Subcritical virtual system (PSi) Program
Demonstration test facility ?
Achievement
Time
New approach by enhancing computer science

## Slide 18
Concept of the new proton irradiation facility
Hold the concept of TEF-T’s multi-purpose use
Heavy neutron irradiation
High-energy neutron beam port
Use of a small fraction of the proton beam (ex. ISOL)
H- beam from Linac
400 MeV, 250 kW
Pb-Bi
Sample specimens （SUS･T91）
400 MeV, 250 kW
PBW
Water or He cooling
Irradiation samples
(accelerators)
Proton beam
Eliminate BT-line to TEF-P
Irradiation samples (fusion & fission)
TEF-T is the baseline design.
TEF-P
PIE specimens
to JAEA’s Hot-labo.
Hot-labo.
PIE specimens
MLF
HD
NU
PIE specimens
･･･
low β part, 10 MeV,
20 mA, 200 kW
Space for accelerator development for ADS
LBE target

## Slide 19
Requirement for JAEA ADS accelerator
- Beam energy : 1.5 GeV
high efficiency of neutron generation per beam power
- Beam power : 30 MW
- Beam duty : CW
decrease thermal shock @ beam window
- Beam current : 20 mA
(cf. J-PARC linac: peak current : 50mA duty : 1.25% (25Hz, 500us)
J-PARC complex: 1 MW @ exit of 3 GeV synchrotron -> pulsed beam)
- Extreme reliability
avoid thermal shock of reactor
300 days for operation + 65 days for maintenance (beam window)
- Pulse mode operation
Transient of start up and shut down operation
⇒ Flexible controlability of beam power is required

## Slide 20: SRFC baseline → Bruce’s presentation
The optimization in the numbers of cavities and were chosen to obtain maximum voltage gain per cavity + smooth transition
Voltage gain was computed
assuming:
Sinusoidal E fields
Synchronous phase of -30⁰
Vmax of 2.0,2.05,4.987,11.9
and 19.9 MV (values of PIP-II)
HWR
βg=0.08
2.5 MeV
10 MeV
SSR1
βg=0.16
SSR2
βg=0.43
EllipR1
βg=0.68
EllipR2
βg=0.89
35 MeV
180 MeV
500 MeV
1500 MeV
162 MHz
324 MHz
648 MHz
SRF cavity start point model |  | 
Cavity type | Freq [MHz] | # of Cell
HWR | 162 | 2
SS | 324 | 2
Elliptical | 648 | 5
2.5 MeV
10 MeV
35 MeV
180 MeV
500 MeV
1500 MeV
JAEA-ADS superconducting linac layout
Low beta’s are replaced by SRF
Family of ellips are reduced → Fault tolerance
Higher current than other ADS linacs
Notes: Based in the J-PARC linac experience and in similar projects(PIP-II,C-ADS, etc..).

## Slide 21
Transient due to beam trip
A
Before beam trip
B
Several seconds
After beam trip
C
Transient
D
Several minutes
after beam trip
H
C
:High temperature
:Low temperature
Pump
SG
Inner barrel
Reactor vessel
Core
Beam
window
Inner
barrel
Reactor
vessel
H
C
C
H
C
H
C
H
Transient analyses were made on the thermal responses of following four parts of the reactor components.
  Beam window
  Fuel cladding
  Inner barrel
  Reactor vessel
Fuel
cladding
Notes: Next, acceptable frequency of beam trips.
These figures show the cross-section of the subcritical core. During normal operation, the cold LBE flows upward through the subcritical core and is heated. Finally, the hot LBE exits into an upper plenum.
In the case of the beam trip, the cold LBE exits from the core into the upper plenum. On the several minutes after the beam trip, the most of the LBE temperature becomes low.
To get the acceptable frequency of beam trips, transient analyses were made on the thermal responses of following four parts of the reactor components. That is, the beam window, the fuel cladding, the inner barrel and the reactor vessel, are picked up.

## Slide 22
Estimation based on the operational data of J-PARC Linac
Trip rate analysis using J-PARC data
The beam trip frequency (T < 10 sec.) is within the acceptable value at the present level of accelerator technology.
While that exceeding five min. should be reduced by about 1/24 to satisfy the acceptable level.
1
10
102
103
104
105
> 5 min
10 s -
5 min
0 - 10 s
Beam trip frequency (times/year)
Beam trip duration
Acceptable beam-trip frequency
1/24
1/5
Beam trip frequency of the JAEA's SC-linac was estimated using the operational data of J-PARC Linac.
Caution: used data is old. Now updating.
T. Sugawara et al., Annals of Nuclear Energy 125 (2019), p242
Notes: Next, comparison of beam trip frequencies.
This is the acceptable beam trip frequencies as a function of the beam trip duration. This axis represents the beam trip duration. And this axis represents the beam trip frequency.
The acceptable frequency of beam trips is shown as this red straight line.
On the other hand, the beam trip frequency of the JAEA SC-linac was roughly estimated as: Nads ~ Ninj + NRFQ + Nacc, where the Ninj, NRFQ and Nacc are the beam trip frequency caused by the injector, RFQ, and accelerator, respectively.
Three values were obtained from the operational data of J-PARC Linac.
Using the operation data, the down time distribution of the JAEA linac is shown as yellow histogram.
A comparison of the straight line and histogram shows that the beam trip frequency for durations of 10 seconds or less is within the acceptable value at the present level of the accelerator technology, while that exceeding five minutes should be reduced by about 1/35 to satisfy the acceptable level.

## Slide 23: Fault tolerance
Full duplication (JAEA proposal)
Low-b duplication + recover by adjacent cavities
(CADS, MYRRHA)

## Slide 24: Reactor start up scheme
J-PARC MEBT Chopper
Beam power (%)
time (h)
CW mode
pulse mode

## Slide 25: Cavity prototyping
Prototype Spoke Cavity for JAEA-ADS Linac
- Frequency : 324 MHz
- Shape : Single Spoke
- βg : 0.188
- βopt : 0.224
- Beam aperture : 40 mm
- Cavity length : 300 mm
- Cavity diameter : approx. Φ500 mm
E-field
H-field
Optimized Cavity Performance
- G : 90 Ohm
- R/Q : 240 Ohm
- Esp/Eacc : 3.8
- Bsp/Eacc : 6.1 mT/(MV/m)

## Slide 26: Japan’s SRF development
KEK 1.3GHz for ILC
H. Padamsee, Lectures given at the CAS course, 2013
No completed Spoke cavity in Japan
JAERI
QWR (‘93)
RIKEN
QWR (‘16)
JAERI 600MHz for ADS

## Slide 27: Summary
JAEA has been developed ADS in these tree decades.
This program including superconducting proton linac development.
We are now redesigning the superconducting proton linac to meet modern trend.
  Beam dynamics for low beta SRF
  Fault tolerance
  Cavity prototyping