## Slide 1: Status of CSNS Project Sheng Wang, Shinian Fu, Huachang Liu China Spallation Neutron Source Institute of High Energy Physics, CAS

## Slide 2: Outline
Project Overview
Accelerator Commissioning
User Operation
Upgrade Plan
Summary
2

## Slide 3
1. Project Overview
3

## Slide 4: Site Area
★

CSNS
Located in Dongguan, Guangdong Province
First spallation neutron source in China and the fourth in worldwide
First large scientific facility in southern China
Location of CSNS
IMP


## Slide 5
The phase-I CSNS facility consists of an 80-MeV H- linac, a 1.6-GeV rapid cycling synchrotron(RCS), beam transport lines, a target station, and 3 instruments.
Project Design
Linac
Project Phase | I | II
Beam Power on target [kW] | 100 | 500
Proton energy [GeV] | 1.6 | 1.6
Average beam current [μA] | 62.5 | 312.5
Pulse repetition rate [Hz] | 25 | 25
Linac energy [MeV] | 80 | 300
Linac type | DTL | +SC
Linac RF frequency [MHz] | 324 | 324/648
Macropulse. ave current [mA] | 15 | 50
Macropulse duty factor | 1.05 | 1.5
RCS circumference [m] | 228 | 228
RCS harmonic number | 2 | 2
RCS Acceptance [mm-mrad] | 540 | 540
Target | 1 | 1
Spectrometers | 3 | 20
The first high-energy high-intensity proton accelerator in China

## Slide 6
Before ground breaking(May.2009)
CSNS Campus, Aug. 2017
Linac building
RCS building
Target station and scattering hall

## Slide 7
H- Linac Design
 | Ion Source | RFQ | DTL
Input Energy（MeV) |  | 0.05 | 3.0
Output Energy(MeV) | 0.05 | 3.0 | 80
Pulse Current (mA) | 20 | 15 | 15
RF frequency (MHz) |  | 324 | 324
Chop rate (%) |  | 50 | 50
Duty factor (%) | 1.3 | 1.05 | 1.05
Repetition rate (Hz) | 25 | 25 | 25
EMQ option in FFDD lattice for DTL
Electrostatic chopper in LEBT

## Slide 8: Linac installed in the tunnel
MEBT
DTL
LRBT
LRBT
RFQ
IS

## Slide 9
Lattice of 4-fold symmetry, triplet.
227.92m circumference.
Four long straight sections for injection, acceleration, collimation and extraction.
24 main dipoles with one power supply.
48 main quadrupoles with 5 power supplies.
Ceramic vacuum chambers for the AC&pulsed magnets.
8 RF ferrite loaded cavities to provide 165 kV.
RCS Design

## Slide 10
Dipole magnet
Collimator
Ring RF
Quadrupole and Extraction magnet
Central control
Power supply for magnet
RCS Installation

## Slide 11
Instruments Suite
High Pressure diffractometer
General Purpose Powder Diffractometer
Single Crystal Diffractometer
D-G Polarized Inelastic
Liquid Relectometer
Multi-purpose Relectometer
SANS
Neutron Physics
Reverse Geometry Chemical
Total Scattering
High energy DG inelastic
Elastic Diffuse Scattering
Atmospheric neutron irradiation
Blue: constructed 3
Red: Near future instruments 7
Green: CSNS upgrade project 10
Energy selected Neutron imaging
Engineering Diffractometer
Proton Beam
Back scattering
Low energy DG inelastic
Spin Echo
High Resolution Diffractometer
VSANS
Coupled Hydrogen Moderator (20K)
Decoupled water moderator(300K), plan change to Decoupled Hydrogen (20K)
Decoupled & Poisoned Hydrogen Moderator (20K）
Notes: CSNS has signed cooperation agreements with local Universities and Institutes to build 7 user instruments, including of High-pressure Powder Diffractometer for the structure studies of materials under extreme conditions （high pressure and high temperature）, Atmosphere Neutron Irradiation Spectrometer for the studies of single particle effect on electric systems and functional materials, Multi-physics Diffractometer for the micro-structure studies of complex materials, High-resolution Diffractometer for the fine structure studies of crystalline materials, High Energy Direct Geometry Spectrometer for the dynamic process studies of Strongly Correlated Electron Systems, and Engineering Materials Diffractometer for the studies of internal residual stress. CSNS is also planning for the development of the other 10 instruments.

## Slide 12
Target Station
Scattering Halls

## Slide 13
Feb. 2001
Jan. 2006
Sep. 2008
Sep. 2011
Proposal for the CSNS Project
prototyping R&D started
May 2012
Oct. 2014
proposal approved
Jan. 2016
Apr. 2017
May. 2017
Aug. 2017
DTL-1 Beam commissioning
Linac beam commissioning
Mar. 2018
Mar. 2021
RCS commissioning start
construction started
civil construction started
installation started
first beam on target, first neutron beam
project complete/operation start
(6.5 years from start)
100kW beam power
Key Milestones (on schedule)

## Slide 14
Budget and Expenditure (within budget)
The total budget approved is 1.86632 B RMB (268M US$)， actual investment is 1.8740665 B RMB (268.7M US$)
The expenditure of the equipment's is within the budget
The deficit of the civil construction is paid by the local governments
NO. | Systems | Approved Budget (Million RMB) | Actual Investment (Million RMB)
1 | Accelerator | 62,664.66 | 62,362.90
2 | Target and Instrument | 39,763.04 | 41,161.86
3 | Utilities | 21,853.81 | 24,914.20
4 | Others | 62,350.49 | 58,967.69
Total |  | 186,632 | 187,406.65

## Slide 15: 2. Accelerator Commissioning

## Slide 16
16
Beam commissioning in 2017
RCS/AC (13 days)
2017.04.15~04.24
2017.05.26~06.07
2017.06.30~07.12
Linac
(10 days)
RCS/DC
(10 days)
First beam on target, first neutron beam
RCS/AC (18 days)
2017.07.21~07.28
2017.08.11~08.28
2017.08.28
RCS/AC (8 days)
RCS/DC (8 days)
2017.07.13~07.20
2017.11.01~11.09
Increase beam power to 10 kW
1 of 4 DTL klystrons was not available in 2017.
RCS was commissioned with 60MeV linac beam from 3 DTL tanks.
It took 67 days to reach the beam power of 10kW.

## Slide 17
17
Beam commissioning in 2018
Time table of commissioning in 2018:
Jan. 4~ 13 Linac to 80MeV
Jan. 14~ 17 RCS/DC
Jan. 18~ 21 RCS/AC
Jan. 22~ Commissioning of instruments and user operation
March Beam power increased to ~25kW
In the beginning of 2018, 4 DTL tanks were available and the beam commissioning were resumed.
It took 18 days to recover the beam power to 10kW with 80MeV linac beam.
From the Jan. 22, the beam was delivered to target for neutron spectrometers commissioning and user operation
By mid-March, the beam power is increased to about 25kW.

## Slide 18
From low duty to high duty: 50  500 μs, 1  25 Hz
(chop rate: 0  50 %) 。
Then, 90 hours continuous operation @25Hz, 500 μs , 50% chop rate。
Best transmission rate for RFQ: 94% 。
Frontend beam commissioning
 | Design | Measured
Ion source current [mA] | 20 | 31
MEBT Peak current [mA] | 15 | 17
MEBT Beam energy[MeV] | 3.0258 | 3.02±0.015
Chopping rate [%] | 50 | 50
Pulse width [μs] | 420 | 500
Pulse repetition rate [Hz] | 25 | 25
Emittance (π mm mrad ) | 0.22 | 0.27

## Slide 19
DTL tanks
DTL 1-3 ：Apr. 2017, Tank-3 output 15mA beam @60MeV.
DTL 4：Jan. 2018, 80MeV beam.
 | Measured（MeV） | Designed（MeV）
DTL1 | 21.81 | 21.67
DTL2 | 41.67 | 41.41
DTL3 | 60.80 | 61.10
DTL4 | 80.57 | 80.09

## Slide 20
PPT模板：www.1ppt.com/moban/ PPT素材：www.1ppt.com/sucai/
PPT背景：www.1ppt.com/beijing/ PPT图表：www.1ppt.com/tubiao/
PPT下载：www.1ppt.com/xiazai/ PPT教程： www.1ppt.com/powerpoint/
资料下载：www.1ppt.com/ziliao/ 范文下载：www.1ppt.com/fanwen/
试卷下载：www.1ppt.com/shiti/ 教案下载：www.1ppt.com/jiaoan/
PPT论坛：www.1ppt.cn PPT课件：www.1ppt.com/kejian/
语文课件：www.1ppt.com/kejian/yuwen/ 数学课件：www.1ppt.com/kejian/shuxue/
英语课件：www.1ppt.com/kejian/yingyu/ 美术课件：www.1ppt.com/kejian/meishu/
科学课件：www.1ppt.com/kejian/kexue/ 物理课件：www.1ppt.com/kejian/wuli/
化学课件：www.1ppt.com/kejian/huaxue/ 生物课件：www.1ppt.com/kejian/shengwu/
地理课件：www.1ppt.com/kejian/dili/ 历史课件：www.1ppt.com/kejian/lishi/
RCS——storage mode（DC）
For controlling beam loss, we started RCS operation with storage mode at single shot.
June 2017, the storage beam was firstly extracted from the ring.
Beam transmission rate higher than 98% through the ring
Measured signal of the extracted beam

## Slide 21
PPT模板：www.1ppt.com/moban/ PPT素材：www.1ppt.com/sucai/
PPT背景：www.1ppt.com/beijing/ PPT图表：www.1ppt.com/tubiao/
PPT下载：www.1ppt.com/xiazai/ PPT教程： www.1ppt.com/powerpoint/
资料下载：www.1ppt.com/ziliao/ 范文下载：www.1ppt.com/fanwen/
试卷下载：www.1ppt.com/shiti/ 教案下载：www.1ppt.com/jiaoan/
PPT论坛：www.1ppt.cn PPT课件：www.1ppt.com/kejian/
语文课件：www.1ppt.com/kejian/yuwen/ 数学课件：www.1ppt.com/kejian/shuxue/
英语课件：www.1ppt.com/kejian/yingyu/ 美术课件：www.1ppt.com/kejian/meishu/
科学课件：www.1ppt.com/kejian/kexue/ 物理课件：www.1ppt.com/kejian/wuli/
化学课件：www.1ppt.com/kejian/huaxue/ 生物课件：www.1ppt.com/kejian/shengwu/
地理课件：www.1ppt.com/kejian/dili/ 历史课件：www.1ppt.com/kejian/lishi/
RCS accelerating mode (AC)
July 2017 RCS started AC mode: the first shot of beam survive only for 4ms，not reaching the final energy.
On the same day, beam was accelerated to 1.6GeV design energy. And soon transmission rate reached almost 100%

## Slide 22
August 2017 the first proton beam hit on the target and produced spallation neutrons. This a important milestone for CSNS project.
Beam commissioning confirms a good performance in design, manufacture and commissioning.
First beam on target on schedule

## Slide 23
  Keep the potential of upgrading beam power to 500kW.
1/10 beam power is required for acceptance, and the design goal will be met in 3 more years.
Beam power | Rep. rate | Ave. Curr. | Beam Energy | Neutron Eff. | Neutron Flux
10 kW | 25Hz | 6.3μA | 1.6GeV | 0.005(n/p/sr) | 105
23 kW | 25Hz | 14.5μA | 1.6GeV | 0.125 | 2.5*106
Design Goal (Sept. 2011)
Achieved in Acceptance (Aug. 2018)
23
All achieved
or exceeded
Beam power | Rep. rate | Ave. Curr. | Beam Energy | Neutron Effi. | Neutron Flux
100 kW | 25 Hz | 63 μA | 1.6 GeV | 0.1 (n/p/sr) | 2*107

## Slide 24
24
CSNS Passed State Acceptance on Aug. 23 2018
The review committee agreed that the performance of the CSNS has reached or is even better than the planned acceptance goal. The highest neutron efficiency of the target station and the three initial instruments reached the international level.
The review committee concluded that some significant innovative technologies in accelerators, target station and instruments were achieved at CSNS.

## Slide 25: 3. User Operation

## Slide 26
10kW
20kW
30kW
40kW
50kW
Spark of RFQ
Summer shutdown
50kW machine study
Spring Festival
80kW machine study
Open to users
CSNS commissioning and operation overview

## Slide 27
Chart: 
| Startup | Maintenance | Accelerator Study | Neutron Beam | Fault | Other
2018.1-2019.5 | 797 | 2556 | 2649 | 4624 | 1108 | 73
Operation statistics (until now)
Availability is 80%

## Slide 28
Downtime statistics (up to now)
Chart: 
| LRF | IS | PS | DTL | RRF | OTHER | RFQ | BI | MAG | CO | VAC
 | 399 | 98 | 69 | 101 | 26.5 | 20 | 615.5 | 6.5 | 6.1 | 4.5 | 21.1
Notes: the linac contributed most of the shut-off time, Especially for the RFQ cavity, the frequent RF breakdown is the highest cause of beam trips

## Slide 29: Problem of RFQ spark
The chopped beam lost in the vane of RFQ, is confirmed to be the reason of RFQ spark
By rotating the chopper 45 degrees, most of the chopped beam passed through the slit between to adjacent vanes.
RFQ vane at entrance
Chart: 
| 43215 | 43216 | 43217 | 43219 | 43220 | 43221 | 43222 | 43223 | 43224 | 43225 | 43226 | 43227 | 43228 | 43243 | 43244 | 43245 | 43246 | 43247 | 43274 | 43275 | 43276 | 43277 | 43278 | 43279 | 43280 | 43281 | 43282 | 43283 | 43284 | 43285 | 43286 | 43287 | 43288 | 43289
 | 0.5 | 0.3 | 4.3 | 13 | 6 | 6 | 10.5 | 14.5 | 5.5 | 9.5 | 13 | 7.5 | 8 | 0.75 | 0.8 | 10 | 10 | 11 | 0.33333 | 0.016667 | 0.033333 | 0.58333 | 0.1 | 0.25 | 0.11667 | 0.25 | 0.15 | 0.13333 | 0.1 | 0.016667 | 0.016667 | 0.083333 | 0.05 | 0.033333
RFQ cavity spark counts per day

## Slide 30
Downtime statistics (from last summ. Maint. to now)
Chart: 
| LRF | IS | PS | DTL | RRF | OTHER | RFQ | BI | MAG | CO | VAC
 | 115 | 69 | 37 | 29 | 12.5 | 9 | 3 | 1.5 | 1.5 | 1.2 | 1.1

## Slide 31: Upgrade the RF source of RFQ
The stability of the RFQ 4616 tetrode is one of the main cause of fault.
The short lifetime and price of 4616 tetrode.
The retired klystron from DTL, can be used for RFQ, zero cost.
LLRF
CPI klystron
Magic T
Arch waveguide
RFQ
Circulator
Dummy Load

## Slide 32: High availability after summer maintenance
With accumulation of the operation experience, the availability of accelerator was quickly increased. After the summer maintenance, the availability is above 90%.

## Slide 33
Operation statistics (from last summ. maint. to now)
Availability is 91%
Chart: 
| Startup | Maintenance | Accelerator Study | Neutron Beam | Fault | Other
2018.10-2019.5 | 58 | 250 | 1562 | 3000 | 298 | 56

## Slide 34
Achievement 80-kW in CSNS/RCS
The equivalent beam power achieved 80kW with the single-shot mode with low beam loss.
Transmission reach ~100% without collimation system

## Slide 35
Achievement 80-kW in CSNS/RCS
Low beam loss by using collimation system, with the beam transmission ~98.5%

## Slide 36
Path to Beam Loss Reduction in CSNS/RCS
Increase the bunching-factor
Correlated-Painting was adopted
Tune was optimized
By using chromatic sextupoles to increase the Chromaticity in horizontal direction and decrease the Chromaticity in vertical direction
……
Designed
Injection
Extraction

## Slide 37: 4. Upgrade Plan

## Slide 38: Necessity of CSNS Upgrade
Facility | Beam power | Upgrade plan | Number of spectrometer | Number of target
SNS | 1.4MW | 2.8MW | 18+5 | 1+1（CD0）
J-PARC | 1MW | 1.5MW | 18 | 1+1?
ISIS | 200kW |  | 20+18 | 1+1
ESS | 5MW |  | 15+7 | 1+?
CSNS | 100kW | 500kW | 3+17 | 1+1？
Notes: Higher neutron intensity can shorten the experimental time, reduce the demand of the sample quantity and improve the signal to noise ratio. In the world, developing new neutron scattering technologies and megawatt spallation neutron sources have become a trend

## Slide 39
39
SC cavities
2nd Harmonic MA cavities
80MeV H- linac
1.6GeV
25Hz
100kW
New injection
More spectrometers
Phase-I status and phase-II upgrade
Target Station

## Slide 40
Beam dynamics requirements for Linac upgrade
 | CSNS Phase I | Linac Upgrade
Output energy | 80.1MeV | >300MeV
Particles | H- | H-
Beam current (peak) | 15mA | 50mA
Pulse width | 0.5ms | 0.6ms
Repetition rate | 25 | 25
RF frequency | 324MHz | 324MHz (648MHz)
length | RFQ(3.6m)+DTL(35m) | RFQ+DTL+95m
Linac length <95m
Peak current 50mA
Pulse width 0.6 ms
Repetition rate 25Hz
Beam energy at exit of linac >300MeV

## Slide 41
SCL option is preferred mainly due to :
Higher gradient( shorter beam line/ higher beam energy)
Upgrading potential
Cheaper operating cost since SCL requires less electricity
Individually powered SRF cavity provides high operational flexibility which leads to high availability
The extremely low vacuum and larger beam acceptance in SCL results in lower beam loss
Make use of the current development results from ADS and heavy ion projects in China
Notes: but the SC linac option can make use of the current development results from ADS and heavy ion
projects in China.• If the SC option is chosen, this machine will be the first machine in the world
to use an SC linac for injection into an RCS.

## Slide 42
 | Cavity type | Freq. (MHz) | g | Energy (MeV) | Max. Vacc. (MV)
Injector I | Spoke012 | 325 | 0.12 | 3.2-10 | 0.82
Main Linac | Spoke021 | 325 | 0.21 | 10-34 | 1.32
 | Spoke040 | 325 | 0.40 | 34-178 | 2.79
 | Elliptical063 | 650 | 0.63 | 178-367 | 7.68
 | Elliptical082 | 650 | 0.82 | 367-1500 | 15.47
Similar SC Cavities Developed at IHEP for ADS
Notes: More than 40 SRF cavities and their CMs have been developed. The fabrication, testing and assembly technics are matuer. The problems that limit the cavity gradient have been solved.

## Slide 43
Layout of the CSNS Linac in Phase-II
H-
DSR,β=0.5
3MeV
80MeV
324MHz
31.5m
9cryomodules
MEBT
RFQ
3MeV
50keV
DTL
154MeV
Elliptical ,β=0.65
648MHz
30m
6cryomodules
303MeV
Option1:
H-
Elliptical,β=0.47
3MeV
80MeV
648MHz
39m
11cryomodules
MEBT
RFQ
3MeV
50keV
DTL
174MeV
Elliptical ,β=0.60
648MHz
31m
5cryomodules
300MeV
Option2:
Notes: The . RF-performance, fabrication, surface treatment/cleaning, mechanical properties, choice of frequency, choice of operation temperature, beam cavity
interaction and cost. SRF community agrees that the lower limit is around a beta of 0.4 - 0.5. which of the two technologies is more advantageous than the other in the transition region around β = 0.5

## Slide 44: Summary
CSNS construction finished successfully within budget and on time.
Accelerator beam commissioning has been completed with a good results.
We reached 50kW beam power on target for user operation with availability higher than 90%.
CSNS started user operation and meanwhile will gradually raise beam power to 100kW.
500kW upgrade is under planning, and the upgrade project is foreseen to be launched as long as we realize 100kW.

## Slide 45
Thank you!