## Slide 1: Challenges, Progress and Prospects of High beam Power in J-PARC
Y. Liu, KEK/J-PARC
On behalf of J-PARC Accelerator Division
SHLiPP-9, Lanzhou, China, 25-27 September 2019

## Slide 2: Outlines
Introduction of J-PARC
Operation Status and Upgrade Plan
Linac
RCS
MR(Slow extraction ≡SX & Fast extraction ≡FX)
Challenges: request of more current, longer pulse, faster cycle, lower beam loss/residue radiation, stable long-term operation, etc.
Summary

## Slide 3
J-PARC Facility Layout at Tokai, JAEA Site
Main Ring Synchrotron, MR (30-50 GeV)
（Circumference 1600m)
Linac (181 -> 400MeV)
(330m)
3-GeV Rapid-Cycling Synchrotron, RCS
(Circumference 350m）
Hadron Experimental Facility
Materials and Life Science Experimental Facility (MLF)
Neutrino Experimental Facility
Joint Project between KEK and JAEA
Multi-Purpose Facility
ADS: Accelerator Driven Nuclear Waste Transmutation System (in the 2nd phase)

## Slide 4: J-PARC Linac Layout
J-PARC linac consists of
50-keV negative hydrogen ion source (RF ion source)
3-MeV RFQ, 324MHz (RFQ3)
50-MeV DTL (Drift Tube Linac) , 324MHz
SDTL (Separate-type DTL) 190-MeV , 324MHz
ACS (Annular Coupled Structure Linac) 400 MeV , 972MHz
Front-end
(7 m)
SDTL
DTL
0-deg dump
30-deg dump
Front-end = IS + LEBT+ RFQ + MEBT
(84 m)
(27 m)
50 MeV
190 MeV
3 MeV
50mA
100-deg dump
90-deg dump
RCS injection
50m
Collimator section
2nd Arc
Injection section
MEBT2
ACS section
(109 m)
400MeV
ADS
Org. Proposed
S.C. section
Suspended

## Slide 5: Rapid Cycling Synchrotron: Parameters
ACS
Dipole Magnets: 24
Quadrupole Magnets: 60 (7 families)
Sextupole Magnets: 18 (3 families)
Steering Magnets: 52
RF Cavities: 12 (Fundamental 440 kV, 2nd 180 kV)
Circumference: 348.333 m
Super-periodicity: 3
Harmonic number: 2
Injection Energy: 400 MeV
Extraction Energy: 3 GeV
Original Design Beam Power: 1 MW
  Large Aperture: 486π mmmrad
              Painting injection during 0.5 ms (307 turns)
  Beam Loss Localization with Collimators
  Lattice for high transition 𝛾: 9.14
Repetition Rate: 25 Hz
Ramping Pattern: Sinusoidal

## Slide 6: MR Design and Operation Modes
FX (2.48 s)
SX (5.2 s)
Circumference: 1567.5 m
Three-fold symmetry
Harmonic number: 9
Original Design Beam Power: 750 kW
  Large Aperture
  Beam Loss Localization
  Imaginary Transition 𝛾 Lattice
Slow extraction mode (SX) for the hadron hall: 2s-spill extraction.
Fast extraction mode (FX) for the neutrino Facility: 1 turn extraction.

## Slide 7: High Power Beams to Users
Materials and Life Science Experimental Facility (MLF) (2008−)
21 Neutron beam lines
3 Muon beam lines
RCS Design Beam Power : 1 MW
Future Program with the Linac Beam :
Proton Irradiation Facility
with laboratories of
Post irradiation examination
Accelerator development for ADS
400 MeV, 250 kW
Future Plan of the MLF Second Target Station
New design of target, moderators, reflectors
Neutron Brightness : > 20 times
Muon Intensity : > 50 times
RCS Beam Power : 1.5 MW
RCS

## Slide 8: High Power Beams to Users
Hadron Experimental Hall (2009−)
Nuclear and particle physics
50kton
Neutrino Facility (2009−)
Long baseline neutrino oscillation experiment (T2K)
Future Plan for the extension of the Hadron hall
More intensity of secondary particles
Purity
Δp/p
+
J-PARC Main Ring
Beam Power Upgrade
Upgrade Plan for the Neutrino Experiment
Far Detector
  50 kton → 260 kton Water Cerenkov detector
MR Beam Power
  750 kW → 1.3 MW

## Slide 9: J-PARC Operation Status

## Slide 10: Recent Linac Status (Current at LEBT)
60mA study #2,3,4,5
50mA
operation
started
mA

## Slide 11
2019.Jul.4
1 MW, 12hr
Trial
1.5 MW eq.
Trial

## Slide 12: Beam Power History at MLF
Beam Power(kW)
Beam Power Accumulated (MWh)
Earthquake
↓
Accident at
Hadron Facility
↓

## Slide 13: MR: Beam Power History
Max. delivered power:
Fast extraction ~ 500 kW (2.6x1014ppp)
Slow extraction ~ 50 kW (5.5 x1013ppp)
FX
SX

## Slide 14: Overview of J-PARC Power Upgrade

## Slide 15: Power Upgrade of Li and RCS
I. Exceed 1MW beam at RCS
1. 1.2MW stable operation
Net 1MW beam deliver to MLF after MR repetition upgrade
 Potential request from the MLF users
2. 1.5MW stable operation
MLF 2nd target station
 One of the future plans currently under consideration in J-PARC
3. >1.5MW operation
 Future beam power upgrade
II. Linac 50Hz operation
To deliver beam both to the RCS and to the Experimental Facility for Nuclear Transmutation Experiments
 One of the future plans currently under consideration in J-PARC

## Slide 16: Roadmap of J-PARC LINAC+RCS Intensity Upgrade
181/190MeV  400MeV: Jan., 2014 Operation/Study 15/30mA  30/50mA: Oct. 2014
400MeV, 50mA: ready for 1MW from RCS (Demo:Dec.2014)
--------------------- Design accomplished ---------------------
40mA in Operation: Jan. 2016
Next step: 5060mA or/and 500600us: aim at 1.2/1.5MW@RCS
1st Trial of 60mA: Jul.5 2017: 68mA(IS) 62mA(MEBT1)
2nd Trial of 60mA: Dec.25,26 2017 60mA(DTL no accel. ), 57mA(Li)
3rd Trial of 60mA: Jul.3, 2018 62mA(Li)
50mA in Operation: Oct. 2018
50mA, 600us injection to RCS : Oct. 19, 2018 (~1.2MW@RCS)
60mA (4th Trial ), 500us injection to RCS : Dec. 26, 2018 (~1.2MW@RCS)
Jul. 2019 60mA (5th Trial ), 600us injection to RCS (for ~1.5MW@RCS)
16

## Slide 17: Residue Radiation/Beam Loss Mitigation/Control for J-PARC Linac
J-PARC Linac Residue Radiation
Sections with higher Residue Radiation：200MeV~400MeV ACS
Several hotspots(surface)3~3.5mSv/h@500kW(40mA) before 2018.7
@ entry of ACS A-cavities
Main source：Intra-beam stripping of H- (IBSt)
Beam loss “localization” (ACS aperture re-arrangement、2018.9 accomplished)
Hottest: ACS A-entry 3~3.5mSv/h@500kW(~2018.7) 
Hottest: ACS bw. QM-doublet ~2.4mSv/h@500kW(~2019.3)
Beam loss mitigation
IBSt-mitigation lattice (2019.4~ TACS=0.7)
 Hottest: ACS bw. QM-doublet ~1.5mSv/h@500kW

## Slide 18: Abnormal Residue Radiation and Aperture Re-arrangement
Empty duct
FCT+SCT, FCT
A
B
① ②
③ ④
③ ④
①
②
Abnormal regularity of residue radiation at ACS since very beginning
Reason 1: CT aperture is 3mm less than else
Reason 2: CT materials is vulnerable to radioactivation
Shown in ATAC2014
Shown in ATAC2016
Aperture re-arrangement 2015:
Latter half: aperture increase, FCT ② removed
aperture increase in #4,7,8, etc.
Aperture re-arrangement 2018:
All the rest: aperture increase, FCT ② removed
All aperture  Φ40
18

## Slide 19: H0 Loss-pattern Simulation(1)
Loss-pattern of H0
By IBSt@ACS06
ACS06
W/m
With uniform aperture 𝚽40mm
19

## Slide 20: H0 Loss-pattern Simulation(2)
MEBT2 ACS 
zoom
20

## Slide 21: Residue Radiation at 500kW, Mar.~Jun., 2018
A
B
A
B
21

## Slide 22: ACS Residue Radiation at 500kW, Nov. 2018~Mar. 2019 After Aperture Re-arrangement at ACS first Half
22

## Slide 23: J-PARC LINAC Lattice and IBSt
T=1
T=0.3
DTL SDTL ACS
23
324MHz  972MHz
IBSt@ACS was verified as the dominant source of beam loss since 2016 by lattice exercises both in simulation and experiment
IBSt=intra-beam striping (of H-): depends almost only on lattice
50 191  400
MeV MeV MeV

## Slide 24: Comparison of IBSt for ACS Lattices
Accumulated loss power
0.675% duty
0.1W/m
24
For 50mA operation with optimized emittance
IBSt loss power is close to 0.1W/m at ACS
T=0.3 helps to reduced more than 50%
Stability?
T=1.0, E0 100%
T=1.0, E0 96%
T=0.3, E0 100%
T=0.3, E0 96%
Simulated envelope
Accumulated loss rate

## Slide 25
T=1
Baseline
design
Longitudinal redesign
Transverse redesign
Tune Diagram for J-PARC LINAC ACS (191~400MeV)
“Temperature ratio”
Stronger quad setting or weaker longitudinal focusing
25

## Slide 26: Experiment Results for Resonance・IBSt Mitigation at ACS
Beam Study on Oct.10, 2016. 40mA, εx,y|nrms =0.3mm*mrad, εz|nrms ~ 0.38mm*mrad(?)
After longitudinal “redesign” Tx/Tz=0.3 was stabilized near Tank level ~95%;
Fine tuning is needed
For Tank level ~90%, loss happened at later 1/3
26
Unstable
Previous best
Comparison
Stabilized
Stabilized
Near z-accept.
ACS01
ACS21

## Slide 27: Trend of Residue Radiation @ACS
50mA
T=1.0
50mA
T=0.7
~ -40%
~ -40%
Zigzag?

## Slide 28: Accomplishment of 60mA*600us from J-PARC Linac on Jul. 8, 2019
L3BT SCT waveform ~0.2kC  1.5MW eq. (if) at 3GeV
600us

## Slide 29
2018.7 1-hour to MLF
- (6.43, 6.32)
- 200p correlated painting
- Dp/p=-0.1%
- Sextupoles used for nx-2ny=-6 corr.
2019.7 10.5-hour to MLF
- (6.46, 6.32)
- 200p anti-correlated painting
- Dp/p=0.1%
- Sextupoles used for nx-2ny=-6 corr.
1 MW@25 Hz, 10.5 hrs
RCS: 1-MW Operation and the Beam Loss Reduction
ー Run#80 (2018.10)
ー Run#79 (2018.7)
BLM IDs
BLM signals (a. u.)
1 MW-eq.
ー Run#82 (2019.7)
Horizontal tune nx
Vertical tune ny
(6.43, 6.32)
(6.46, 6.32)
Random resonances

## Slide 30: RCS: High Power Operation beyond 1 MW
The upgrade is planned for 1.5 MW with the 2nd target station of MLF.
The operation of 1.2 MW equiv. was demonstrated for the acceleration of up to 1 GeV.
RF system will be upgraded this summer for the beam loading compensation for the beam power beyond 1 MW.
1.2 MW equiv.
Beam Intensity

## Slide 31
Mid-term Plan of MR Power Upgrade
JFY | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024
Event |  |  | HD target |  | Long shutdown |  |  | 
FX power [kW] SX power [kW] | 475 50 | 500 50 | 500 50 | 500 70 |  | >700 > 80 | 800 > 80 | 900 > 80
Cycle time of main magnet PS New magnet PS | 2.48 s | 2.48 s | 2.48s | 2.48s |  | 1.32 s | <1.32s | <1.32s
High gradient rf system 2nd harmonic rf system |  |  |  |  |  |  |  | 
Ring collimators | Capacity 2 kW |  |  |  | Capacity 3.5kW |  |  | 
Injection system FX system |  |  |  |  |  |  |  | 
SX collimator / Local shields |  |  |  |  |  |  |  | 
Ti ducts and SX devices with Ti chamber | Ti-ESS-1 |  |  |  |  |  |  | 
Mass production/installation/test
Kicker PS improvement, Septa manufacture /test
Kicker PS improvement, FX septa manufacture /test
New buildings
Manufacture, installation/test
Local shields
FX: Faster cycling: 2.48 s ➝ 1.32 s for 750 kW ➝ 1.16 s for 1.3 MW
SX: Mitigation of the residual radiation for 100 kW

## Slide 32
MR FX Beam Power Upgrade Concept
 | Beam Power | Cycle Time | Number of accelerated protons | Equivalent beam power in RCS
Present | 500 kW | 2.48 s | 2.6×1014 ppp | 780 kW
Original Design | 750 kW | 1.32 s | 2.1×1014 ppp | 610 kW
New Plan | 1.3 MW | 1.16 s | 3.3×1014 ppp | 1 MW
For the Beam power upgrade of 500 kW ➝ 1.3 MW
  Factor of 2 by faster cycling
  ~30% gain by intensity increase

## Slide 33
New Magnet Power Supply for Faster Cycling
A new power supply was designed with capacitor banks for the cycle of 1.3 s.
The power supplies for the BM families are being constructed and tested.
Energy Recovery with Capacitor Banks
Capacitor Banks for BM3
New PS for BM3
Issue：Large power variation @ AC main grid
ΔPin > 100MVA
1.3 sec cycle
Requirement : Higher Repetition Rate (2.48 s ➝ 1.3 s )
ΔPin~ 60MVA
Not allowed by Electric Power Supplier
Interior of Container

## Slide 34: MR Slow Extraction Tunings and the Beam Loss Reduction
Extraction scheme with a third order resonance of νx = 22.33
The extraction efficiency of 99.5% was achieved with fine tunings of
  Main Quadrupole Magnets
  Resonant Sextupole Magnets
  Bump Magnets
  Electro-Static Septum (ESS) 30 μm W ribbons at high β=40 m
  Septum Magnets (SMS)
ESS1 2
SMS1 2 3
Extraction Beam
Beam @ flattop
with Bump Orbit
Beam Envelope
during Injection
Fixed Bump
Dynamic Bump
x – x’
phase space
Step size 20 mm
Bump 1 – 4
current
vs. time
Beam Loss Distribution

## Slide 35: MR SX for the μ to e conversion search experiment
The COherent Muon to Electron Transition (COMET) experiment to search for the process of lepton flavor violation requires
  slow extraction of 8 GeV beam for suppression of the anti-proton production and
  sparse bunched beam for the signal detection with the extinction ratio of 10−10 for the empty bucket.
    Empty bucket production with RF chopper
    1 bunch acceleration in RCS
    Injection kicker timing shift in MR
The proton beam required for the phase 1 was delivered to Hadron hall to measure extinction factor of secondary beam.
8GeV 1MHz pulsed beam
Empty bucket
1.6×1012 ppb
6.2×1012 ppb
< 6×10−11
We found the solution for the extinction for K4_rear.

## Slide 36
Multi-MW Scenarios for the Neutrino Experiment with a New Booster
3.2 MW with a new 8-GeV Booster in J-PARC
9 MW with a 9-GeV proton driver in the KEKB Tunnel after the B-factory project.
Conceptional Design of 8 GeV Ring
Circumference 696.666 m
Super-periodicity 4
Transition gamma ~15 GeV
1.2 GeV
3.3 GeV
6.2 GeV
9 GeV
To Kamioka
For the acceleration in the 2nd to 4th straight section, the ILC cavity is adopted.
- Peak current : 100 mA (pulse)
- Beam duty : 1 %
- Beam power : 9 GeV x 0.1 A x 1 % = 9 MW
R&Ds : High duty horn, higher gradient SC cavity, high power target...
J-PARC Tokai site
KEK Tsukuba site

## Slide 37: Summary
J-PARC accelerators have been providing high power beams for 10 or more years to users at
  Materials and Life Science Experimental Facility
  Hadron Experimental Hall
  Neutrino Facility.
The Linac original design current of 50 mA was achieved with efforts of beam loss reduction.
  The operation of 60 mA was demonstrated in the beam study.
With RCS, the 10.5-hour stable operation of 1 MW was achieved with the loss of 10−3 level.
  The beam power of 1.2 MW equivalent was demonstrated in the beam study.
  The beam power of 1.44 MW has been tested for the upgrade plan.
MR delivers the SX beam to the hadron hall with the beam power of 51 kW and the extraction efficiency of 99.5%.
  Hadron target will be upgraded this summer for the capacity of 57 kW → 95 kW.
  The proton beam of 8 GeV required for the phase 1 of the muon to electron conversion search experiment (COMET) was delivered to hadron hall to measure extinction factor of secondary beam.
The beam power of 500 kW was achieved for the MR FX operation.
  The beam power upgrade of 1.3 MW is planned with
    faster cycling : 2.48 s ➝ 1.16 s, and accelerated protons : 2.6×1014 ppp ➝ 3.3×1014 ppp.
  Possibilities are being explored for the beam power of multi-MW for the neutrino experiment.