## Slide 1
Status and new developments of HIAF
High-Intensity Heavy Ion Accelerator
Institute of modern physics, CAS
26 September, 2019, Lanzhou
SLHiPP-9
Jiancheng Yang

## Slide 2
HIAF introduction and status
High-Intensity Heavy Ion Accelerator Facility-HIAF

## Slide 3
Outline
Background and science motivations
General description of project
Design concept and unique features
Innovative technologies and developments
Present status and summary
Notes: In my talk, I will give a brief introduction of HIAF status, because the proposed EicC will be constructed in the same campus of HIAF, and some of main accelerator components will be used for EicC. So the construction progress is very important for EicC.

## Slide 4
Next-generation high intensity facilities are required for advances in
nuclear physics and related research fields:
To explore the limit of nuclear existence
To study exotic nuclear structure
Understand the origin of the elements
To study the properties of High Energy
and Density Matter
……
SPIRAL2 at GANIL in Caen, France
FAIR at GSI in Darmstadt, Germany
FRIB at MSU in the U.S.
NICA at JINR, Dubna, Russia
EURISOL in Europe
High Intensity Heavy-ion
Accelerator Facility
HIAF in China
Available today
Fascinating and crucial questions
Next-generation facilities are being constructed or proposed worldwide:
HIAF introduction and status

## Slide 5
HIAF introduction and status
iLinac: Superconducting linac
Length:100 m
Energy: 17-22 MeV/u(U35+-45+)
BRing-S: Booster ring
Circumference: 650 m
Rigidity: 86 Tm
Beam stacking
Beam acceleration
MRing: Figure “8” ring
Circumference: 273m
Rigidity: 15 Tm
Ion-ion merging
SRing: Spectrometer ring
Circumference: 273m
Rigidity: 13-15 Tm
Electron/Stochastic cooling
Two TOF detectors
Four operation modes
L: 180m, Bρ: 25 Tm
BRing-N: Fast cycle ring
Circumference: 570 m
Rigidity: 34 Tm
Large acceptance (250/120)
Two planes painting injection
Fast ramping rate（5-10Hz, 20Hz）
Main accelerator components
These tunnels will be built in a cut and cover method and will be filled with 5 m overlay of soil. This conforms to the requirements of radiation safety.
Notes: The design concept and layout of HIAF facility has evolved from the scientific requirements. This is the whole layout of the HIAF accelerator, it consists of superconducting ECR source, superconducting linac as injector, synchrotron booster, radioactive beam separator, and storage rings for in-ring experiments. ECR source is the next generation ECR source with high operation frequency, the superconducting linac can provide the highest intensity heavy ion beam for low energy research and synchrotron injection. The output energy is the about 17-25MeV, we keep the free space for update to 100MeV/u in the future. The central part of the HIAF facility is a synchrotron complex consisting of two rings. Both rings have nearly the same circumference and will be installed in the same tunnel.

## Slide 6
iLinac
SECR
BRing-N
Chopper
Switch
Parallel mode
Switch
Highest beam Intensity （Comparison with HIRFL）:
Primary beam intensity increases by x 1000 - x 10000
Secondary beam intensity increases by up to x 10000
Highest heavy ion beam intensity in the world
Unprecedented parameters and unique features:
Precisely-tailored beams - Precision frontiers
Beam cooling (Electron, Stochastic, laser; high quality, very small spot )
Beam compression (Ultra-short bunch length: 50-100ns)
Super long period slow extraction (Super long, high energy, quasi-continuous beam )
Versatile operation modes:
Parallel operation, beam splitting ( increase of target time, high integrated luminosity)
HIAF introduction and status
Notes: With this design concept and layout, HIAF can provide unprecedented parameters and unique features for research program. Such as beam intensity, if compare with our exiting facility HIRFL, the

## Slide 7
HIAF introduction and status
Heavy ion beam intensity
 | Ions | Energy | Intensity
SECR | 238U35+ | 14 keV/u | 0.05-0.1 pmA
iLinac | 238U35+ | 17 MeV/u | 0.028-0.05 pmA
BRing-N | 238U35+ | 0.8 GeV/u | ~2.01011 ppp
BRing-S | 238U35+ | 2.3 GeV/u | ~1.01012 ppp
 | 238U76+ | 5.8 GeV/u | ~5.01011 ppp
 | 238U92+ | 7.3 GeV/u | ~5.01011 ppp
SRing | RIBs: neutron-rich, proton-rich | 0.84 GeV/u(A/q=3) | ~109-10 ppp
 | Fully stripped heavy ions H-like, He-like heavy ions | 0.8 GeV/u(238U92+) | ~1011-12 ppp

## Slide 8
Concepts for approaching the highest heavy ion intensity
BRing-N
Novel two planes painting injection scheme - 2.01011 ppp
Fast ramping rate operation mode- 3-5 Hz
BRing-S
Innovative timing system of RF synchronization
5 times increase of intensity
1.01012 ppp
Barrier bucket stacking longitudinal
BRing-S
BRing-N
High intensity beam

## Slide 9
High intensity beam
Simultaneous injection in H and V planes using tilted septum
Two planes painting injection

## Slide 10
High intensity beam
The beam intensity could reach 2.0 1011 with two planes painting, nearly 10 times over the conventional single-plane injection.
Simulation results
Ions | Plane | Injection Turns | Single injection
238U35+ | H | 33 | 3.31010
 | V | 16 | 1.61010
 | H+V | 150 | 2.01011

## Slide 11
iLinac
BRing
SRing
HFRS
SECR
iLinac: Superconducting linac
Length:100 m
Energy: 17-22 MeV/u(U35+-45+)
SRing: Spectrometer ring
Circumference: 273m
Rigidity: 13-15 Tm
Electron/Stochastic cooling
Two TOF detectors
Four operation modes
L: 180m, Bρ: 25 Tm
BRing: Fast cycle ring
Circumference: 590 m
Rigidity: 34 Tm
Large acceptance (250/120)
Two planes painting injection
Fast ramping rate（5-10Hz）
HFRS: Radioactive beam line
SECR:
Superconducting ECR source
HIAF: First phase

## Slide 12
Low energy nuclear
structure terminal
Low energy irradiation
External target station
Nuclear Matter study-CEE
Hypernuclear
High energy irradiation
BRing
iLinac
SECR
RIBs physics station
High precision
spectrometer ring
e-ion recombination
spectroscopy
SRing
HFRS
Around the whole facility, there are a series of experiments terminals
High Energy
Density Physics
Terminal
HIAF: Experiment terminals

## Slide 13
Gas-target
TOFdetector
Stochastic cooling pick-up
Electron target
Operation modes
  Isochronous mode
  Normal Mode
  Internal-target Mode
  Ion-ion merging Mode
Experiment programs
  Gas-jet target experiments
  DR experiments
  IMS & SMS
  Ion-ion merging experiments
Key devices
  Electron cooling
  Stochastic cooling
  Two TOF detectors
  Electron target
Multi-function storage ring
SRing
Precision frontiers machine for in-ring experiments
HIAF introduction and status
Unique feature-1
Notes: Storage ring is unique in their capability to store, cool, bunch and stretch beams and thus fulfill the stringent requirements from experiments. For SRing, advanced cooling technologies, including the electron cooling, stochastic cooling and laser cooling will be used, we designed different operation modes for different research programs, such as …..

## Slide 14
Beams：58Ni, 78Kr, 86Kr and 112Sn
Isochronous mode with two TOF
HIRFL-CSRe
HIAF-SRing
∆M/M~10-7-10-8
Demonstrated the TOF mode first time in the world
43 masses are measured
Measured for the first time: 16
Precision improved: 27
HIAF introduction and status
Precision achieved: ∆M/M~10-7
Notes: Especially the Isochronous mode with two TOF detectors, we have demonstrated the two TOF mode in our exiting machine HIRFL-CSRe and improved the precision of mass measurement. Two TOF system of SRing has been optimized based on the CSRe and the precision will reach 10^-8, that will be the highest precision of isochronous mass measurement.

## Slide 15
HIAF introduction and status
Unique feature-2
Bound pair production
QED
A fundamental question of QED-spontaneous electron-positron pair creation in supercritical Coulomb fields
Theory prediction: occur in the collisions of two very heavy ions with the total atomic number Z1 + Z2 ≥ 173.
Failed to observe in fixed target experiments due to the interference of extranuclear electrons.
Spontaneous electron–positron pair production
First figure-8 shape ring for ion-ion merging
Notes: The second unique feature of HIAF is the ion-ion merging scheme based on figure“8”storage ring. The science motivation is

## Slide 16
First figure-8 shape ring for ion-ion merging: pair production
HIAF introduction and status
SRing
MRing
Unique features:
“8” shape ring
Coasting beam merging with itself scheme
Based on SRing
Sharing the injection and cooling system
No powerful RF system
Bare heavy nuclei, e.g. 238U92+,
Z1 + Z2 =184 ≥ 173
Advantages:
No electron-electron correlation
Ultra-low background signals
Small angle collision provides the energy (6~8MeV/u) to cross column barrier
Notes: This is the first ion-ion merging machine in the world. The features are: Figure 8 shape and coasting beam can support the ion merging with itself. This design is based on SRing, Sharing the injection and cooling system with SRing, the coasting beam confirm the merging without the powerful RF system for beam bunching, so this is a cost-effective scheme

## Slide 17
HIAF introduction and status
Schedule
Notes: The planed construction period is about 7 years, and we hope we can finished the projector in end of 2025.

## Slide 18
HIAF introduction and status
New campus
HIAF site
HIAF
HIAF site

## Slide 19
Innovative technologies and developments
Notes: These unprecedented parameters and unique features can only be met with new technical solutions. So a series of new and innovative technologies have been proposed for HIAF accelerator. Now let me introduce the new technology developments.

## Slide 20
HIAF
Superconducting ECR ion source-45GHz
旋转
驱动系统
高真空
旋转密封
HFRS-CCT（Canted Cosine Theta）coils
High intensity super conducting linac
Inclined electro-static septum
Dynamic vacuum collimator
Magnetic alloy core loaded cavity
Innovative technology development
Notes: A series of new and innovative technologies have adopted for HIAF, such as …….Here is just a selection of these technologies. The prototypes have been developed for these system for the varication of the feasibility, reliability and performance.

## Slide 21
Fast cycling power supply
Parameters | Values
Resistance of load | 24mΩ
Inductance of load | 88mH
Current | 5000A
Voltage | 3462V
Rising time | 130ms
Max. ramping/falling rate | ±38000A/s
Tracking error | ≤1×10-4
Platform error | ≤5×10-5
Operation Waveform
Challenges:
A broad dynamic current range
A high precision and reproducibility
Very low tracking errors relative to current reference
The strong shock of large return power to the power grid
The main magnets for BRing consist of 48 dipoles in twelve groups of four magnets, load specification and performance requirement featured by fast ramping rate

## Slide 22
Innovative concept based on full-energy store principle
Voltage-changed stimulation asymmetrical multi-level cascaded PWM
Low voltage source for injection & extraction platform, high voltage source for fast ramping stage
Energy capacitor will be used to store energy.
Asymmetrical PWM cascade Structure: keep high accuracy and fast output dynamic response
Modular designed circuit schematic diagram
The energy can be controlled by PWM rectification technology, only active power will be taken from the grid!
Fast cycling power supply

## Slide 23
Fast cycling power supply
Power unit of 2000A/1100v

## Slide 24
Thin wall vacuum chamber
Due to high ramping rates, thin wall vacuum chambers are needed for all magnets to keep eddy currents at a tolerable level.
The traditional technology is ribs supporter thin wall chamber, ribs supporter parallel to the magnetic field lines
Stainless steel-0.3mm
L=1.2m, 2.0m long, curved thin wall chamber prototype have been developed

## Slide 25
A novel thin wall vacuum chamber are designed for HIAF
(chamber supported by ceramic rings )
Static structural equivalent stress
Chamber with ceramic supporter
Thin wall vacuum chamber

## Slide 26
Thin wall vacuum chamber
Chamber supported by ceramic rings
Inside view of chamber
Bake system
Outgassing
4.0×10-12 mbar

## Slide 27
Present status and summary
Notes: In the past several years, a series of prototypes have been developed for technical challenges and critical issues. The machine design was optimized based on these prototypes developments, details of technical design has been finished and some hardware systems already go into production. The civil construction and common system are also going smoothly,

## Slide 28
BRing
SRing
HFRS
iLinac
SECR
Details of technical design has been finished and most of hardware systems are under production.
Present status and summary

## Slide 29
BRing arc section
iLinac section
Beam transfer line
SRing arc section
BRing straight section
Tunnel mechanical installation
Tunnel utilities and mechanical installation
Present status and summary
Notes: The civil construction and common system are also going smoothly

## Slide 30
Present status and summary
Layout of tunnel and cross sectional view of the tunnels
Notes: Also engineering design of the tunnel

## Slide 31
Present status
Present status and summary
Notes: The campus civil construction started serval months ago, this is the view before groundbreaking, and this is the latest view
Five years later a more beautiful campus will come into being.

## Slide 32
Present status
Present status and summary

## Slide 33
High-Intensity Heavy Ion Accelerator Facility-HIAF
Present status and summary
2025-Huizhou, HIAF welcome all of you !!!

## Slide 34
Thanks for your attention!

## Slide 35
2025-Huizhou, HIAF welcome all of you !!!
Present status and summary

## Slide 36
RFQ
0.5MeV/u
QWR005
2.4MeV/u
HWR010
5.8MeV/u
HWR015
17.0MeV/u
SECR
45GHz
Pulsed 50 pμA U35+, U4x+
CW 20 pμA U35+
The Front-End and iLinac
SECR
Pulsed 28 pμA U35+, U4x+
CW 15 pμA U35+
iLinac
Notes: The first is Front-End and iLinac, the front-end includes superconducting ECR and RFQ and the iLinac includes three different cavities. These numbers are very challenging.

## Slide 37
LEBT
MEBT
LEAF Platform
FECR
L-RFQ
The Front-End and i-Linac
Prototype for HIAF Front End
  45 GHz FECR
  81.25 MHz 4-vane RFQ
Notes: So for challenges of the front-end, a LEAF Platform is under development in our institute to demonstrate the ECR and RFQ, this is the layout of the LEAF. …… The most important ones are ECR and RFQ.

## Slide 38
4th G. ECRIS Development
Nb3Sn magnet
Cryogenic system
Microwave system
Beam extraction and transmission
All technical challenges and critical issues have been verified and full size prototype is under development
Notes: The challenges of ECR are

## Slide 39
L-RFQ RF training log
RFQ fully commissioned to its designed RF power of 66.8 kW (70 kV vane voltage)
CW beam operation with He+ and N2+ have been done, total operation time >700 hours
RFQ Development
Notes: For RFQ prototype, fabrication has been finished and now is under on beam test. The results show the performance of RFQ can meet the requirement of HIAF.

## Slide 40
SRF Cavity Development
ADS Front-end Demo Linac (2011-2017)
 | RFQ/IMP | CM1/IMP | CM2/IMP | CM3/IMP | CM4/IHEP
frequency | 162.5 MHz | 162.5 MHz | 162.5 MHz | 162.5 MHz | 325 MHz
output energy | 2.1 MeV | 5 MeV | 10 MeV | 18.5 MeV | 25 MeV
cavity type | 4-vane | HWR010 | HWR010 | HWR015 | Spoke021
cavity number | 1 | 6 | 6 | 5 | 6
Proton, 25 MeV, 10 mA, CW, ~ 35 m, 4.5 K operation
To demonstrate the technology of superconducting linac:
CW RFQ, Superconducting cavities, Cryomodule
Supported by “Strategic Priority Research Program” of the Chinese Academy of Sciences
Notes: and also the SFR technologies for iLinac has been verified with the ADS Demo Linac, in order to demonstrate the technology of superconducting linac, a 25MeV SC linac has been built and run with proton beam successfully, several types of SC cavities have been developed for this demo facility.

## Slide 41
SRF Cavity Development
High performance SRF cavities
162.5 MHz Taper HWR015
βopt | 0.15
Vmax (MV) | 1.8
Epeak (MV/m) | 32
βopt | 0.246
Vmax (MV) | 1.75
Epeak (MV/m) | 32.5
βopt | 0.10
Vmax (MV) | 1.06
Epeak (MV/m) | 28
Notes: Such as HWR 010 cavity and HWR 015 cavity and Spoke cavity with good performance.

## Slide 42
162.5 MHz HWR010
4
ECRIS + RFQ + CM1 + CM2
Energy is ~10 MeV
First beam September 15th, 2016
Achievement ~ 2.7 mA, 9.55 MeV
3
ECRIS + RFQ + TCM6
Energy is ~5 MeV
First beam June 6th, 2015;
achievement 2.7 mA, 5.3 MeV; ~7.5 hours 2 mA 4 MeV operation
162.5 MHz HWR010
2
ECRIS + RFQ + MEBT + TCM1 (single HWR)
Energy is ~2.5 MeV
First beam October 1st, 2014;
achievement 11 mA, 2.55 MeV
162.5 MHz HWR010
ECRIS + RFQ + CM1 + CM2 + CM3 + CM4
Energy is ~25 MeV
First beam May 28th, 2017
Achievement 0.2 mA 25 MeV
5
1
ECRIS + RFQ
Energy is ~2.1 MeV
First beam Jun. 6th, 2014;
achievement 10 mA, 2.1 MeV, 4.5 hours
162.5 MHz RFQ
SRF Cavity Development
Notes: All these cavities have been tested by beam. Here are the beam commissioning records and we realized 11mA pulse beam and 0.2mA CW beam with these cavities.
The 25MeV SC demo facility has been built and run with proton beam successfully, including CW RFQ, high performance SC cavities, CMs . Tens of kilowatt CW beam achieved in the SC front-end of Chinese ADS.
The dumper and radiation shielding is a limit for tuning higher power beam.
Beam loss，higher power and operation stability will be the key issues to be demonstrated in the future.

## Slide 43
Parameters | Values
Resistance of load | 24mΩ
Inductance of load | 88mH
Current | 5000A
Voltage | 3462V
Rising time | 130ms
Max. ramping/falling rate | ±38000A/s
Tracking error | ≤1×10-4
Platform error | ≤5×10-5
Operation Waveform
Challenges:
A broad dynamic current range
A high precision and reproducibility
Very low tracking errors relative to current reference
The strong shock of large return power to the power grid
The main magnets for BRing consist of 48 dipoles in twelve groups of four magnets, load specification and performance requirement featured by fast ramping rate
Fast cycling power supply
Notes: A plenty of experience have been got from LEAF and ADS demo linac for HIAF injector. There are also challenges for fast ramping rate high intensity synchrotron, first is

## Slide 44
Innovative concept based on full-energy store principle
Voltage-changed stimulation asymmetrical multi-level cascaded PWM
Low voltage source for injection & extraction platform, high voltage source for fast ramping stage
Energy capacitor will be used to store energy.
Asymmetrical PWM cascade Structure: keep high accuracy and fast output dynamic response
Modular designed circuit schematic diagram
Low voltage source
High voltage source
The energy can be controlled by PWM rectification technology, only active power will be taken from the grid!
Fast cycling power supply
Notes: So innovative concept based on full-energy store principle was designed for HIAF, this new technology based on

## Slide 45
Full energy storage testing prototype
450A full energy storage technology test
Power supply based on PWM rectification technology
Results of the PWM rectifier prototype
PWM rectification and full energy storage technology have been tested on the low power prototype, for the verification of this new design concept.
Fast cycling power supply

## Slide 46
Distribution of the prototype
Structure of one power unit
A full prototype (4000A/2770V) is being manufactured in the factory. The distribution and process structure design have been established already.
Fast cycling power supply

## Slide 47
Fast cycling power supply
Power unit of 2000A/1100v

## Slide 48
Fast cycling power supply
The test results show the feasibility and reliability of full-energy store principle, will go into production

## Slide 49
Due to high ramping rates, thin wall vacuum chambers are needed for all magnets to keep eddy currents at a tolerable level.
Thin wall vacuum chamber
The traditional technology is ribs supporter thin wall chamber, ribs supporter parallel to the magnetic field lines
Stainless steel-0.3mm
L=1.2m, 2.0m long, curved thin wall chamber prototype have been developed

## Slide 50
A novel thin wall vacuum chamber are designed for HIAF
(chamber supported by ceramic rings )
Static structural equivalent stress
Chamber with ceramic supporter
Thin wall vacuum chamber
Notes: So a novel technique has been successfully developed for HIAF in our institute, the chamber

## Slide 51
Chamber supported by ceramic rings
Thin wall vacuum chamber
Fabrication process

## Slide 52
Chamber supported by ceramic rings
Thin wall vacuum chamber
Inside view of chamber
Bake system
Outgassing
4.0×10-12 mbar

## Slide 53
Chamber supported by ceramic rings
This new technology greatly reduce the cost of manufacture process, the difficulty, shorten the production cycle, and improve the quality.
Thin wall vacuum chamber

## Slide 54
Items | 1st phase (MRMB)
iLinac | 360
BRing | 350
Beam transfer line | 50
Experiment setups | 240
Cryogenics | 80
Civil engineering | 190
Tunnel construction | 160
Contingency cost | 100
Total of facility | 1530 (central government)
Infrastructure & common systems | 1000 (local government)
Total | 2530
Budget

## Slide 55
Electromagnetism design
Inclined E-Septum
Key technical-1
Inclined E-Septum
Notes: The septum foil is tilted by 30°to cope with the combined longitudinal and transverse injection scheme. A new septum has been constructed to cope with the extremely tight vacuum requirements of LEIR. By optimising the internal surface under vacuum and increasing the pumping speed and beam scrubbing, a dynamic vacuum in the low 10-12 mbar range is expected. The technical specification is shown in Table 3 and a
cross section in Fig. 3.

## Slide 56
Multi-Differential Vacuum System was designed, a small prototype has been developed
for the verification of this system
Big challenge – Vacuum seal in the extreme high vacuum -10-12 mbar
Inclined E-Septum
Key technical-1
Inclined E-Septum
Notes: The rotation system is one of the most challenging aspects, mainly because of the vacuum seal in the extreme high vacuum. A full size prototype is under fabrication and will be accomplished in this year.
2.Finally, we present a new type of XHV electrostatic saddle field ionization gauge which features very small electrode sizes and low outgassing/ sorption rates and high sensitivity.
3. A novel technique has been successfully developed to calibrate the ultra high vacuum ( UHV) and extra high vacuum ( XHV), whichconsists of XHV/ UHV chambers, a flow separation and a gas supply.
4.On the studies of this subject, design and implement a small prototype and the control system. Also research of the nonlinear motion system algorithm for the control system, verification of control system is reasonable.

## Slide 57
High voltage: 240kV
Gap voltage and phase waveform of BRing RF system
Two functions: acceleration & compression
MA core loaded cavity
MA core loaded cavity
Key technical-3
Short rise time: ≤10μs
Notes: Beside the fast cycling power supply, another challenge of fast ramping is RF system, the challenges for RF are high voltage and short rise time, the rise time less than 10 microsecond.

## Slide 58
MA core loaded cavity
Key technical-3
Established test bench and completed measurement under power and cold state
MA ring core test
Power test result
Measurement result
Measured under power
Notes: But there will be some challenges for hardware system. Such as RF system and power supply system. The first challenge for RF is high voltage.