## Slide 1: RSFs & categorisation
www.europeanspallationsource.se
10 December, 2018

## Slide 2: Basis for definition of Radiation Safety Functions
To conclude which systems shall be assigned radiation safety functions
  Holistic perspective
  Accident scenarios that mainly happen internal to the monolith
  Release of the radioactive inventory and radiological consequences for the public.
The assigning of radiation safety functions determine the safety classification, and mechanical/electrical/etc. quality classification, for the systems, structures and component.

## Slide 3: Grouping of accident scenarios
Since the studied accident scenarios relate to different parts of the facility and to some extent are different in their character, it is possible to group them into smaller and essentially independent subsets:
Subset 1, events internal to the monolith
  AA1 Target wheel rotation stop during beam on target
  AA2 Proton beam events on target and proton beam window
  AA3 Loss of target wheel cooling during beam on target
  AA4 Leakage from target cooling circuit into monolith (no beam on target)
  AA5 Global bypass and local blocking of target
  AA9 Moderator hydrogen combustion
  AA10 Water leakage in monolith vessel
  AA12 NBG/chopper failure – missile effect on monolith systems
Subset 2, events in the utilities block
  AA6 Increased radiation level in the Target primary cooling system
  AA7 Leakage between Primary cooling and Intermediate cooling systems
  AA8 Loss of confinement in Target He system – release into utility rooms
  AA11 Water leakage into connection cell and utility rooms
  AA22 Target Helium Purification Getter Vessel Rupture
Subset 3, beam dump events
  AA13 High power beam on beam dump
Subset 4, events related to the active cells facility
  AA15 ACF - Intrabay doors unintentionally open
  AA16 ACF - Worker inside Process Cell next to worst case inventory
  AA17 ACF - Worker inside Maintenance Cell next to worst case inventory
  AA18 ACF ventilation stop
  AA19 ACF open doors/hatches
  AA20 ACF fire
Subset 5, global seismic event
  AA14 Earthquake – Monolith
  AA21 Earthquake – Active Cells Facility

## Slide 4: Grouping of accident scenarios
Since the studied accident scenarios relate to different parts of the facility and to some extent are different in their character, it is possible to group them into smaller and essentially independent subsets:
Subset 1, events internal to the monolith
  AA1 Target wheel rotation stop during beam on target
  AA2 Proton beam events on target and proton beam window
  AA3 Loss of target wheel cooling during beam on target
  AA4 Leakage from target cooling circuit into monolith (no beam on target)
  AA5 Global bypass and local blocking of target
  AA9 Moderator hydrogen combustion
  AA10 Water leakage in monolith vessel
  AA12 NBG/chopper failure – missile effect on monolith systems
Subset 2, events in the utilities block
  AA6 Increased radiation level in the Target primary cooling system
  AA7 Leakage between Primary cooling and Intermediate cooling systems
  AA8 Loss of confinement in Target He system – release into utility rooms
  AA11 Water leakage into connection cell and utility rooms
  AA22 Target Helium Purification Getter Vessel Rupture
Subset 3, beam dump events
  AA13 High power beam on beam dump
Subset 4, events related to the active cells facility
  AA15 ACF - Intrabay doors unintentionally open
  AA16 ACF - Worker inside Process Cell next to worst case inventory
  AA17 ACF - Worker inside Maintenance Cell next to worst case inventory
  AA18 ACF ventilation stop
  AA19 ACF open doors/hatches
  AA20 ACF fire
Subset 5, global seismic event
  AA14 Earthquake – Monolith
  AA21 Earthquake – Active Cells Facility

## Slide 5: Accident events internal to the monolith
AA1 – Target wheel rotation stop during beam on target
AA2 – Proton beam events on target and proton beam window
AA3 – Loss of target wheel cooling during beam on target
AA4 – Leakage from target cooling circuit into monolith
AA5 – Global bypass and local blocking of target
AA9 – Moderator hydrogen combustion
AA10 – Water leakage in monolith vessel
AA12 – NBG/chopper failure – missile effect on monolith systems

## Slide 6: Generic approach for deriving classification from accident analyses
Accident Analysis space
Classification space
Normal operation conditions & facility configuration
Accident analyses
Implicit preconditions & design solutions
Assumptions
Event categorisations
Proposed preventive & mitigative measures
Dependencies
Safety Functions (Safety related)
Safety Functions (Safety)
Safety related SSCs
Safety SSCs

## Slide 7: AA3 initiating events

## Slide 8: AA3 Operational system status
Monolith rough vacuum system non-operational (conservative)
HVAC system- no impact on dose to public
Accelerator- operating at full power (conservative)
Target vessel- fails directly (conservative)
Moderator cooling- PBW no impact
Monolith relief line and burst disc operational (conservative)
Inner shielding cooling unoperational (conservative)

## Slide 9: Safety Functions derived from Event categorisations (for PIEs) for AA3
Accident Analysis space
Classification space
AA3
Event categorisations
Safety Functions (Safety related)
Safety related SSCs
Analysis report ESS-0374897 states that all PIEs in consideration are to be categorised as H3 events. | Control energy source (L2): Monitor specific process parameters, and inhibit beam if any of these parameters exceeds limits. MPS Protection Functions (PF): | MPS Protection Functions (PF): specific equipment to be defined

## Slide 10: Safety Functions derived from Proposed mitigative measures for AA3
Accident Analysis space
Classification space
AA3
Proposed preventive & mitigative measures
Safety Functions (Safety)
Safety SSCs
Radiation dose consequences for public is well above acceptable limits for H3 events, thus mitigative measures are mandatory. | Control energy source (L3): RSF-69: Detect unacceptably low helium pressure and prevent proton beam from hitting wheel | Target Safety System (TSS)
 | Control energy source (L3): RSF-70: Detect pressure change in monolith and prevent proton beam from hitting wheel | Target Safety System (TSS)
 | Control energy source (L3): RSF-71: Detect unacceptably high helium temperature and prevent proton beam from hitting wheel | Target Safety System (TSS)
 | Control energy source (L3): RSF-72: Detect unacceptably low helium flow rate and prevent proton beam from hitting wheel | Target Safety System (TSS)

## Slide 11: AA3 scenario release and dose Unmitigated/mitigated

## Slide 12: AA3 credited safety functions

## Slide 13
Identification and classification of safety important components, according to ESS-0016468

## Slide 14
Identification and classification of safety important components, according to ESS-0016468
TSS
RSF-68
RSF-69
RSF-70
RSF-71
RSF-72
Most operational systems
Monolith components; Target, MRP, etc.
Cooling pipes system and components
He purification system
Control systems (BPCS, MPS)
Monolith vessel, PBW
Monolith atm pressure control system

## Slide 15: Categorisation of Radiation Safety Functions and associated Safety and Safety related SSCs
Conclusions:
Several radiation safety functions in operational group, DiD levels L1 or L2, are identified, and the SSCs selected to implement these are to be categorised as Safety related, Q2, Cat. 5.
Since the radioactive dose consequence is much above the allowable limit for H3 events (event class for the PIEs) it is required to define radiation safety function(s) in the safety group and DiD level L3. General requirements for the SSCs selected to implement these safety functions shall be RFPD* (Redundancy, Functional separation, Physical separation and Diversity). These SSCs are to be categorised as Safety, Q1, Cat 1.
Mechanical classification according to ESS-0033258, ”ESS Rules for Radiation Safety Classification of Mechanical Equipment”
Electrical classification according to ESS-0054158, ”ESS Rules for Radiation Safety Classification of Electrical and Instrumentation & Control Equipment including Design and Quality Requirements”

## Slide 16: Electrical classification acc to ESS-0054158

## Slide 17: Electrical classification acc to ESS-0054158

## Slide 18: Summary – Credited radiation safety functions in the safety group (RSF/SG)
AA1 – Target wheel rotation stop during beam on target
  TSS stops beam based on rotational speed or other measurement.
AA2 – Proton beam events on target and proton beam window
  TSS detect monolith pressure increase or helium system pressure decrease; and stop beam.
AA3 – Loss of target wheel cooling during beam on target
  TSS detect helium system pressure decrease, flow decrease, temperature increase, or monolith pressure increase; and stop beam.
AA4 – Leakage from target cooling circuit into monolith
  No RSF/SG expected for this specific AA
AA5 – Global bypass and local blocking of target
  No RSF/SG expected for this specific AA
AA9 – Moderator hydrogen combustion
  No RSF/SG expected for this specific AA
AA10 – Water leakage in monolith vessel
  Conclusion that there is no need for any RSF/SG for this specific AA
AA12 – NBG/chopper failure – missile effect on monolith systems
  No RSF/SG expected for this specific AA