## Slide 1: Postulated TSS limits
ESS-0287373
Per Nilsson
CFD Specialist
www.europeanspallationsource.se
10 December, 2018

## Slide 2: Outline
General remarks on setting limits
Target helium cooling
Target rotation
Monolith pressure
Procedure to set limits

## Slide 3: TSS limits – limits operation space
Operation limit
MPS: Machine Protection
TSS: Safety
E.g. pressure or temperature

## Slide 4: Simple solution to complicated problem
For easy understanding and explaining
For robustness
Keep measurements simple
Avoid combinations and control

## Slide 5: Limits
Quantity | Limit | Time
Mass flow rate | 1.75 kg/s | 25 s
System pressure | 8 bar(a) | 25 s
Inlet temperature | 70 C | 25 s
Rotation speed | 9 rpm | 3 s
Monolith vessel pressure | 0.5 bar(a) | 2.5 s

## Slide 6: Helium Cooling System AA3 Problem : Insufficient cooling

## Slide 7: TSS limits – limits operation space
0: Normal operation
1: TSS limits
MPS should be inside
System function limits
1.75 kg/s
8 bar
70 C
Notes: Previous analyses -> Need to limit p,T,m
Generates a space: - normal operation, with varied parameters
- TSS limits
- MPS inside - System function limits and operation inside

## Slide 8: Target assessment based on CFD Assessed in accident analyses (mitigated)
Normal, ESS-Bilbao ESS-0058358 (not released)
Notes: Basis for the limits: An analysis of when systems fails leading to unacceptable consequences
Analysis is not sufficient/approved yet

## Slide 9: Indirect measurements in helium cooling
ESS-0012527 SDD-Sol
p
m
T
Notes: Cannot measure the direct quantity

## Slide 10: Example: Target cooling mass flow tests
ESS-Bilbao, ESS-0066301 not yet verified model, will be in design report
Higher temperature
Could give unacceptable
Dose consequence
~ 1.65
Notes: Based on the not verified model

## Slide 11: Scenario Inertia -> Margin
Tmax
Temperature may increase after
-> Beam off in advance
t
Beam off
Notes: Margin in terms of parameter and time

## Slide 12: Trigger quantities, Margins
Tmax
Tin
pout
m
Tolerances
Detection lag Action lag
t
Beam off
Temperature may increase after
-> Beam off in advance
Notes: Indirect parameters, similar margins

## Slide 13: Compressor operational limits
Nominal, 2 compressors: m = 2.85 kg/s dp(design) = 142 kPa
dp(draft) = 158 kPa
1 compressor
1 of 2 parallel compressors
design
draft
TSS limit 1 compressor
System will be simulated (Modelica)
Specifications still missing
Simulation methods not yet reliable
[UJV/OFTTech]
1 compressor:
[Emil Lundh]
Notes: Operational limits

## Slide 14: Operation space
Requested simulations for this points
ESS-0287373

## Slide 15: Example: Timing for lost cooling stop
Stainless steel melts at about 1400 C
The normal tungsten temperature is about 400 C
The time to heat the differing 1000 C is estimated 1000 C / (100 C/pulse * 14 pulse/s / 36 ) ~ 26
Maximum time to beam off for loss of cooling -> 25 s
(the melting may finally not be the criterion)

## Slide 16: Opposing interests, pushing limits together
Operation limit
MPS: Machine Protection
TSS: Safety

## Slide 17: Target Wheel Rotation AA1 Problem : Insufficient cooling time

## Slide 18: Target assessment based on CFD Assessed in accident analyses (mitigated)
Normal, ESS-Bilbao ESS-0058358 (not released)

## Slide 19: Target rotation
(WP2 Target wheel, drive and shaft description of operational limits [ESS-0060625]: LLL=7 rpm)
Normal speed is 23.3 rpm
Footprints overlapping ½ gives 9 rpm
Unacceptable dose consequences after 3 s
Notes: Normal rotation 23 rpm Phase error relevant
Protection at half ~ 13 rpm
Safety at half ~ 7 rpm

## Slide 20: Monolith Vessel Pressure AA2 Problem : Too high heat density

## Slide 21: Target assessment based on CFD Assessed in accident analyses (mitigated)
Normal, ESS-Bilbao ESS-0058358 (not released)
No detection in tungsten
-> Indirect detection
Hole may be small
-> faster detection in monolith than in helium system
Notes: Various defocussing or non-rastering -> sharp beam

## Slide 22: Pressure
Figure from relief document ESS-0305844
Notes: Release into monolith, depending on hole size

## Slide 23: Monolith pressure
Simulation AA4, ESS-0150712
~0.07 s
0.5

## Slide 24: Monolith pressure
Simulation for AA2, ESS-0150710
=10 s
0.5
Limit may be refined calculating pressure after one rotation
Notes: Simulation depends on hole

## Slide 25: Timing for focused beam stop
Small holes around the perimeter, area increasing during first rotation then maybe same holes
Holes needed for pressure, earliest detection after one rotation
Latest detection after one additional rotation I.e. beam must be off at 36/14 ~ 2.5 [s] after the limit pressure is reached

## Slide 26: Procedure

## Slide 27: Procedure
Postulating limits now Likely to change during first years
Analyses to further confirm: - Accident mitigation - Operability
(Commissioning) Tests will decide limits finally Changes must be few and under strict control

## Slide 28: Questions?