## Slide 1: APTM and GRID interface requirement PBIP and PBW
Mattias Wilborgsson
Work Unit Leader PBW and PBIP, Target Division
European Spallation Source ERIC
2019-01-09

## Slide 2: Target Station Layout
Proton beam envelop
representation
Proton Beam Window
Proton Beam Instrumentation Plug
Target Wheel
Moderator and Reflector Plug
Neutron Beam Extraction

## Slide 3: Target Station Components
Function
  Support, cool and align the PBI (APTM and GRID)
  Allow an optical view of the PBW and the BEW
PBIP components
  Beam instrumentation slices (3)
  Optical slices (2)
  Support Structure
Minimum lifetime of PBI parts
  Two years at full power operation (5 MW)
Proton Beam Instrumentation Plug (PBIP)
Instrumentation slices
Position of first mirror
Optical slices
Shielding block
Actively cooled support structure

## Slide 4: Target Station Components
Function
  Separating the monolith atmosphere from the high vacuum in the accelerator beam pipe
  Support, cool and align the PBI (APTM)
PBW components
  Proton Beam Window
  Inflatable pillow seals
  APTM flange
Minimum lifetime of PBI part
  Two years at full power operation (5 MW)
Proton Beam Window System (PBW)

## Slide 5: Proton Beam Instrumentation
Mechanical interface
  Outer dimensions must be less than
    APTM: TCS-X: 25 mm, TCS-Y: 260 mm, TCS-Z: 140 mm
    GRID: TCS-X: 44 mm, TCS-Y: 260 mm, TCS-Z: 140 mm
  PBIP and PBW will position APTM and GRID within ±0.5 mm in TCS-Y and TCS-Z directions
  APTM and GRID need to have the possibility for ± 5 mm adjustment along TCS-Y and TCS-Z during installation. (PBW and PBIP will be equipped with 4xM6 holes)
APTM and GRID interface requirements

## Slide 6: Proton Beam Instrumentation
Cable routing
  Cables specified in ICD-R
APTM and GRID interface requirements
System | Cable type | Diameter (mm) | Quantity
APTM | K-type thermocouples | 5 | 24
 | Triax | 10 | 16
GRID | 16PR20WCTC3V | 32 | 8 cables (≈150 channels)
 | 1C10SLW | 10 | 2

## Slide 7: Proton Beam Instrumentation
Cooling of PBI parts
  Conductively cooled through mechanical interface with PBIP slices and PBW structure
  Each APTM and GRID shall not heat the PBIP and PBW with more than 300 W
  Allowed temperatures for in-beam PBI parts not defined
APTM and GRID interface requirements

## Slide 8: Proton Beam Instrumentation
APTM and GRID interface requirements
Cable feedthroughs
  3 x DN250 CF in Connection Ring
  1 x DN250 CF in PBW Vessel
  1 x DN63 CF in PBW plug
  Design pressure 2 bar(g)
  ESS Vacuum handbook