## Slide 1: Cryogenic Supply for the Facility for Antiproton and Ion Research

## Slide 2: GSI – Introduction
Existing facility: GSI Darmstadt (Foundation: 1969)
Shareholders: federal government (90%), Hesse (8%), Rhineland-Palatinate (1%), Thuringia (1%)
Further locations in Mainz and Jena
Future facility: FAIR (Foundation: 2010)
Employees on location: approx.1450
Integrated organization FAIR and GSI under one management since 2017

## Slide 3: FAIR – the facility
Collector ring CR
Intensity
Precision
Storage rings
Ring accelerator
SIS100
Production of new nuclei
Production
of antiprotons
Antiproton ring
Experimental and storage ring
Linear accelerator
Ring accelerator
100 meters
Existing facility
Planned facility
Experiments

## Slide 4: The four scientific pillars at FAIR
NUSTAR Nuclear Structure, Astrophysics and Reactions: Stars and nuclei (850 scientists)
CBM Compressed Baryonic Matter: Inside a neutron star (500 scientists)
PANDA Antiproton-Annihilation at Darmstadt: Antimatter research (500 scientists)
APPA Atomic, Plasma Physics and Applications: From atoms to planets to cancer research (720 scientists)

## Slide 5: Shareholders worldwide
Shareholders
Germany
Finland
France
India
Poland
Romania
Russia
Sweden
Slowenia
Associated
United Kingdom
Aspirant
Czech Republic

## Slide 6: Scientific users worldwide
–
• Locations
of scientific partners

## Slide 7: Construction volumes
2 million m3
600,000 m3
65,000 tons
  As much as nine Eiffel Towers
  As much as for 5,000 single-family homes
  As much as eight Frankfurt soccer stadiums
of earth
to be moved
of concrete
to be used
of steel
to be utilized
Completion until
Investments
Area covered by the land-use plan
2025
> €2 billion
70% of this amount will be provided by the German federal government and the State of Hesse
686,373 m2

## Slide 8
Germany
Finland
France
India
Poland
Romania
Russia
Sweden
Slowenia
building permit
operation licence
operation
construction
legal completion
beam
personal
Strict regulation on site
Turn-key delivery requested
(Compatibility to cryo demands not really fulfilled)
In kind delivery

## Slide 9: Cryogenic topology
SIS 100
(SIS 300)
SuperFRS
CBM
R3B
APPA
Cool down/
Warm up Unit
CWU
CRYO plant: CRYO2
common
compressor station
no cavities
PANDA

## Slide 10: SIS100
iron dominated magnet design:
dipole: 1.9 T, 4 T/s @ 1 Hz; 109 pcs. stat. load: 8 W dyn. load: 0...12...56 W
quadrupole module: 27 T/m; 84 pcs. stat. load: 6-21 W dyn. load: 0...12...60 W
Photo: Babcock Noell
Photo: JINR

## Slide 11: SIS100 – By-pass line system
BPL design status
  FDR (05/18): 3 BPLPs: 1S12YP, 1S32YP, 1S52YP
  CDR (06/18): the other BPLPs without end boxes
BPL types
  many different types
    straight types, arc termination types,
    types with/without interconnections (magnet, FIL)
    flow direction
    BB system
    15 different types (out of 27)
  3 major families
    standard straight BPLPs (1S52YP)
    BPLPs connected to arc termination (1S4EYP)
    end boxes (1S40YE)

## Slide 12: SIS100 – By-pass line system
Design:
WrUT
Production:
KrioSystem
Testing:
GSI
Installation:
FAIR
polish in-kind

## Slide 13: Super-FRS - Magnet cryostats
Super-FRS
2-Stage In-Flight Separator with 3 Branches to Experiments
* Large Acceptance (2.5 % ∆p/p, 40 mrad φ); exotic beams
* Large Apertures for Beam Line
* Large magnetic rigidity (20 Tm)
 Superconducting Magnets
Driver Accelerator (SIS 18 / SIS 100)
Stable Ion Beams (p – U)
~ 1 GeV / u
Pre-Separator
Main-Separator
~ 250 m
Production Target
 Fragmentation
Focusing System
Low-Energy
Branch
High-Energy
Branch
Ring Branch
Exotic
Beams
7 Short Multiplets
* Cold Iron and Coils, LHe-Bath
* Cold Mass: ~ 25 tons
* LHe Volume: ~ 1000 liters
* Heat Load: 12 W / 110 W
28 Long Multiplets
* Cold Iron and Coils, LHe-Bath
* Cold Mass: ~ 45 tons
* LHe Volume: ~ 2000 liters
* Heat Load: 16 W / 160 W
27 Dipoles
* Warm Iron, Cold Coils
* Cold Mass: ~ 1.1 tons
* LHe Volume: ~ 50 liters
* Heat Load: 12 W / 100 W
For more information:
Felix Wamers
poster session
Notes: Large Brho for large energies for avoiding other than bare-ion charge states

## Slide 14: Experiments
Thermo siphon cooling
R3B
Panda
CBM
APPA
forced flow cooling
supply from central plant
supply from individual plants
CEA
Saclay
BINP
BINP
IHEP

## Slide 15: Experiments - R3B
length = 3.5 m; width = 7 m; height = 4 m
total weight = 50 tons; cold mass weight = 20 tons
R3B
first beam time 2018
with refurbished cryo plant
UNICOS based SCADA system
designed @GSI/ ACO-IND
GSI Large Acceptance Dipole (GLAD)
Design:
CEA

## Slide 16: Experiments - CBM
CBM
Superconducting Dipole Magnet
Free aperture: 1.44 m vertically * 3.0 m horizontally
Field integral: 1 T*m, maximal field ≈ 1 T
wire
first beam time 1996
dedicated cryo plant
Nitrogen cooled shield

## Slide 17: Experiments - PANDA
Panda
Frame
Yoke
Cryostat
Control Dewar
Free aperture: ~1m
Field integral: 3 T
in-beam position
parking position
12 m
40W @4.5K
480W @50K
dedicated refrigerator
LN2 cooled helium circuit
supply
heat load
400W @80K

## Slide 18: Experiments - APPA
APPA
Safety
diaphragm
Inlet and outlet
branch pipe 4 K and 50 K
The weight of the quadrupole
is about 9 t.
Box of the current
leads
Vacuum
Pump Outlet
Place of installation of the safety valve
Vacuum vessel
Material is stainless steel 1.4307
Superconducting Dipole Magnet
(Wide) aperture: 0.2 m
Field: 6T
Tc: 5.9K
cable with of the rectangular trapezium cross-section
heat load per magnet:10W/magnet @4.5K
60W/magnet @50K
minimal helium flow rate: 30g/s @4.5K

## Slide 19: Cryo plant - heat loads
Chart: Heat Loads for FAIR @ 50 K
| [W] | [W] | [W] | [W] | [W] | Static SIS 100 | Static Super-FRS | Static infrastructure | Dynamic load SIS100 | CL HeFl@50K
Heat Loads for FAIR 4K Equivalent | 12607 | 14630.675 | 5045 | 2232 | 103.11
Chart: Heat Loads for FAIR @ 4.4 K
| [W] | [W] | [W] | [W] | [W] | Static SIS 100 | Static Super-FRS | Static infrastructure | Dynamic load SIS100 | CL HeFl@4K
Heat Loads for FAIR 4K Equivalent | 3565 | 1829.6 | 927.5 | 4320.688 | 1031.1441
Helium inventory: 9.6t for FAIR
SIS100: 0.6-1.2 t, Super-FRS: 6.5t, experiments: 0.1t, infrastructure: 1.7t
Cold mass: 2000t for FAIR
SIS100: 400 t, Super-FRS: 1400t, experiments: 100t

## Slide 20: Cryo plant - specification
Chart: Heat Loads for FAIR @ 4.4 K
Due to the time schedule of the experimental set-up of FAIR (CBM supplied directly from GSI)
5-line transfer line between north (SIS100) and south
Due to the uncertainties of the heat loads caused by the experimental schemes in the start phase
single plant in the north, later adaptation to the real needs (=> second plant)
Due to the large cold mass of the Super-FRS
Dedicated cool-down (and warm-up) unit in the south (nitrogen based)
Specification
June 17

## Slide 21
May 2019
Cryo plant - location

## Slide 22
Operation Modes | Refrigeration at 4.4 K | Shield 50-80 K | Hybrid current leads | Resistive current leads
 | [kW] | [kW] | [g/s] | [g/s]
 | E1 - R1 | E2 - R2 | E2 – R4 | E1 - R4
Option A |  |  |  | 
Maximum load | 14 | 49 | 33 | 17
Max. liquefaction | 7.4 | 49 | 33 | 45-60?
SIS100 min. ramp | 9.7 | 49 | 33 | 17
Super-FRS | 3.1 | 25 | 0 | 17
80 K hold | 0 | 49 | 11 | 0
Minimum load | 3 | 8 | 11 | 0
Option B |  |  |  | 
Maximum load | 16 | 60 | 33 | 26
every mode will be operated > 8h
for all modes (except 80K hold and Minimum load) the operating temperatures (4.5K; 50K) and pressures (3 bar; 18 bar) have to be observed
The operating pressure in the cold box may deviate.
purchasing ongoing
warm storage tanks will be tendered next year

## Slide 23: Topology of the Cryogenic System for FAIR
negotiation will start later this week
Main Transfer Line and MPL
south
Cryo2

## Slide 24: FAIR construction
Movie of the FAIR civil construction on 24th June 19
https://www.youtube.com/watch?v=WJGs68298YA

## Slide 25
Thanks for your kind attention
Felix
Wamers
Brano
Streicher
Franz
Walter
Marko
Pospiech
Holger
Kollmus
Andreas
Beusch
Marion
Kauschke
Eugen
Momper
Thomas
Eisel
Katharina
Kopp
Claus
Schroeder
Alexander
Täschner
Yu
Xiang
Matteo
Chesi
Ivan Remolina
Raimund Trockel