## Slide 1: Design of the ESS Cryogenic Moderator System (CMS) and Target Moderator Cryoplant (TMCP)
Hideki Tatsumoto, Philipp Arnold
European Spallation Source ERIC
07. October, 2019

## Slide 2: Introduction
Rotating Tungsten
target wheel
Proton beam window
5 MW proton beam
(at repitation rate
of 14 Hz)
Upper Downstream Cold Moderator
u.u.c.M
Proton beam
ESS Spallation neutron source
ESS hydrogen moderator requirements
ESS moderator is optimized for a maximum neutron brightness under the condition of a para-H2 > 99.5%
- Equilibrium p-H2 fraction
99,5% @22.5 K and 99,95% @17K
- Ortho-para-H2 converter (IONEX)
(2) Average temperature rise through moderator < 3 K.
Cryogenic Moderator System (CMS) has been designed to ciculate subcooled LH2 (T=17 K, P=10 bar and pH2=99.5%) at 1 kg/s.
Moderator | Nuclear heating at 5 MW (kW) | Require flow rate for T =3.0 K (g/s)
u.d.cM | 3.79 | 148
u.u.cM | 2.91 | 114
l.d.cM | (5.96) | (233)
l.u.cM | (4.60) | (180)
Total | 6.7 (17.25) | 262 (675)
Moderator | Nuclear heating at 5 MW (kW) | 
u.d.cM | 3.79 | 148
u.u.cM | 2.91 | 114
l.d.cM | (5.96) | (233)
l.u.cM | (4.60) | (180)
Total | 6.7 (17.25) | 262 (675)
l.u.c.M
l.d.c.M

## Slide 3: Cryogenic Moderator System (CMS) Overview
1 kg/s (0.5 kg/s)
He Refrigerator:30.3 kW
(Target Moderator
CryoPlant)
35 m
Subcooled liquid hydrogen (17 K and 10 bar)
Design pressure: 17 bar.
 | Number of moderators | 
 | 2 | 4
LH2 inventory (L) | 321.8 | 375.8
GH2 inventory (L) | 65.8 | 
Circulation flow rate (kg/s) | 0.5 | 1.0
17 K
Hydrogen pump | Two pumps in series
O-p-H2 converter | IONEX
p-H2 measurement | In-situ Raman spectroscopy
Pressure mitigation | PCB (65 L)
Thermal compensation | TMCP through HX

## Slide 4: Pressure Drop
Fluid properties of pH2 at 17 K and 1.0 MPa given by GASPAK.
Friction factor : Colebrook equation
(surface roughness = 0.05 mm)
Pressure drops of the moderators are calculated by a CFD simulation.
Component |  | Two-moderator |  | Four-moderator | 
 |  | (kg/s) | (kPa) | (kg/s) | (kPa)
Feed piping in the cold box |  | 0.50 | 6.0 | 1.00 | 16.7
Main feed transfer line (HTL) |  | 0.50 | 6.6 | 1.00 | 24.7
Feed and return distribution lines via bayonets and moderator. | u.d.cM | 0.24 | 71.0 | 0.24 | 71.0
 | u.u.cM | 0.24 | 78.2 | 0.24 | 78.2
 | l.d.cM | - | - | 0.26 | 78.8
 | l.u.cM | - | - | 0.26 | 78.7
Main return transfer line (HTL) |  | 0.50 | 5.0 | 1.00 | 16.7
Return piping in cold box |  | 0.50 | 4.9 | 1.00 | 19.5
Total pressure drop |  |  | 100.8 |  | 156.4
Component |  | Two-moderator |  | Four-moderator | 
Feed piping in the cold box |  | 0.50 | 6.0 | 1.00 | 16.7
Main feed transfer line (HTL) |  | 0.50 | 6.6 | 1.00 | 24.7
Feed and return distribution lines via bayonets and moderator. | u.d.cM | 0.24 | 71.0 | 0.24 | 71.0
 | u.u.cM | 0.24 | 78.2 | 0.24 | 78.2
 | l.d.cM | - | - | 0.26 | 78.8
 | l.u.cM | - | - | 0.26 | 78.7
Main return transfer line (HTL) |  | 0.50 | 5.0 | 1.00 | 16.7
Return piping in cold box |  | 0.50 | 4.9 | 1.00 | 19.5
Total pressure drop |  |  | 100.8 |  | 156.4
Required LH2 pump head > 156.4 kPa.

## Slide 5: Hydrogen Pump
A ball-bearing type hydrogen pump
Required pump heads are 156.3 kPa for 1 kg/s and 100.8 kPa for 0.5 kg/s.
If one pump fails, the other is ramped up to get the required flow rate.
For the two-pump operation, the required rotation speeds are 7,500 rpm and 10,000 rpm for the two- and four-moderator arrangements.
It turns out that, even if one pump fails, the revolution speed required for the remaining pump is lower than the maximum speed of 14,000 rpm.
Two-pump operation in series
Single pump operation
17K and 1.0 MPa
17K and 1.0 MPa

## Slide 6: Heat Load
Component | Two-moderator | Four-moderator
Two hydrogen pumps ( 0.72) | 934.8 | 2,908.5
PCB, HXs, o-p-H2 converter | 36.7 | 36.7
Piping, valves and auxiliary pipes in Cold box | 14.5 | 14.5
HTL feed and return lines with valves (MLI=20 layers) | 126.4 | 126.4
Distribution piping, valves and auxiliary pipe | 118.1 | 231.2
Moderators and their pipe without MLI | 227.2 | 454.3
Spacers in MRP | 420.8 | 850.0
Total static heat load | 1,878.5 | 4,618.6
Dynamic heat load: Nuclear heating at moderators | 6,696.0 | 17,248.0
PCB Active Control | 1,960.0 | 1,960.0
Total static + dynamic heat load | 10,534.0 | 23,826.6
Component | Two-moderator | Four-moderator
 | 934.8 | 2,908.5
PCB, HXs, o-p-H2 converter | 36.7 | 36.7
Piping, valves and auxiliary pipes in Cold box | 14.5 | 14.5
HTL feed and return lines with valves (MLI=20 layers) | 126.4 | 126.4
Distribution piping, valves and auxiliary pipe | 118.1 | 231.2
Moderators and their pipe without MLI | 227.2 | 454.3
Spacers in MRP | 420.8 | 850.0
Total static heat load | 1,878.5 | 4,618.6
Dynamic heat load: Nuclear heating at moderators | 6,696.0 | 17,248.0
PCB Active Control | 1,960.0 | 1,960.0
Total static + dynamic heat load | 10,534.0 | 23,826.6
Total heat loads are lower than the maximum TMCP cooling power of 30.3 kW.

## Slide 7: Ortho-para-hydrogen Converter
An ortho-para-hydrogen converter is installed in a bypass.
Iverson has predicted that p-H2 (99.5 %) decreases to 99.488% due to a neutron irradiation in the moderators for the 5MW proton beam at 14 Hz.
- In order to keep 99.5 % of pH2 fraction,
Required bypass flow through the o/p converter is31.5 g/s.
(on the assumption that the conversion efficiency is 80%)
O-p-H2 converter
=0.8
17.3 K
Moderators
99.5%
99.488%
1 kg/s,
(99.5%)
kg/s,
(99.5%)
kg/s (99.5%)
kg/s,
(99.488%)
1 kg/s,
(99.5%)
kg/s
0.8 x 99.96+0.2 x 99.5%
Catalyst | IONEX® Type OP (Ferric oxide)
Catalyst particle size (mm) | 0.5
Catalyst bed size (L) | 35 (9.6:calculated value)
Porosity (-) | 0.4
Flow rate (g/s) | 31.5
Pressure drop (kPa) | 24.6
Space Velocity (min-1) | 2170
Conversion efficiency (%) | 80
Dia.=273 mm

## Slide 8: In-situ Ortho-para-hydrogen Fraction Measurement System
ESS plan is to measure the para-hydrogen concentration in situ, using Raman spectroscopy through a small sapphire glass window to ensure the 99.5% of para-hydrogen requirement.
=3.94 kPa
Sapphire glass windows (dia.< 20mm) are placed in a bypass and are isolated from the main loop by feed and return valves.
-> If a hydrogen leak occurs due to a failure of the glass window, it is completely isolated from the main CMS loop.
Piping size:
½” tubing
-> The remaining LH2 is released and depressurized, while the leaked hydrogen leaked in the vacuum space is released through a vacuum safety device.
Design result | 
Design pressure (MPa) | 1.7
Volume (L) | 0.6
Flow rate (g/s) | 1.0
Pressure drop (kPa) | 1.47
Heat load (W) | 10
Temperature rise (K) | 1.0
Sapphire glass windows
(dia.< 20mm)
Now high reliable sapphire glass window is being developed.

## Slide 9: Pressure Control Buffer (PCB)
LH2 density change due to the nuclear heating (DT=2.1 K for 5 MW beam) would result in a pressure rise.
Unlike SNS and J-PARC, ESS plans to use ”Subcooled LH2” (17K and 10 bar).
It is expected that GH2 phase (behaving as a compressible fluid) would mitigate the sudden large pressure fluction.
Pressure Control Buffer tank has been designed to mitigate the pressure fluctuation below 1bar..
DP
PCB (65 L) is placed in the pump discharge.
Evaporated gas is liquified passing through HX-61200 and then come back to the LH2 pump suction.
Pressure in the CMS is controlled by the bypass valve .
For the nominal operation, the bypass flow is estimated to be 0.33 g/s and 200 W is removed by HX-61200.
For the case of a large pressure rise, it would be mitigated by increasing the bypass flow and liquefying it. -> ”Active control”

## Slide 10: Mitigation of the Pressure Fluctuation Caused by the Nuckear Heating by Using the PCB
HX
4 Moderators
1 kg/s
Travel time from moderator to HX = 11.5 s
T1=17 K
T2=17.5 +DT(=2.1K)
Before a proton beam injection
V2=179 L
T1=17 K
P1=10 bar
V2=179 L
V1=162 L
T2=17.5 K
After a 5MW proton beam injection
V1=162 L
Calculation of the mass balannce on the assumption that
all the heat load applied at the moderators is completely removed through the HX.
17.2 kW
for 4 moderators
LH2:V3, T3=T1
GH2:V4=65-V3,
T4=45 K
DV
Simple calculation model

## Slide 11: Simulation Results
It is predicted that the pressure rise would be below 1 bar for V3=20 L, if the thermal compensation by the TMCP works well.
Effect of liquid H2 volume in PCB
Effect of proton beam power
Pressure rise (bar)
Proton beam power (MW)
Pressure rise (bar)
Liquid hydrogen volume in PCB,V3 (L)
V3=20 L
Four moderators
Two moderators
For 5 MW proton beam opeation
Four moderators
Two moderators

## Slide 12: CMS Schedule
Manufacturing CMS cold box (until January, 2020)
TUV inspection and preparation for FAT (January to March, 2020: )
FAT for the CMS cold box at Forschungszentrum Jülich (March and April, 2020 )
Manufacturing HTL
Installation at ESS site (October, 2020 to March, 2021 ).
Commissioning (August, 2021 to April, 2022)

## Slide 13: Summary
ESS cryogenic moderator system (CMS) where subcooled liquid hydrogen (17 K and 10 bar) has been designed and is being manufactured.
- Two pumps in series
- Two kinds of heat exchangers
- Ortho-para hydrogen converter
- Pressure control buffer (PCB) for passive and active pressure control.
- In-situ para-hydrogen measurement system
- Hydrogen transfer line (HTL)
- Hydrogen vent line
It is confirmed that the pressure drop and the heat load meet the design requirement.
The simple simulation result says that the PCB can mitigate the pressure fluctuation caused by the nuclear heating below 1 bar if the nuclear heating can be completely removed through the HX by TMCP.

## Slide 14: ESS Cryogenic System Block Diagram
Pure Helium
Gas Storage
Standalone Helium Purifier
Helium Recovery System
Accelerator
Cryoplant
5 m3
LHe Tank
Target Moderator
Cryoplant
LHe Mobile Dewars
Test Stand Cryodistribution System
Instruments & Experiments
LN2 Storage Tanks
LN2 Mobile Dewars
Cryodistribution System for Elliptical Linac
Elliptical
Cryomodules
Test Stand Lund 2
Target Cryodistribution System
Hydrogen Circulation Box
Hydrogen Moderator
Cryodistribution System for
Spoke Linac
Spoke
Cryomodules
20 m3 LHe Tank
Test & Instrument Cryoplant

## Slide 15: The Target Moderator Cryoplant (TMCP)
Duty Specification Helium Refrigeration System
Heat load: 30.3 kW @ >15 K feed and < 20 K return temperature
Large turndown-ability: static heat load ~ 5 kW with max energy efficiency
Handle beam trips, long term and short term
Cool down and warm up TMCP, CTL, CMS
Acceptance testing TMCP alone
Acceptance testing integrated TMCP-CTL-Jumper Spool Box
Target Moderator
Cryoplant
Target Cryodistribution System
Hydrogen Circulation Box
Hydrogen Moderator

## Slide 16: TMCP simpliefied flow scheme
u.u.cM
l.d.cM
l.u.cM
u.d.cM
O-p-H2
converter
Filter
PCB
(65 L)
NV-62016
NV-82016
CMS cold box
Feed valve
Distribution box
U-shaped
Bayonet
HTL
Distribution lines
MRP
Moderators

## Slide 17: TMCP simpliefied flow scheme
Ambient heater: central equipment
Heat load for Coldbox acceptance test
Warm-up of Coldbox
Heat load for integrated system
Heat load during beam trip
Temperature control during hydrogen circuit warm-up / cool-down
Mitigation of pressure increase during power shut-down
Switching compressor operation while keeping CTL inventory stable

## Slide 18: TMCP Compressor system

## Slide 19: TMCP Coldbox
TMCP consist of
Coldbox 3.5m diameter, 10m long, 5.7m high inc. 3 expansion turbines
Combined ACCP and TMCP Coldbox platform
Jumper Spool valve box in target building
2 identical GEA compressors in Enerproject skids, 1200 kW power
Bulk oil removal, final oil removal, gas management, analysers
Long single helium VJ transfer lines being procured now

## Slide 20: Current status
Successful completion of TMCP alone acceptance testing
Excellent compressor performance (efficiency, cooling water control, slide valve control, documentation)
Acceptable coldbox and overall performance, few punch points
Cryoline project to start soon
Integrated testing in 2021 / 2022
Questions?