## Slide 2
First operational results of large liquid argon volume membrane cryostats and their cryogenic systems at CERN
Johan Bremer on behalf of the
CERN Neutrino Platform Collaboration

## Slide 3
Content
Introduction to DUNE
Prototyping
  One of the possible detection principles
  The Membrane cryostat principle
  Detector integration
  Liquid argon purity
  Cryogenics
Purging, cool-down and filling
Stable operation results (pressure and temperature stability, purity level)
Conclusions

## Slide 4: Introduction to DUNE
An international collaboration of more than 1000 scientists is working on the next large neutrino experiment, containing the creation as well as the detection of neutrino’s:
  These proton will hit a graphite target generating particles which will decay in muon neutrino’s;
DUNE (Deep Underground Neutrino Experiment) near detector at the Fermilab site
DUNE far detector at 1300 km from Fermilab
LBNF (Long-Baseline Neutrino Facility) supplying the experimental infrastructure (caverns, cryogenic infrastructure, electrical power,…)
New PIP-II at Fermilab: 250 meter long superconducting Linac. Proton beam then passes the existing Booster and Main Injector-Recycler, creating a proton beam with an energy of 120 billion electronvolt (120 GeV).

## Slide 5: Introduction to DUNE FD
Interesting from the cryogenics point of view:
The Far Detector
1300 km from Fermilab;
1,5 km underground;
Detector housed in four cryostats holding a total volume of 70.000 tons of liquid argon;
Use of membrane cryostat principle;
Argon purity needed in ppt O2 equivalent;
Uninterrupted cooling power based on evaporation of LN2.
From no experience to 17.500 tons cryostat: Proto-typing needed

## Slide 6: Prototyping
35 T
35 T
Program finished
(2016/17)
(Fermilab)
SBNND
263 T
2020
(Fermilab)
Proto Dune DP
840 T
Cool-down in August 2019
(NP02, CERN)
Proto Dune SP
840 T
Cool-down in August 2018
(NP04, CERN)
1 x 1 x 3
17 m3
26 T
Program finished
(2016/17)
(CERN)

## Slide 7: Prototype cryostats (NP02 and NP04) at CERN
At CERN a test station has been build containing two detectors, each housed in a cryostat with a volume of about 600 m3 and equipped with its complete infra-structure (including cryogenic system, purification system, electrical power supply etc.). These systems were conceived to test:
two detection principles (single phase, and double phase);
the membrane cryostat principle;
the experimental set-up (how to build and insert the detector);
the high purity principle;
the cryogenic system;
Foreseen to be tested wit SPS beam

## Slide 8: Single phase detection principle
Wire number
Drift time

## Slide 9: Single phase detection principle
175 kV over detector volume

## Slide 10: The membrane cryostat principle
Advantages:
No insulation vacuum: cannot break the vacuum;
Rectangular constructions can be build, gaining space;
Several tenths of year experience with the storage transport of large volumes of natural gas (111 K);
LAR only in contact with stainless steel membrane (cleanness);
Dis-advantages:
High heat load through walls (5 W/m2);
Membrane cannot support forces, which have to be transferred to a heavy outer structure;
System supports only very low over pressure (forces on outer structure) and under pressure (forces on membrane);
System has never been used to support experiments nor to be equipped with connection at the bottom and signal feed throughs

## Slide 11: The membrane cryostat construction

## Slide 12: The membrane cryostat

## Slide 13: Detector integration (no support from membrane)

## Slide 14: Cryogenic principles
Molecular Sieve
Moisture adsorption
Demands:
The cryogenic system needs to be able to adsorb the heat-load into the cryostat and cryogenic system;
The cryogenic system has to guarantee a cryostat gas pressure staying well within the -30 mabrg and 350 mbarg limits (set pressure of safety valves);
Cryogenic system needs to assure an operational availability over a long period;
Cryogenic system needs to assure an oxygen equivalent impurity of the liquid argon in the detector within the low ppb O2 eq (10-9) level;
Temperature gradient over the detector volume shall be within one Kelvin;

## Slide 15: Cryogenic principles
Molecular Sieve
Moisture adsorption
Solutions:
The cryostat is protected by two pre-safety valves: venting argon or entering argon gas when system comes close to safety valve opening pressure;
All supply systems are backed-up (electrical, compressed air, …), and cryostat system will “survive” without attendance (= without control/supply systems)
All detector wiring will leave the cryostat via the top: push the gas, created by the heat load into the argon bath, out of the cryostat via these cable feed-throughs. This gas is re-liquefied, and passed through a purifier system before being returned to the cryostat volume;
A circulation pumps takes continuously liquid argon from the bottom of the cryostat, passes it through a purifier, and returns it to the bottom of the cryostat;
Cooling is supplied by evaporation of liquid nitrogen;

## Slide 16
Molecular Sieve
Moisture adsorption
to purifier
from purifier
720 Tons of Liquid Argon
1.9 kg/s
Cryogenic principles

## Slide 17: Liquid argon purity
Demanded liquid argon purity: < 1 ppb O2 equivalent
Cryostats can not be vacuum pumped. Open loop purge: enter clean argon over the cryostat bottom surface and push air out at the top. At the correct speed (about 1 m/s) arrived at a gas purity of < 1 ppm O2 eq. after having passed 15 cryostat volumes;
Closed loop purge: cycle gas volume through warm purifier with help of warm circulator;
Purifier (warm and cold): Molecular Sieve (H2O) and active Cu pellets (replacement of Oxysorb). These systems can be regenerated on-line.
Molecular Sieve
Moisture adsorption
Cu-226 (Cu coated Al2O3)
Oxydation (RT and -87 K):
Reduction (420 K)

## Slide 18: Purging, cool-down and filling
At the start of operation, each cryostat has been purged: enter clean argon gas (< 2 ppm O2 eq.) at the bottom of the cryostat via a distributed system. Keep the vertical gas flow speed at about 1 m/s. In this way no turbulences and no back diffusion (open loop purge);
Closed loop purge: push cryostat gas in close loop through a purifier: O2 level will drop (<100 ppb), but what is N2 percentage doing: leak / no leak?
Start liquid argon delivery: specified < 2 ppm O2 eq., at delivery measured: < 0.7 ppm;
Distribute argon via liquid purifier to bottom lines and top sprayers. Within two days coldest point cryostat < 100 K and during this cool-down temperature gradient over detector < 70 K.
Then: start liquid argon filling

## Slide 19: Purging, cool-down and filling
About 950 tons of LAr to be delivered at a rate of 40 tons per day (5 days/week): a logistic nightmare!

## Slide 20: Purging, cool-down and filling
Chart: Date
| 43649.340277777781 | 43650.614583333336 | 43651.354166666664 | 43656.350694444445 | 43656.55972222222 | 43657.383333333331 | 43657.614583333336 | 43658.381249999999 | 43658.481249999997 | 43661.591666666667 | 43662.59652777778 | 43662.680555555555 | 43663.357638888891 | 43663.554166666669 | 43664.356944444444 | 43664.427083333336 | 43665.350694444445 | 43665.351388888892 | 43668.354166666664 | 43668.604166666664 | 43669.465277777781 | 43669.510416666664 | 43670.354166666664 | 43670.569444444445 | 43671.354166666664 | 43671.493055555555 | 43672.34375 | 43672.638888888891 | 43675.489583333336 | 43675.586111111108 | 43676.363194444442 | 43676.440972222219 | 43677.345138888886 | 43679.42083333333 | 43679.493055555555 | 43682.404166666667 | 43682.588888888888 | 43683.347222222219 | 43683.60833333333 | 43684.345833333333 | 43684.456250000003 | 43685.34375 | 43685.369444444441 | 43686
Cumul Lar (T) | 19.08 | 42.99 | 63.77 | 84.41 | 106.17 | 128.19 | 152.214 | 171.954 | 193.734 | 215.234 | 234.414 | 258.079 | 280.159 | 301.539 | 323.639 | 344.119 | 365.659 | 386.979 | 407.559 | 428.399 | 449.646 | 471.566 | 490.266 | 511.386 | 534.286 | 555.849 | 576.469 | 596.669 | 616.829 | 638.949 | 662.248 | 683.928 | 704.768 | 725.428 | 742.988 | 758.188 | 778.748 | 799.408 | 823.308 | 845.108 | 865.348 | 888.368 | 909.108 | 929.967
Delivery number | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44

## Slide 21: Purging, cool-down and filling

## Slide 22: Stable operation results
Once the cryostat is filled, the liquid argon pumps are started to push the liquid through the purifier system. The liquid is then returned to the bottom of the cryostat, introducing thermal movement in the bath (breaking the stratification). The re-condensation loop is constantly active (compensation of heat loads).
Stability of argon bath pressure
Stability of argon bath temperature

## Slide 23: Stable operation results
purity (ppb)= = 35 ppt
The passing of the liquid through the purifier system lowers the oxygen content in the detector. After one month of circulation level from about 50 ppt!
HV over detector volume operational at 175 kV!

## Slide 24: tracks
7/29/19
24
1 GeV - Pion Interaction (Absorption —> 2 p)
2 GeV - Electron shower
3 GeV - Pion Interaction(s)
(and decay)
7 GeV - Pion Interaction
LArTPC data of unprecedented quality

## Slide 25: Conclusions
CERN is via the Neutrino Platform participating in the proto-typing for the DUNE experiment;
DUNE asks for large volume liquid argon based detectors;
Recently two DUNE prototype detectors, each housed in a 600 m3 membrane cryostat, have been brought to operation conditions;
The cryogenic system full-fills largely the requirements (temperature gradients, pressure stability, impurity level,..) demanded by the DUNE experiment;
……. First DUNE detector cryostat foreseen to be filled by end 2028!