## Slide 1: The ESS Accelerator/Target interface and status of the A2T
Iñigo Alonso
Lead Engineer, Linac Group
European Spallation Source ERIC
2019/04/11

## Slide 2: Outline
Context
Accelerator systems
Accelerator/Target interfaces
Integrated operations
Installation schedule
Table of contents

## Slide 3: Context
Accelerator sections
Dogleg
DmpL
HEBT
PBDR
NSW
A2T
TBD
Target
HEBT: High Energy Beam Transport
DmpL: Dump Line
A2T: Accelerator to Target
TBD: Tuning Beam Dump
NSW: Neutron Shield Wall
PBDR: Proton Beam Drift Room
Notes: HEBT+A2T ~40% of the 601m linac
+DmpL ~45%of total beam line

## Slide 4: Context
Top view
Target
Gallery Support Area (GSA)
Proton Beam Drift Room
A2T tunnel

## Slide 5: Accelerator systems
Systems in the DmpL and A2T sections of the Linac
HEBT
DmpL
A2T
Emergency exit
Target
Raster magnets
Gamma Blockers
Beam Instrumentation
Phase Reference Line
Vacuum
Magnets: quads, correctors, dipoles
Magnets Power Supplies
MPS & PSS
Tuning Beam Dump
Electrical support
Cooling support
Instrument air
WP 6 Beam Deliver Systems
WP 6 Beam Delivery Systems
WP 7 Beam Diagnostics
WP 8 RF Systems
WP 12 Vacuum
WP 14 Linac
WP17 Power Converters
Integrated Control System
Target
Infrastructure Project (former WP15)
Infrastructure Project (former WP16)
Infrastructure Project (former WP16)

## Slide 6: Accelerator systems
Magnets
6
Q8 Quads
Raster
D1 Dipole
Q7 Quads
C8 Correctors
C6 Correctors
Q6 Quads

## Slide 7: Accelerator systems
Danish contribution by Aarhus University
Beam optics by Heine Dølrath Thomsen, in collaboration with the ESS Beam Physics section
Raster magnets and power supplies produced by Danfysik, expected delivery in May 2019
Raster magnets and beam optics
By By Bx Bx | Bx Bx By By
AP
QP1-4
QP5,6
2.0 GeV: Bx = ±1.96 mT.m, By = ±2.28 mT.m, ±5 mT.m
PBW
BEW
Centroid
10 x RMS beamlet
RMs
CO
Courtesy Heine Dølrath Thomsen, ISA, Aarhus University

## Slide 8: Accelerator systems
Raster magnets and beam optics
5/4 pattern
113/83 pattern (200 kHz filter)
Beamlet RMS
Hor / Ver wfm
(ax, ay, σx, σy) = (60, 20, 12, 4.5) mm
Closed pattern (fx/fy, ϕxy, ax, ay) within a beam pulse:
T0 = 2.86 ms = (350 Hz)-1 fx = nx / T0, fy = ny / T0
Triangle waveforms => No lingering near edges, crosshatch
fx / fy ~ 1 => A single (magnet + supply) design
fx = 39.6 kHz
fy = 29.1 kHz
Courtesy Heine Dølrath Thomsen, ISA, Aarhus University

## Slide 9: Accelerator systems
Vacuum
9
Turbo Molecular Pumps
Sector Gate Valves
NEG Pumps
Primary Dry Pumps
Pirani, cold-cathode and thermo couple gauges also present
Target Isolation Valve

## Slide 10: Accelerator systems
Vacuum
https://confluence.esss.lu.se/display/VG/Vacuum+Section

## Slide 11: Accelerator systems
Beam Instrumentation
11
BCM
BIF (NPM)
WS
APTM
APTM
IMS
GRID
IMG
BPM
IMG

## Slide 12: Accelerator systems
Lattice synoptic view
https://confluence.esss.lu.se/display/ALSV/Accelerator+Lattice+Synoptic+Viewer
See talk by Tom Shea
Notes: Refer to Tom Shea’s presentation

## Slide 13: Accelerator systems
Other systems
13
A2T Gamma Blocker
Dump Line Gamma Blocker
Crane
Phase Reference Line

## Slide 14: Accelerator systems
Vacuum chamber with a sliding steel core inside, tasked with blocking the line of sight to the target wheel/dump while maintenance happens in the accelerator tunnel, to shield workers against gammas from those highly activated components.
Interface switches to MPS and PSS
Core sizes:
  A2T: 20cm * Ø20cm
  DmpL: 5cm * Ø37.5cm
In-kind contribution from NCBJ, Poland
Delivery expected mid April 2019
Gamma Blockers
A2T
DmpL

## Slide 15: Accelerator/Target interfaces
ESS.SyR-192 | Target Station shall receive proton beam from accelerator.
ESS.SyR-312 | Target Station shall limit its backscattering of particles to the accelerator.
ESS.SyR-313 | Target Station shall protect the accelerator from contamination by its by-products.
ESS.SyR-314 | The Target Station monolith atmosphere shall be prevented from entering into the accelerator beam pipe so that the accelerator vacuum is preserved.
ESS.SyR-410 | At the completion of the milestone ‘5MW’ of the ESS Construction Phase, the accelerator shall be designed and constructed to be capable of delivering to the Target Station a time averaged proton beam power of 5 mega-Watts.
ESS.SyR-420 | At the completion of the milestone ‘First protons to target’ of the ESS Construction Phase, the accelerator shall be designed and constructed to be capable of delivering to the Target Station a time averaged proton beam power of 1 mega-Watts
ESS.SyR-430 | The nominal operational repetition rate of accelerator acceleration cycles shall be 14 Hertz.
ESS.SyR-450 | The nominal operational beam pulse length shall be 2.86 milli-Seconds.
ESS.SyR-460 | The nominal peak beam power delivered to Target Station averaged over a period of 200 micro-Seconds shall not vary more than 5 percent from the peak beam power delivered to Target Station averaged over the nominal macro pulse length.
ESS.SyR-463 | The time averaged beam power delivered to the Target Station shall not vary more than 5 percent pulse to pulse.
ESS.SyR-465 | The time averaged beam power delivered to the Target Station shall be able to be varied in steps to its nominal value of 5 mega-Watts with a maximum step size of 500 kilo-Watts and with a precision of 125 kilo-Watts.
High level ESS System Requirements
ESS Systems Architecture Specification, ESS-0005699

## Slide 16: Accelerator/Target interfaces
Beam on Target Requirements
Proton beam current density spatial distribution at the PBW (left), and the BEW (right) at 5 MW beam power. The blue rectangle illustrates the outline of the raster pattern
Parameter | Value at PBW | Value at BEW
Maximum beam footprint enclosing 99% beam fraction (mm2) | 140 H × 52 V | 160 H × 60 V
Maximum beam footprint enclosing 99.9% beam fraction (mm2) | 160 H × 56 V | 180 H × 64 V
Nominal time-averaged peak current density (µA/cm2) | 89 | 56
Maximum time-averaged peak current density (µA/cm2) | 112 | 71
Maximum displacement of footprint from nominal position (mm) | ±4 (horizontal) | ±5 (horizontal)
 | ±3 (vertical) | ±3 (vertical)
Minimum sxsy for rastered Gaussian beam (mm2) |  | 50
Minimum horizontal raster frequency (kHz) |  | 35

## Slide 17: Accelerator/Target interfaces
Target Station
  Beam on Target Requirements, ESS-0003310
Beam Instrumentation
  ICD-R: Proton Beam Instrumentation Plug - Proton Beam Instrumentation, ESS-0060563 (Preliminary)
  ICD-R: Proton Beam Window - Proton Beam Instrumentation, ESS-0060561 (Rev.2 Preliminary)
  ICD-R Monolith Systems – Proton Beam Instrumentation, ESS-0032631
  ICD-R Inner Shielding - Proton Beam Instrumentation, ESS-0084051
  ICD-R Outer Shielding - Proton Beam Instrumentation, ESS-0084052
  ICD-R Covers, Penetrations and Monolith Vessel 1067 - Proton Beam Instrumentation A117, ESS-0078254 (Preliminary)
Target Safety System
  ICD-R Target Safety System - Accelerator, ESS-0030068
Tuning Beam Dump
  ICD-R Tuning Beam Dump and Shielding, Target – Accelerator, ESS-0034025
  ICD-R: CWS02 Water Cooling System - Tuning Beam Dump Shielding, ESS-0104429
Vacuum
  Monolith Systems
  Moderator vacuum insulation
Cryogenics
  TMCP
  Target cryogenic systems
Interface Control Documentation
Interface Control Document Target Systems- Accelerator Systems, ESS-0022919
Notes: Old ICD: ESS-0005734 (Obsolete)

## Slide 18: Accelerator/Target interfaces
Neutron Shield Wall
Manhole
Heavy Concrete
Normal Concrete
Vacuum Pipe penetration
Courtesy Alexander Hermansson
Notes: CDR 12 March 2019

## Slide 19: Accelerator/Target interfaces
Physical interface near the NSW
PBDR Pipe
VAT Isolation Valve
Bellow DN40
Beam Position Monitor (BPM)
Aperture Monitor (APTM)
Gamma Blocker (GB)
4
6
5
3
2
Proton Beam Direction
1
Interface point
Courtesy Alexander Hermansson

## Slide 20: Accelerator/Target interfaces
Prompt dose rates
Beam losses
Combined dose rate
Backscattering
ESS-0322246 - ESS Proton Drift Tube; UKAEA Prompt Radiation Transport Calculations for the ESS Proton Drift Tube Room

## Slide 21: Accelerator/Target interfaces
Activation and shutdown dose rates
Shutdown dose rate in µSv/hr
2 µSv/hr
0.8 µSv/hr
Activation of components in Bq/g for T= 0
Shutdown dose rate in µSv/hr from the target wheel source
ESS-0679987 - ESS Proton Drift Tube; UKAEA Shutdown Dose Rate Calculations for the ESS Proton Drift Tube and Accelerator to Tunnel Rooms

## Slide 22: Integrated operation of Accelerator and Target
The normal operation of the Neutron Source (linac + target) will be performed from the Main Control Room
  See talk by Lali Tchelidze
Communication between accelerator and target developed by the Integrated Control System division:
  EPICS
  Timing System
TSS
More high level coordination is needed
Notes: higher-level coordination should be strengthen to avoid surprises later on
AA2 - Accident Analysis Report - Proton Beam events on Target and Proton Beam Window, ESS-0063901 https://chess.esss.lu.se/enovia/link/ESS-0063901/21308.51166.46337.1618/valid
AA13 - Accident Analysis Report - Public: High power beam on Beam Dump, ESS-0057359 https://chess.esss.lu.se/enovia/link/ESS-0057359/21308.51166.16384.7257/valid

## Slide 23: Installation schedule
Current status of the buildings

## Slide 24: Installation schedule
Accelerator + ICS
2018
2019
2020
2021
2022
2023
2024
2025
Beam on Dump
(570 MeV)
Accelerator Schedule Float
Accel RBOT
Warm LINAC Commissioning Steps
BOT
SOUP
EOC
Hi-Beta Install
1.3 GeV Capability Installed
ES
Notes: HEBT 2019
TBD Q4 2019
NSW Q4 2019
PBDR Q1 2020
Dump Line
Dogleg
A2T, access 2020/01/20
GSA, access ~2021
RBOT 2021/09/13

## Slide 25: Installation schedule
2019
2020
2021
2022
TBD
NSW
PBDR
DmpL
DgLg
A2T
GSA
RBOT
HEBT
BOT
Notes: HEBT 2019
TBD Q4 2019
NSW Q4 2019
PBDR Q1 2020
Dump Line
Dogleg
A2T, access 2020/01/20
GSA, access ~2021
RBOT 2021/09/13

## Slide 26: Thank you for your attention
Questions?

## Slide 27: Raster Scanning Magnets System
Pre-series testing at Aarhus University
Termination box
RSM2 RSM1
RSM2 RSM1
PLC
Power cables
Girder
Local PC
PicoScope
EVR
Bdot, Interlock
Courtesy Heine Dølrath Thomsen, ISA, Aarhus University

## Slide 28: Other pictures
Civil construction
GSA chicane conduits (2018)
A2T walls 1st level (2018)
GSA (Feb 2019)

## Slide 29: Accelerator/Target interfaces
Monolith general layout
3D perspective view
Side view along the vertical plane of the incident proton beam

## Slide 30: Accelerator tunnel
Main dimensions
30
TCS: Target Coordinate System
Section A-A:
6000
3500
2850
3150
1500
4°
52400
22222
60900
A
A
TCS