## Slide 1: Beam monitors and detectors: Utilities and services
Anders Lindh Olsson
Presented at IKON17
Wednesday 11/9-2019 in Lund, Sweden

## Slide 2: Beam monitors and detectors: Utilities and services
Monitors
  Ionisation chamber
  GEM
  MWPC
  Fission chamber
  Parasitic
Non-utility I/O (baseline readout)
  Time
  Controls
  Signal
    Pre-processing (pulse-shaping, amplification)
    Readout
Dependencies and restrictions
  Geographical: Grounding zones and electrical supply
Requirements

## Slide 3: Beam monitors and detectors: Utilities and services
Power
  HV for detectors, LV for electronics
Network
  Fibre for Neutron Instrument Network (NIN; events) & timing and across grounding zones
  Fibre for Technical Network (TN; controls) for Detector Systems
Readout
  Front-end electronics (digitisation, pre-processing)
  Generic readout master
Utilities/services (gas, cooling, motion, etc.)
  COTS
  Beckhoff terminals for generic IO
“Standard detector hardware”

## Slide 4: Beam monitors and detectors: Utilities and services
Detector (…)
Detector rack (19”, 1200mm*800mm, 37+U)
UPS (On-Line; 3-phase 400V AC-> 1-phase 230V AC)
PDU (1-phase 230V AC -> IEC/SCHUKO)
PSU (HV and LV distribution, low noise)
Readout (FEE + ESS back-end)
Utilities (gas, motion, etc.)
Cooling (liquid)
System monitoring (chamber, electronics, rack, environment)
Detector racks

## Slide 5: Beam monitors and detectors: Utilities and services
Mainly geographical
Grounding zones
Distance(/separation?) from noise-inducing equipment
Cable lengths and signal integrity (analogue)
Area usage
Accessible infrastructure (power, gas feeds)
Constraints

## Slide 6: Beam monitors and detectors: Utilities and services
Standard detector rack, possibly mini-rack
Space estimate—worst case:
  BM readout 6U
  Crate for modular electronics 5U
  Switch(es) 3U
  UPS 6U
  IOC machine/EVR host 1U
  IFB300 1U
  Sum total = 21U // Approximately half the volume of our detector racks
More reasonable to assume something like 10U total
  i.e. very small footprint compared to full detector system (thousands of channels, etc.)
Beam monitor systems

## Slide 7: Beam monitors and detectors: Utilities and services
Architecture overview as shown on previous IKONs
The data will be available to all users, instrument team, technical experts, facility in appropriate views as enabled by the proposed architectures
Data infrastructure architecture

## Slide 8: Beam monitors and detectors: Utilities and services
Vertical Integration Project: V20 tests, controls and readout
ESS beam monitor readout demonstrated
Full data path from detectors to file writing and Mantid analysis/visualisation demonstrated
http://arxiv.org/abs/1908.08041

## Slide 9: Beam monitors and detectors: Utilities and services
Partners and In-Kind collaborators
DMSC ECDC
ICS Work Package 12—NSS integration
Beamline Controls Team
Experiment Controls Project
Control system integration

## Slide 10: Beam monitors and detectors: Utilities and services
Control system integration: tools and user interfaces
DMSC’s Daquiri for live streaming of pulses and events
EPICS integration of standard detector equipment
Engineering interfaces in CS-Studio

## Slide 11: Beam monitors and detectors: Utilities and services
Prototyping

## Slide 12: Beam monitors and detectors: Utilities and services
Hardware evaluation
Identifying remaining hardware and suppliers
Fine-tuning specifications
Testing and integration
For controls
Identifying, defining, and fine-tuning use cases to enable commissioning and smooth operations
e.g.
Optimal parameters, calibration and handling these
EXPERT and ENGINEERING perspectives
Current status

## Slide 13: Thank you for listening!
Anders Lindh Olsson
Detector Group, European Spallation Source ERIC
anders.lindholsson@esss.se

## Slide 14: Beam monitors summary
Achievements since start of project
Integration to back-end readout electronics
Official ESS DAQ chain used
4 beam times collecting BM data of various fluxes and time resolutions
Systematic approach to data analysis
Simulations to
  aid absolute flux and time resolution estimates
  support derivation of design specs
Communication with suppliers established
Good interaction with instrument engineers - CAD reservations in place
Work on beam monitor racks, utilities, and services initiated
All info presented today will be communicated in confluence and in the PDR
https://confluence.esss.lu.se/display/DG/Beam+monitors+common+project
No show stopper so far in terms of BM technology choice
Please indicate your intentions to join the project by ICB (Oct 9)!

## Slide 15: Beam monitors summary
Monitors per location and function
Location | BM options | Desired functionality
Bunker | Fission chamber ✅ | Flux Timing Discrimination (thermal n vs. fast n vs. gamma)
 | GEM ❓ | 
 | Ionisation chamber ✅ | 
Guides/choppers | GEM ❓ | Flux Timing
 | Parasitic γ-monitor ❓ | 
 | Semi-parasitic V monitor ✅ | 
Pre- and post-sample | MWPC ✅ GEM ❓ | Flux Timing