## Slide 1: Instrument Shielding Requirements Due to Non-Designated Areas
Ken Andersen
IKON-17
Lund, 10th September 2019

## Slide 2: Radiological Requirements and Guidelines for Instrument Shielding Design (ESS-1108220)
Calculations of dose rates in non-designated areas from all of ESS
  consequences for instrument shielding
Implementation for instrument shielding of high-level radiological requirements for ESS
  summarised on Confluence page “Advice on shielding and radiological safety for instruments”
Authors: Ken Andersen, Senad Kudumovic
Reviewers: Andrew Jackson, Sigrid Kozielski, Günter Muhrer
Approver: Shane Kennedy

## Slide 3: Supervised zones at ESS
Supervised areas: 3 μSv/hour
Non-designated areas: 100 μSv/year
Occupancy factors for non-designated areas
  ESS-1095920 approved
  2000 hours/year of baseline occupancy
  × 65% occupancy for offices
  × 10% occupancy for outdoor areas, stairs, corridors, toilets, meeting rooms, …
Safety factors apply to all dose rate calculations
  × 2 for approved Monte Carlo code, × 3 for handbook

## Slide 4: 13 Reference Points Defined
Considered to be worst-case positions within non-designated areas
1
2
3
4
56
7
8
910
11
12
13

## Slide 5: 13 Reference Points Defined
Considered to be worst-case positions within non-designated areas
1
2
3
4
56
7
8
910
11
12
13
2
1
3
4
10m
10m
E04
E04
Level 100
E05
Level 110
HEIMDAL
T-REX
MAGIC
MIRACLES
HEIMDAL
T-REX
MAGIC
MIRACLES

## Slide 6: 13 Reference Points Defined
Considered to be worst-case positions within non-designated areas
1
2
3
4
56
7
8
910
11
12
13
Level 100
Level 110
Level 120
10m
10m
10m
5
6
7
8
D08
D08
D08

## Slide 7: 13 Reference Points Defined
Considered to be worst-case positions within non-designated areas
1
2
3
4
56
7
8
910
11
12
13
9
D04
10
D04
10m
10m
Level 100
Level 110

## Slide 8: 13 Reference Points Defined
Considered to be worst-case positions within non-designated areas
1
2
3
4
56
7
8
910
11
12
13
Closest outdoor point to accelerator, target, bunker, instruments
Closest and highest point in campus area to instruments in E01
Closest and highest point in campus area to instruments in D01 and D03
11
12
13

## Slide 9: Accelerator Contribution
Gamma dose rate assumed negligible
Neutron dose rate taken from ESS-0063681
  “ESS accelerator skyshine dose rate maps during normal operations”
Apply occupancy factors

## Slide 10: Accelerator Contribution
1
2
3
4
56
7
8
910
11
12
13

## Slide 11: Target Contribution
Gamma radiation
  assume uniform contact dose rate of Dγ = 0.75 μSv/hour and rescale with
Fast neutrons
  use result from ESS-0065565 “Handbook assessment of the contribution of the target station to the dose at the site boundary through skyshine”: D = 6e-8 mSv/hour at 300 m from target station
  rescale with
Apply occupancy factors
from ESS-0134533 “Dose assignment in the offices for zoning discussion”
from A.H. Sullivan
“A guide to radiation and radioactivity levels near high energy particle accelerators”

## Slide 12: Contribution from the Active Cells Facility
Reference points 5-8 and 11 only
1
2
3
4
56
7
8
910
11
12
13
Gamma radiation
  assume uniform contact dose rate of Dγ = 1.5 μSv/hour and rescale with
Fast neutrons
  assume negligible
Apply 100% occupancy factor

## Slide 13: Contribution from the Bunker
Conservative calculation of radiation dose rate at bunker surface
  ESS-0416081 “Neutronic design of the bunker wall and roof”
  26 instruments with very large beams and fast-neutron spectra
MCNP transport from bunker surface to all reference points
  takes target building into account
  fast neutron contribution ~100x greater than gamma radiation contribution
Apply occupancy factors

## Slide 14: Dose Budgets for Instruments
Out of the total dose constraint of 100 μSv/year
1
2
3
4
56
7
8
910
11
12
13
Reference Point | Occu-pancy factor | Accelerator [μSv/year] | Target (incl. ACF) [μSv/year] | Bunker [μSv/year] | Instruments Budget [μSv/year]
1 (E04) | 10% | 2 × 0.6 | 3 × 0.1 | 2 × 0.3 | 97.9
2 (E05) | 10% | 2 × 0.6 | 3 × 0.1 | 2 × 0.3 | 97.9
3 (E04) | 10% | 2 × 0.6 | 3 × 0.1 | 2 × 0.3 | 97.9
4 (E04) | 65% | 2 × 3.9 | 3 × 0.5 | 2 × 1.8 | 87.1
5 (D08) | 10% | 2 × 1.2 | 3 × 3.4 | 2 × 1.0 | 85.4
6 (D08) | 10% | 2 × 1.2 | 3 × 3.4 | 2 × 0.9 | 85.6
7 (D08) | 10% | 2 × 1.2 | 3 × 3.5 | 2 × 0.8 | 85.5
8 (D08) | 65% | 2 × 7.8 | 3 × 5.5 | 2 × 5.2 | 57.5
9 (D04) | 10% | 2 × 20 | 3 × 1.6 | 2 × 1.0 | 54.8
10 (D04) | 10% | 2 × 20 | 3 × 1.6 | 2 × 0.8 | 55.2
11 (outdoors) | 10% | 2 × 3.0 | 3 × 2.7 | 2 × 5.8 | 74.3
12 (B01) | 65% | 2 × 1.7 | 3 × 0.9 | 2 × 2.9 | 88.1
13 (B02) | 65% | 2 × 1.7 | 3 × 1.0 | 2 × 2.2 | 89.2

## Slide 15: Calculating Dose Contributions from Instruments
Gamma radiation
  scales with the solid angle of the shielding surface seen from the reference point
  scales with cos(θ) – the surface normal to the shielding
  travels in straight lines: stopped by other shielding components
  attenuated by air
Fast neutrons
  only significant for shielding around components within line-of-sight of fast-neutron source
  within 100m: same method as gamma radiation (without air attenuation)
  outside 100m: use Sullivan sky-shine formula
Assume contact dose rate of 1.5 μSv/hour
Apply occupancy factors
from all instruments to all reference points

## Slide 16: Calculating Dose Contributions from Instruments
from all instruments to all reference points
Ref.Pt. 4
HEIMDAL
T-REX
MAGIC
MIRACLES
BIFROST
Ref.Pt. 4
Vertical cut
Horizontal cut
Example 1: T-REX seen from reference point 4

## Slide 17: Calculating Dose Contributions from Instruments
from all instruments to all reference points
Example 2: BEER seen from reference point 12
horizontal cut

## Slide 18: Calculating Dose Contributions from Instruments
from all instruments to all reference points
guide end
cave end
cave start
guide mid-point
guide start
Example 2: BEER seen from reference point 12
Vertical cuts

## Slide 19: Results of Instrument Dose Calculation
calculation compared to dose budget
Ref. Point |  | Total | LOKI | FREIA | ESTIA | SKADI | VESPA | DREAM | ODIN | NMX | BEER | CSPEC | BIFROST | MIRACLES | MAGIC | T-REX | HEIMDAL | Test BL
1 | 18.4 |  |  |  |  |  | 0.1 | 0.1 | 0.0 | 0.0 | 0.8 | 2.4 | 7.7 | 5.8 | 0.5 | 0.5 | 0.3 | 0.2
2 | 31.9 |  |  |  |  |  | 0.1 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.6 | 2.0 | 21.4 | 7.6 | 0.2
3 | 26.0 |  |  |  |  |  | 0.1 | 0.0 | 0.0 | 0.0 | 0.4 | 1.1 | 3.8 | 16.6 | 2.4 | 1.0 | 0.5 | 0.2
4 | 103.1 |  |  |  |  |  | 0.3 | 0.3 | 0.3 | 0.0 | 2.0 | 4.2 | 11.2 | 52.4 | 16.8 | 10.1 | 4.5 | 1.0
5 | 8.3 |  |  |  | 0.0 | 0.0 | 0.3 | 5.3 | 2.1 |  |  |  |  |  | 0.1 | 0.1 | 0.0 | 0.3
6 | 8.4 |  |  |  | 0.0 | 0.0 | 0.3 | 5.4 | 2.1 |  |  |  |  |  | 0.1 | 0.1 | 0.0 | 0.3
7 | 7.4 |  |  |  | 0.0 | 0.1 | 0.3 | 4.6 | 1.6 |  |  |  |  |  | 0.1 | 0.1 | 0.1 | 0.5
8 | 27.4 |  |  |  | 0.2 | 0.3 | 1.6 | 12.3 | 7.7 | 1.0 | 0.3 |  |  |  | 0.6 | 0.6 | 0.3 | 2.4
9 | 4.8 |  | 0.7 | 0.9 |  |  | 0.7 | 0.2 | 0.2 |  |  |  |  |  | 0.2 | 0.2 | 0.2 | 1.5
10 | 4.8 |  | 0.8 | 0.9 |  |  | 0.7 | 0.2 | 0.2 |  |  |  |  |  | 0.2 | 0.2 | 0.2 | 1.5
11 | 34.0 |  | 3.8 | 0.0 |  |  | 0.5 | 0.3 | 0.4 |  |  |  |  |  | 0.0 | 0.0 | 28.0 | 1.0
12 | 38.4 |  |  |  |  |  | 0.6 | 0.8 | 0.7 | 16.3 | 8.7 | 3.9 | 3.0 | 1.6 | 0.3 | 0.8 | 0.4 | 1.3
13 | 15.2 |  |  |  | 0.3 | 0.3 | 0.5 | 1.7 | 1.3 | 3.7 | 2.4 | 1.2 | 1.0 | 0.6 | 0.2 | 0.4 | 0.2 | 1.2
 | Reference point is within LOS of the instrument shielding |  | Reference point is outside LOS of the instrument shielding
Guide system blocks fast-neutron transmission out of the bunker | Only gammas |  | No contribution
Guide system transmits fast neutrons out of the bunker – instruments named in bold | Ref.pt. < 100m: gamma + direct fast neutrons | Ref.pt. > 100m: gammas + fast neutrons by sky-shine | Only fast neutrons by sky-shine
3×18.4 / 97.9
3×31.9 / 97.9
3×26.0 / 97.9
3×103.1 / 87.1
3×8.3 / 85.4
3×8.4 / 85.6
3×7.4 / 85.5
3×27.4 / 57.5
3×4.8 / 54.8
3×4.8 / 55.2
3×34.0 / 74.3
3×38.4 / 88.1
3×15.2 / 89.2
safety factor × calculation
compared to dose budget
dose calculations in μSv/year

## Slide 20: Worst-Case Reference Points
New Dose Rate Requirement Needed
4
8
11
12
1 | 3×18.4 / 97.9
2 | 3×31.9 / 97.9
3 | 3×26.0 / 97.9
4 | 3×103.1 / 87.1
5 | 3×8.3 / 85.4
6 | 3×8.4 / 85.6
7 | 3×7.4 / 85.5
8 | 3×27.4 / 57.5
9 | 3×4.8 / 54.8
10 | 3×4.8 / 55.2
11 | 3×34.0 / 74.3
12 | 3×38.4 / 88.1
13 | 3×15.2 / 89.2
New Requirement:
Ensure calculated dose rate is < 0.5 μSv/hour
averaged over the shielding surfaces
Average 4 cave walls separately
Average guide shielding over 10m sections
No change to 1.5 μSv/hour contact dose rate
Use worst-case H1 scenario(s)
Expectation that new requirement can be met with minimal changes
  average over non-uniform area
  average over time (all H1 scenarios)
    would require verification

## Slide 21: Effect of Converting Cave Roofs to Blue Controlled Areas
Increasing cave roof dose rate from 1.5 μSv/hour to 12.5 μSv/hour in calculation
Effect is very small
  Averaged over all reference points: increase < 0.2 μSv/hour
  Worst-case reference point (#8): increase = 1.1 μSv/hour
Still comfortably within dose budget for instruments
  negligible effect on reference point 4
Conclusion: no problem with converting cave roofs to blue controlled areas
  dose rate limit = 25 μSv/hour
  prohibit access with PSS
= essentially negligible

## Slide 22: Effect of Going to 22 Instruments
Analysis is robust to addition of more instruments
  reference point 4: E01 already full
  reference point 8: < 50% of dose budget used. S1 foreseen for short instrument. S4-S11 instruments partially shielded by DREAM
  reference point 11: < 50% of dose budget used. If necessary, access can be prohibited with fence
  reference point 12: E01 already full. D01 contribution is very small, due to shielding of target station and active cells facility
Plenty of time to study dose rates in halls during accelerator power ramp-up
Upgraded instruments will need to comply with same area-averaged dose rate limits
no problem

## Slide 23: Conclusions
New requirement: area-average dose rate of 0.5 μSv/hour
  time-averaging is also allowed, if necessary
Essential input: approved H1-H2 scenarios
  updating needed, following change of H1 definition (Andrew’s talk)
Instruments only need to demonstrate that their own shielding satisfies dose rate requirements
  at shielding surface
NSS accepts the risk relating to combined effect of all instruments
  in supervised areas
  in non-designated areas

## Slide 24: Thank You!