## Slide 1: Lessons, status and plans of installation
Viatcheslav GRISHIN
European Spallation Source ERIC
24 October 2019 , BI & WUT forum

## Slide 2: BD team and IS&LEBT 2018

## Slide 3: ESS Project – The Big Picture
2018
2019
2020
2021
2022
2023
2024
2025
ISrc to LEBT
ISrc to DTL1
ISrc to DTL4
Beam on Dump (BOD)
Accelerator Ready for Beam on Target (RBOT)
Beam on Target (BOT)
End of Construction
Start Of User Program (SOUP)
Courtesy Ciprian Plostinar
2018
2019

## Slide 4: Lessons from IS&LEBT
2018
2019

## Slide 5: 1) Cables

## Slide 6: 1) Cables
The presently installed cable is 4P18IOSLSHF. This cable is rigid, hard to bend and twist, and difficult to connect in many places due to the large bending radius. Additionally, the wires tend to slip out after some disconnections and connections. The weight and stiffness also makes the wires to slip out of the connectors. We have the same problem on rack side too, the rack crates are not that strong so these cables need extra support.
Braid wires fasten with metal strap and nut. The wires tend to slip out after a while.
Big bending radius necessary

## Slide 7
Former patch-panel to be able to connect NPM & EMU.
2) Patch panels

## Slide 8: 3) 3D integration
3D drawings
are not all absolutely correct
WUT PP!
PP
NPM PP LEBT 2018

## Slide 9
3) 3D integration 2019

## Slide 10: Solution 1 . (Mounting a new patch-box/panel “Yellow figure”)
Patch-box/panel design. For 26 connectors
A solution is to making the cables shorter by cutting and re-mounting the heavy cables to one side of a new patch box/panel. New smoother patch cables will connect the beam line elements with the patch panel.

## Slide 11: Solution 2. (Best option!)
The replacement cables are already ordered. For the rest of LINAC the heavy cables have been replaced with smaller ones, as an extra quantity of cables are already ordered by default. Routing are rather easy since the cables simply will replace already existing ones.
This solution makes it possible to skip the patch panel for all of the cables, except 4 (EMU), as the replacement cable can connect directly to the beam line elements. There will be some savings in patch panel design and termination costs.
In total 24 Cables for the NPM, DPL, EMU and FC systems are affected. The total cable length can be estimated to approximately 1km.

## Slide 12: 4) Repair in time
the Doppler actuator was stuck in inserted position in the LEBT permanent tank , removed and moved to the BI lab.

## Slide 13: MEBT

## Slide 14: MEBT BD check

## Slide 15: MEBT: BSM and Bilbao

## Slide 16: MEBT manifold and BD

## Slide 17: MEBT manifold and BD

## Slide 18: Infra structure support

## Slide 19: Installation schedule

## Slide 20: Installation schedule