## Slide 1: Aperture monitor and grid readout status
Anders J Johansson, Lund University

## Slide 2: Scrapers, Aperture Monitors and Grid
Scrapers
Grid
APTM
All three of these instruments intercepts the beam and generates a current in a connected conductor.

## Slide 3: Current measurement: FMC module
CAENels AMC-Pico-1M4
Range: max +/- 10 mA
300 kHz bandwidth
+/- 300 V floating input
1 MSPS
Conversion time: 650 ns
20 bit ADC
  Effective number of bits: 16.3 / 14.7

## Slide 4: MTCA-system
FMC Carrier Struck SIS8160
  Xilinx XCKU060 or XCKU040 FPGA
  4 GB memory
MRF timing receiver
Concurrent CPU board
MPS interface (TBD)
Handles 2 FMC cards, 8 current sensing channels in total.

## Slide 5: MTCA crate loadout
CPU
Timing
FPGA + FMC
Backplane
Minimum 3 slots
8 channels
CPU
Timing
FPGA + FMC
Backplane
Maximum 12 slots
80 channels
FPGA + FMC
FPGA + FMC
FPGA + FMC
FPGA + FMC
FPGA + FMC
FPGA + FMC
FPGA + FMC
FPGA + FMC
FPGA + FMC

## Slide 6: MTCA crate loadout, separate MPS interface
CPU
Timing
FPGA + FMC
Backplane
Minimum 4 slots
8 channels
CPU
Timing
FPGA + FMC
Backplane
Maximum 12 slots
72 channels
FPGA + FMC
FPGA + FMC
FPGA + FMC
FPGA + FMC
FPGA + FMC
FPGA + FMC
FPGA + FMC
FPGA + FMC
MPS
MPS

## Slide 7: Number of channels
 | Scraper | APTM | Grid
# Systems |  | 3 | 1
# Channels / system |  | 12 | 144 TBC
# FMC Cards / system |  | 3 | 36
# FPGA cards / system |  | 2 | 18
# Crates / system |  | 1 (5-slot) | 2 (12-slot)

## Slide 8: Bias-unit
Adding bias to detector plates.
Size of bias TBD (se Wednesday talk on J-Parc experiments )
Implementation of bias generator TBD.
Implementation of Bias-T’s TBD for different systems.

## Slide 9: Software architecture Overview
Function
Algorithm
Procedure
What: GUI, data archiving, statistics
Implementation: Python
Excecution: CPU in control room / server hall
What: Beam profile matching
Implementation: Python
Excecution : CPU in crate
What: MPS trigger by channel thresholding
Implementation: VHDL
Excecution: FPGA

## Slide 10: Firmware
Framework running
  Records data from ADCs
  Saves data to memory
Development of application firmware started
  Threshold detectors
For details: see talk by Kaj Rosengren

## Slide 11: Misc.
Scraper also needs motion control
  4 motors / scraper
  Implemented using ESS standard in Beckhoff modules.
Aperture monitors include thermal sensors
  24 sensors per APTM
  Implemented using ESS standard in Beckhoff modules.