## Slide 1: Target Station Facility Safety ASPECTs

## Slide 2: TARGET Station Facility - Global Working Plans
Efficiency
Safety
Reliability
Target Station Facility Sub-Systems
Target Station Facility Features*
Power Supply System
Target Station
Power Supply Unit
Cooling System
Stripline Connection
Target Station
Target + integration
Horn
Four Horn Support
Proton Beam extraction
Fluid System
Closed cooling Fluid
(Helium gas, Water)
Radioactive Effluents
Confinement System
Handling and Logistic
Active Cell
Casks
Remote Handling
*Inspired from
ESS Target Station Report

## Slide 3: TARGET Station Facility - Global Working Plans
Efficiency
Safety
Reliability
Target Station Facility Sub-Systems
Target Station Facility Features*
Power Supply System
Target Station
Power Supply Unit
Cooling System
Stripline Connection
Target Station
Target + integration
Horn
Four Horn Support
Proton Beam extraction
Fluid System
Closed cooling Fluid
(Helium gas, Water)
Radioactive Effluents
Confinement System
Handling and Logistic
Active Cell
Casks
Remote Handling
*Inspired from
ESS Target Station Report

## Slide 5: TARGET Station Facility - Global Working Plans
Dosimetry
Objectives
ALARA
Approach
Analyse
Dosimetry
Performances
ALARA Approach:
Anticipate and reduce individual and collective exposition to radiations.
Building “rooms”
Open Top geometry for the Target Station Room, Decay Tunnel, Beam Dump
Hot Cell (Repair Target Station elements)
Morgue (Store radioactive wastes)
Horn Power Supply Room , Power supply outside of the main building ?
=> Energy Deposition and Dose Rate Estimation with FLUKA Simulation
Beam Direction
Horn Power Supplies
Concrete Shield
Iron Shield
External Shield Blocks
Vessel Lid
Feedback from previous experiments is crucial

## Slide 6
Safety : Preparation Phase  Design Study
  Non-radiological risks
    Electrical risk, cooling system, maintenance operation….
    Earthquake
  Radiological risks
    Determine the radiological risks (external or internal contamination) for each part of the facility.
    Investigate biological protections with respect to the prompt dose and residual dose
    Environmental impact studies (Tritium, 22Na,..)

## Slide 7: Target Station Facility
Building Structure:
Proton Driver line
Experimental Hall
  MW Target Station
  Decay Tunnel
  Beam Dump
Maintenance Room
Service Gallery
  Power supply
  Cooling system
  Air-Ventilation system
Waste Area

## Slide 8: Target Station Facility
MW Target Station :
Focusing System
Crane System
Automated robot
Mechanical structure for the for horn
Dose Rate Monitoring System
Residual Dose Rate Plateform
Operation under helium Atmosphere
  flushing with air
  filter to measure radioactive pollution (dust, tritium …)
Investigation of other radionucleides transport (environmental constraint)
…

## Slide 9
Non Radiological Risks

## Slide 10: Target Station
Four horns station:
Solid Static target (Titanium)
Use multiple 4 targets+ horns
Beam frequency 56 Hz
Cooling
Power distribution due to Joule losses & secondary particles
Energy balance, to maintain working temperature
Flow rate
Jet distribution along the outer conductor
h correlation for jets’ geometry

## Slide 11: TARGET Station : Feed Back from other experiments
Recommandations from others facilities:
  Cracks in welds
  Use flexible pipes to reduce stress and fatigue
  Water leaks due to galvanic corrosion => avoid trapped water and choose material carefully
  Use semi flexible conductor because of important magnetic force between stripline => can break cable
  Heat dissipation of the stripline
  Remote design for repairing/exchange
  Need Spares
  …
Striplines plate with soft
transition

## Slide 12: HORN INVESTIGATION FAILURES
Failure | Causes | Consequences | Solution | Action/Safety
Cracks, weld junction | Material faults In the weld junction | Water leaks Current discontinuity | Check quality of weld junctions | Electrical shutdown Water flow shutdown
Cracks in the aluminium all, pipes connections | Peak stress too high | Water leaks Large displacement Crack growth Horn destruction | Stress analysis of the pipes connections; Of the details connections | Electrical shutdown Water flow shutdown
Cracks in the aluminium wall | High cyclic stress Fatigue cracks | Water leaks Large displacement Crack growth | R&D studies | Electrical shutdown Water flow shutdown
Striplines/horn connection cracks | Localised high cyclic Stress Corrosion Fatigue cracks | Electrical discontinuity Change in the magnetic field | R&D studies in the stripline horn/connection | Electrical shutdown Water flow shutdown
Striplines/connections Cracks initiation | Stress corrosion | Electric resistance increase | R&D studies | Electrical shutdown

## Slide 13: Energy Deposition : Cooling Power (5MW/4MW)
P tot = 4.2 / 3.4 MW
Beam dump :
Graphite = 950/778 kW
Iron = 195/229 kW
Surr. concrete = 4/4 kW
Decay tunnel
Iron vessel = 424/390 kW
Upstream iron = 670/610 kW
Surr. concrete = 467/485 kW
Horns/Target gallery
Iron = 613/437 kW
Horn = 50/ 32 kW
Target = 168/ 85 kW
IPAC’17 Proceedings: E. Bouquerel et al, “Energy deposition and activation studies of the ESSnuSB Horn Station”, MOPIK029

## Slide 14: Power Supply
length 20m
Width 16m
PSU room
This is a first estimation:
 Length of strip-lines limited to 34,3M
 Cost of PSU: X2,23 Euronu
 Consumption of 580KWRMS power on 380VAC
 335KW refreshed by water cooling, 136KW by air cooling
(study chargers refreshed on
water cooling)
Dimensions 20X12M, hight of 3,2m, could be decrease to 2,7m
Need a crane of 3 tons

## Slide 15
Radiological Risks

## Slide 16: Target Station Facility
Four horn station layout
Chemical composition of Material*:
Target => Ti(100%)
Horn => Anticorodal 110 alloy
Al (95.5%), Si(1,3%), Mg(1,2%), Cr(0.2%), Mn(1%), Fe (0.5%), Zn(0.2%), Cu(0.1%)
Decay Pipe => Steel P355NH
Fe(96.8%), Mn(1.65%), Si(0.5%), Cr(0.3%), Ni(0.3%), C(0.2%)
Tunnel => Concrete
O(52.9%), Si(33.7%), Ca(4.4%), Al(3,49%), Na(1,6%), Fe(1.4%), K(1,3%), H(1%), Mn(0.2%), C(0.01%)
Surrounding Environment => Molasse
O(49%), Si(20%), Ca,(9.7%), Al(6.4%), C(5%), Fe(3.9%), Mg(3.2%), K(1%), Na(0.5%), Mn(0.1%)
*TO BE UPDATE FOR ESSNUSB

## Slide 17: RADIATION SIMULATION (FROM EURONU)
Evolution of the target activity with cooling time:
(Titanium density 66%)

## Slide 18: RADIATION SIMULATION (FROM EURONU)
Evolution of the horn activity with cooling time:
Radionucleides after 1 day (Z,A)
Radioactivity after 1 day (Bq.cm-3)

## Slide 19: Radiation LAyout
Radiation layout
Simulation Parameters :
Beam Power : 4MW
Irradiation Times : 200 days
One Horn : Geometry Updated
Cooling times : 1d,1w,1m, 6m,1y, 10y
Chemical composition of Material:
Target => Titanium
Horn => Anticorodal 110 alloy
Al (95.5%), Si(1,3%), Mg(1,2%), Cr(0.2%),
Mn(1%), Fe (0.5%), Zn(0.2%), Cu(0.1%)
Decay Pipe => Steel P355NH
Fe(96.8%), Mn(1.65%), Si(0.5%), Cr(0.3%),
Ni(0.3%), C(0.2%)
Tunnel => Concrete
O(52.9%), Si(33.7%), Ca(4.4%), Al(3,49%),
Na(1,6%), Fe(1.4%), K(1,3%), H(1%),
Mn(0.2%), C(0.01%)
Scoring Region : [-200,200]x[-200,200] [-500,500], cell dimension 20cm*20cm*20cm

## Slide 20: Dose Equivalent Rate (All Layout)
After 1day
After 1 week
After 6m
After 1y

## Slide 21: Dose Equivalent Rate contribution (cooling time 1d)
Target Contribution
Horn Contribution
Vessel Contribution
Tunnel Contribution

## Slide 22: Nuclear WASTE MANAGEMENT
Classification of Radioactive Waste – Safety Series
No 111-G-1.1
IAEA Waste Classification:
HLW High Level Wastes
  Highly Radioactive liquid
  Heat Generating (>2kw/m3)
LILW Low and Intermediate Wastes
  LL Long Lived,
    ‘Half-life > 30 years
    Long lived alpha emitters >400Bq/g average
    >4000Bq/g individual package
  SL Short Lived
    Half-life <30 years
EW Exempted Wastes
Clearance Levels:
Clearance Index :

## Slide 23: Environmental impact
of all the radionuclide's created 22 Na and tritium could represent a hazard by contaminating the ground water. Limits in activity after 1y=200days of beam:
Activation in molasse
molasse @ CERN
concrete
concrete

## Slide 24
Outline
  Adapt Study with ESSnSB Parameters on going
  Feedback from other experiments crucial !!!
    Regular meetings with ESS people in charge of the safety is necessary
    Safety Meeting between Safety people has been organized at CERN during EUROnu and should be renewed