## Slide 1
MYRRHA Injector Design and Related R&D
2nd Open Collaboration Meeting on Superconducting Linacs for
High Power Proton Beams (SLHiPP-2)
LNS-INFN Catania
3.-4. May 2012
Holger J. Podlech
H. Klein, D. Mäder, R. Ratzinger, A. Schempp, R. Tiede, M. Vossberg, C. Zhang
Institute for Applied Physics (IAP)
University of Frankfurt, Germany

## Slide 2: The MYRRHA Proton-Driver
Notes: Struckturen durchgehen
Warum normalleitend / supraleitend
CH-Design
Solenoid-Design
Ein Kryomodul

## Slide 3: Scheme of the MYRRHA Injector
Notes: Aufbau eines Teststandes

## Slide 4
176 MHz: Advantages
Lower RFQ energy (1.5 MeV vs 3.0 MeV)
Use of 4-Rod RFQ (less expensive, less sensitive, lower voltage)
Thermal power RFQ: ≈25 kW/m  safe
Larger aperture in CH-cavities
Total injector length independent of f (almost)

## Slide 5: Shunt Impedance of RFQ-Structures
MYRRHA
Notes: Struckturen durchgehen
Warum normalleitend / supraleitend
CH-Design
Solenoid-Design
Ein Kryomodul

## Slide 6
4-Rod-RFQ
+Transmission line resonator
+Excellent Tuning
+Easy acces (tuning, repair)
+Proven Technology
+„Inexpensive“
+Less sensitive against tolerances
-Locally higher power densities

## Slide 7
176 MHz 4-Rod-RFQ
Voltage reduced to 40 kV (from 65 kV @ 352 MHz)
Expected shunt impedance: >67 kWm
Specific power: 25 kW/m (47 kW/m demonstrated)
Length: ≈ 4m
Total losses: 100 kW
RF power with beam (5 mA): 107 kW
RF amplifier: 150-180 kW

## Slide 8
Stem Design 176 MHz RFQ

## Slide 9
RFQ test cavity for thermal analysis
P/L up to 40 kW/m

## Slide 10
High Power cw-RFQ 50 kW/m thermal power load
(A. Schempp, IAP, A. Bechtold, NTG)

## Slide 11
CH-Cavities
CH-Structure
Crossbar-H-Mode-Structure
rt or sc multi-cell cavity
KONUS or EQUUS Beam Dynamics

## Slide 12: rt CH cavities
Dominik Mäder
Notes: Schwingkreis
Design CH1/2 abgeschlossen
Einbuchtungen für Tripletts
H211 mode

## Slide 13: MAX CH-Prototype (rt)
Notes: Aufbau eines Teststandes

## Slide 14: Parameters MAX CH-Prototype (rt)
Parameter | Unit | Value
RF Structure | --- | CH
Frequency | MHz | 175
Duty cycle | % | 100
Length (inner) | mm | 382.5
Diameter | mm | 674.6
Aperture diameter | mm | 24
Effective voltage | kV | 325
Q-value (90% MWS) | --- | 12300
Zeff (90% MWS) | MW/m | 70
Pc | kW | 5
P max | kW | 12
P/L max | kW/m | 40
Notes: Aufbau eines Teststandes

## Slide 15: RT Part: Comparison RF Power
Notes: Aufbau eines Teststandes

## Slide 16: Code Benchmarking (LORASR-WINTRACE)
LORASR
WINTRACE
Notes: Aufbau eines Teststandes

## Slide 17: MYRRHA sc CH cavities
CH3
CH4
CH5
CH6
First CH (sc) prototype
Notes: Peakfelder, Statistikprogramm
Predesign CH4-CH6
Rippen, mechanische Stabilität
CH3 → CH6, weniger Spalte, weniger Kapazität, größerer Radius (Thomsonsche Schwingungsforme))
KONUS Strahldynamik, Rebunching & Beschleunigen

## Slide 18: Field Distribution – Gap voltage
1. sc CH-cavity
Notes: Vorgabe und erreichte Verteilung
Elektrische Spitzenfelder
residual resistance ratio (RRR)
  impurities
    crystal impurities
    surface impurities (condensed gases)
    buffered elecropolishing
    buffered chemical polishing
multipacting
  secondary electron emission
thermal breakdown

## Slide 19
Bellow Tuner
Static Tuners
Helium Vessel
Coupler Flanges
325 MHz CH-Prototype
Praparation Flanges
b | 0.1545
Frequency (MHz) | 325.224
Cells | 7
Length bl-def (mm) | 505
Diameter (mm) | 348
Ea (MV/m) | 5
Ep/Ea | 5.1
Bp/Ea [mT/(MV/m)] | 13
G (W) | 64
Ra/Q0 (W) | 1248
RaRs (W2) | 80000

## Slide 20
Strategy to Hit the Frequency
Bad circumstances:
Countermeasures:
fabrication inaccuracy (Δf = ? MHz)
thermal shrinkage (Δf ≈ +450 kHz)
pressure sensitivity (Δf ≈ +200 kHz)
surface preparation (Δf = ? kHz)
underground noise (Δf = ± 50 Hz)
helium bubbles
tank / end cell offset 10 mm (Δf ≈ ±1 MHz)
static tuners (Δf ≈ +1.3 MHz, -2.2 MHz)
slow bellow tuners (Δf ≈ ±250 kHz)
fast bellow tuner (Δf ≈ ± 700 Hz)

## Slide 21
Cavity Fabrication

## Slide 22
Cavity Fabrication

## Slide 23
325 MHz CH-Prototype

## Slide 24
325 MHz CH-Prototype

## Slide 25
325 MHz CH-Prototype: First Measurements

## Slide 26
325 MHz CH-Prototype: First Measurements
Design Position
Deviation from Design frequency:
500 kHz < 0.2%

## Slide 27
f=217 MHz
A/q<6.5
9 sc CH-cavities
Ea=5 MV/m
Utot=35 MV
Sc Solenoids (8T)
Future GSI/FAIR Injector Complex
cw Linac I

## Slide 28
Parameter | Unit | CH-1
Beta |  | 0.059
Frequency | MHz | 216.816
Gap number |  | 15
Total length | mm | 687
Cavity diameter | mm | 409
Cell length | mm | 40.82
Aperture | mm | 20
Ua | MV | 3.369
Energy gain | MeV | 2.97
Accelerating gradient | MV/ m | 5.1
Ep/ Ea |  | 6.4
Bp/ Ea | mT/ (MV/m) | 5.4
R/ Q | Ω | 3320
Static tuner |  | 9
Dynamic bellow tuner |  | 3
Main parameters of the 217 MHz CH-structure
cw SHE-Linac Demonstrator
3D-view of the 217 Mhz cavity with helium vessel, without tuners
Helium vessel
Coupler flange
Pickup flange
Inclined
end stem
Tuner flange
Preparation
flange
Cavity construction has started April 2012

## Slide 29
cw Linac Demonstrator
CH-cavity
Cryo module
sc solenoids
First sc CH-cavity will be tested with beam at GSI
b=0.059, f=217 MHz, 15 cells
RF power 5 kW (10 kW)
Cryo module and sc solenoids ordered

## Slide 30
Clean room 100/10000
Vertical cryostats (400mm, 600mm, 900mm diameter)
Horizontal cryostats
Amplifiers
Refrigerator
And everything you need for cavity testing
Infrastructure at IAP Frankfurt
Linde L140 liquifier, 90 l lHe/hr @ 4K

## Slide 31: Amplifiers
175 MHz, 300 kW, cw
175 MHz, 12 kW, cw
108 MHz, 100 kW, 10%
87.5 MHz, 18 kW, cw
217 MHz, 5 kW, cw
330-370 MHz, 2 kW, cw
325 MHz, 40 kW, 1%
100-400 MHz, 500 W, cw
Notes: Aufbau eines Teststandes

## Slide 32: Next Steps
Tests of rt CH-cavity (RF+Beam)
Tests of sc CH-cavities (RF+Beam)
Coupler Test Stand
Test of RFQ-Protoype (RF)
Design of Cryomodule
Construction and Test of 4-Rod RFQ (RF+Beam)
Notes: Aufbau eines Teststandes

## Slide 33: Summary
Frequency of MYRRHA Injector changed from 352 to 176 MHz
4-Rod RFQ 1.5 MeV
2 rt CH-cavities as booster (1.5-3.5 MeV)
4 sc CH-cavities for main acceleration (3.5-17 MeV)
For required reliability two injectors are foreseen
Prototypes will be tested with beam
Notes: Aufbau eines Teststandes