## Slide 1
Spoke cavities for ESS and MYRRHA
G. Olry, P. Duchesne (IPN Orsay)
SLHiPP-2, 3-4 May 2012, Catania

## Slide 2
Outline
(A few) specifications for ESS and MYRRHA spoke cavities
RF design
Mechanical calculations

## Slide 3
Specifications for cavities
 | ESS | MYRRHA
 | Double-spoke | Single-Spoke
Beam mode | Pulsed | CW
Frequency [MHz] | 352 | 352
Beta optimal | 0.50 | 0.37
Bpk [mT] | 70 | 50 to 70
Epk [MV/m] | 35 | 25 to 35
Temperature (K) | 2 | 2
Nominal gradient Ea [MV/m] | 8 | 5 to 6
Beam tube diameter [mm] | 50 (min) | 50 (min) to 60 (ideal)
P max [kW] | 300 (450 upgrade) | <10
Lacc (=beta optimal x nb of gaps x c / f) [m] | 0.639 | 0.158

## Slide 4
Outline
(A few) specifications for ESS and MYRRHA spoke cavities
RF design
Mechanical calculations for ESS (P.Duchesne)

## Slide 5
Double-Spoke for ESS
Main goal:
Epk/Eacc < 4.5
Bpk/Eacc (mT/MV/m) < 8.8
CST MicroWave Studio 2011
Model created with the 3D CAD tools of MWS
Symetries: ¼, BC: Magnetic planes, Nb meshcells~100 000points
1st mode calculated (TM010)

## Slide 6
Double-Spoke for ESS
Some parameters that could be optimized…
Hspokebase
Lcav
Liris-to-iris
Htop
Hbottom
WSpokecenter
Rspokebase
rtop1
rtop2
Hspokecenter
Dspoke
rtop3

## Slide 7
Double-Spoke for ESS
2 examples: with parameter Lcav (=overall length of the cavity from end-caps) and Rspokebase (=radius of the spoke base)
1/ Rspokebase varies : variation of d from 0 to 40 mm (Lcav unchanged)
2/ Lcav varies : Rspokebase is fixed and Lcav1 varies from 0 to 200 mm
Lcav=3*beta*lambda/2+Lcav1
Rspokebase= (Lcav/8)+d)

## Slide 8
Double-Spoke for ESS
1/ Rspokebase varies : variation of d from 0 to 40 mm while Lcav unchanged

## Slide 9
Double-Spoke for ESS
2/ Lcav varies : Rspokebase is fixed and Lcav1 varies from 0 to 200 mm
Lcav1 [mm] | Epk [V/m] | Variation (w.r.t Epk@Lcav1=0)
0 | 1.17E+07 | 0%
20 | 1.21E+07 | 3%
40 | 1.23E+07 | 5%
60 | 1.25E+07 | 7%
80 | 1.25E+07 | 7%
100 | 1.23E+07 | 5%
120 | 1.20E+07 | 3%
140 | 1.17E+07 | 0%
160 | 1.12E+07 | -4%
180 | 1.08E+07 | -7%
200 | 1.05E+07 | -10%
Lcav1 [mm] | Hpk [A/m] | Variation (w.r.t Hpk@Lcav1=0)
0 | 1.11E+04 | 0%
20 | 1.05E+04 | -5%
40 | 1.00E+04 | -10%
60 | 9330.50391 | -16%
80 | 9284.22754 | -16%
100 | 8883.86035 | -20%
120 | 8851.58008 | -20%
140 | 8832.0459 | -20%
160 | 8892.72461 | -20%
180 | 8741.48242 | -21%
200 | 8738.99023 | -21%

## Slide 10
Power coupler port sizing
 |  | SNS | ESS |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  | Max diam with DN100 flange |  |  |  |  |  |  |  | Max diam with DN160 flange | 
order (n) | Coupler port diam (mm) | 96 | 56 | 90 | 100 | 100 | 110 |  | 110 | 120 | 120 |  | 150 | 150
 | Impedance (Ohms) | 50 | 50 | 50 | 50 | 75 | 50 |  | 75 | 50 | 75 |  | 50 | 75
 | Antenna diam (mm) | 42 | 24 | 39 | 43 | 29 | 48 |  | 31 | 52 | 34 |  | 65 | 43
 |  | P[kW] = (f[MHz].Diam_port[mm])^4.Z[Ohm].h(1/(n+1)) |  |  |  |  |  |  |  |  |  |  |  | 
1 |  | 8811 | 37 | 249 | 379 | 569 | 555 | 833 |  | 786 |  | 1180 | 1920 | 2880
2 |  | 6088 | 26 | 172 | 262 | 393 | 384 | 576 |  | 543 |  | 815 | 1327 | 1990
3 |  | 3499 | 15 | 99 | 151 | 226 | 221 | 331 |  | 312 |  | 468 | 762 | 1144
4 |  | 2069 | 9 | 58 | 89 | 134 | 130 | 196 |  | 185 |  | 277 | 451 | 676
5 |  | 1285 | 5 | 36 | 55 | 83 | 81 | 122 |  | 115 |  | 172 | 280 | 420
6 |  | 847 | 4 | 24 | 36 | 55 | 53 | 80 |  | 76 |  | 113 | 185 | 277
7 |  | 599 | 3 | 17 | 26 | 39 | 38 | 57 |  | 53 |  | 80 | 131 | 196
8 |  | 460 | 2 | 13 | 20 | 30 | 29 | 44 |  | 41 |  | 62 | 100 | 150
9 |  | 386 | 1.5 | 11 | 17 | 25 | 24 | 37 |  | 34 |  | 52 | 84 | 126
10 |  | 352 | 1 | 10 | 15 | 23 | 22 | 33 |  | 31 |  | 47 | 77 | 115
Empirical multipacting calculations

## Slide 11
RF results
Simulation with 1.3 millions of meshpoints
E field
H field
 | ESS | MYRRHA
Beta optimal | 0.50 | 0.37
Epk/Ea | 4.96 | 4.92
Bpk/Ea [mT/MV/m] | 7.03 | 8.3
G [Ohm] | 133 | 115
r/Q [Ohm] | 428 | 244
E field
H field

## Slide 12
Outline
(A few) specifications for ESS and MYRRHA spoke cavities
RF design
Mechanical calculations for ESS (P.Duchesne)

## Slide 13
Donut ribs (left and right side)
Niobium : 4 mm
Stiffener: donut (welded connection between cavity and tank)
4 HPR ports
Pick-up port
Beam tubes: 4,5mm
Design of the cavity with helium vessel
Design of the cavity
Helium vessel
Titanium : 3 mm
4 HPR Flanges
Coupler port
Bellows

## Slide 14
Config. 1 : Cavity without helium vessel
(leak test)
Mechanical behavior under pressure
Config. 2 : Cavity with helium vessel
(Cool down)
Hypothesis :
Loads:
Cavity walls : Pext = 1 bar
Vessel walls : Pint = 1 bar
Boundary conditions:
Only one end beam tube fixed
 = 30 MPa
 = 30 MPa
 = 26 MPa
 = 28 MPa
max = 58 MPa
on HPR ports
Niobium:
E = 107 GPa
n = 0,38
Re (20°C) = 50 MPa
Titanium grade 2:
E = 105 GPa
= 0,3
Re (20°C) = 350 MPa
Hypothesis :
Loads:
Cavity walls : Pext = 1 bar
Boundary conditions:
Only one end beam tube fixed
 = 30 MPa

## Slide 15
 | ANSYS
Frequency [MHz] | 352
Beta | 0.5
Bpk/Eacc [mT/(MV/m)] | 7,08
Epk/Eacc | 4.4
G [Ohm] | 130
r/Q [Ohms] | 407
Lacc = Ngap.b.l/2 [m] | 0.6386
Temperature (K) | 2
Q0 Cu@ 300K | 27042
Q0 Nb@ 2K | 1.22*1010
RF parameters with ANSYS

## Slide 16
Mechanical characteristics | 
Cavity with donut on each end-cap | 
Stiffness of the cavity Kcav [kN/mm] | 11.8
Tuning sensitivity Df/Dz [kHz/mm] | 200
Sensitivity due to the pressure KP [Hz/mbar] (free ends) | -141.
Sensitivity due to the pressure KP [Hz/mbar] (fixed ends) | 4.2
Mechanical-RF coupling analysis
Numerical analysis performed with ANSYS
Remark: Connections with helium vessel not taken into account

## Slide 17
RF frequency change due to Lorentz detuning
Numerical analysis performed with ANSYS
Lorentz Factor: KL = Df / E²acc | 
cavity with donut ribs | 
KL [Hz/(MV/m)2] (free ends) | -11
KL [Hz/(MV/m)2] (fixed ends) | -3.7
Pressure on cavity walls (Pa)
Pmax = 628 Pa (Push out)
Pmin = -2450 Pa (Pull in)
For Eacc = 8 MV/m
Emax = 35 MV/m
Bmax = 57 mT
Lorentz pressure: P = ¼ (µ0 H² - e0 E²)
Remark: Connections with helium vessel not taken into account

## Slide 18
Outline
(A few) specifications for ESS and MYRRHA spoke cavities
RF design
Preliminary mechanical calculations for MYRRHA (P.Duchesne)

## Slide 19
External pressure of 1 bar
Cavity without helium vessel
Boundary conditions: one free end
No external ribs, nor stiffeners…
Stresses with Nb = 3mm
Stresses with Nb = 4mm
In red: σ > 50 MPa

## Slide 20
External pressure of 1 bar (con’t)
Cavity without helium vessel
Boundary conditions: one free end
External stiffener on each end-caps
Niobium and stiffeners thickness: 3mm
Displacements
Stresses
In red: stresses > 50 MPa
59 MPa on stiffener

## Slide 21
THANK YOU FOR YOUR ATTENTION