## Slide 1
Notes: Slide 1: Company Logo Full Page
Before you start editing the slides of your talk change to the Master Slide view:
Microsoft Office :Menu: View > Slide Master;
Macintosh – View > Master > Slide Master
Edit the following items:
On the Slide Master (first master slide) – lower area
a) On the left Delete the text and write the title of the event/Conference, Location
b) On the right delete the text and write the name and surname of the speaker and the date (day, month , year)
Close Master View

## Slide 2: 26 RFPS IK Contribution Safety & Regulations
Notes: Slide 2: Title of the Presentation
Before you start editing the slides of your talk change to the Master Slide view:
Microsoft Office :Menu: View > Slide Master;
Macintosh – View > Master > Slide Master
Edit the following items:
On the Slide Master (first master slide) – lower area
a) On the left Delete the text and write the title of the event/Conference, Location
b) On the right delete the text and write the name and surname of the speaker and the date (day, month , year)
Close Master View
To start adding slides insert a new slide and select a Layout:
For Title & Subtitle
For text with bullet points
For Text
For Picture, graphs, visuals
Two columns
Blank

## Slide 3: Let me introduce the Safety issue...
“It will never happen to me”
E.J. Smith, Titanic’s Commander
“Safety is defined and measured more by its absence than by its presence”
James Reason, Psychologist, UK
The way we think about our lives and our exposition to adverse events tends to ignore, or at least to underestimate, the fact that ‘risk is the likelihood that a person may be harmed or suffers adverse health effects if exposed to a hazard’.
So, no matter where, when, or what we do, we can’t set this “likelihood” to zero value.
That leads to the development of a Safety approach, within a Safety culture.

## Slide 4: Safety as a culture
“A safe culture is an informed culture, one that knows continually where the ‘edge’ is without necessarily having to fall over it. The ‘edge’ lies between relative safety and unacceptable danger.
In many industries, proximity to the ‘edge’ is the zone of greatest peril and also of greatest profit.
Navigating this area requires considerable skill on the part of system managers and operators. Since such individuals come and go, however, only a safe culture can provide any degree of lasting protection”
James Reason, Psychologist, UK
Safety culture shall…
be informed
be updated
involve skilled managers and operators
last over and beyond individuals

## Slide 5: Key elements for RFPS design
The RFPS is to be considered as a system working in connection with other systems, and interfacing human operators in different conditions.
So it shall be safety-integrated in order to:
eliminate the identified hazard,
  informed design steps, according to and compliant with the Regulatory Framework
reduce risk of those unavoidable,
  RFPS control system, fail-safe, pro-active, visualizing status to involved personnel
signalize the residual risks associated with the machinery
RFPS safety user guide and related elements
Notes: Slide 3 – (..) : Content of the presentation
Insert a new slide: Home > “New Slide” and choose a slide Layout:
For Title & Subtitle
For text with bullet points
For Text
For Picture, graphs, visuals
Two columns
Blank
If you want Copy & paste an element from the Clip Board to the particular slide: 1. Click on a box to mark it.
2. Position the mouse pointer on the box frame: Copy! 3. Click on the particular slide: Paste!
How you intend to use the elements is your choice. You can combine the text block style with the background colour in different manner.

## Slide 6: RFPS as specified
A whole chapter has been dedicated to specify the required frameworks, both legislative and technical, regarding design, manufacturing, operation, maintenance, quality, documentation and safety that apply to the Radio Frequency Power Station (RFPS) to be used for Spoke accelerating cavities in ESS ERIC premises.

## Slide 7: Regulatory Framework - I
The RFPS is a system, composed by different elements which relate to different regulatory areas. A list of European Union Directives cover these areas.
Besides, each area is covered also by multiple standards from different International and European Organizations or Committees.
In ESS, National Swedish standards and internal documents and rules apply also.
Area | EU directives | Topics
Machinery Safety | 2006/42/EC | Machinery safety
 | 89/391/EEC | Measures to improve safety and health at work
Electrical Safety Wiring | 2014/35/EU | Electrical safety: low-voltage electrical equipment
 | 2006/95/EU | Electrical equipment designed for use within certain voltage limits
Electromagnetic Compatibility | 2004/108/EC | Electromagnetic compatibility of electrical and electronic apparatus
Non-Ionizing Radiations | 2013/35/EU | Limiting the exposure of workers to risks from electromagnetic fields
Ionizing Radiations | 2013/59/Euratom | Basic safety standards for exposure to ionising radiation (from 2018)
RoHS | 2011/65/EC | Restrictions on the use of certain hazardous substances in electrical and electronic equipment
Noise Emissions (audio) | 2003/10/EC | Health and safety at work: exposure to noise
Documentation |  | Structure and preparation of technical information and documentation
Notes: Slide 3 – (..) : Content of the presentation
Insert a new slide: Home > “New Slide” and choose a slide Layout:
For Title & Subtitle
For text with bullet points
For Text
For Picture, graphs, visuals
Two columns
Blank
If you want Copy & paste an element from the Clip Board to the particular slide: 1. Click on a box to mark it.
2. Position the mouse pointer on the box frame: Copy! 3. Click on the particular slide: Paste!
How you intend to use the elements is your choice. You can combine the text block style with the background colour in different manner.

## Slide 8: Regulatory Framework - II
Machinery Safety
 | Standard ID | Description
Swedish | AFS 2008:3 | Swedish version based on the EU regulation 2006/42/EG safety of machinery
European | EN 62061:2005 | Safety of machinery – Safety related parts of control systems
 | EN 61511 | Series, Functional safety, safety instrumented systems for the process industry sector
International | IEC 61508:2010 | Series, Functional safety of electrical/electronic/programmable electronic safety related systems
 | ISO 13489-1:2006 | Safety of machinery – Safety related parts of control systems
 | ISO 12100:2010 | Safety of machinery – General principles for design – Risk assesment and risk reduction
 | ISO 5349-2:2001 | Safety of machinery – Mechanical vibration
Directive 2006/42/EC states about machinery and «moving parts» in article 2 subtitle (a).
RFPS will not have such components, however the Annex I, chapter 1 in 2006/42/EC holds for «safe design and construction» and «proper installation and maintenance».
EN 62061:2005 expresses the concept of System Approach and SIL as Safety Integrity Level. It links 61508:2010 for high degree of complexity in systems, 13489-1:2006 for low complexity ones.
Notes: Slide 3 – (..) : Content of the presentation
Insert a new slide: Home > “New Slide” and choose a slide Layout:
For Title & Subtitle
For text with bullet points
For Text
For Picture, graphs, visuals
Two columns
Blank
If you want Copy & paste an element from the Clip Board to the particular slide: 1. Click on a box to mark it.
2. Position the mouse pointer on the box frame: Copy! 3. Click on the particular slide: Paste!
How you intend to use the elements is your choice. You can combine the text block style with the background colour in different manner.

## Slide 9: Regulatory Framework - III
Electrical Safety and Wiring
 | Standard ID | Description
Swedish | ELSÄK-FS 2000:1 | Swedish version based on the EU regulation 2006/95/EG Low voltage directive
 | ELSÄK-FS 2008:1 | The Swedish Electrical Safety Authority regulations and general guidelines how electrical installations must to be performed
 | SS 436 40 00 | General regulations for low voltage electrical installations
 | SS 424 14 38 | Cable management in buildings
 | ESS-0015433 | Handbook for Electrical Design (draft status)
European | EN 60204 | Safety of machinery - Electrical equipments of machines
 | EN 61439-1 | Low-voltage switchgear and control gear assemblies - Part 1: General rules
 | EN 62368-1:2014 | Safety of electronic equipments
 | EN 60079-14:2014 | Explosive atmospheres. Electrical installations design, selection and erection
 | HD 308 S2:2001 | Identification of cores in cables and flexible cords
International | IEC 60215:1987/AMD2:1993 | Safety requirements for radio transmitting equipment
 | IEC 60445:2010 | Interface marking and identification
Notes: Slide 3 – (..) : Content of the presentation
Insert a new slide: Home > “New Slide” and choose a slide Layout:
For Title & Subtitle
For text with bullet points
For Text
For Picture, graphs, visuals
Two columns
Blank
If you want Copy & paste an element from the Clip Board to the particular slide: 1. Click on a box to mark it.
2. Position the mouse pointer on the box frame: Copy! 3. Click on the particular slide: Paste!
How you intend to use the elements is your choice. You can combine the text block style with the background colour in different manner.

## Slide 10: Regulatory Framework - III
Electromagnetic Compatibility
 | Standard ID | Description
Swedish | ELSÄK-FS 2007:1 | Swedish version based on the EU regulation EMC- Directive 2004/108/EG
 | SSG 5150E | Earthing and screening of electronic equipment
 | SS-EN 50310 | Application of equipotential bonding and earthing in buildings with information technology equipment
 | SS-EN 62305 | Protection against lightning
European | EN 55011:2013 – CISPR 11 | Radio disturbance in ISM equipments
 | EN 55022:2010-12 | Radio disturbance in IT equipments
 | EN 55024:2010-11 | Immunity in IT equipments
International | IEC 61000-3-12:2011 | EMC – Part 3-12 – Limits for harmonic currents produced by input current > 16A and < 75A
 | IEC 61000-4 | EMC – Testing and measurement techniques Levels 1 – 2 – 3 – 4 – 5 – 6 – 34
Notes: Slide 3 – (..) : Content of the presentation
Insert a new slide: Home > “New Slide” and choose a slide Layout:
For Title & Subtitle
For text with bullet points
For Text
For Picture, graphs, visuals
Two columns
Blank
If you want Copy & paste an element from the Clip Board to the particular slide: 1. Click on a box to mark it.
2. Position the mouse pointer on the box frame: Copy! 3. Click on the particular slide: Paste!
How you intend to use the elements is your choice. You can combine the text block style with the background colour in different manner.

## Slide 11: Regulatory Framework - IV
Non-Ionizing Radiations
 | Standard ID | Description
Swedish |  | Best practice adopted by Swedish Radiation Safety Authority Microwave RF power leakage shall not exceed 3.5 W/m2
European | EN 61566:1997 | Measurement of exposure to RF electromagnetic fields in range 100 kHz – 1 GHz
Ionizing Radiations
 | Standard ID | Description
 |  | Maximum acceptable dose rate 1.0 μSv/h at point of contact (after background subtraction), nearby any equipment
The RFPS system will be hosted in a non-restricted access area.
Notes: Slide 3 – (..) : Content of the presentation
Insert a new slide: Home > “New Slide” and choose a slide Layout:
For Title & Subtitle
For text with bullet points
For Text
For Picture, graphs, visuals
Two columns
Blank
If you want Copy & paste an element from the Clip Board to the particular slide: 1. Click on a box to mark it.
2. Position the mouse pointer on the box frame: Copy! 3. Click on the particular slide: Paste!
How you intend to use the elements is your choice. You can combine the text block style with the background colour in different manner.

## Slide 12: Regulatory Framework - V
RoHS – Restrictions on the use of certain Hazardous Substances
 | Standard ID | Description
European | EN 50581:2012 | Assesment of electrical and electronic products with respect to RoHS
Documentation
 | Standard ID | Description
Swedish | SS-EN 61355 | Structuring of technical information and documentation
 | SS-EN 61082 | Preparation of document used in electrotechnology
Noise Emissions (audio)
 | Standard ID | Description
European | EN ISO 9612:2009 | Determination of occupational noise exposure
 | EN ISO 11688-1:2009 | Recommended practice for the design of low-noise machinery and equipment
Notes: Slide 3 – (..) : Content of the presentation
Insert a new slide: Home > “New Slide” and choose a slide Layout:
For Title & Subtitle
For text with bullet points
For Text
For Picture, graphs, visuals
Two columns
Blank
If you want Copy & paste an element from the Clip Board to the particular slide: 1. Click on a box to mark it.
2. Position the mouse pointer on the box frame: Copy! 3. Click on the particular slide: Paste!
How you intend to use the elements is your choice. You can combine the text block style with the background colour in different manner.

## Slide 13: RFPS control system
The RFPS is, from the point of view of safety systems, a SIL-3 system
ONLY for the High Voltage CABINET
SIL-3 means in this context
Hardwired safety system
Redundant circuit
No dependencies by any microprocessor, PLC or programmable logic device
The RFPS control system shall perform interlock protection over the equipment, and shall guarantee personnel protection via fail-safe design.
The RFPS shall also be equipped with:
Emergency Stop, cat.0 device, on main electrical supply
Manually-operated mains isolating device
Manual discharger of electrostatic accumulation on high voltage capacitors
Interlocked cabinet doors, against electric shock
Earthed metallic cabinet and doors
Notes: Slide 3 – (..) : Content of the presentation
Insert a new slide: Home > “New Slide” and choose a slide Layout:
For Title & Subtitle
For text with bullet points
For Text
For Picture, graphs, visuals
Two columns
Blank
If you want Copy & paste an element from the Clip Board to the particular slide: 1. Click on a box to mark it.
2. Position the mouse pointer on the box frame: Copy! 3. Click on the particular slide: Paste!
How you intend to use the elements is your choice. You can combine the text block style with the background colour in different manner.

## Slide 14: RFPS safety documents
The RFPS’s safety user guide and operating manual shall define:
Operational limits of the machine, the proper functionalities and the prohibited operations.
The safe requirements in term of space for installation, operating and maintenance of the machine.
The safe environmental factors.
The expected useful life of the machine or of its components and their replacement timescale.
RFPS shall present a clear and visible rating plate, in English, for the electrical parameters on the whole station, and dedicated ones for any associated circuit.
RFPS shall have all terminals, connectors and cables marked as for the related documents. Labels shall be clearly displaced as warnings about any residual risk.
Pushbuttons and led colour coding shall be chosen to uniquely identify the conditions:
RED Emergency, fault
ORANGE Warning
YELLOW Abnormal condition
GREEN Normal, safe operation
Notes: Slide 3 – (..) : Content of the presentation
Insert a new slide: Home > “New Slide” and choose a slide Layout:
For Title & Subtitle
For text with bullet points
For Text
For Picture, graphs, visuals
Two columns
Blank
If you want Copy & paste an element from the Clip Board to the particular slide: 1. Click on a box to mark it.
2. Position the mouse pointer on the box frame: Copy! 3. Click on the particular slide: Paste!
How you intend to use the elements is your choice. You can combine the text block style with the background colour in different manner.

## Slide 15: RFPS safety elements
RFPS design shall take care of IP2x Ingress Protection, according EN 60529, on enclosures and covers for electrical parts, to avoid accidental human contact.
Under worst-case conditions, thermal behavior for each component shall be:
Power resistors < 120°C in air / < 100°C in oil
Semiconductor junction temperature < 110°C
General-purpose capacitors -25°C to +85°C
Any other component - 75% of its rated value
Materials for polymer and cable insulators shall be halogen free, flame retarding and shall not release any toxic or corrosive substance when exposed to fire.
All metal parts shall be non-corrosive, or be treated against corrosion. If painted, they shall be treated with a primer beneath the visible colour.
Wiring and cross-section for cables shall respect the related standards.
Selection of types and modes of implementation within the RFPS shall respect an optimal deployment and an easy-to-identify approach.
Cable trays shall simplify the disposition of elements in the RFPS. They shall not created obstacles or point of risk for operators, internal or external respect to the RFPS.
Notes: Slide 3 – (..) : Content of the presentation
Insert a new slide: Home > “New Slide” and choose a slide Layout:
For Title & Subtitle
For text with bullet points
For Text
For Picture, graphs, visuals
Two columns
Blank
If you want Copy & paste an element from the Clip Board to the particular slide: 1. Click on a box to mark it.
2. Position the mouse pointer on the box frame: Copy! 3. Click on the particular slide: Paste!
How you intend to use the elements is your choice. You can combine the text block style with the background colour in different manner.

## Slide 16: RFPS as verified
For each directive/rules the Contractor shall provide the relevant declaration ( for example according to the 2014/35/EU Low Voltage Directive the Declaration of Conformity is required )
or
compile and issue the EMC Pre-compliance declaration which states that RFPS and all of its subsystems comply with all the relevant rules and Standards cited above, and it is available, on Elettra’s request, in agreement with INFN, to conduct measurements according the cited CISPR 16 rule, for the relevant parts.
In any case, it is not mandatory to provide neither whatsoever Certificate for EMC Conformity, nor seek any accredited Laboratory for certification purposes.

## Slide 17: RFPS as verified
Bare RFPS with the electrical wires in place but no electrical load

## Slide 18: RFPS as being verified
All the sacrificial devices of the mains distribution unit have been removed and the 24 VDC power supply to be used for the control and interlock logic has been disconnected. The wire ends connected to insulating clips, see figure 6. EMI filters have been also by-passed.
The used instrument is the AVO RM125 L/2 AC/DC breakdown tester equipped with acoustic warning. Output Vrms and frequency were previously checked with a digital multimeter
2014/35/EU Low Voltage Directive and wire insulation test.

## Slide 19: RFPS as being verified
Specification: design and material’s selection and implementation of the RFPS and subsystems shall fulfil the technical specifications tasks in accordance with the best engineering practices and the state of the art for each technical sector.
Visits to the Contractor – together with ESS, the final USER, for visual inspection and check of the chosen components and installation procedure
Air filtering cascade - two stages
for the Thales tube rack
Cooling water pipes and circuit pressure check
EMC shielding detail of the rack doors
THD filter for the electrical grid quality

## Slide 20: RFPS status

## Slide 21: RFPS status
HV Modulator rack

## Slide 22: RFPS status
RF distribution for the tetrode ready
RF drivers connections ( cooling water- RF and PS) ready
RF high power combiner ready on the RFPS roof

## Slide 23
Notes: Last Slide 1: Thanks to the audience

## Slide 24
Notes: Last Slide 2: Aerial Photo of Elettra