## Slide 1: Spallation target for CiADS
Institute of Modern Physics (IMP), CAS
Xueying Zhang

## Slide 2: OUTLINE
Research Aims
Granular target
LBE target with window
Collaboration

## Slide 3: The preliminary Design of CiADS
The overall design of CiADS facility has been worked out
LINAC: 500 MeV@5 mA with CW mode
Spallation Target: spallation target, 2.5 MW
Sub-critical core: 10 MWt, LBE cooled
China initiative Accelerator Driven System

## Slide 4: Target: Research strategy
Designing platform construction  Conceptual design
Comparing with the existing data and bench test experiments  Code V & V
Optimizing the codes  Optimizing the design
Constructing a prototype
Preliminary design
……
Starting with LBE target design, coming to a new type of granular target
LBE target with window as the backup of the granular target

## Slide 5: OUTLINE
Research Aims
Granular target
LBE target with window
Collaboration

## Slide 6: Granular Target Concept
In principle, it can stands for tens of MW beam power
Increasing flexibility to use other target materials to increase the neutron yields

## Slide 7: Granular Target Design
physics design
Sidewall leakage neutron spectrum
Neutron flux distribution
energy deposition
Temperature distribution (2.5MW=250MeV@10mA)
velocity distribution
Packing factor
Secondary radioactive decay
Radiation damage of pipe

## Slide 8: Granular Target Design
Main Parameters | 
Granular material | Tungsten/Tungsten alloy
Structure material | Tungsten alloy/SiC
Granular size | ~1mm
Inlet temperature | ~250 C
MAX Outlet temperature | ~650 C
Proton beam | 500eV@5mA=2.5MW
Intensity of beam | >100 μA/cm^2
Diameter of beam spot | ~10cm
Average velocity of granular flow | ~0.5m/s

## Slide 9
EM
lift
Beam-Target interface
Heat exchanger
Granular flow loop
Storage vessel
Target
Emergency container
Guanular flow monitor
Neutron monitor
beam diagnostics
Spallation target
Beam-Target interface
Electromagnetic lift
Heat Exchanger
Remote handling system
Target safety system
Granular flow loop
Granular Target Design
Grain filter

## Slide 10: Test Bench – Granular Flow
Coupled with electron beam
(2MeV@10mA, cover gas: He@1atm)
Heat exchanger test
The difference between inlet and outlet
Temperatures field of outlet

## Slide 11: Test Bench – Granular Flow
Integrated principle prototype
The temperature of grain
The temperature of cooling water

## Slide 12: OUTLINE
Research Aims
Granular target
LBE target with window
Collaboration

## Slide 13: LBE Target with Windows
Heat exchanger
EM pump
shielding
LBE vessel
Support structure;
Beam pipe and window
Nozzle
Main Parameters | 
Diameter of Beam | 10cm
Beam Energy | 500MeV
Beam Current | 0.5mA
LBE average flow | ~30 kg/s
LBE max velocity | 0.63 m/s
Window Thickness | 2mm （T91）
Temp. Difference of Heat Exchanger | 50K
Max velocity of cold fluid | 1.52m/s
Wall Thickness of Heat Exchanger | 1.75mm

## Slide 14: LBE Target with Windows Design
IMPORTANT REMARKS:
Temperature, hydrodynamics and structure coupled analysis employed
Highest beam power limited by window

## Slide 15: Test Bench - LBE
Water flow experimental loop of window target
Spallation target experimental loop for the ADS
A water loop for window/windowless LBE target has been established, and is used to investigate flow behavior. 8.4 – 20 m3/h flow range
A liquid metal test stand, LiMeTS has been shifted to IMP from PSI
A LBE test loop, STELA is built to study the thermal-hydraulics, circulation methods, measurement techniques, etc.
Constructing a prototype
STELA
LiMeTS from PSI

## Slide 16: OUTLINE
Research Aims
Granular target
LBE target with window
Collaboration

## Slide 17: Collaboration
1 Remote Handling Systems design and engineering
Active Cells Facility
Process Cell and Maintenance Cell
Shipment casks
Changing target technology
Technical Galleries
2 Accelerator-Target Interface design and technique
Beam window
Beam scan unit
Target protecting and beam diagnostics in front target
3 Helium system
filter unit
radiation purification unit
……
Notes: Alumium 6061
95 ligt limits
25 usv/h
3 3 minits
7 types casks
Double gate .

## Slide 18
Thank You!
&
Welcome to Collaboration !