## Slide 1: Modeling of the Cryogenic Distribution System
Riccard Andersson
(Part of) Master’s Thesis
AD and ICS Retreat
December 11, 2013

## Slide 2: Some Quick Things About Me
Engineering Physics
  Accelerator Physics
One-year project
  Master’s thesis
  Two project courses
http://www.freeworldmaps.net/ europe/sweden/sweden-map.jpg

## Slide 3: Some Quick Things About Me
http://upload.wikimedia.org/wikipedia/en/7/72/World_Map_WSF.svg.png

## Slide 4: Some Quick Things About Me
Engineering Physics
  Accelerator Physics
One-year project
  Master’s thesis
  Two project courses
http://www.freeworldmaps.net/ europe/sweden/sweden-map.jpg

## Slide 5: Distribution System Layout
Deliver cooling medium from cryoplant to cryomodules
  13 spoke cryomodules (light blue)
30 elliptical cryomodules
  9 medium-β (green)
  21 high-β (orange)
Cryoplant
Distribution line
Transfer line
Medium-β
High- β
Spoke
Courtesy of J. Fydrych

## Slide 6: Flow Scheme
Two circuits
  Cold helium circuit
  Thermal shield circuit

## Slide 7: 3D Model
Distribution line
Valve box
Jumper connection
Cryomodule
Valve box
Cryoline
Jumper connection
Cryomodule
Courtesy of P. Tereszkowski

## Slide 8: Linac CDS isometric
Valve box
Warm lines
Cryoline
Jumper connection
Modular structure of the cryogenic distribution line
Courtesy of P. Tereszkowski

## Slide 9: Linac CDS isometric
Valve box
Warm lines
Jumper connection
Cryoline
Cryomodules
Modular structure of the cryogenic distribution line
Courtesy of P. Tereszkowski

## Slide 10: The Cryogenic Distribution Line
Pipes
One valve box
One jumper connection
One cryomodule
Courtesy of P. Tereszkowski
8.52 m

## Slide 11: The Cryogenic Distribution Line
MultiLayer Insultation (MLI)
  Process lines: 10 layers
  Thermal shield: 30-40 layers
Lecture series by John Weisend. Michigan State University, 2012

## Slide 12: Dymola (The Software)
DYnamic MOdeling LAnguage
Modelica Association
  Consulting
  Providing Modelica libraries
  Providing helium properties

## Slide 13: Modelica (The Language)
  Object-oriented language
    Similar to C++ syntax
Declarative equations: As derived from physics
Modelica is acausal
http://i.stack.imgur.com/gPnim.png

## Slide 14: Modeling and Simulating
In Modelica models
  Model
  Default parameters
  Equations
In Dymola’s simulation environment
  Parameters
  Initial values
  Simulation setup

## Slide 15: Modeling and Simulating
Component models – reusable
Parameters and components
  Scalars
  Vectorized
  Matricized
Results and plotting in Matlab

## Slide 16: Example Model
Graphical and text layers describe the same thing

## Slide 17: Example Model
Components
  Developed
  Tested
individually
Connected to more complex systems
Parameters propagated to the top level

## Slide 18: Matlab – The Sidekick of Dymola
Side scripts in Matlab:
Choked Flow
Pressure Characteristics
Plotting and results
Etcetera

## Slide 19: Initial Results
First project
2∙300 m stainless steel pipes
  Constant helium flow
  Matlab and Dymola

## Slide 20: Initial Results
Matlab
  Preliminary cool-down time
  Pressure difference  Limited available flow
  Initially at 80 K, then at 4.5 K
  CP varies with temperature
  Result: 31.5 hours
Assuming
  Homogeneous cooling
  Friction-less flow
  No thermal radiation or conduction

## Slide 21: Results In Dymola
Example plot from Dymola
  Parameter plotted with one click
  Against time or any other parameter
    But that’s it

## Slide 22: Further Work
Further development of
  Thermal radiation
  Losses and frictions
  Connections to valves
  Connecting 43 modules
Helium properties available shortly (?)
Models available for steady-state simulations etc.

## Slide 23: To Sum Up
Modular structure
Two circuits with flowing helium
Dymola is both graphical and code
Multi-engineering modeling

## Slide 24: To Sum Up
Initial results: 31+ hours to cool
Some more work on components
Simulating using smoking fresh cryogenic helium properties
http://news.psu.edu/sites/default/files/styles/ threshold-992/public/iStock_000023736179Small.jpg

## Slide 25: Thank you