## Slide 1: Kevin Jones Technical Director
ESS Machine Update
IKON#18, Grand Hotel Lund, 24 February 2020

## Slide 2: The machine is being built by a diverse collaboration
Spokes
Medium β
High β
DTL
MEBT
RFQ
LEBT
Source
HEBT & Contingency
Target
2.4 m
4.6 m
3.8 m
39 m
56 m
77 m
179 m
75 keV
3.6 MeV
90 MeV
216 MeV
571 MeV
2000 MeV
352.21 MHz
704.42 MHz

## Slide 3: Machine Status
January 2020
  Robust activity in the Accelerator Buildings (G01/G02)
  Low Energy Beam Transport re-installed after modification post-commissioning, with new variable iris beam chopper
  Radio-frequency Quadrupole (RFQ) accelerating structure in place, bead pull complete, and being fitted for operation

## Slide 4: Machine Status
January 2020
  Robust activity in the Accelerator Buildings (G01/G02)
  RF couplers to the RFQ structure are in place, along with all waveguides
  Medium Energy Beam Transport (MEBT) is in place and is being fitted with services

## Slide 5: Machine Status
January 2020
  Robust activity in the Accelerator Buildings (G01/G02)
  Medium Energy Beam Transport (MEBT) is in place and is being fitted with services
  Over 3600 pieces of high-power radio-frequency waveguide (352 and 704 MHz) have been installed throughout the machine

## Slide 6: Machine Status
January 2020
  Robust activity in the Accelerator Buildings (G01/G02)
  Valve boxes and cryogenic service piping for the Spoke Cavity superconducting linac are being received
  Valve boxes and cryogenic distribution for the medium beta linac cryomodules are in place and undergoing site acceptance testing

## Slide 7: Machine Status
January 2020
  Robust activity in the Accelerator Buildings (G01/G02)
  Cryogen distribution and 704 MHz wave guides in the G01 tunnel
  Linac Warm Units (focusing magnets and beam diagnostics) in the High Energy Beam Transport area

## Slide 8: Machine Status
January 2020
  Robust activity in the Accelerator Buildings (G01/G02)
  The prototype medium-beta cryomodule is undergoing cryogenic testing in Test-Stand 2 in building G02 – a milestone for the cryoplant and test-stand capability – achieve 2K operation last week

## Slide 9: Machine Status
January 2020
  Robust activity in the Accelerator Buildings (G01/G02)
  Modulators for powering klystrons in Test-Stand 3 in G02
  High Power RF components being installed in G02

## Slide 10: Machine Status
January 2020
  Robust activity in the Accelerator Buildings (G01/G02)
  Assembly of Tank 1 of the Drift Tube Linac (DTL) is well underway and will be ready for installation in the late Spring 2020

## Slide 11: Machine Status
January 2020
  Tuning Beam Dump
  The tuning beam dump has been received and is being installed

## Slide 12: Neutron Beam Extraction System (NBEX)
January 2020
  Verification of the NBPI design continues at FZJ by use of the Insert Installation Tool and the Horizontal Handling Test Stand.
  Modified wheel solution has shown good results.

## Slide 13: The Monolith Vessel is nearing completion
January 2020
  Manufacturing ongoing.
  Unforeseen fabrication challenges pushes the delivery to April.
Lower body completely welded
Inside view
Weld penetrant test detail

## Slide 14: Outer monolith shielding is ready for shipment
January 2020

## Slide 15: Questions?