## Slide 1: High power IOTs
Anders Sunesson/Morten Jensen
Accelerator Division RF group leader
www.europeanspallationsource.se
May 16 2014

## Slide 2: Overview
ESS Linac and the driving parameters
IOT function
Examples of IOT
IOT possibility for high beta section?
ESS IOT parameters

## Slide 3: ESS Linac Layout
Low Energy Front end
DTL RF
Spoke RF
Medium beta RF
High beta RF
Spoke cryo-modules
Medium beta cryomodules
High beta cryomodules
DTL tanks

## Slide 4: ESS accelerator
Key parameters:
    -2.86 ms pulses
    -2 GeV
    -62.5 mA
    -14 Hz
    -Protons (H+)
    -Energy efficient
Design Drivers:
High Average Beam Power
5 MW
High Peak Beam Power
125 MW
High Availability
> 95%
Staged installation
i) 570 MeV
ii) 2000 MeV

## Slide 5: ESS Linac
 | Energy (MeV) | Frequency /MHz | No. of Cavities | βg | Temp / K | RF power /kW
Source | 0.075 | - | 0 | – | ~300 | –
LEBT | 0.075 | - | 0 | – | ~300 | –
RFQ | 3.6 | 352.21 | 1 | – | ~300 | 1600
MEBT | 3.6 | 352.21 | 3 | – | ~300 | 15
DTL | 90 | 352.21 | 5 | – | ~300 | 2200
Spoke | 220 | 352.21 | 26 (2/CM) | 0.5 βopt | ~2 | 330
Medium β | 570 | 704.42 | 36 (4/CM) | 0.67 | ~2 | 870
High β | 2000 | 704.42 | 84 (4/CM) | 0.86 | ~2 | 1100
HEBT | 2000 | – | 0 | – | ~300 | –
Spokes
Medium β
High β
DTL
MEBT
RFQ
LEBT
Source
HEBT & Contingency
Target
2.4 m
4.5 m
3.6 m
40 m
54 m
75 m
174 m
75 keV
3.6 MeV
90 MeV
220 MeV
570 MeV
2000 MeV
352.21 MHz
704.42 MHz

## Slide 6: RF Systems
RF powers all cavities of the linac
Meets the requirements for each part of the linac
Section | Power /kW | Solution
RFQ | 1600 | Klystron
MEBT | 15 | Solid state
DTL | 2200 | Klystron
Spoke | 330 | Tetrode
Med β | 870 | Klystron
Hi β | 1100 | IOT

## Slide 7
IOT = Inductive Output Tube
Invented in 1938 by Andrew V. Haeff as a source for radar
To overcome limitation of output power by grid interception
Pass beam trough a resonant cavity
Achieved: 100 W at 450 MHz, 35% efficiency
Used first in 1939 to transmit television images from the Empire State Building to the New York World Fair
IOTs then lay dormant until the 80’s
Intense competition with velocity modulated tubes - klystron had just been invented by the Varian Brothers
Difficult to manufacture
The IOT is often described as a cross between a klystron and a triode hence Eimac’s trade name ‘Klystrode’

## Slide 8
IOT
(Density modulated)
Biased
Control Grid
RF input
RF output
Reduced velocity spread compared to klystrons
Higher efficiency
Lower gain
No pulsed high voltage
Cheaper modulator
No current without drive
Control
Acceleration
Deceleration = RF Output
Magnetic field
How does it work?
Source
Beam

## Slide 9
Klystron (Velocity Modulated)
RF output
RF input
Collector
Cathode
(DC Beam)
Class A amplifier – needs pulsed HV
Bunching of electrons via cavities
Longer than IOT
Higher gain (40-50 dB)
High power (several MW)

## Slide 10
Klystrons
IOTs
Electrical Power Consumed
Power delivered to beam
Power delivered to beam
High Beam Current
Low
Beam Current
Cartoon!

## Slide 11: Power transfer IOT vs klystron
Pin
Pout
Klystron/MBK
IOT
MB-IOT
Operating
Power Level
+6 dB
hsat ~ 65-68%
~ 52-55%
ESS estimate <45%
Back-off for feedback
High gain
Low Gain
Long-pulse
excursions possible
Short-pulse
excursions possible
Unstable region
IOT’s don’t saturate.
Built-in headroom for feedback.
~ 70%
Courtesy of CPI
*** Klystrons: Back-off for feedback costs 30% ***
*** IOTs: Operate close to max efficiency***

## Slide 12
Typical Broadcast IOT
Courtesy of e2v

## Slide 13
3rd Generation Light Source
Storage Ring
Three 500 MHz 300 kW amplifier for SR
- 4 x 80 kW IOT combined
One 80 kW for the Booster
Serial Number
Filament Hours
30000
20000
10000
In Operation
Test system
Operational Hours at Diamond
Peter Martin, Diamond

## Slide 14
CPI 90 kW IOT (K5H90W1)
> 33 000 operating hours
Metrology Light Source
(Willy Wien Laboratory)
Elettra
500 MHz
150 kW IOT based amplifier for Combination of 2x80 kW
CERN
800 MHz
60 kW
Other Facilities using IOTs
12 IOTs

## Slide 15
Easy? Use IOTs instead of klystron?
Klystrons are the standard choice for high power accelerators
They exist at the power levels needed for ESS
They are really pretty good, reliable and quite efficient
IOTs at ESS parameters don’t exist
Typical power 80-100 kW
Lower gain (20-25 dB)
They may be more complicated
They need to be developed
More risk

## Slide 16: But: Schedule opportunity
2010
14
11
12
13
15
19
16
17
18
20
21
22
23
ESS ADU starts
CM prototypes launched
First SC cavity ordered
Ellip CM productionlaunched
Early access to tunnel
NC linac ready
SC linac 570 MeV ready
First protons to target
Early access cryo and test buildings
1370 MeV protons available
2 GeV protons available
NC and FE IK contracts
Spoke CM prototype available
Redesign approved
Prototype klystrons delivered
Injector test at Saclay
Decision IOT or klystrons
Cryoplant ready
Conceptual Design
SC RF
NC linac
RF
Cryogenics
Services, installation and com.
Decision on
Scope
Klystrons and IOTs ordered
RF for medium beta ready
RF for High beta ready
Acc cryoplant ordered
Cryo dist. line ordered
Prototype IOTs delivered CERN
Test stand Lund University
Test stand on site
IOT delivery

## Slide 17: High beta: Superpower IOT
Superpower IOT – a multi-beam IOT aimed at powering the high beta section. The target peak power is 1.2 MW
    Advantages: higher efficiency than klystrons, smaller footprint
    Lower voltage, operation at nominal power
    Disadvantage: device does not exist, must be developed
    Collaboration with CERN:
      ESS to tender and buy prototype tubes (delivery 2016)
      CERN to test (test stand in preparation)
      Decision IOT/klystron end 2017
    If the IOTs fail, go klystron (the medium beta klystron prototyped has the right specification)

## Slide 18: How to reach the power needed?
Power requirement 500 kW – 1.5 MW
Single beam – Large cathode
  High voltage
  High cathode loading
  Oil in the modulator and gun
Multi beam - Several smaller cathodes
  Higher total perveance
  Lower voltage
  Lower cathode loading
  Scalable for higher power levels (100-140 kW per cathode)

## Slide 19
Design and Simulation
Analytical and Numerical codes available
Commercial codes well developed in addition to manufacturers own
Increased computing power allows improved simulation of grid structures, trajectory and PIC modeling
Gun simulation
IVEC 2009
CPI
CPI
TED

## Slide 20: 700 MHz HOM IOT experience CPI
Design Parameters value units
Power Output 1000 kW (min)
Beam Voltage 45 kV (max)
Beam Current 31 A (max)
Frequency 700 MHz
1dB Bandwidth ± 0.7 MHz (min)
Gain 23 dB (min)
Efficiency 71 % (min)
Diameter 30/76 in/cm
Height 51/130 in/cm
Weight 1000/450 lbs./kg
Collector Coolant Flow 220 gpm
Body Coolant Flow 10 gpm
O/P Window Cooling (Air) 35 cfm
  VHP-8330A IOT
@ 31kV
RF Input
Collector
Solenoid,
O/P Cavity
Gun
RF Output
Test Results (pulsed)

## Slide 21: Some IOT publications by Labs
Applications of High Power Induction Output Tubes in High Intensity Superconducting Proton Linacs
Testing of Inductive Output Tube based RF amplifier for 650 MHz SRF Cavities, A. Mandal et al, PCaPAC2012
90 kW CW IOT development at L3 Communications Electron Devices, M Boyle et al, CWRF Workshop, 2012
Development of a 402.5 MHz 140 kW IOT, M Read et al, PAC2011
The first continuous wave and long pulse operation, DESY, 2011
Simple Model of an Inductive Output Tube, R. Carter, IEEonED 2010
CPI’s 1.3 GHz, 90 kW Pulsed IOT Amplifier, M. Marks et al, IPAC2010
Modelling and Design of High-Power Inductive Output Tubes, E. Wright et al, PAC2009.
Highly stable IOT based 1.3 GHz/16kW RF Power Source for CW operated SC Linacs, SRF2009
The ALBA RF Amplifier System based on IOTs, P. Sanchez et al, EPAC2008
Installation and Commissioning of the new 150 kW plant for the Elettra RF System Upgrade, A Fabris et al, PAC07
Grid less IOT for Accelerator Applications, C. Wilson et al, PAC2007
IOT testing at the ERLP, J Orrett at al, EPAC2006
First Results of the IOT Based 300 kW 500 MHz Amplifier for the Diamond Light Source, M. Jensen et al, EPAC05
IOT RF Power Sources for Pulsed and CW Linacs, H. Bohlen et al, Lunac2004
Comparison of Klystron and Inductive Output Tubes Vacuum-Electron Devices for Amplifier service in Free-Electron Laser, EPAC04

## Slide 22
 | Single Beam Klystron | MB IOT | 
Peak output Power | 1 | 1 | MW
Cathode Voltage | 95 | 50 | kV
Beam Current | 21 | 31 | A
Efficiency at saturation | 65 | 65 (min) | %
Est. efficiency for operation | <45 | >60 | %
Gain | 48 | 23 | dB
A 700 MHz Comparison
1.3 m
0.6 m

## Slide 23: Where next?
ESS requirements
    Carbon Neutral
    Innovative
    Green
Accelerating Structure | Freq. (MHz) | Quantity | Max Power (kW)
RFQ, DTL | 352 | 5 | 2200**
Spoke | 352 | 26 | 330**
Elliptical Medium Beta | 704 | 36 | 860**
Elliptical High Beta | 704 | 84 | 1100**
Power saving from high beta about 20 GWh per year
** Plus overhead for control

## Slide 24: IOT tender
Parameter |  | Comment
Frequency | 704.42 MHz | Bandwidth > +/- 0.5 MHz
Maximum Power | 1.2 MW | Average power during the pulse
RF Pulse length | Up to 3.5 ms | Beam pulse 2.86 ms
Duty factor | Up to 5% | Pulse rep. frequency fixed to 14 Hz
Efficiency | Target > 65% | 
High Voltage | Low | Expected < 50 kV
Design Lifetime | > 50,000 hrs | 
Target: Approval for ESS series production in 2017/18
Work is being carried out in collaboration with CERN
ESS to procure prototypes
CERN to make space and utilities available for testing

## Slide 25: Conclusion
The IOT is an alternative as RF source for accelerators
It can offer high efficiency
It does not require pulsed HV
To develop an IOT at ESS specification, going multibeam offers the possibility of HV low enough to avoid oil
The use of IOTs in the high beta section is proposed
The staged installation provides schedule opportunity
ESS has tendered for a 1.2 MW IOT according to ESS parameters
The development is done in collaboration with CERN

## Slide 26
Thank you