## Slide 1: SM18 Klystron Modulator
Sven Pütz
Project Description
System Parameters
Electrical Schematic & Layout
Pulse Waveforms
Resistive Dummy Load
Project Schedule

## Slide 2: Project Description
In 2011, a modulator requirement identified for a high power 704MHz teststand at CERN
  Deliver 2.8MW electrical pulsed power to a klystron
  Flexible enough to adapt to several specifications, including ESS and SPL parameters
Modulator supplied by ESS through superconducting cavity collaboration
  Contract prepared and managed by ESS with some CERN input
  Selection of best offer which was based on simple LR bouncer topology
  Contract placed in 2011

## Slide 3: System Parameters
Zk
Parameter | SM18 / ESS | SPL | LINAC4 | 
Uk | -115 | -110 | -110 | kV
Ik | 25 | 25 | 50 | A
Ppulse | 2.88 | 2.6 | 5.5 | MW
Pavg | 161 |  | 20 | kW
PRR | 20 | 50 | 2 | Hz
Zk | 4.6 | 4.4 | 2.2 | kΩ
τpulse / τflat-top | 2.8 / 2.5 | 1.0 / 0.8 | 1.8 / 1.5 | ms
droop | 3 | 1 | 1 | %
droop compensation type | LR |  | LC | 
Design / Production | AMPEGON PPT GmbH |  | CERN / JEMA sa | 

## Slide 4: System Parameters
Zk
Parameter | SM18 / ESS | SPL | LINAC4 | 
Uk | -115 | -110 | -110 | kV
Ik | 25 | 25 | 50 | A
Ppulse | 2.88 | 2.6 | 5.5 | MW
Pavg | 161 |  | 20 | kW
PRR | 20 | 50 | 2 | Hz
Zk | 4.6 | 4.4 | 2.2 | kΩ
τpulse / τflat-top | 2.8 / 2.5 | 1.0 / 0.8 | 1.8 / 1.5 | ms
droop | 3 | 1 | 1 | %
droop compensation type | LR |  | LC | 
Design / Production | AMPEGON PPT GmbH |  | CERN / JEMA sa | 

## Slide 5: Electrical Schematic & Layout

## Slide 6: Electrical Schematic & Layout

## Slide 7: Electrical Schematic & Layout

## Slide 8: Electrical Schematic & Layout

## Slide 9: Test Site Assembly

## Slide 10: Test Site Assembly

## Slide 11: Pulse Waveforms
Mar 2014: reception test in Dortmund (PPT)
  Pavg limited to 25%
  burst tests with full pulse voltage/current
  operation with resistive dummy load
  arc protection validated
CH1 Uk 114kV (droop: 3%)
CH2 Ik 29A (droop: 3%)
CH3 main pulse cmd
CH4 Ip 633A

## Slide 12: Resistive Dummy Load
air insulated
water cooled
Pavg 161 kW
oil insulated
forced convection
Pavg 10 kW (per tank)
SM18/ESS
LINAC4
11 m3 / 6 m2
1.6 m3 / 1 m2
2400
2300
2000
1500
1300
800

## Slide 13: Resistive Dummy Load
NICROM WP500.100 |  |  | 
Unom | 150 | kV | tested @115 kV operated @58 kV
Prms,nom | 2 | kW | tested @2 kW operated @0.8 kWrms/15 kWpk
R | 220 | kΩ | ±10 % ±100 ppm/K
Epulse,10ms | 2.2 | kJ | singe pulse, 10 ms
Epulse,1ms | 0.44 | kJ | singe pulse, 1 ms operated @42 J / 20 Hz
Q | 6 | l/min | per element

## Slide 14: Resistive Dummy Load
192 Resistors / 4 Modules
diode to simulate reverse blocking
2nd HV outlet to connect spark gap
NICROM WP500.100 |  |  | 
Unom | 150 | kV | tested @115 kV operated @58 kV
Prms,nom | 2 | kW | tested @2 kW operated @0.8 kWrms/15 kWpk
R | 220 | kΩ | ±10 % ±100 ppm/K
Epulse,10ms | 2.2 | kJ | singe pulse, 10 ms
Epulse,1ms | 0.44 | kJ | singe pulse, 1 ms operated @42 J / 20 Hz
Q | 6 | l/min | per element

## Slide 15: Project Schedule
2012
2013
2014
2011
07 - call for tender
09 - TDR presentation
10 - dummy load revised TDR
03 - reception @25% (PPT)
05 - reception @100% (CERN)
09 - commissioning SM18
12 - contract start
10 - TDR approval (except dummy load)
10 - approval of dummy load TDR

## Slide 16: ToDo
Reception Test @100%
  Fast Interlocks (e.g. arc detection)
  Output Performance
  Remote Control
  EMC & Efficiency
  Heat-Run
Gain Operational Experience
Commissioning with Klystron in SM18
  Electrical Power and Cooling
  Signal Interfaces
  Filament Heater
  Anode Control
LEP Klystron

## Slide 17: Thank you for your attention!