## Slide 1: New Fermilab Plans (PIP II)
Slava Yakovlev
4th SLHiPP Meeting
May 15-16, 2014

## Slide 2: Outline
Short History of Project X and Logic of its Development
Since Last Time
Motivation/Goals
Strategy
Preferred Option
R&D Strategy
PIP-II versus Project X Stage I
Requirements, problems and status
Summary

## Slide 3
Proton Driver - 4 times larger flux than Booster
  Ring based(end of 90th - ~2002)
  Pulsed 8 GeV SC linac (~2001-2006)
Project X
  Pulsed 8 GeV SC linac (2006)
    Aligned with the ILC technology
  CW SC 2 GeV linac and RCS (2009)
    Aligned at experiments in the HEP intensity frontier
  CW SC 3 GeV linac and 8 GeV Pulsed linac (2010)
    Added kaon experiments and has potential to be used as a proton driver for muon collider
    Project Staging (2012)
PIP-II
  Utilizes technology developed for Project X
Short History of Project X and Logic of its Development

## Slide 4: Since Last Time
CSS (Snowmass) Workshop
  Project X “Book” released
New Fermilab Director
  Established LBNE as laboratory flagship
  Requested rework of Project X concept to provide significant enhancement to LBNE, at an affordable cost to DOE
  Requested a new name
P5 formed to provide advice to DOE
  Plan for the next ten years, within context of next twenty
PIP-II concept developed
  Whitepaper published
  Presentation to P5 at BNL meeting
  Funding requirements to P5
Fermilab assumes major role in SRF cryomodule production for LCLS-II

## Slide 5: Motivation/Goals
Our goal is to construct & operate the foremost facility in the world for particle physics utilizing intense beams.
Neutrinos
  MINOS+, NOvA @700 kW (now)
  LBNE @ >1 MW (2025)
  LBNE @ >2 MW (>2030)
  Short baseline neutrinos
Muons
  Muon g-2 @ 17 kW (2017)
  Mu2e @ 8 kW (2020)
  Mu2e @ 100 kW (>2023)
Longer term opportunities
This will require more protons!

## Slide 6: Design Criteria
Support long term physics research goals by providing increased beam power to LBNE while providing a platform for the future
Design Criteria
  Deliver 1.2 MW of proton beam power from the Main Injector to the LBNE target at 120 GeV, with power approaching 1 MW at energies down to 60 GeV, at the start of LBNE operations
  Continue support for the current 8 GeV program, including Mu2e, g-2, and the suite of short-baseline neutrino experiments; provide upgrade path for Mu2e
  Provide a platform for eventual extension of beam power to LBNE to >2 MW
  Provide a platform for extension of capability to high duty factor/higher beam power operations
  At an affordable cost to DOE

## Slide 7: Strategy
Increase Booster/Recycler/Main Injector per pulse intensity by ~50%.
  Requires increasing the Booster injection energy
Select 800 MeV as preferred Booster injection energy
  30% reduction in space-charge tune shift w/ 50% increase in beam intensity
  Provides margin for lower beam loss at higher intensities
Modest modifications to Booster/Recycler/Main Injector
  To accommodate higher intensities and higher Booster injection energy
Cost effective solution: 800 MeV superconducting pulsed linac, extendible to support >2 MW operations to LBNE and upgradable to continuous wave (CW) operations
  Building on significant existing infrastructure
  Capitalizing on major investment in superconducting RF technologies
  Eliminating significant operational risks inherent in existing linac
  Siting consistent with eventual replacement of the Booster as the source of protons for injection into Main Injector

## Slide 8: PIP-II versus Project X Stage I
What was changed?
  Beam energy: 1 GeV→ 0.8 GeV. It is large enough
    to avoid problems with beam space charge and
    To have high enough efficiency of pion and muon production
  Beam current: 1 mA → 2 mA
    Reduces number of turns for Booster injection
    Large enough to support ~ 100 kW for m-to-e upgrade (long pulse)
  At the beginning: a single purpose facility with the only goal
    Support of power increase for LBNE by ~1.7 times
  Operational mode: CW → Pulsed (15 Hz, 0.6 ms)
Why? - Cost reduction: Cryogenics & Use of existing infrastructure
Long-term goal is the same
  CW operation for intensity frontier experiments
  Design has to support future CW operation and >2 MW in MI

## Slide 9: Project X → PIP-II (Structure changes)
The same as the Project X the PIP-II includes
  warm front-end
    MEBT chopper capable to chop out bunches coming to Booster at the RF buckets boundary
  SC cryo-modules
    pulsed operation
      limited by power of the cryo-plant
        ~5% duty factor for cryo
  Reduced number of HB-650 cryo-modules (7→4)

## Slide 10: PIP-II Major Parameters
Performance Parameter | Requirement | 
Linac Beam Energy | 800 | MeV
Linac Beam Current | 2 | mA
Linac Beam Pulse Length | 0.6 | msec
Linac Pulse Repetition Rate | 15 | Hz
Linac Upgrade Potential | CW | 
Booster Protons per Pulse (extracted) | 6.4×1012 | 
Booster Pulse Repetition Rate | 15 | Hz
Booster Beam Power @ 8 GeV | 120 | kW
8 GeV Beam Power to LBNE | 80‐120* | kW
Beam Power to 8 GeV Program | 40‐0* | kW
Main Injector Protons per Pulse (12 batches; extr.) | 7.5×1013 | 
Main Injector Cycle Time @ 120 GeV | 1.2 | sec
Main Injector Cycle Time @ 60 GeV | 0.8 | sec
LBNE Beam Power @ 60 GeV | 0.9 | MW
LBNE Beam Power @ 120 GeV | 1.2 | MW
LBNE Upgrade Potential @ 60‐120 GeV | >2 | MW
*1st number refers to MI operations @ 120 GeV; 2nd number to 60 GeV. The PIP-II configuration is capable of maintaining 1.2 MW down to 80 GeV.

## Slide 11
PIP-II Linac Requirements:
Linac Beam Energy | 800 | MeV
Linac Beam Current | 2 | mA
Linac Beam Pulse Length | 0.6 | msec
Linac Pulse Repetition Rate | 15 | Hz
Linac Upgrade Potential | CW | 
Low beam loading;
Long filling time compared to pulse length;
Low efficiency at pulse mode.

## Slide 12
SRF Cavity Type | Freq, MHz | Energy (MeV) | Cav/mag/CM | CM type, length
HWR (G=0.11) | 162.5 | 2.1-11 | 8 /8/1 | scscscscscscscsc, 5.3m
SSR1 (G=0.22) | 325 | 11-38 | 16 /8/ 2 | csccsccsccsc, 4.8m
SSR2 (G=0.51) | 325 | 38-177 | 35 /21/ 7 | sccsccsc, 6.5m
LB 650* (G=0.61) | 650 | 177-480 | 30 /20/5 | cccfdccc, 7.1m
HB 650 (G=0.9) | 650 | 480-800 | 24 /6/ 4 | cccccc, 9.5m
PIP II
SRF Linac Technology Map
*3-cavity option is under consideration; CM has no focusing elements.

## Slide 13
Accelerating cavity types and
characteristics for the SC linac.
Name | bG | bopt | Freq (MHz) | Type of cavity | Bpeak (mT) | Epeak (MV/m) | Eacc (MV/m) | DE (MeV)
HWR | 0.094 | 0.112 | 162.5 | Half wave resonator | 41 | 38 | 8.2 | 1.7
SSR1 | 0.186 | 0.222 | 325 | Single‐spoke resonator | 58 | 38 | 10 | 2.05
SSR2 | 0.431 | 0.515 | 325 | Single‐spoke resonator | 70 | 40 | 11.2 | 5.32
LB650 | 0.61 | 0.647 | 650 | Elliptic 5‐cell | 70 | 37.5 | 16.5 | 11.6
HB650 | 0.9 | 0.95 | 650 | Elliptic 5‐cell | 64 | 35.2 | 17.5 | 17.7
Epeak ≤ 40 MV/m, for CW (Field emission);
Bpeak ≤ 75 mT, for CW (medium field Q-slope)

## Slide 14: Primary Technical Risks
Future CW operation → cryo-losses → high Q0 is desired;
Low beam loading → microphonics;
High-Order Modes → “to damp, or not to damp?”
Lorentz Force Detune (LFD) may be an issue in a pulsed mode, and should be analyzed (addressed in Brian Chase’s presentation).

## Slide 15: PIP-II Duty Factors
The average RF power has 2 contributions:
  the energy transferred to the beam (~10%)
  the energy required to fill and discharge the accelerating cavities (90%)
For a fixed average power the cost of RF increases with peak power
  therefore its cost achieves minimum with minimum peak power
    i.e. power equal to the power required for beam acceleration => duty factor for the RF power amplifiers ≈12%
    In this case the cost savings associated with the pulsed power amplifiers is modest and therefore CW capable RF amplifiers are planned from the beginning
More details on cavity filling are in the B. Chase presentation

## Slide 16: PIP-II Cryogenics
To minimize the cost a system will be assembled using existing Tevatron cryogenic infrastructure
    including the Central Helium Liquefier (CHL)
    transfer line
    compressors
  Cryogenic duty factor is ~5%
  The total cryogenic heat load at 2K is dominated by the static load, and is about 16% of the CW load
Future upgrade to CW operation would require a new 2K cryogenic plant
Rms pressure fluctuations have to be <0.1 mbar!!!
Total CM Heat Loads [W] |  |  | 
 | 70 K | 5 K | 2 K
Pulsed | 2,860 | 895 | 256
CW | 2,860 | 895 | 1819

## Slide 17: Limitations on Operation in Pulsed Regime
The Lorentz force detuning represent a problem which needs to be diligently addressed
  Cavity design with suppressed sensitivity to microphonics and LFD
  Fast tuner (piezo-based) & Low level RF
  Over coupling and additional RF power
 | Eacc (MV/m) | LFD (Hz/(MV/m2) | DfLFD [Hz] | Qloaded opt. for CW | Df=f/2Q [Hz] | Microphonics ampl. [Hz]
HWR | 8.2 | - | - | 2.4∙106 | 34 | 20
SSR1 | 10 | 1.5* | 150 | 3.6∙106 | 45 | 20
SSR2 | 11.2 | No data |  | 6.0∙106 | 27 | 20
LB 650 | 16.5 | <1♦ | <272 | 1.12∙107 | 29 | 20
HB 650 | 17.5 | <1♦ | <306 | 1.05∙107 | 31 | 20
* Measured
♦ Estimated

## Slide 18: Limitations on Operation in Pulsed Regime (continue)
All cavities with the exception of HWRs will have fixed coupling
Operation in pulsed regime with coupling adjusted for CW requires ideally working fast tuner which suppresses the LFD
  Adaptive digital feedback with feedforward controlling the fast tuner operation is the must
Presently we assume
  that external stub tuners are used for Qloaded decrease
    Couplers are capable to operate at required (increased) power levels
  Increased priority for the R&D directed at LFD compensation with fast tuner
  Excessive RF power for LFD and microphonics compensation
Final adjustments of cavity coupling values and RF power requirements will be done later
More details on cavity filling are in the B. Chase presentation

## Slide 19
  Status of the PIP II cavity
  and CM design
  SSR1
  10 SSR1 325 MHz, low-beta cavities are manufactured;
  9 of them are processed, tested and qualified;
  New He vessel with reduced df/dP is designed, one SSR1 cavity is dressed.
  Tuner design is in progress;
  RF coupler design is completed, 3 couplers will be ready for HP tests.
  Design of the focusing solenoid is completed, the 1st solenoid is manufactured and is tested.
  Concept design of the CM is ready, main parts (vacuum vessel, strong back and supports) are ordered.
  SSR2
  EM design is finished,
  mechanical design is in progress.

## Slide 20
SSR1 He Vessel and tuner
Pressure of LHe can vary by ± 0.1 Torr in the cryomodule
SSR1 must operate within a small bandwidth ± 20 Hz
A self-compensating design was developed allowing low sensitivity
Despite non-negligible deformations (see picture), net shift is very low
Bare cavity ~ 600 Hz/Torr, with He vessel ~ 10 Hz/Torr (measured)
Ease of tuning 39 N/kHz (bare), 40 N/kHz (with He vessel)
Actuating elements of the tuning system
Dressed SSR1

## Slide 21
The coupler is designed for 30 kW traveling wave (TW) at full reflection
Three couplers are manufactured, measured (reflection -22 dB at 325 MHz) and will be tested in few weeks.
The test stand is ready
SSR1 Couplers:
Coupler test stand

## Slide 22
SSR1 Solenoids:
Number, total | 4
Operating temperature, K | 2
Maximum current, A | <100
∫B2dL, T2m | 4.0
Alignment precision, RMS: center position [mm] | ±0.5
Alignment precision, RMS: angle [mrad] | ±1
Magnetic field on the walls of the cold cavity should not decrease its quality factor by the factor of more than | 2
Prototype lens PXIE_SSR1_L01P has been tested for performance on February 5, 2014.
The lens reached quench current without training both at 4.58 K and 2.15 K. At 4.58 K, the quench current was 68 A. At 2.15 K, the quench current of ~92 A was measured. This coincides to the model prediction.

## Slide 23
The SSR1 cryomodule
The concept design is complete
Procurement is started

## Slide 24
SSR1 Schedule:
Chart: SSR1 Cryomodule for PXIE
| Bare cavity fab (*) | Dressed cavity fab | Cryomodule detail design | Cryomodule component fab | Tuner design and prototype | Input coupler fab | Solenoid fab | Current lead fab | Tooling design | Tooling fab | Cold mass string assy | Cryomodule assembly
 | 41243 | 42277.5 | 41821.5 | 42218.5 | 42064 | 42186 | 42003.5 | 42187.5 | 42368.5 | 42551 | 42643.25 | 42735.25
 | 40148 | 41730 | 40909 | 41671 | 41699 | 41821 | 41821 | 42005 | 41821 | 42186 | 42552 | 42644

## Slide 25
  LB/ HB 650
  EM design of both LB and HB 650 is ready.
  Two singe-cell LB 650 cavities are manufactured, processed and tested (JLAB);
  Six single-cell cavities HB 650 are manufactured by AES, processed and tested at Fermilab.
  Two HB 650 cavities are processed and tested.
  Four 5-cell HB 650 cavities are manufactured by AES and ready for processing and tests.
  Five additional single cell and five five-cells HB cavities ordered from industry (PAVAC) on ARRA funds
  Design of He vessel for HB 650 with low df/dP and the tuners (slow and fast) are completed.
  Concept design of the CM for HB 650 is ready.

## Slide 26
LCLS II: Fermilab participation
2014 - 2015 :
One 1.3 GHz pre-production cryo-module: ILC-type 8-cavity CM with minimal modifications for CW operation at 16 MeV/m
Extensive use of existing parts (vacuum vessel, cavities, couplers)
Design modifications (CM, He vessel, tuner, HOM coupler, main coupler)
Part procurement
CM assembly
CMTF and ASTA modifications to allow CW tests of full LCLS-II CM
R&D for Q0 improvement
2015-2018:
Production of LCLS II cryo-modules
Eighteen 1.3 GHz cryomodules (144 TESLA – type 9-cell cavities);
Two 3.9 GHz cryo-modules (16 FNAL- type 9-cell cavities).
Major new initiative for FNAL. Previous ILC work has positioned us very well
Care will be required to minimize impact on PIP II R&D effort

## Slide 28: Conclusions
PIP-II is aimed at the long-time program in the accelerator based HEP intensity frontier
A required cost reduction at the first stage is achieved by
  Reduction of CW linac energy,
  transition to pulsed regime
  and reuse of existing infrastructure
Reuse of Booster creates a cost effective way to increase power for the neutrino experiments
For LBNE it should yield a power increase of ~1.7 times
SC PIP-II will can be used for the m-to-e upgrade with reasonably large duty factor
Transition to the CW regime will require new cryo-plant
  All other major system will be CW compatible