## Slide 1: Detector possibilities for LoKI
Kalliopi Kanaki

## Slide 2: Topics to be addressed
Detector options for LoKI
Related detector group R&D activities
Highlights of results
Instrument phase 1

## Slide 3: Making decisions
NASA TRL (wikipedia)
What should we take into account?
Requirements matching
Cost
Technology availability
Technology readiness level (TRL)

## Slide 4: LoKI options
Zero angle detector
Low angle
  Anger cameras
  MultiBlade
  MultiGrid
  bGEM
High angle
  10B tube
Zero angle detector
Low angle
  Anger cameras
  bGEM
  MultiBlade
Mid-angle
  Anger cameras
  bGEM
  MultiBlade
High-angle
  Macrostructures
  MultiGrid
Rate & resolution limitations make 3He an unrealistic option

## Slide 5: The ESS Detector Group
5
ESS
ILL
IFE
Linkoping
CERN
Lund U, LTH, MAXlab
Carina Höglund
Mewlude Imam*
Anton Khaplanov
Isabel Llamas
Xiao Xiao Cai
Thomas Haraldsen
Kevin Fissum
Björn Nilsson
Julius Scherzinger*
Vladimir Pastukov*
Dorothea Pfeiffer
(+5 bachelors/Masters Projects+2 interns)
(31 Dec 2010, detector group comprised of ... Carina!)
3 PhD Students (*)
Richard Hall-Wilton
Kalliopi Kanaki
Thomas Kittelmann
Scott Kolya
Luis Ortega
reorganization of the group & work breakdown structure to change focus
from R&D to instrument classes and construction

## Slide 6: LoKI related ESS R&D activities
10B technology (ILL/ESS/FRM-II/Linköping)
  Multi-Grid detector (multiple converter layers)
  Macrostructures (multiple converter layers)
  Tube detector (single converter layer)
  B4C coatings
bGEM (Italy/CERN)
Simulation framework
Neutron energy determination

## Slide 7: Technology strategies
No 3He developments internally
Expect a need of ca. 2000 bar-litres of 3He
Do not buy 3He directly, secured by in-kind partners
B4C coatings can be mass produced very cheaply
New deposition machine at Linköping will provide 100-300% of expected ESS needs
Production will be partly by ESS, partly by in-kind partners
Act as centre of excellence for the technology: i.e. simulation, standards, expertise concentrated at ESS
Numerous groups already working on scintillator technologies: ISIS, SNS, Jülich, JPARC
Resources not available: ESS should be a client for scintillator technologies
In-kind ISIS (WLS), Jülich (WLS, Anger cameras)

## Slide 8: Multi-Grid design (ILL/ESS/Linköping)
neutron efficiency: analytically calculated, simulated,
measured, understood
γ efficiency comparable to 3He
scattering understood
detector induced background understood
large scale IN5 detector to be produced
by October 2014, 3m x 0.8m
working on definition of detector standards
for reliable comparisons
Multiple conversion layers (30)
MWPC concept
A. Khaplanov et al., Nucl Instr. & Meth. in Phys. Res. A, 720, 116-121 (2012)
A. Khaplanov et al., JINST 8, P10025 (2013)
F. Piscitelli and P. van Esch, JINST 8, P04020 (2013)
F. Piscitelli, Ph.D. thesis, University of Perugia (2013)

## Slide 9: Macrostructures design (FRM-II/ESS)
Multiple conversion layers (5)
MWPC concept
Uniform coating performs better
Macrostructures increase (layer) efficiency by a factor 1.5
Performance simulated, measured, understood
I. Stefanescu et al., Nucl. Instr. Meth & Phys. Res. A, 727, 109-125 (2013)
I. Stefanescu et al 2013 JINST 8 P12003

## Slide 10: Tube detector
vacuum tank
detector banks
10B4C coating
10m
0.5m
Analytical calculations in place
Detailed simulations in progress
Prototyping phase (proportional counter)
Tests with AmBe source and beam in progress
0.5m

## Slide 11
Analytical evaluation I: Efficiency
K.Kanaki et al., J. Appl. Cryst. 46, 1031–1037 (2013)
F. Piscitelli and P. van Esch, JINST 8, P04020 (2013)
F. Piscitelli, Ph.D. thesis, University of Perugia (2013)
Capture and ion escape included in the calculations
Back-scattering efficiency higher than transmission -> working choice
Room for optimization by
  further increasing the neutron incident angle
  varying the boron layer thickness
  additional converting layers
back-scattering

## Slide 12
Analytical evaluation II: Resolution
δθ = | θn-θn-1|
δθ/θ < 10% at the detector area with highest occupancy, far better than what required
λ and Q resolutions are detector-specific
Impact of azimuthal angle negligible
Resistive wires or segmented cathodes can be used for 2D resolution
12
polar angle resolution
wavelength resolution
pitch = 5cm
Q resolution
pitch = 5cm

## Slide 13
Simulation tools:
Diffractive processes in Geant4
For neutrons of a few Å diffractive scattering becomes important
Respective physics processes not included in Geant4
Functionality added with the integration of NXSLib library from McStas
NXSLib – Geant4 integration extends the capabilities of Geant4 to become a complete tool for investigations at neutron scattering facilities
T. Kittelmann, poster NPO2-138, NSS IEEE 2013
T. Kittelmann, CHEP 2013 proceedings
13

## Slide 14
Efficiency: Geant4 vs. analytical
simplified cylindrical geometry
neutron wavelength = 2 Å
Al vacuum vessel window = 0.3cm
Al detector window = 0.3cm
below 2°-3° the comparison is
not reliable due to detector edge effects
14
Geant4 is validated for coherent neutron scattering!!

## Slide 15
Impact of scattering on efficiency
15
Geant4 realistic LoKI geometry with octagonal cross section
Al vacuum vessel window = 0.3cm
Al detector cathode window = 0.1cm
Scattering impact on efficiency has to be minimized
no scattering
with scattering

## Slide 16: Neutron energy determination
Idea: deconvolution of neutron energy spectrum
with statistical inference methods
Method is applicable for all multi-layer detectors
Bonner sphere-like deconvolution
Exploit the depth of interaction
Absorption profile measurements from 3 facilities
as first approach (monochromator & chopper lines)
1 MSc and 1 PhD student working on the topic
First results are very encouraging!

## Slide 17
Deliverables for Phase 1: documents to be prepared by November 2014
Monthly discussions &
quarterly document revisions
with:
instrument scientist (Andrew)
instrument engineer (Stewart)
detector scientist (Kelly)
communication folders
forgotten in the official list, added by us
mercurial screenshot

## Slide 18
Snapshot of the LoKI detector schedule
Not redone yet
Covers first year
Assumes all people are already hired
Generic approach for beam monitors: will be done commonly for all instruments

## Slide 19: Summary
Extensive 10B technology development at ESS/ILL/FRM-II
Several geometries are considered
Other technologies monitored and supported
Final decisions on LoKI detectors in 2016
Advanced simulation tools in place for detector optimization
The outlook is positive 