## Slide 1
Software Core Components (ICS WP3)
Suzanne Gysin
Work Package Lead
www.europeanspallationsource.se
February 22, 2014

## Slide 2: What are the "Software Core Components”?
  5 Databases
  15 Software Services
  and
  the Naming Convention

## Slide 3: Control System - Software Core Compents
WBS: Project 14 Integrated Control System (ICS)
  WP 3. Software Core Components
    WU 3.1 Configuration Data Management
    WU 3.2 Control System Services
    WU 3.3 Naming Convention

## Slide 4: Lattice Database
Contains the ESS Accelerator configuration as it is simulated prior to being built.
It includes the geographical and physical information for:
  Simulated beam line elements
  Accelerating structures
  Auxiliary elements
  Beam diagnostics
  Vacuum
[1] Lattice Database Requirements Document v1.1, S.Gysin
[2] Lattice Browser Requirements Document v1.0, S.Molloy
Notes: Software Requirements:
  Import data from the simulation
  Lattice Browser (web application)
  API (Java)
  Restful Interface (other languages)
  Relational database (Postgres)
  Exports and reports for OpenXAL, Mechanical Engineering, Global Coordinate report, comparison between versions.
  Requirement for versioning: current baseline, history of prior baselines, and the Lattice under Development (LuD)

## Slide 5: Controls Configuration Database - CCDB
Scope: the physical attributes of a specific device. (barcode, location, status calibration test results, user defined attributes)
What devices/data is included: Control Boxes, MPS devices, PSS devices. Devices controlling vacuum, RF, Cryogenics, target, neutron instruments, and conventional facilities.
Software Requirements:
  Water connections, callibration records, test records
  History, documentation, user defined attributes
  Authentication and authorization of users
  Integraged with naming convention
  Relational Database (Postgres)
  Reports and exports
  API – java
  Restful interfaces
  1 million records
[3] ICS Configuration Database – Requirements v1.7, S.Gysin
[4] Evaluation of selected DISCS collaboration modules, M.Vitorovik

## Slide 6: CCDB Home screen

## Slide 7: Logical components (system)

## Slide 8: Physical devices

## Slide 9: Properties

## Slide 10: Cable Database
Scope: A database of cables and their connectors, and software tools to label the physical cables.
What is included:
  ICS is responsible for data of cables to and from the Control Boxes, MPS devices, and PSS devices.
  The software tools are available for use by all ESS for cable data.
Typical question the configuration database can answer are:
  Which devices are connected to port A of device SSSS-BBBB:DDDD-III ?
  How long is the cable connecting HBL-PBI:BPM-01a to its power supply.
Software requirements:
  Cable request form
  Standard cable list to choose from
  Import from spreadsheet
  Routing information
  Relational DB (Postgres)
  Web based GUI
  Search and reports
[5] Cabling Requirements, K.Rathsman

## Slide 11: Device Configuration Database DCDB
Scope: Stores the configuration files for the EPICS IOC’s and PLC interface
What is included:
  Version control and storage for EPICS configuration files and PLC interfaces
  Verifying ESS standards in the configuration files in the EPICS files
  Design and testing of files at remote sites
  Integration into the central database at Factory Acceptance Testing (FAT) and Site Acceptance Testing (SAT)
Strategy:
  Collaboration with TATA Consulting Services to:
  Adapt ITER’s SDD to be a generic open source tool to store device configuration
  Adapt ITER’s SDD to ESS

## Slide 12: SDD Translator generates all configuration files
SDN C++ program
EPICS records
EPICS IOC files
Generate config files
STEP-7 files

## Slide 13: Unit Conversion Database
Scope: magnet unit conversion, between engineering unit (Ampere), physics unit (Tesla), and model unit (K1, K2).
Candidates: DISCS unit conversion module (NSLS II)

## Slide 14: WU 3.1 Configuration Data Management
Scope: The collection, storage, and distribution of configuration data.[9]
[9] Work Unit Description document Configuration Data Management
Device Configuration Database (DCDB):
EPICS devices
Cable Database
Lattice Database
Virtual components
Controls Configuration Database (CCDB)
Physical components
Unit Conversion Database:

## Slide 15: WU 3.2 Control System Services
Provide the common software services to the users of the control system [10]
  A software service is software that benefits from having a single standard implementation. For example Role Based Access Control.
  Services can be combined by other software applications to provide the complete functionality of a large software application.
  The service includes the applications, application programmer interface, and repositories that provide the service.
  Includes Accelerator, Target, Instruments and Conventional Facilities
[10] Work Unit Description document Control System Services

## Slide 16: Archive, Alarms, and Logbook
ESS-CODAC package (based on ITER’s CODAC):
  CS Studio (EPICS control system studio)
  Operator Screen GUI builder (BOY)
  Short term archive/logging (BEAUTY)
  Logbook (Olog)
  Alarms Server (BEAST)

## Slide 17: Measuring Alarm Problems
EEMUA Guidelines
Plant statistics
  Before / after snapshots
  Donald Campbell Brown numbers
Classify alarm situation
  Average alarms per hour
  Max alarms per hour
  Percentage of hours with > 30 alarms
Plants classified in 5 categories
  Overloaded dangerous alarm revision, alarm shelving
  Reactive bad alarm revision, alarm shelving
  Stable regularly bad situations root cause analysis, state-based alarm priority
  Robust good root cause analysis, state-based alarm priority
  Predictive excellent root cause analysis
  ** Slide was Provided by GoalArt AB
Per hour | Max / hour | Percent | Classification
> 600 | > 6000 | > 50% | Overloaded
> 60 | > 6000 | > 25% | Reactive
> 6 | > 600 | > 5% | Stable
> 6 | > 60 | > 1% | Robust
< 6 | < 60 | < 1% | Predictive

## Slide 18: RBAC – Role Based Access Control
Role Based Access Control for EPICS IOC’s and control system applications
  Extend the design of LHC RBAC to EPICS and Applications
  Authentication service using LDAP
  RBAC database
  Authorization by roles/location/beam mode in the IOC server.
  RBAC is not IT security, it is a means to prevent mistakes by a well meaning user.
  DISCS collaboration: security module

## Slide 19: The RBAC database
Roles:
  Each role has a Role Manager
  The Role Manager assigns the users to the role
Resources:
  Each resource has an RBAC Resource Manager
  The Resource Manager defines the permissions and assigns the roles to the permissions
  Permissions paramters are: role, ip address, and machine state (regular expression

## Slide 20: Long Term Archive
Scope: PV archive for a longer time ( 30+ years?)
Smaller set of process variables, saved less frequently
Write once, read often, optimized for fast read (data warehouse technology)
Candidates:
  SLAC’s archive service
  CSS with Cassandra back end
Timeframe: 2Q 2016

## Slide 21: Save, Compare and Restore
Scope: Save machine settings, compare live values with saved values, restore saved values.
Features include
  a golden snapshot,
  grouping PV’s into snapshots,
  grouping snapshots into machine configurations,
  highlighting changed values and database storage of the information.
Candidates: MASAR
Timeline:
  Requirements are complete [6]
  Development has not started
  2Q 2016 – operational
[6] Save, Compare & Restore Requirements, S.Gysin

## Slide 22: Other Control System Services
Fast Data Acquisition
  Data on Demand:
    Archiving on a trigger from the timing system
  Post Mortem Support:
    Collecting the post mortem buffers and providing the tools for analysis
Diagnostic Logging Service
  Centralization of the diagnostic logs of distributed systems.
Directory Service
  Finds PV’s based on search criteria
  Candidate – Chanel Finder
EPICS Naming Service
  EPICS PV to IP address/TCP port mapping

## Slide 23: Other Control System Services
Video Service
  Live image stream from instrumentations
  How large are the images?
Maintenance Log
  log of preventive maintenance
Operations Logistics
  Beam statistics, run hours, shift summaries, down time, experiment schedules, reliability statistics and analysis.
Search Service
  Google like search on all ICS
On-line/Off-line Model Service
  Accelerator Modeling as a service, indpenedent of simulation software
Device Oriented Access Service
  Provide the ability to change an IOC/PV based on a higher level unit.

## Slide 24: WU 3.3 ESS Naming Convention
Scope: provides the tools, repositories and processes to generate meaningful and consistent names for devices
  Scope includes all of ESS
  Name database includes 1000 items now
  Definition of the naming syntax[7][8] : SSSS-BBBB:DDDD-III:TTTIIIXXX
  Tools:
    WEB GUI to generate a name for a device and let the user browse the names
    Database to keep track of the names and convention rules
[7]The ESS Naming Convention
[8] ESS Naming Convention, K. Rathsman

## Slide 25: Software Core Components
Thank you
DISCS

## Slide 26: References
[WP3 - 1] Lattice Database Requirements Document v1.1, S.Gysin
[WP3 - 2] Lattice Browser Requirements Document v1.0, S.Molloy
[WP3 - 3] ICS Configuration Database – Requirements v1.7, S.Gysin
[WP3 - 4] Evaluation of selected DISCS collaboration modules, M.Vitorovic
[WP3 - 5] Cabling Requirements, K.Rathsman
[WP3 - 6] Save, Compare & Restore Requirements, S.Gysin
[WP3 - 7] The ESS Naming Convention, K.Rathsman
[WP3 - 8] ESS Naming Convention, K. Rathsman
[WP3 - 9] Work Unit Description document “Configuration Data Management”
[WP3 - 10] Work Unit Description document “Control System Services”
[WP3 - 11] Work Unit Description document "Naming Convention"

## Slide 27: The Team
Name | Role | 
Suzanne Gysin (ESS) | Work Package Leader | 
Karin Ratsman (ESS) | Naming Convention Work Unit Leader Lattice Database Developer | 
Stephen Molloy (ESS – 25%) | Lattice Browser developer | 
Jakob Battelino (Cosylab) | Lattice Database and Naming tools developer | 
Jaka Bobnar (Cosylab) | RBAC lead developer | 
Miki Pavleski (Cosylab) | Development Environment and Cosylab’s Project Manager | 
Andraz Poznar (Cosylab) | Lattice Database developer | 
Miha Vitorovic (Cosylab) | Controls Configuration Database Lead |