## Slide 1: Control System Tools for Beam Commissioning
Timo Korhonen
Controls Division Chief Engineer
www.europeanspallationsource.se
April 8, 2014

## Slide 2: Outline
Early preparations for machine commissioning
What is needed at the early stages
Tools outline – (partly) early ideas
  EPICS
  Databases
  Application development

## Slide 3: Early stage requirements
Component-level controls
  EPICS infrastructure
  Engineering GUIs
Timing infrastructure
  Everything connected
  Repetition rate control
Machine protection
  Setting up machine modes
    Where should the beam go
  Beam modes
    Pulse length, intensity

## Slide 4: At start of commissioning...
Assume design model
  Verify step by step
Tools have to be
  Flexible : anticipate frequent changes
  Robust
    Avoid debugging several things at a time
  Simple
    Everybody is learning at this stage
Installation information should be available
  Where to find systems and components
Machine design easily accessible
  Lattice
  Comparisons with model

## Slide 5: Tools outline
Basic controls toolbox: EPICS
  Version 3 provides good low-level control tools
    Abstraction level is low, though
  Version 4 is becoming mature
    Introduced in machine operation at BNL, SLAC
    More about EPICS V 4 in later slides
Design and infrastructure information
  Databases in preparation
    Lattice
    Controls configuration
    Cabling
Logbook
  Electronic logbook from EPICS collaboration (oLog)

## Slide 6: Basic tools
EPICS provides tools for device contol
  CSS/BOY for writing device-level GUIs
  CSS integrates many other tools
    Alarm manager
    Trend display, archive viewer, etc.
  Can be extended with plugins
Archiving tool to be evaluated
  CSS/BEAUTY
    Not for high volume data
  SLAC Archiver Appliance
    High throughput, scalable
      Targets “millions” of channels
  Others? ...to be looked at

## Slide 7: EPICS version 4
EPICS version 3 is control-oriented
  Flat list of records
  No standard easy way to build applications
  Put together structures in a higher layer
    No (easy) guarantees of synchronizity
EPICS version 4
  Keep the low-level IOC (works well)
  Add capability to handle structured data
  New protocol supports some new access methods
    Query with parameters,put-get
    Plus the known put, get, monitor
  High performance
    Can also transport large datasets

## Slide 8: Why EPICS 4?
EPICS 4 makes writing applications easier
  With help of other infrastructure
    Databases
      Configuration, calibration, measurements
    Synchronous data services
      Pulse-to-pulse data
  Work with high-level concepts
    E.g. Orbit, Matrices (Twiss parameters, response matrix)
  Transparent access to different data sources with one interface (pvAccess)
    EPICS channels, databases, model services
  Straightforward access from e.g. Matlab and Python

## Slide 9: Databases for integration
Lattice database
  Contains devices that “touch the beam”
  Machine description for design
  Design is evolving, version 2 in preparation
  Source of lattice information for the online model
Controls Configuration Database
  Device level information
  What is connected to what, where it is located
Databases for calibration
  RF, magnet field maps, etc.
  Calibration data for instrumentation
  To be looked at, no ready solutions yet.

## Slide 10: System architecture with EPICS 4
Very generic application architecture diagram
  Access all data with a single interface, regardless of data source
  (CA: EPICS 3 protocol, PVA: EPICS 4 new protocol)

## Slide 11: SUMMARY
Concentrate first on making basic infrastructure robust
Collect configuration information during planning and construction phase into databases
  To be accessed online
Provide appropriate tools for the commissioning crew
  Flexible, allow for rapid changes
  Avoid complexity where not needed
  Machine protection has to catch risky situations
    Avoid costly mistakes
We are still in early phase
  A lot of work to be done, but we still have time to think through the issues properly

## Slide 12
Questions?