## Slide 1: experiences of Ion Source commissioning at CEA Saclay
Workshop ESS (Lund) / 2014-04-08
CEA SACLAY DSM/Irfu/SACM/LEDA
Tuske Olivier

## Slide 2: Summary
Ion source design and assembly
  Principle of ECR
  Design and techniques
2. Dos and Don’ts for Ion source characterization
  Magnetic measurements
  Vacuum & Electrostatic “formation” of electrodes
  Pressure, Plasma ignition / Tunning
  Current measurement
  Fraction / Proportion measurement
  EMU at source exit
  Long time run

## Slide 3: Ion source design
  Notion and Principle
  Design and technics

## Slide 4: Principle ECR
Magnetic shield
Insulator
High Voltage
Magnetic system
RF
Adap
RF Generator
Wave guide
2,45GHz
2.45GHz
Pulsé ou continu
Pcrète=2 kW
H2
D2
Adapted extraction system

## Slide 5: Simulations of heating zone magnetism + RF
Module Bz
Iso-Module Bz
Opera code
B1
B2
B1
B2
Magnetic simulation
RF simulation
 Design a geometry to concentrate energy at the « right » location.
BEAM
BEAM
HF
HF
2.45GHz
HF
CST

## Slide 6: Ions extraction  Potential + geometry + electrostatic
25 mrad
rf=10 mm
AXCEL code
Opera code

## Slide 7: Ion Source developped at CEA Saclay
Projet /Source | High Voltage | Current | Magnetique Configuration
SILHI  IPHI | 100kV | 100mA H+ | Coils
IFMIF EVEDA | 100kV | 140mA D+ | Coils
SPIRAL2 | 20kV 40kV | 5mA H+ 5mA D+ | Permanent Magnets
ALISES | 40kV 100kV | 15mA Not yet tested | Coils
SILAP-1 | 40kV | 30mA / 60mA | Permanent Magnets
SILHI2 | 50kV | 40mA | Permanent Magnets
IFMIF-1
SILAP-1
SP2

## Slide 8: SILHI Source
 Beam Extraction (10 kW)
Deuteron beam
AXCEL CODE
Magnetic and electrostatic calculations
Opera CODE
Source working since years

## Slide 9: IFMIF Injector at Saclay
OPERA 3D CODE
AXCEL CODE
Source delivered in Rokkasho

## Slide 10: SPIRAL2 injector at Saclay
Source delivered at GANIL in Caen

## Slide 11: Technic to be mastered
 Magnetic, thermal and electrostatic calculations
 Materials
 Beam Extraction
 Control system
 RF injection and coupling
 HV Technic
 EMC

## Slide 12: Ion source characterization during commissioning
  Magnetic measurements
  Vacuum & Electrostatic “formation” of electrodes
  Pressure, Plasma ignition / Tunning
  Current measurement
  Fraction / Proportion measurement
  EMU at source exit
  Reliability run

## Slide 13: Setup up for source commissioning  Magnetic measurements
Ion
source
Diag Chamber
Pumping
Beam Stop
DIAG
BEAM
HF
Before vacuum,
generate the magnetic field with theoretical values obtained with Opera code
check the position of the 875 Gauss iso-surface with a gaussmeter inside the source at the RF injection point
For easy plasma ignition

## Slide 14: Setup up for source commissioning  Vacuum & electrostatic formation of electrodes
With the pumping system on, without and with gas injection :
Formation of GAP1: Puller electrode connect to ground potential
Formation of GAP2: Puller electrode connect to HV potential
Ion
source
Diag Chamber
Pumping
Beam Stop
DIAG
GAP1
GAP2
Get rid of all the electrods surface imperfections for drastic reduction of sparks rate

## Slide 15: Setup up for source commissioning  Gas injection, Plasma Ignition & tunning (2)
Sometimes
Fringe field B and E field can be orthogonal !
On ALISES ion source Penning discharge forbade us to bias more than 17kV
Opera code has been used to simulate electron trapping in the accelerating column
PhD thesis S. Nyckees
Experimental Test
Simulation validation
Simulations
 This simulation is now use where design is realized before realization

## Slide 16: Setup up for source commissioning  Gas injection, Plasma Ignition & tunning (1)
Gas injection, pressure in the Diag Chamber must around 1 or 2.10-5 mbar for one day before starting RF in order to “fill up” the BNi plates inside the source chamber.
RF in Pulse mode for plasma ignition 250 ms at 1 Hz
Shift to CW and put the Automatic tuning for the lowest RF reflected power
Tune the magnetic coil value at RF injection
Ion
source
Diag Chamber
Pumping
Beam Stop
DIAG
Preparation of the plasma chamber
First BEAM
OK
boss
Not OK

## Slide 17: Setup up for source commissioning  current measurement
Compare the HV power supply drain current vs the collected Beam Stop current
Tune the source for reducing
  the noise of the extracted current
  and the current rise time
by changing gas, magnetic values and RF adaptation
Ion
source
Diag Chamber
Pumping
Beam Stop
DIAG
The sharper is the rise the more stable will be the source

## Slide 18: Setup up for source commissioning  proton and ion fraction
Measure the proportion of proton in the beam.
To increase proton fraction :
the gas, RF reflected power, magnetic field
Ion
source
Diag Chamber
Pumping
Beam Stop
Wien Filter
Or
Doppler shift
Reduce the beam loss due to molecular ions
Halbach magnetic structure
(FAIR project)
Wave-length (nm)
D (res. gas)
D (D3+)
D (D2+)
D (D+)
Species fractions obtained with Doppler shift method for pulsed beam at 50% duty cycle
θ

## Slide 19: Setup up for source commissioning  emu
Get the beam divergence, beam profile at source exit in horizontal and vertical
Ion
source
Diag Chamber
Pumping
Beam stop
EMU
Real Twiss parameter for LEBT simulation
Allison scanner
(IFMIF project)

## Slide 20: Setup up for source commissioning  Long time run
Estimate the spark rate and if the source stops when sparks occur
Also test specific high level program : feed-back on the extracted measured current intensity that change the RF power
Ion
source
Diag Chamber
Pumping
Beam stop
DIAG
Control the source stability with more accuracy to compensate the temperature drift and other long time effect

## Slide 21: Setup up for source commissioning  Long time run (SPIRAL2)
A : 14h59 Start the long run 5.1mA and 0.2mA regulation
B : 9:11 regulation @ 5mA with delta 0.05mA  regulation more drastic
C : 19:14 10ms short electrical distribution failure at CEA  it stops the RF generator, the High level program restart the source
D : 00:59 100ms stops on the phase2 of electrical distribution  it stops the current power supplies of the line
E : restart @9:51.
F : 17 :23 Q14 power supplies fails again (as usual!)
G : 11 :53 Q14 again
H : 13:17 Q14 again  stop the long test run
A
B
C
D
E
F
G
H

## Slide 22: ConclusionS
Source commissioning is an important step !
And it is usually made too quickly because of lack of time.
Start with Source + small diag chamber as B. Cheymol recommended it (24 Fev 2014)
Better to take some time for measurements to be able to confront them with early simulations and adjust next simulations for the LEBT start/commissioning.
Robust Diagnostic are NEEDED and already calibrated ! And not calibrate the diagnostic with the new ion source
Source must work as much as possible (pulsed “plasma mode” when not using it)
Vacuum break only with Nitrogen to avoid BNi pollution.
WHAT | W1 | W2 |  | W3 |  | W4 | W5++
Electrical field + vacuum |  |  |  |  |  |  | 
Current optimization |  |  |  |  |  |  | 
Doppler measurements |  |  |  |  |  |  | 
EMU measurements |  |  |  |  |  |  | 
Long run |  |  |  |  |  |  | 
Alice Wonderland
Schedule in
a ideal world