## Slide 1: Commissioning of the A2T: DC and AC Magnet Systems
Heine Dølrath Thomsen, ISA, Aarhus University

## Slide 2: HEBT Layout (4 deg ACH)
UHB, 15 periods
EWU with quadrupole doublet
ACH
A2T
128 m
10 RMS, X, Y,
DUMP

## Slide 3: Assumptions
MAGNETS:
All magnet polarities have been verified after installation in tunnel
Quadrupoles have auxillary coils to generate a dipole corrector field (1D).
  Separate correctors in the A2T though…
BPMs in immediate vicinity of almost every quad
BEAM:
Low-power beam mode available, 1 Hz x < 10 microsec ~ kW avg. power
Beam-based alignment is applied to correct the beam centroid
Beam parameters at the SCL exit are roughly known (beam stops & dump).

## Slide 4: Accelerator-to-Target (a2T)

## Slide 5: Raster Pattern
x,y [arb. units]
One pattern cycle
fy / fx = 5:4
fw ~ 40 kHz, Tp-p = 12.5 us (w = x,y)
Max(∆x) ~ 90 mm, max(∆y) = 16 mm,
RMS(x-∆x) = 12.6 mm, RMS(y-∆y) = 6.3 mm
Notes: 113/83

## Slide 6: Beam Optics: LANL MTS Concept (B. Blind et al)
ACH
Matching Q’s
AP
CO
Target
A2T
RMs
CO Q’s

## Slide 7: ‘Raster25’
ACH
By By Bx Bx | Bx Bx By By
AP
A2T
QP1-4
QP5,6
2.0 GeV: Bx = ±1.96 mT.m, By = ±2.28 mT.m, ±5 mT.m
PBW
BEW
Centroid
10 x RMS beamlet
RMs
CO

## Slide 8: A2T Commissioning: DC optics

## Slide 9: How to Tune Your DC A2T: 1/3
Condition | Measure | Scan | Adjust | BI Resolution
R12,AP-CO = 0 R34,AP-CO = 0 | Apparent CO location; deduced from BPMs near CO + dedicated BPM near target | DC raster corrector pair | QP5-6 | CO: ~0.5 mm M: ~2 mm
CO
AP

## Slide 10: How to Tune Your DC A2T: 2/3
Condition | Measure | Scan | Adjust | BI Resolution
Beam size @ CO | Wire scanner @ AP: + QP5-6 size magnification (0.22 & 1.1) | --- | QP1-4 | 0.1 mm
Beam size @ Target | Wire scanner @ PBW |  |  | TBD
CO
AP

## Slide 11: How to Tune Your DC A2T: 3/3
Condition | Measure | Scan | Adjust | BI Resolution
Max. deflection at target | CO BPMs + Monolith BPM | DC raster corrector pair | --- | CO: ~0.5 mm M: ~2 mm
 |  |  |  | 1 mm, (3 mm accuracy)
 | Target imaging system |  |  | 
CO
AP

## Slide 12: A2T Commissioning: AC optics

## Slide 13: Modulator: DC supply (V0w) + H-bridge
doi: 10.1016/j.nima.2004.09.034
fw: clock (memory array)
Slope: V0w, (L/R)
aw: slope / 4fw
Notes: Switching times tabulated in 2D memory array

## Slide 14: Checking the Raster Pattern
40 kHz: 0-aw in 6.25 us
Magnification is verified with DC correctors
Raster pattern is cyclic:
  Short beam pulses
  RM deflection: dedicated BPM (1 us interval)
  ϕx += δt, ϕy += δt
  Shot-to-shot consistency
Increase pulse length and check intensity profiles
Notes: Beam sweep waveform

## Slide 15: Jmax @ Target (BEW)
Notes: Coating: 2% amplitude resolution

## Slide 16: Commissioning the A2T
DC Elements
2 x 2 (XY corrector + BPMs)
6 quadrupoles
  2 x CO quads: R12 + R34, (BPMs)
  4 x Matching quads: Beam sizes at CO (profile monitor, indirectly) and target (thermolum. coating)
  Check angular magnification
AC Elements
8 x RMs (2 families)
DOFs: fw[2], ϕxw[2], V0w[8] (fx, fy, V0x, V0y)
Beam sweep waveforms can be sampled with short bunches (dedicated BPMs)
Shot-to-shot reproducibility

## Slide 17: Extra slides

## Slide 18: Commissioning An Achromat
30 MeV detuning in 5 steps
Condition | Measurable quantity | Scan? | Adjust | BI Resolution
R26,ACH = 0 ϕy,ACH = 2π | Δy = R26,ACH x dp/p | Final SCL cavity, dp/p = 1.2% | Ach. quads | 0.5 mm (ση~50 mm)
 | Δy, R34 = sqrt(β1β2)sin(ϕy) | Corrector kick |  | 
ACH

## Slide 19: A History of Beam Expander Systems…
200 mm
160 mm
140 mm
By
x
By
x
fraster ~40 kHz
By
x
Suitable for CW or long-pulse machines
Linear focusing and pattern is decoupled
Non-linear DC field distorts phase space and focuses tails
Complex tuning
Overfocusing of halo
Dodecapole comp.: overfocusing is neutralized
SFM: cheap magnet?

## Slide 20: Hardware

## Slide 21: Magnets: EWU Quads
Laminated:
  Scans & tuning less time consuming
  Cheapest solution, given the quantities (N > 20)
  Longer versions? Add laminates + change coils!
Magnetic shield
Technology study:
    DC-powered:
      Off the shelf power supplies
      Limited resistive losses (low J)
  Pulsed operation?
    Expensive power supplies (10x) with limited benefit
Notes: Longer versions?

## Slide 22: Raster System
Raster magnets:
  Window frame ferrite yoke
  Cu windings (air-cooled)
  Ceramic pipe, Ø80 mm
  NI = 4 x 340 A (peak)
  ± 5 mT.m peak field
IGBT-based H-bridge
200 mm
160 mm
140 mm

## Slide 23: Hardware
Detailed studies: Impact of non-ideal waveforms

## Slide 24: HEBT: 4 Principal Sections
Upgrade High Beta (UHB)
  Contingency towards unexpectedly poor SC linac performance: extra HB cavities can be installed!
  Transport section being mechanically identical to the MB+HB linac (apart from cryomodules, etc.)
  Adjustable collimators (would be excluded by upgrade)
Achromat (ACH)
  4.5 m vertical shift of the beam from linac to target level
  Reduce dispersive effects
Accelerator to Target (A2T)
  Reduce the beam peak intensity on the target (BEW) and proton beam window (PBW), cooling + radiation damage.
  Strong requirements for the beam on PBW + BEW (several zones defined for each element)
Beam Dump Line (DMPL)
  Dispose pilot beam during tuning of the linac.
  Up to nominal beam energy x low duty cycle => 50 kW (7.5 kW avg. beam power, passively cooled)
  Insensitive to energy fluctuations (in line of sight with linac)

## Slide 25: Contingency Region ~ HB Linac
C
M
R
ACH