## Slide 1: Structure and Operation of the Collimator System in J-PARC 3-50BT Line
Including:
J-PARC and 3-50BT
Required specifications
Design and structure of collimators
Operation
Estimation of the residual radiation
M. Shirakata
KEK(J-PARC), Japan
Lund, 13/05/2014

## Slide 2
Neutrino beams to SK
JFY 2009
50GeV ＭＲ
Hadron experimental hall
MLF
JFY 2008
3GeV RCS
JFY 2006 / 2007
Linac
3-50BT
J-PARC Site View
Japan Proton Accelerator Research Complex
120km from Tokyo

## Slide 3: 3-50 Beam Transport Line
Pulsed bending magnet
BT collimators
Length 230 m
Dipole 1 (pb), 3 (h), 2 (v)
Quadrupole 38
Steering 14
Collimator 12 units (120 - 54 p mm mrad)
Monitor
BPM / MRPM / OTR 17 / 10 / 1
FCT / BLM 5 / 50
Slope section
3NBT
3-50BT
50mrad downwards

## Slide 4
Required Specifications
Purpose: MR protection
Particle: proton
Beam energy: 3 GeV
Allowed beam emittance: 216 p mm mrad
(full, before the collimator area)
Collimator range: 120 to 54 p mm mrad
                for transverse only
Allowed beam loss: 450W/unit and 2kW/12 units
Number of installable space: 6
Drift Length: 3,300 mm for two collimators
High availability (Do not be broken)
Maintenance ability (Accessibility)

## Slide 5: Optics of Collimator System
QDS1
QFS1
QFS2
QFS3
QDS2
QDS3
QDB1
One unit has a pair of jaws: single unit can collimate both H and V planes.
Unit 1 and 2 make one collimator set: The center and span are adjustable.
Two hexagonal halo rejection systems (set 1,3,5 and set 2,4,6)
Distance in 3-50BT line [m]
Phase advance [rad]
Vertical
Horizontal
Layout of 3-50BT collimator units
120 deg
rotation
Peel the both sides in one collimator set
beam core
halo
Schematic view of the hexagonal halo rejection
A pair jaws in almost middle of drift space
QDS1 to QDS2 120 deg. (2.094 rad) phase advance both in horiz. and vert. planes
Collimator units (6 sets)
Jaw
120 deg
rotation
Radiation
shield

## Slide 6
Technical choise
No machine in vacuum for high availability
Movable block style of jaws, beam duct and radiation shield (The weight of moving block is up to 10 t)
All drive mechanism is put out of the radiation shield for protection
Horizontal jaw
Ti pipes
Fe shield
bellow-pipe-bellow joint structure
(used in the beam mask of KEK-B)
One duct goes through two units.
Bellow-pipe-bellow joint allows large duct shift over 10 mm.
Gear jack and linear motion(LM) guide are used in order to make the precise adjust system of heavy blocks.
Vertical jaw
Range： ±10 mm
Structure of Collimator Duct

## Slide 7
Example of beam collimation
Layout of the jaw locations of the required apertures
In order to achieve them, the beam duct including the jaws should be moved ±10 mm.
In case of collimator unit-11

## Slide 8
Collimator Jaw
Collimator jaws are made of Tantalum. The jaw is bonded by hot isostatic pressing method (HIP)
Jaw block piece
Collimator duct
Jaw-2 behind jaw-1
Jaw-1
Ti
Ta
Notice:
We also used tungsten in MR collimators

## Slide 9
Tensile Strength of HIP between Ti and Ta
test piece
405℃
Tantalum
Titanium
Titanium
Thermo couple
Test pieces are made of the jaw sample.
cut to the specified diameter
Higher than TIG welding at the duct making

## Slide 10
Ta
Ti-2
Yamanashi Industrial
Technology Center
Test piece： Ti-Ta HIP
Env. temp： 22℃
Env. humidity： 20%RH
Test type： tensile
Full load cell： 5000 kgf
Full extension： 10 mm
velocity： 2 mm/min
Extension [mm]
Load [N]
Break at 965 kgf
Strength = 19.2 kg/mm^2

## Slide 11
Unit-1
Unit-2
The collimator set
For example:
When the first unit has jaws at up and right, the second unit has ones at down and left.
50 cm

## Slide 12
Collimator duct is 3,300 mm long.
It is located through two collimator units.

## Slide 13
Heat sink (Cu) at jaw position
Jaws are cooled from outside of beam duct by water.

## Slide 14
LM guide for
horizontal motion
Gear jack for
Vertical motion
Jaw Position Shifter
Span: ±12 mm (14 mm)
The grease was exchanged for what has strong tolerance for radiation.

## Slide 15
Installation of Collimators
The central blocks of two units are joined and carried as one part by 10 t crane.
It is removable when something became wrong.

## Slide 16
Continued
Additional shields are installed at the front and top positions.
The weight is limited by the crane. The thickness of the shield of central block become 30 cm.

## Slide 17
Chart: 
| -8070 | -6020 | -4000 | -2100
01UR | 1.3 | 0.51 | 0.18 | 0.051
02DL | 9.1 | 3.5 | 0.91 | 0.44 | 0.22
Chart: 
| -6030 | -7070 | -8010 | -4060
07UL | 0.73 | 1.51 | 2.73 | 0.091
08DR | 0.092 | 0.41 | 1.35 | 2.55
Chart: 
| -6010 | -5000 | -3990 | -3000
11UL | 1.7 | 0.72 | 0.34 | 0.16
12DR | 3.9 | 1.42 | 0.43 | 0.07
Chart: 
| -6020 | -10030 | -10990 | -11990 | -12860
03UL | 0 | 0.077 | 0.39 | 1.53 | 3.74
04DR | 0 | 0 | 0.007
Chart: 
| -5980 | -10180 | -11050 | -12600
05UR | 0 | 0.017 | 0.095 | 0.27
06DL | 0.064 | 0.72 | 4.2 | 1.66
Chart: 
| -13250 | -12030 | -11060
09UR | 0.53 | 0.19 | 0.068
10DL | 0.18 | 0.57 | 1.64 | 7.5
Calibration of Collimator Position by AIC Monitor
The AIC (Air Ionization Chamber) monitor covers the collimator area. Beam loss measured by long AIC monitor is plotted , inserting collimators. The beam size is not large. Some units are used in the edge of the range.
The balanced unit positions are calculated based on these data.
Vertical plane
Jaw position [x0.001 mm]
misalignment?

## Slide 18
Six collimator sets
are located here!
Loss monitor signal with the typical operation
09/05/2014
Beam Losses by Collimator Jaws
Measured beam loss with 2.8 x 10^13 protons/batch beam
(equivalent to 213kW in Main ring)

## Slide 19
ZX-plane cross section
Ta
Fe
Assuming 500 W loss
2009 5/25
M. Hagiwara
Residual Radiation Estimation for the Hands-on-maintenance

## Slide 20
YX-plane cross section
Evaluation point 3 to 8
Ta
Fe
EP-1
EP-9
50 cm

## Slide 21
RESIDUAL DOSE RATE (mSv/hr) IN A TISSUE-EQUIVALENT BODY ON CONTACT WITH MATERIAL IM = 1 VOLUME= 1.75000E+02 CM^3
AT AINT = 1.000E+12 P/SEC
**********************************************************************************************
IRRADIATION TIME = 1/2d 1day 5days 30days 100days 1yr 20yr
Tcool Tcool (sec)
1sec 1.000E+00 5.252E+04 6.311E+04 7.194E+04 8.379E+04 8.587E+04 8.817E+04 9.163E+04
1min 6.000E+01 4.971E+04 6.029E+04 6.910E+04 8.096E+04 8.304E+04 8.534E+04 8.881E+04
10min 6.000E+02 4.009E+04 5.057E+04 5.926E+04 7.115E+04 7.322E+04 7.553E+04 7.899E+04
0.5hr 1.800E+03 3.222E+04 4.251E+04 5.103E+04 6.288E+04 6.494E+04 6.725E+04 7.072E+04
1hr 3.600E+03 2.700E+04 3.701E+04 4.533E+04 5.708E+04 5.913E+04 6.145E+04 6.491E+04
2hr 7.200E+03 2.209E+04 3.154E+04 3.955E+04 5.105E+04 5.309E+04 5.541E+04 5.888E+04
4hr 1.440E+04 1.768E+04 2.604E+04 3.349E+04 4.440E+04 4.644E+04 4.877E+04 5.225E+04
6hr 2.160E+04 1.537E+04 2.298E+04 3.001E+04 4.045E+04 4.247E+04 4.480E+04 4.828E+04
12hr 4.320E+04 1.059E+04 1.625E+04 2.215E+04 3.129E+04 3.329E+04 3.565E+04 3.911E+04
1day 8.640E+04 5.661E+03 9.092E+03 1.341E+04 2.072E+04 2.266E+04 2.506E+04 2.852E+04
2days 1.728E+05 2.297E+03 3.947E+03 6.516E+03 1.167E+04 1.352E+04 1.597E+04 1.943E+04
7days 6.048E+05 2.356E+02 4.368E+02 1.049E+03 2.862E+03 4.397E+03 7.005E+03 1.043E+04
30days 2.592E+06 2.086E+01 4.144E+01 1.820E+02 9.459E+02 2.013E+03 4.534E+03 7.843E+03
0.5yr 1.577E+07 5.603E+00 1.119E+01 5.423E+01 3.141E+02 8.059E+02 2.220E+03 4.914E+03
1yr 3.154E+07 2.755E+00 5.505E+00 2.695E+01 1.580E+02 4.390E+02 1.318E+03 3.501E+03
2yr 6.307E+07 1.240E+00 2.478E+00 1.226E+01 7.275E+01 2.192E+02 7.176E+02 2.210E+03
5yr 1.577E+08 3.694E-01 7.386E-01 3.668E+00 2.184E+01 6.731E+01 2.259E+02 7.361E+02
10yr 3.154E+08 6.182E-02 1.236E-01 6.141E-01 3.658E+00 1.134E+01 3.825E+01 1.417E+02
20yr 6.307E+08 5.110E-03 1.022E-02 5.098E-02 3.051E-01 9.923E-01 3.527E+00 2.713E+01
30yr 9.461E+08 2.934E-03 5.867E-03 2.932E-02 1.759E-01 5.826E-01 2.112E+00 1.934E+01
Residual Radiation of Jaws

## Slide 22
RESIDUAL DOSE RATE (mSv/hr) IN A TISSUE-EQUIVALENT BODY ON CONTACT WITH MATERIAL IM = 3 VOLUME= 2.00000E+02 CM^3
AT AINT = 1.000E+12 P/SEC
**********************************************************************************************
IRRADIATION TIME = 1/2d 1day 5days 30days 100days 1yr 20yr
Tcool Tcool (sec)
1sec 1.000E+00 4.038E+00 4.274E+00 5.053E+00 6.150E+00 6.962E+00 7.957E+00 9.117E+00
1min 6.000E+01 3.747E+00 3.983E+00 4.753E+00 5.859E+00 6.668E+00 7.666E+00 8.825E+00
10min 6.000E+02 3.108E+00 3.340E+00 4.086E+00 5.215E+00 6.016E+00 7.021E+00 8.180E+00
0.5hr 1.800E+03 2.494E+00 2.719E+00 3.433E+00 4.590E+00 5.382E+00 6.395E+00 7.554E+00
1hr 3.600E+03 1.979E+00 2.192E+00 2.872E+00 4.058E+00 4.843E+00 5.864E+00 7.021E+00
2hr 7.200E+03 1.419E+00 1.615E+00 2.246E+00 3.469E+00 4.244E+00 5.275E+00 6.432E+00
4hr 1.440E+04 8.340E-01 1.004E+00 1.579E+00 2.847E+00 3.611E+00 4.663E+00 5.825E+00
6hr 2.160E+04 5.745E-01 7.268E-01 1.261E+00 2.542E+00 3.290E+00 4.344E+00 5.501E+00
12hr 4.320E+04 2.363E-01 3.607E-01 8.217E-01 2.124E+00 2.839E+00 3.920E+00 5.077E+00
1day 8.640E+04 1.244E-01 2.262E-01 6.185E-01 1.898E+00 2.586E+00 3.686E+00 4.841E+00
2days 1.728E+05 8.900E-02 1.690E-01 5.017E-01 1.692E+00 2.363E+00 3.462E+00 4.615E+00
7days 6.048E+05 4.524E-02 8.835E-02 2.964E-01 1.146E+00 1.754E+00 2.836E+00 3.976E+00
30days 2.592E+06 1.074E-02 2.128E-02 8.815E-02 4.300E-01 8.716E-01 1.883E+00 2.964E+00
0.5yr 1.577E+07 2.221E-03 4.439E-03 2.171E-02 1.271E-01 3.457E-01 1.015E+00 1.783E+00
1yr 3.154E+07 1.322E-03 2.641E-03 1.298E-02 7.641E-02 2.133E-01 6.435E-01 1.158E+00
2yr 6.307E+07 5.623E-04 1.124E-03 5.534E-03 3.264E-02 9.210E-02 2.810E-01 5.143E-01
5yr 1.577E+08 5.024E-05 1.004E-04 4.948E-04 2.920E-03 8.278E-03 2.538E-02 5.172E-02
10yr 3.154E+08 1.721E-06 3.440E-06 1.707E-05 1.016E-04 3.127E-04 1.049E-03 6.575E-03
20yr 6.307E+08 6.897E-07 1.380E-06 6.897E-06 4.137E-05 1.374E-04 4.995E-04 4.862E-03
30yr 9.461E+08 5.937E-07 1.187E-06 5.936E-06 3.560E-05 1.183E-04 4.303E-04 4.209E-03
Residual Radiation on the surface of 50 cm Iron
Equivalent to the EP1 extraction BL of KEK-PS: 800 mSv/h with 400W loss

## Slide 23
Residual Radiation after the Installation of Gate-type Shield in 2010
In 2010, the radiation shield was upgraded according to the increase of total loss:
450W  2kW, because there is a public road above the collimator area.
The gate-type shield was installed in order to protect the above public road. The shield consists of 19 shield blocks which can be moved along the LM railway. The shield can be opened for the maintenance of quadrupole magnets, collimator units, beam monitors, and so on.
After the installation of the shield, the residual radiation over 500mSv/h was observed 4 hours later from the beam stop though the total beam loss at the collimator was about only 80W. The radiation is highest on the wall of the tunnel. On the other hand, the radiations were almost same inside and outside of the shield??? That’s under investigation.
Mystery?
Highest
Same level