## Slide 1
Shielding calculation for ESS accelerator
Lali Tchelidze
TAC meeting
April 2, 2014

## Slide 2: A bit of history
Earth berm shielding was initially calculated based on maximum 1 W/m beam loss limit.
  Also, shielding towards the klystron gallery and all personal and equipment access routes was calculated based on this beam loss limit.
No agreed accidents were included in the calculations.

## Slide 3: November 2013 Review
Recommendations related to beam loss and shielding :
”Basic assumption of 1 W/m used for shielding calculations needs to be confirmed by realistic end-to-end beam simulations, showing sufficient margin. Normal operations scenario should include beam loss scenarios.”
“Accidental beam loss: need to establish “worst case” scenarios based on risk analysis and to conduct simulations to determine appropriate shielding and system interlocks for personnel protection.”

## Slide 4: Plan to follow recommendations
Assign beam spill limits to existing event classes H1 – H5 (normal operations – incidents of various types)
  ESS-0008309 “Beam Spill Limits for Various Event Classes”.
  ESS-0008351 “Hands-on Maintenance Conditions at ESS Accelerator”.
    Both documents reviewed and approved at SAG.
    Next/final step – get an approval at EPG.
Verify that shielding is sufficient for all possible loss scenarios.
  Verify that shielding is sufficient for normal operations 1 W/m plus additional short-term beam loss cases as/if defined in the previous item (include both realistic and simplified geometry models).
  Technical note ESS-0007143 “ESS Linac Shielding Strategy and Calculations” – reviewed and approved internally and externally (March, 2013). A follow up version due by May, 2014.

## Slide 5: Agenda
Beam spill limits.
Shielding calculations.
  Earth berm shielding.
  Shielding towards the klystron building.
  Etc.

## Slide 6: Event classes at ESS
Classification of event likelihood and corresponding exposure limits to radiation workers at ESS:

## Slide 7: Normal operation H1
In high intensity proton accelerators the residual activity is a dominant source for exposing personnel. Tolerable beam losses are driven by requirements for activation/hands-on maintenance limits.
Adopt 1 W/m (SNS specification above 100 MeV)
  dose rates below ~1 mSv/h measured at 30 cm from component surface.
Calculations and experimental measurements for various facilities at Oak Ridge, Los Alamos and Fermilab verified the validity of 1 W/m limit.
Residual activation is machine dependent, but not to the first approximation.
1.1 mSv/h
At 30 cm
1 W/m
1 GeV protons on beam pipe/bulk copper
100 days/4 hours.
FLUKA simulations from I. Strasik et al., Phys. Rev. ST AB 13, 2010.

## Slide 8: Hands on maintenance limits elsewhere
According to U.S. radiation regulations, if the ambient dose equivalent rate (a conservative estimate), which is according to International Commission on Radiation Units and Measurements, is below 1 mSv/h, the high radiation area classification can be avoided [15]. Assessment of ambient equivalent dose rate is commonly done for 100 days of irradiation and 4 hours after shutdown, at 30 cm from any component surface [16, 17]. The following access allowance is used (see Table 1) [18]. An additional criterion can exist, limiting the average residual dose rates at 30 cm from all components to 0.1 – 0.2 mSv/h [16].
According to German Radiation Protection Ordinance, areas with ambient dose equivalent rate below 3 mSv/h are classified as radiation controlled areas and “hands-on” maintenance is still allowed under specially defined conditions [19].

## Slide 9: Anticipated events H2
Adopt 30 MJ beam spill.
  A burn through at LANSCE at 800 MeV proton coupled cavity linac occurred with an estimated 40 J of beam spill.
  At PSI, at 600 MeV proton beam experience showed that leak at vacuum seal occurred at deposited energies of 30 kJ.
  TJNAF (Thomas Jefferson National Accelerator Facility), 10 MJ energy spill.
  No spill events greater than 30 MJ were identified!
  Proton driver - ~ 1.7 MJ of credible accident was considered.
  Currently, the Fermilab Radiological Control Manual (FRCM) requires that the machine designers describe and justify what a possible “credible worst case accident” is, and design the shielding—or modify operation of the machine—accordingly.

## Slide 10: Unanticipated events and DBA H3 & H4
ESS (Accelerator) |  | 
Event | Beam spill limit | Exposure limit
Unanticipated even | 150 MJ | 50 mSv
Design Basis Accident | 600 MJ | 50 mSv

## Slide 11: Beam Spill Limits Summary
Comparing
  LANSCE at 1.7 mSv/MJ
  TRIUMF at 2.2 mSv/MJ
  SLAC at 0.6 mSv/MJ
  ESS at 0.08 mSv/MJ.
Frequency (1/y) | Name | Description | Exposure limit
> 1 | Normal operation | 1 W/m | 10 mSv/y
10-2 – 1 | Anticipated events | 30 MJ/event | 20 mSv/event
10-4 – 10-2 | Unanticipated events | 150 MJ/event | 50 mSv/event
10-6 – 10-4 | Design basis accident (DBA) | 600 MJ/event | 50 mSv/event
< 10-6 | Beyond DBA | - | -

## Slide 12: Accident duration as a function of lost beam power

## Slide 13: Shielding calculations Analytical approach
Analytical calculations: lateral shielding for 1 W/m beam loss.
  H_0 is a source term, representing
  a dose equivalent per interacting
  proton, at 1 m from the interaction
  point and no attenuation = 0.4 Sv/h
  λ is a hadron attenuation
  mean free path
  t is a thickness of a shield
  R is a distance from beam
  loss to outside of the shield.
3.91 m earth berm (no safety factor)
ESS-0007143

## Slide 14: Shielding calculations Monte-Carlo (MARS) simulations
Geometry includes:
  Linac tunnel, tunnel walls and earth berm around it.
  Klystron gallery building.
  Waveguide penetrations.
  Cable penetrations.
  Personal emergency exits.
  HEBT loading bay.
  Smoke evacuations.
  Alignment penetrations.
  Cryogenic transfer line.
Source term: Beam energy 5 MeV –
2 GeV, 1 W/m on a beam pipe.
ESS-0007143

## Slide 15: Earth berm thickness Normal Operation
5 m earth berm
Max 8 μSv/h
(no safety factor)
450 m section of Linac.
Energy 5 MeV – 2 GeV.
1 W/m beam loss upwards at shallow angle on a 2 mm stainless steel beam pipe.
70 cm concrete roof on top of linac, 50 cm concrete walls on the sides.
ESS-0007143

## Slide 16: Earth berm thickness Why MARS more conservative?
The source term used in MARS is ~ 10 times higher than that given by “Sullivan”!
Reason: it was agreed that the first calculations should be done in a conservative way:
  Losses are simulated upwards.
  Losses are simulated on thin beam pipe (no realistic accelerator components were considered at the point)
Next: redo calculations for realistic accelerator model – ongoing! Due by May, 2014 (next review)!
ESS-0007143

## Slide 17: Ongoing work and some preliminary results
Linac layout updated based on new lattice (Optimus +)
Energy as a function of location – updated based on new lattice.
1 W/m beam loss simulated uniformly around the beam pipe.
SCL geometry model including spoke/elliptical cryomodules and quadrupole magnets almost complete.
Warm linac model – ongoing.
DET (mSv/h) Side view across the tunnel.
Left: 2 mm stainless steel
Right: 20 cm copper
A factor of 5-10 less total dose equivalent outside of berm shielding.

## Slide 18: Neutron flux on top of berm
ESS-0007143

## Slide 19: Shielding towards klystron gallery
450 m section of Linac.
Energy 5 MeV – 2 GeV.
1 W/m beam loss upwards at shallow angle on a 2 mm stainless steel beam pipe.
7 meters between the outside wall of linac tunnel klystron gallery outside wall.
ESS-0007143

## Slide 20: Shielding towards klystron gallery
< 0.1 µSv/h with no penetrations!
ESS-0007143

## Slide 21: RF waveguide penetrations Stubs
DET (mSv/h) Top view at ground level
DET (mSv/h) Top view at 1 m
DET (mSv/h) Top view at 2 m
ESS-0007143

## Slide 22: RF waveguide penetrations Stubs
Max 54 µSv/h
Additional shielding block is required!
ESS-0007143

## Slide 23: Skyshine
Close to public limit (3.4 nSv/h) at the site boundary.
Possibility to increase thickness of berm exists.
Skyshine radiation around ESS site
(contribution from the linac, excluding the A2T)
ESS-0007143

## Slide 24: Accidents
Point beam loss is considered:
“Sullivan” – 0.31 Sv/h maximum total dose equivalent rate outside of berm (for Full Beam Loss at 5 MW).
With 600 MJ DBA beam spill limit - > ~ 10 mSv (limit is 50 mSv).
MARS calculations – ongoing – due by May, 2014.
5 MW of beam lost in s single point, upwards, at 2 GeV.
DET (mSv/h) Side view across a linac section ->

## Slide 25: Other items
ESS-0007143

## Slide 26: Other items Cryogenic Transfer Line
No elevated dose rate in the klystron gallery.
ESS-0008240

## Slide 27: Other items Cable penetrations
Two adjacent openings with 1.2 m x 1.2 m
24 160 mm cable ducts in each one of them
Filled with copper wires, 30 % filling factor.
< 0.01 μSv/h in klystron gallery
ESS-0008382

## Slide 28: Summary
List of items covered:
  Earth berm shielding – optimized for radiation workers as well as public during normal operations as well as accident defined in accelerator scope!
  Shielding towards the klystron gallery.
  RF waveguide penetrations.
  Cable penetrations.
  Emergency exits.
  Smoke evacuations.
  Alignment penetrations.
  HEBT loading bay.
  A2T shielding alternatives.
  Skyshine.
  Cryogenic transfer line.
List of ongoing shielding activities:
  Front End Building shielding (RFQ/MEBT/DTL) – by R. Bevilacqua – due by mid-May, 2014.
  Running linac shielding simulations for realistic linac geometry due by May, 2014.
  Verifying that 5 meters of earth berm is enough for the worst DBA.
List of future activities:
  Revisit A2T shielding.
  Complete neutron-induced activity calculations for accelerator.

## Slide 29: Review/approval process
Review by Gunter Muhrer (internal expert)
Studsvik (external)
Review by SAG
Approval by SAG
SAG – safety advisory group

## Slide 30: References
[1] A.H. Sullivan, “A Guide to Radiation and Radioactivity Levels Near High Energy Particle Accelerators”, Nuclear Technology Publishing, 1992.
[2] Proceedings of the 7th ICFA Mini-Workshop on High Intensity High Brightness Hadron Beams, Wisconsin, USA, 1999, edited by N. Mokhov and W. Chou.
[3] A. Fertman et al., Nucl. Instrum. Methods Phys. Res., Sect. B 260, 579, 2007.
[4] I. Strasik et al., Nucl. Instrum. Methods Phys. Res., Sect. B 266, 3443, 2008.
[5] I. Strasik, E. Mustafin, T. Seidl , and M. Pavlovic, Nucl. instrum. Methods Phys. Res., Sect. B 268, 573, 2010.
[6] I. Strasik et al., Nuclear Technology 168, 643, 2009.
[7] E. Kozlova et al., Nuclear Technology 168, 747, 2009.
[8] J. Alonso, “Beam Loss Working Group Report”, 7th ICFA, Lake Como, Wisconsin, 1999.
[9] R. Santoro, J. Johnson, and J. Drishler, “Dose rate inside the SNS linac tunnel from activation of the magnet copper conductor and the concrete wall”, SNS Technical Note SNS/TSR-0130
[10] M. Fikani, “Activation Dose Rates in the Accelerator Tunnel”, APT memo PPO-TPO-mem-01551, November 1998.
[11] I. Strasik et al., Phys. Rev. ST AB 13, 2010.
[12] O. E. Krivosheev and N. V. Mokhov, Proceedings of the 7th ICFA Mini-Workshop on High Intensity High Brightness Hadron Beams, Wisconsin, USA, 1999, p. 85.
[13] R. M. Ronningen, G. Bollen, and I. Remec, Trans, An, Byck, Sic. J. 99, 597, 2008.
[14] R. M. Ronningen, G. Bollen, and I. Remec, Nuclear Technology 168, 670, 2009.

## Slide 31: References
[15] U.S. Department of Energy, DOE Standard: DOE-STD-1098-99 Radiological Control, 2004.
[16] A.I. Drozhdin, O.E. Krivosheev and N.V. Mokhov, “Beam Loss, Collimation and Shielding at the Fermilab Proton Driver” , FERMILAB-FN-693, July 2000.
[17] O. E. Krivosheev and N.V. Mokhkov, “Tolerable Beam Loss at High-Intensity Proton Machines”, FERMILAB-Conf-00/192, August 2000.
[18] R.A. Hardekopf, “Beam Loss and Activation at LANSCE and SNS”, LA-UR-99-6825, Los Alamos National Laboratory, September 1999.
[19] M. Palm, Kerntechnik 67, 8, 2002.
[20] T. Hansson, “Supervised Area versus 3rd Safety Barrier”, ESS-0001786, 2012.
[21] T. Hansson, “ESS Radiation Protection Strategy for Employees”, ESS-0003520, 2013.
[22] C. T. Kelsey IV and M. J. Baumgartner, “Lansce Design Basis Beam Spill Accident”, ICANS XIX, 2010.
[23] R.A. Hardekopf, “Beam Loss and Activation at LANSCE and SNS”, LA-UR-99-6825, Los Alamos National Laboratory, September 1999.
[24] R. Santoro, J. Johnson, and J. Drishler, “Dose rate inside the SNS linac tunnel from activation of the magnet copper conductor and the concrete wall”, SNS Technical Note SNS/TSR-0130, 3/99.
[25] J. Alonso, “Beam Loss Working Group Report”, 7th ICFA, Lake Como, Wisconsin, 1999.
[26] M. Fikani, “Activation Dose Rates in the Accelerator Tunnel - 2”, APT memo PPO-TPO-mem-01551, 11/98.

## Slide 32: Thank you