## Slide 1: ESS STRATEGY for supply of chopper systems to NSS project Science directorate Instrument technologies division Neutron chopper group leader --- DRAFT ----
“ Strategy, the human attempt to get to desirable ends with available means".
Max McKeown
V 4.1

## Slide 2: Objectives
The strategies objectives are aligned those of the NSS project, the ESS project and the facilities operating requirements.
The primary goals of can briefly be stated as;
To supply of chopper systems, which enables the world leading performance of instruments in neutronic terms at acceptable cost and within schedule.
To supply and support of chopper systems, which enable the achievement of the facilities objectives in terms of quality service to the scientific community
  (ie: high instrument availability and low operating costs)

## Slide 3: Drivers
Raising Performance
  Neutronic performance
  Availability
Reducing Costs
  Procurement
  Operations
In-kind
  Harness experience
  Maximise in-kind potential
  Equitable distribution

## Slide 4: ESS Instrument suite
Notes: Baseline dimensions for target monolith, R6m
Baseline design of instrument halls
Reference suite of instrument from TDR
Operation considered during normal operation
  225 Scheduled days at nominal power (5MW)
Beam lines were operationally independent when separated by 1.4m of lateral shielding
The reference suite represents a vision of a suite of instruments designed to meet the communities needs.
It is a working assumption of the types and balance of instruments which the community will themselves choose and is used for engineering studies preparing for construction.

## Slide 5: Spallation source instruments
PHOTO ISIS Instrument
- overlay schematic components
CHOPPER 3
CHOPPER 1
CHOPPER 2
NEUTRON OPTICS
- GUIDE
NEUTRON OPTICS
- POLARIZER
NEUTRON OPTICS
- COLLIMATION
DETECTOR
-ARRAY
DETECTOR
-BEAM MONITOR
DETECTOR
-BEAM MONITOR
FLIGHT TANK
BEAM LINE SHIELDING
SAMPLE
ENVIRONMENT
DETECTOR
-BEAM MONITOR
NEUTRON OPTICS
- IN MONOLITH GUIDE
BEAM SHUTTER
-LIGHT
BEAM SHUTTER
-HEAVY
Instrument
Shielding
Choppers
Sample area
Detectors
Control systems
Optics

## Slide 6: An new approach to the engineering of instruments …
The Facility as a whole does not benefit from a purely ‘case by case’ approach to designing or building instruments.
  Potential for commonality and synergies are lost
  Procurement advantages of scale are lost
  Scientific and engineering effort is duplicated redesigning a solution the same requirements again and again
The facilities goals of performance, cost and quality and maximizing in-kind potential are more successful addressed by ensuring a degree of standardization of approach and equipment on an ‘Instrument suite wide basis’.
  Though the establishment of Equipment standards, and design guidelines
  The coordination of technology development & procurement through technical groups
  Though ensuring an optimal match to build partners and a maximal use of in-kind potential.
Cake - Cross cut approach
Cake - traditional approach

## Slide 7: CROSS CUT APPROACH ‘5 tools’
Systems thinking, modular design.
Targeted development
Component standardization & interchangeability
Full cost & full cycle
Coordinated procurement

## Slide 8: The ‘cross cut’ Benefits
Benefits
Maximize instrument performance by considering the needs of the instrument suite and that of the facility globally and not case by case.
Increase the effectiveness of collaborations by matching partner competence and capacity to equipment needs.
Reduce development costs by avoiding duplication of effort and sharing equipment across several instruments
Ensure high serviceability to achieve highest standard of support to instruments in operation.

## Slide 9: Chopper Interfaces & Stake holders
DMSC
Servo Control
Electronics & Parameters
Control box
Software
(device driver)
Motion control
Software
Control Network
HW / SW
Electronic
Hardware &
Middleware
Instrument
control Software
ICS
E &E Group
Control
Box
Chopper
Hi level Control algorithms
Communication
protocols
Data acquisition
Software
Chopper Integrated Slow motion
Control
Facility
Instrument specific components
Instrument specific installations
Instrument # 22
Instrument specific control parameters
Instrument #2
Instrument availability
Machine Protection Systems
Personnel Safety
Systems
Timing
signals
Instrument #1
Health &
Safety
Safe working
practices
Containment
Contamination
Detectors
Optics &
Shielding
Guide-Chopper Interface
Alignment
Neutron optics
Vacuum systems
Crane access & capacity
Chopper
Control
HW/SW
Chopper
Support
Systems
Building Services
Cooling /
heat recovery
Electrical Power & UPS
Ventilation
Integrated
Beamline
shielding
Sample
Environment
Operating schedule
Target
Monolith / instrument interface
Chopper
Mechanic
systems
Time stamping
Data Veto
Neutron Chopper Systems
Notes: In fact if you just try to identify the primary stakeholders and proximate issues concerning choppers you come up with something like this
I think you will agree it’s quiet a bundle
Establishing interfaces and tying up the loose end is currently proving quiet a challenge
But it’s a vital building block to enable the design and operation of instruments
Lets look at just one of these interfaces …

## Slide 10: THINK ‘SUITE’
Identify the common requirements
Explore solutions which can meet ‘sub sets’ of requirements.
Exploit Synergy across instruments.
Consider global issues – crane access, shutter placement …
Consider facilities requirements of Serviceability, maintainability, instrument availability, and life cycle cost effectiveness…
Handle ‘boundary issues’
Handle interfaces between systems generically (across the board)

## Slide 11: DESIGN
Coordinated design
Avoid duplication of effort
Common interfaces facilitating integration
Promote standardization where beneficial
Mitigate technical risk & development costs
Modular design
Component platforms
Reduces the cost of optimization
Increases serviceability (reliability
Reduces procurement costs
Reduced spares costs

## Slide 12: Coherent Equipment placement & packaging
INSTRUMENT 01
<-------------- 15 degree ------------- >
INSTRUMENT 03
< 5 degree >
INSTRUMENT 02
TARGET MONOLITH
F : Curved guide
& Light shutter
Chart: Installed Equipment
| Black | Purple | Red | Orange | Green
A-B | 1 | 0 | 0 | 0 | 0
C-D | 0.066116 | 0.2314 | 0.1686 | 0.25289 | 0.28099
E | 0.45455 | 0.033058 | 0.049587 | 0.19008 | 0.27273
F | 1 | 0 | 0 | 0 | 0

## Slide 13: Coherent policies on common issues Access , Interfaces , RAS
  ABOVE ONLY!
  CHOPPERs ABOVE GUIDE
  CHOPPERS DECOUPLED FROM GUIDES
  ADVANTAGES
  Does not requires side access for removal
  Chopper Extraction from TOP
  Fastest intervention time
  Small sideways footprint
  DISADVANTAGES
  Long support path for choppers
  Large vertical footprint
    More complicated shielding?
ACCESS & REMOVAL
> ICDs & GUIDELINES for Instruments
Notes: What ever measures are made to improve equipment reliability
one issue that we must take concrete action on is to ensure the best access to it possible.

## Slide 14: STANDARDS & COMMONALITY
Common approach
  Standardise where it makes sense …
  else facilitate optimisation
High level
  Component platforms
Standardised interfaces
  Mechanical
  Electrical
  Control

## Slide 15
Common component platforms
6 ‘platforms’
LOW
SPEED
PA-02 (-M-14)
INTERMEDIATE
SPEED
PA-02 (-M-14)
HIGH
SPEED
2PA-02 (UO)
LARGE
ROTOR
2PA-02 (FTF)
FAN
PPSc
PA-10 (PPSc)
Notes: Average choppers 7.5
Which 22 inst 150 -160 axis
By configuration, performance and requirements can be sub divided into 6 broad families
Small rotored disc chopper
Low / intermediate / high speed
Large rotored choppers

## Slide 16: Platform
Within each platform….
A common mechanical & control architecture.
Motor & Drive
Rotor fixation
Support structures
Support systems
Control commands (?)
Monitoring system
MPS & PPS functions

## Slide 17: CONTROL SYSTEM
NCG / E&E / DMSC
NCG / E& E / Integrated Control Systems
NCG / E & E Group
NCG & SUPPLIER

## Slide 18: ELECTRICAL

## Slide 19: Interfaces: Chopper-Optics-Shielding
Key Objectives
  Highest neutronic performance for instruments
  Low back ground @ Detector
  Highest instruments availability
  Lowest lifetime costs
Input to instrument construction projects
  Interface definitions
    Chopper-Optics
  Guidelines for design
    Installation
    Access / Serviceability
    Integration of shielding
  Policies
    Alignment /Vacuum /Access /Activation
  Equipment standards for procurement
Common housing strategies
Vertical split
Guide removed with Choppers
Horizontal split
Guide remains in lower housing
Notes: Very obvious and real interface Choppers / Guides
With the increased complexity of ESS choppers systems the number of these interfaces is increased
Intergration
with guides
with shielding
Ensuring serviceability within shielding…
The list goes on…
The result of this effort will be condensed into a number of documents – many in the form of guidelines for instruments
Its important to the design of each instrument
But equally to the operation of the instrument as a whole
We do …. so you do not have to.

## Slide 20: Full cost & Full cycle
Procurement costs
  ‘Per unit cost’ is reduced through ‘economies of scale’ (-25%)
  Procurement process streamlined with grouped purchases of standardized equipment (-2%)
Design & Integration costs
  Reduces duplications of engineering effort developing solutions case by case for each instrument across the suite.(-5%)
  Reduces effort require to customize due to common Interfaces
Development cost
  Avoidance of duplication of engineering effort across suite of instruments (-5%)
  Common development shares effort / costs / risks across the suite of instruments and promotes formation of in-kind partnerships
Operational Costs
  Parts/ systems commonality Increases reliability, serviceability and availability (-2%)
  Reduced cost of parts stock and support personnel throughout the life of the facility
Chart: Full Cost
| Design | Procurement | Operation | Disposal
Sales | 15 | 50 | 25 | 10

## Slide 21: TARGETED DEVELOPMENT
Neutron Chopper
Technologies WP
PPS Chopper Technologies (PPSc)
Disc Chopper Technologies (DC)
Small Rotor
(DC-SR)
Large Rotor
(DC-LR)
Management
Conventional
Low Maintenance
Fermi Chopper Technologies
Facilities
Support Systems
Serviceability
Methods & Technologies
Service Tooling
Radiation hardness
Operations
1 & 2
Chopper Lab
Equipment standards
Pit systems
Vacuum
Cooling
Design standards
Rep Rate Multiplication
Wave frame Multiplication
Imperative for use of straight guides
Reliability
Availability
Serviceability
Infra-structure
Instrument performance issues
Facility performance Issues
Reducing facility operating costs
Notes: Chopper development work package is composed on a number of work unit each intended to address the principal issues in the field
On the left
Units related to Instrument performance
Development of technology which is vital to instruments and which is not available commercially
Long pulse requires a number of specific techniques to be employed
These in turn require specific solutions to be developed
RRM
WFM
Long pulse PPS systems
All these techniques are critical to harnessing the power of the long pulse and making instruments possible.
On the right
Units relating to facility issues
Measures to reduce operating costs
Ensure reliability and instrument availability
Infra-structure

## Slide 22: TARGETED DEVELOPMENT - PRIORITIES
Enable instruments requiring new tech
  DC-LR (Large rotor)
  PPSc ‘Long pulse’
Project driven
  DC-SR Low Speed (cost effective/enabling inkind)
  Handling systems (Access – Remote handling)
Notes: The facilities goals of performance, cost and quality are attained by the retaining of high level control over design and procurement parameters and the selection of equipment on and ‘Instrument suite wide basis’.
Establish Standards, Guidelines
Manage development & procurement through technical groups via the delegation of instrument work units.
An optimal match to build partners and a maximal use of in-kind potential.
Facility does not benefit from the ‘Fruit cake’ model of building instruments.
  Commonality is lost
  Cost advantages of scale are lost
  Duplication of effort

## Slide 23: Rotors (Disc Choppers)
Type 1 & 2
  Diameters 500 – 1000mm & 1000-2000m
  Collaborate with ISIS to develop a ‘simple & flexible’ cost effective solution (Aluminum) for low risk applications based on existing design.
  Identify partner for development for complex large diameter rotors if required
Type 3 (high performance)
  Use proprietary designs where possible. (Astrium / Mirrotron / Julich)
  Explore Partnership with TUM for development of CFRP rotor if/as required

## Slide 24: Support systems
Pit systems / Vacuum / Cooling / etc
  Highly Standardised systems with strong integration to facility systems & instruments
  In-house design is required to ensure good integration compliance with standards and commonality to reduce costs and ensure quality.
The potential for grouped equipment procurement through in-kind partners.

## Slide 25: Potential partners for development identified to date…
Chopper Type | Supply Quantity | Potential Partners ? | Development required
(P1) Low speed Disc chopper | 50 -70 | ESS – ISIS – SKF Spain Mirrotron | ***
(P2) Intermediate speed Disc chopper | 15 -35 | SKF / Mirrotron / Astrium / FZJ | *
(P3) High speed Disc chopper | 25 - 30 | FZJ / TUM / Astrium | **
(P4) Large rotor Disc chopper | 30 | ESS – ISIS collaboration | ****
(P5) Fan chopper | 3 - 5 | FZJ / JCNS + ESS ? | ***
(P6) Prompt pulse Suppression chopper | 4 - 10 | ESS – ISIS - SKF collaboration | *****

## Slide 26: SUPPLYING THE NEED …
Preliminary estimations

## Slide 27: Procurement - Some options : for ‘standard’ systems
SYSTEMS INTERGRATORS
TECHNOLOGY PROVIDERS
SYSTEMS
Notes: Despite the fact that ESS unique many of the systems may be constructed for existing industry standard or ‘near standard’ components
Typical disc choppers / fermi
Commercial suppliers

## Slide 28: Procurement options - some ideas for ‘long pulse specific’ systems ?
SYSTEMS INTERGRATORS
Notes: ESS unique requirements
Unique Long pulse will require some equally unique solutions
Special PPSc choppers adapted to the long pulse and higher energies
Completely unique large rotor choppers
Diameters 2 or more meters
Critical to employing the WFM and (RRM ?) techniques an harnessing the potential of the long pulse
No european commercial suppliers for complete systems
Current spallation sources design own
Suppliers of critical subsystems are known and we propose to work with them in much the same manner

## Slide 29: COORDINATED PROCUREMENT
Harness the existing technical competences and capacities of in-kind build partners
Increase efficiency and quality through matching work packages to partners with requisite competences. (Harnessing partner strengths)
Maximize in-kind though commonality and procurement flexibility via ownership of IP rights (Layer cake model)
Share development risk equitably with build partners through co-development with experienced in-house groups.
Prefer partners with which IP generated can be shared and an agreement to share with the community.
Employ own IP to generate additional ‘flexible’ in-kind potential through the manufacture of ‘co-developed choppers’ with other partner countries to increase engagement.

## Slide 30: Procurement process - for ‘Long pulse specific’ systems
ESS Instrument Neutron Chopper systems
Standard
Systems
Standardised Components
Standardised design
Custom
Systems
One - Off or
Very High Performance
ESS Instrument Neutron Chopper systems
Standard
Systems
Standardised Components
Standardised design
Custom
Systems
One - Off or
Very High Performance
ESS Instrument Neutron Chopper systems
Standard
Systems
Standardised Components
Standardised design
Custom
Systems
One - Off or
Very High Performance
REQUIREMENTS
SPECIFICATION
& STANDARDS
DESIGN
PROTOTYPING
SUPPLY
INTEGRATION
ESS
IN-KIND Potential ?
Commercial
Expertise
ESS Led ‘Inter-facility’ collaboration
ESS Led ‘Inter-facility’ collaboration
ESS
IN-KIND Potential ?
Commercial
Components
DC-LR
PPSc
Instruments projects
ESS

## Slide 31
Development & Build partners the discussion is open …
LOW
SPEED
INTERMEDIATE
SPEED
HIGH
SPEED
LARGE
ROTOR
FAN
PPSc
POSSIBLE BUILD PARTNERS ?
BUILD PARTNER ‘F’
BUILD PARTNER ‘C+G’
BUILD PARTNER ‘B’
BUILD PARTNERS ‘A+H’
BUILD PARTNER ‘E’
BUILD PARTNER ‘D’

## Slide 32: Chopper system breakdown
Neutron Chopper System
Mechanical systems
Control systems
Support systems
Pit systems
Chopper 1-2 Low speed
Chopper 3-4 Low speed
Rack & Cabling
Control Hardware
Software
Vacuum
Power supply
Cooling
Monitoring
Pit 1 module
Pit 2 module
Extraction tooling
Service pack
Tooling
Critical Spares
Chopper 5 PPsc
Chopper 6–7 Hi-Speed
Procurement value ~70 % of total
Procurement value ~10%
Predominantly generic systems
Procurement value ~20%
Predominantly Instrument specific
Notes: The facilities goals of performance, cost and quality are attained by the retaining of high level control over design and procurement parameters and the selection of equipment on and ‘Instrument suite wide basis’.
Establish Standards, Guidelines
Manage development & procurement through technical groups via the delegation of instrument work units.
An optimal match to build partners and a maximal use of in-kind potential.
Facility does not benefit from the ‘Fruit cake’ model of building instruments.
  Commonality is lost
  Cost advantages of scale are lost
  Duplication of effort

## Slide 33
 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028
Operations Schedule |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
#1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
#2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
#3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
#4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
#5 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
#6 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
#7 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
#8 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
#9 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
#10 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
#11 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
#12 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
#13 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
#14 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
#15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
#16 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Initial Design | Final Design | Procurement & Fabrication | Construction | Installation | Cold Commissioning | Hot Commissioning
1st Neutrons
Instrument projects overview

## Slide 34: Chopper & Instruments The ‘first 3’
Initial Design | Final Design | Procurement & Fabrication | Construction | Installation | Cold Commissioning | Hot Commissioning
1st Neutrons
On site Installation
Delivery, Integration & Test
Procurement
Development
Commissioning Interventions
Target Operations Schedule |  |  |  |  |  | 
#1
#2
#3
T-60m T-48m T-36m T-24m T-12m T0

## Slide 35: THE END
Thank you for you attention