## Slide 1: Beam Instrumentation mini-workshop Conclusions from the Hardware, Timing and MPS mini-workshop Lund, 2012-03-20
Miha Reščič
Deputy Head of ICS @ European Spallation Source
Cosylab

## Slide 2: Introduction
Integrated Control System
Control Box
HW Platform Discussion
Timing Discussion
MPS Discussion
Summary

## Slide 3: Integrated Control System
Design Update -> Accelerator -> Accelerator Science -> Controls
Preparation To Build -> ICS XFunctional task force
@ Accelerator, Target & Instruments level
Construction -> Integrated Control System
-> Accelerator
-> Target
-> Instruments
…

## Slide 4: Control Box, purpose
1. Allow independent but standardized subsystem controls development
2. Encourage and enforce consistency between sub-systems
3. Facilitate new component testing (e.g. EPICS drivers)
4. Allow factory acceptance testing of subsystems through the control system
5. Validate technology decisions
6. Mediate early risk reduction, to prevent unexpected surprises at project integration time
7. Force the controls group to make and document early decisions

## Slide 5: Control Box, schematic

## Slide 6: Hardware Platform Decisions
  cPCIe is the prototyping platform for applications that do not require extensive synchronization over the backplane
  uTCA "for physics" (MTCA.4) is the prototyping platform for applications that do require the above.
  cPCIe is the PRIMARY platform choice, uTCA is the platform for solutions that CANNOT run in cPCIe
  The OS running on both crates is Linux
  ICS is responsible to provide and support Control Boxes running Linux, EPICS and the Timing system for both crates
  The platform provides remote firmware update possibilities

## Slide 7: HW Decision support
  Standardization
    Definition of the backplane (e.g. ATCA having multiple substandards)
    Vendor support and availability (e.g. low number of vendors for PXI (excluding cPCI(!) solutions))
  EPICS integration
    Driver availability for Linux
  Backplane limitations
    maximum number of available slots
    synchronization and inter-communication
    bandwidth (supports the 'express' choice)
  Robustness of mechanical deployment
    RTM (rear transition module), no 'front panel brick'o'lage'
    RTM analog support (shielding of the signals)
    [more info in Hooman's presentation]

## Slide 8: Hardware Action Items
  Look into the possible solutions of HW interfaces between EPICS and other OS/CS solutions (LabView)
  The ICS should make a "shopping" list (ITER CODAC model) of supported crates, cards, cpu units, etc ...
  Research the (DESY, SLAC ...) uTCA drivers and Linux support for the various cards and other HW
  Research on the redundancy front (PS, fans, online health-checks, hot-swaps, MTBF, 'predictability‘ of failures, failure identification and time to repair
  Get more information on the DESY uTCA possible in-kind contribution

## Slide 9: Timing System Decisions
  Primary prototyping transport layer is MRF
  Primary prototyping HW platform is cPCIe (secondary is uTCA)
  Current required accuracy is 1 ns (precision of the timestamp, jitter of the clock)
  Currently there is no need for a BI-directional Timing transport layer
  Instruments use the same timing transport layer as Accelerator and Target
  The timing master generates '14Hz' phase locked to the clock signal from MO
  Timing system prototype architecture allows change of transport layer in the future
  Decision support
    Availability and performance of the transport layer (WR, NI1588, custom)
    HW platform discussion and decisions

## Slide 10: Timing Action Items
  Find correlation between 14Hz and 352.21MHz in the scope of the event table (event granularity; n*RF, n=?)
  Research the possibility of timestamping with pulse sequential number (RF counts, ticks from princess visiting)
  Look into supercycles concepts, pulse structure and commissioning pulse ramping
  Look into the different modes of operation (e.g. running the machine with insertion devices)
  Write requirements document for ESS Timing (based on SNS requirements (strip down SNS requirements to match ESS))
  Start defining event table (and iterate with stakeholders), static and dynamic
  Look into the integration between the post-mortem data acquisition (and analysis) and MPS, Timing and CS
  Integration of Control Boxes with Timing receivers and the neutron guide choppers (infrastructure)
  Build a functioning timing system prototype
  Research the local mode operation in case of master timing link failure, loss-of-link, loss-of-signal

## Slide 11: MPS System Decisions
  Two MPS requests defined: Fast Abort (intra-pulse), Beam Permit (inter-pulse)
  Currently, Fast Abort pulls the Beam Permit
  Currently, the interface to MPS system is binary (e.g. 1/0, ok/nok) and fail(2)safe
  MPS response time is a function of energy
  Beam Fast Abort should use redundant mitigation devices
  The MPS system timestamps all MPS input changes and all the nodes need to be synchronized with the same precision as the Timing system
  MPS supports different modes of operation (e.g. commissioning stages)
  Target upon failure pulls the Beam Permit (no Fast Abort)
  Target can take a hit from one pulse after pulling the Beam Permit Inhibit
  Instruments never provide any input into MPS

## Slide 12: MPS Action Items
  Identify possible mitigation devices and their speeds and redundancy (LEBT / MEBT chopper, dephase RFQ, source; listed in decreasing order of speed)
  MPS post-mortem support (implication for device integration (e.g. interfaces))
  Find the number and types of inputs to MPS or MPS nodes (order of magnitude) and their actions (FA, BP)
  Define responsibilities for tresholds for devices that trigger (input) MPS

## Slide 13: Summary
  cPCIe is the primary and uTCA is the secondary prototyping platform.
  The OS running on both crates is Linux and ICS is responsible to provide EPICS and the Timing system for both crates
  Primary prototyping transport layer is MRF and current required accuracy is 1 ns
  Timing system architecture allows the change of transport layer in the future
  Fast Abort and Beam permit MPS requests and a binary interface
  MPS supports different modes of operation

## Slide 14: Thank you!